## Slide 1: EarthScope’s Transportable Array
Seismic Instrumentation Technology Symposium
June 16-17, 2011
Albuquerque, NM
Bob Busby, TA Manager
Katrin Hafner, Chief of Operations
Frank Vernon, PI Array Network Facility
Bob Woodward, USArray Director
Key Technical Challenges in Large-Scale Temporary Networks

## Slide 2: Overview
Introduction to Transportable Array Operations
Highlight a few technical challenges
535A Dale TX
A typical operating TA Station

## Slide 3: The Transportable Array
Large scale - 450 broadband stations
Transient stations – network configuration changes daily
Large investment – high expectations
1,680 sites
19 sta / month
4.5 Gb / day
$10M / year
Red = current array location
Grey = stations already removed
2011 - 2013

## Slide 4: TA Performance
Network availability typically exceeds 98%
Station noise highly uniform and quite low for temporary installations

## Slide 5: Recent Enhancements
Adding pressure transducers to create a 400 station atmospheric acoustic (infrasound) network
Span frequency band from DC to 20 Hz
TA Station 345A, MS

## Slide 6: Pressure Sensor Response
Overlapping pass-bands provides continuous coverage from DC to 20 Hz
6
MEMS Barometer
EP - LDM
Setra Barometer
EP - LDO, EP - BDO
NCPA Infrasound Microphone
EP - LDF, EP - BDF

## Slide 7: O&M Future
1683 grid points to occupy at 19 per month
The next 3 years…

## Slide 8: Alaska 2013-2018
272 sites
85 km
grid

## Slide 9: Key Technical Challenges
TA applies concepts from manufacturing to high quality seismic station production.
Design process
Design verification
Acceptance testing of production elements
Defined procedures
Engineering Change Notices
Inventory tracking / Maintenance database
Quality Assessment of product
http://www.passcal.nmt.edu/taweb

## Slide 10: Key Technical Challenges
Some Specific Topics - the challenge
  The Station Building Process, information management
  Cellular Communications, swift evolution
  Station Power, conditioning and control
  Sensor emplacement , better horizontals

## Slide 11: Design Principles of Station
Solar Powered to avoid cultural noise sources, maximize siting opportunities, avoid line surges.
compact footprint to ease siting.
Fast construction, uniform and modular.
Good quality long period data.

## Slide 12: Station Design- tank vaults

## Slide 13: Station Design- tank vaults
RFP selected Freeman Engineered Products
for a custom rotomolded tank
$1200
105 kg

## Slide 14: Station Building Process
Reconnaissance- which may involve office evaluation, field visits, landowner interaction but ends with the selection of a Candidate Site-that is a site for which we will seek a permit. A document called a recon report, which includes the outline of how the specific station will be provisioned including power and communication strategy.
Permitting- meaning the negotiation with landowner, paperwork necessary to obtain written permission to access the property and to install a station. Permits and the expertise to acquire them increase in complexity from a simple private landowner agreement, through cooperative ownerships, corporate ownership to state or federally managed lands.
Construction- digging a hole, pouring concrete, trenching cables and erecting a mast. This task can be accomplished by a backhoe operator and a laborer assistant. While construction details are important for good quality data, the task itself does not require scientific expertise.
Installation- installation of electronics, power system, communication system and sensor. Generally ends with data communication back to ANF. This step involves detailed understanding of seismic instrumentation, communications and power electronics and requires at least one highly trained person on site.
Removal-removal of the station and tank and preparing the equipment for shipping.

## Slide 15: Well developed method
2005: >76 sites
  8 students
  Oregon State University
  Pilot Program
2006: 115 sites
  12 students
  4 Universities
2007: 156 sites
  20 students
  4 Universities
2008: 326 sites
  32 students
  10 Universities
  Enables backlog of permits
2009: 164 sites
  16 students
  5 Universities
2010: 131 sites
  12 students
  7 Universities
Recon Process

## Slide 16: Construction
… No Student Involvement

## Slide 17: Installation
Lava Cap Winery. Site layout
Vault Interface Enclosure, Cell modem, charge controller, Baler44, Barometer
View into vault. Sensor encased in sand, Q330 on shelf, foam insulation
Mast supports 80 W solar panel, GPS antenna, Cell omni directional antenna
VSAT located in barn with AC power
Sensor alignment, leveling and insulation
Takes 20 minutes
3-5 weeks later,
1 pickup, 2 people
Notes: 17

## Slide 18: Completed Installation

## Slide 19: Information Management
Recon: Students prepare, staff verifies a Reconnaissance Report.
Construction: formatted email report and photos placed on Flickr archive with tags.
Installation: formatted email report and photos placed on Flickr archive with tags.
Operation: database of station information-creates mseed dataless. Station service activities logged by formatted email reports, photos placed on Flickr archive with tags.
TA Flickr Archive has 72,000 photos

## Slide 20: Data Communications
Cellular Modem
AC VSAT
Solar VSAT
90% Cellular
8% AC VSAT
2% Solar VSAT

## Slide 21: Cell Modem Operation
Features
  Static IP address
  5 Gbyte/mo, continuous connection
    Real-time 0.9-1.4Gbyte
    SEED 400-800 Mbyte
  IP forwarding makes datalogger config simple
  Roaming issue at international borders
Management
  Monitor Seismic Data throughput & latency
  SNMP status, RRD
  Web based control
  Batch programming & firmware updates
Managing software updates of remote systems is tricky.
New Policies, features, and rapid obsolescence.
Sierra Wireless Raven X modems: 410 Verizon, 85 AT&T, 5 Sprint

## Slide 22: Web-based Monitoring
Identify changes and how they accumulate over time
  E.g., - in last 24 hours: number of reboots, number of IP changes, number of link cycles
E-mail Alerts: Some status changes result in an email alert to distribute more information immediately about the change: Pump active signal, Q330 reboot
http://anf.ucsd.edu/tools/webdlmon
Monitoring system renders data into actionable format
Information then feeds weekly management prioritization for all service activities

## Slide 23: Real-time QC Webdlmon
Cells can be selected to bring up an accumulated result view.
Round Robin Database is a recursive downsampling of mseed timeseries which enables us to efficiently form views of Last Hour, Day, Week, Month or Year.
Mass position of three elements for a year.
Vault temperature & station power supply for a month.

## Slide 24: Station Power
Independent regulation / distribution
Power control of comms device
Switching of backup power

## Slide 25: Device Integration
16x16x8” Enclosure, hangs inside vault.
    IP68, 0.5” Lexan Clear lid, bulletproof!
Q330 interfaces converted to industrial standard connections;
    IDC flat ribbon, RJ45.
Custom power regulation circuit
    Faultfree switchover to alkaline backup battery
    Signalling via existing data channels for power SOH
    Sensor power regulation, filtered power for Q330 and Baler
    High efficiency regulation, load shedding/mode switch on backup power
    Independent fault isolation of powered devices.
Station Integration
    Integration of Baler44CT, Environmental sensor
    Reset power cycle for comms equipment
    Remotely controlled power interrupt for sensor
    Monitor and signalling of pump operation
Protected housing for electronics and auxiliary equipment-allowing better flexibility and increased reliability.
    Allows economical packaging choices for small ancillary devices
    Protects commercial modems, charge controllers and circuit boards.
    Simplifies troubleshooting, acts as a field replacable unit.
Uniform cabling for installation
    MS style connectors, molded termination
Commercial production in large runs; Enclosure, cables, PCB, testing, etc
    Custom cable fabrication, custom metal, factory assembly and testing.
Vault Interface Enclosure (VIE)

## Slide 26: Sensor Performance

## Slide 27: Sensor Performance

## Slide 28
Noise PDF
Power Density Functions
TA Vertical
GSN Horizontal
TA Horizontal
GSN Vertical

## Slide 29: Pressure – Seismic Correlation
Pressure observations are strongly correlated to seismic data
Both vertical and horizontal seismic components
LDM - pressure
LHE- seismic
4 days
1000 s
100 s
10 s
Pressure – Seismic Coherence
Applications
Use pressure signal to reduce seismic noise
Use forcing function (pressure) and response (tilt) to constrain crustal properties

## Slide 30: Buried Sensors
Hole Characteristics
3-5m depth
<8” diameter hole
Minimal casing
Sensor Characteristics
Cylindrical-ish
Impervious to water
Remote unlock or unpark
Mating surface for alignment tool
Internal levelling
Toolik Lake LTER, North Slope Alaska
IMPROVE the performance of TA stations by using a shallow borehole deployment to reduce, we hope, the horizontal noise. The technique may also be more amenable to tundra or swamp setting in which the current vault is unwieldy (or impossible) and prone to leaking.

## Slide 31
TA Team

## Slide 32
400 station network operating at >98% availability
  Uniform, autonomous, low-power stations
  Careful evolution of station and process
Sensor emplacement
– an emerging technology?
Summary
EarthScope is funded by the National Science Foundation.
EarthScope is being constructed, operated, and maintained as a collaborative effort with UNAVCO, and IRIS, with contributions from the US Geological Survey, NASA and several other national and international organizations.
Info on the Web
EarthScope
  www.earthscope.org
USArray
  www.usarray.org
National Science Foundation
  www.nsf.gov

## Slide 34: 34 Team Members
Management: 2.0
Recon: 5
2.5 office
2.5 field team
Construction: 4
1 office
3 field crew
Installation: 4
4 field crew
Service: 4
4 field crew
Removal: 3
3 field crew
Support Facilities: 12
AOF NM Tech 6
ANF UCSD 6
Organization Summary
Notes: Split content slide example

## Slide 35: Information Management
Equipment Inventory - a database
Equipment maintenance records - a database
Site reconnaissance – files, FLICKR 65k photos
Landowner database
Software system trouble ticketing

## Slide 36
Design Principles Seismic Network

## Slide 37: Guralp SNOFLU
Sudden Noise Onset, Fixed by Lock / Unlock
  Sudden increase in LP noise, remains noisy for days-weeks until a Lock / Unlock
  Managed by vigilance. Guralp has no remedy so far.
Two nearby stations
Vertical channel, 1 day
Z30A on top, normal
Z31A bottom, SNOFLU
Spectra:
Red Z30A normal
Green Z31A SNOFLU

## Slide 38: Trillium Issue
Weeks long episodes of high horizontal noise levels
Occurs usually with high vault temperatures >27C
Correlates with Charge controller or Solar Insolation
X33A 60 days LHE, LHN and LHZ showing diurnal noise.

## Slide 39: Trillium Issue
Weeks long episodes of high horizontal noise levels
Occurs usually with high vault temperatures >27C
Correlates with Charge controller or Solar Insolation
Stations 633A, 634A and 635A showing effect at 634A(a trillium).
Note that there seems to be some effect at 635A which has an STS2.
633A is a trillium that does not have the effect.

## Slide 40: Amplitude Anomalies
Amplitude anomalies –overall 9 stations exhibit half amplitude on a channel
  Sudden decrease in single analog channel amplitude, reflected in all associated SEED channels-e.g. BHZ, LHZ, VHZ.
  Often fixed by remote calibration
  4 instances are due to a single datalogger.

## Slide 41: Accumulated views
IRIS DMC QUACK process creates PDF color power grid.
Signal Quality performance, catches rare cases…
http://crunch.iris.washington.edu/stationinfo/TA/ABTX/PDFMode/PDFMode-BHZ_colorgrid.png

## Slide 42: Webdlmon
Some changes accumulate over time to allow you to recognize it happened and how many times may be significant.
In Last 24 hours: number of reboots, number of IP changes, number of link cycles
http://anf.ucsd.edu/tools/webdlmon
EMAIL Alerts: Some status changes result in an email alert to distribute more information immediately about the change: Pump active signal, Q330 reboot.

## Slide 43: 440 Operating Stations
Geographical Status
Operating
Constructed
Permitted
Planned
Notes: Split content slide example

## Slide 44: Cell Modem Operation

## Slide 45: Status Capture
Q330 packets
  Last boot time
  Pump indicator
  Packet buffer queue
  330 firmware version
SNMP service
  Cell Radio signal strength
  Modem power
  Last reset
Structure of current values (pktmon -> JSON files)
A database record when certain values change; reboot time, Q330 firmware
Accumulate count of changes over a period; ip_address, link cycles
SOURCES of Status Information
CAPTURE Method of Status Information

## Slide 46: Coherence
Good coherence in overlapping portions of passbands