## Slide 1: Data Processing Workshop session 1: Fundamentals
Gary Pavlis

## Slide 2: Time series
What is a time series?
Why is this fundamental to seismology?

## Slide 3: Time Series Element 1: time
Seismic data always use a uniform sample rate, dt
Constant dt = uniform grid in time dimension
  Allows time to be computed, not stored t=t0+i*dt
  Requires t0 and dt be stored with the data or you have nothing
  This data model is reason Fourier methods are so ubiquitous in seismology
What is t0?
  Reflection seismology: t0=shot time
  Passive arrays like USArray = no such natural standard

## Slide 4: Passive Array Time
What is epoch time and why do we use it?
Answer
  Seconds since January 1, 1970 (this is t0)
  Ever try to compute time difference between 2003001:12:18:22.0 and 2006254:01:22:15.34
The sample rate is tightly controlled in digitizers
  Model 1: servo and dither time continuously claim fixed dt=target (data would have dt=0.05 s)
  Model 2: stay as close as possible and tag each block with computed sample rate (dt might be something like 0.0499215 s) using an external clock (GPS)

## Slide 5: OTHER TIME REFERENCES
Fixed time window slice (t0=window start)
Event origin time (ok, BUT)
  Teleseismic travel times times require many minutes of preevent noise
  Origin time is only an estimate, wrong for different solution
  Bottom line: no one uses origin time for sample 0
Arrival time reference
  Depends on concept of a seismic phase with a predictable arrival time
  Options:
    Set t0 at each station based on theoretical arrival time
    Set t0 at each station based on measured arrival time

## Slide 6: Example 1 of Abstraction
Abstraction means answering the “is a” question
Let’s look at a concrete example: SEISPP::BasicTimeSeries
http://geology.indiana.edu/pavlis/software/seispp/html/d7/dbb/classSEISPP_1_1BasicTimeSeries.html

## Slide 7: Amplitude: the other dimension Discussion/Quiz Session
What is an A to D converter and how does it work?
How is amplitude measured and what does it mean when people talk about 16 bit or 24 bit A/D converters?
What is dynamic range?
What do people mean when they refer to “counts”?
What does it take to go from counts to ground motion?

## Slide 8: Discrete sampling
http://en.wikipedia.org/wiki/File:Sampled.signal.svg

## Slide 9: Digitized signal
http://en.wikipedia.org/wiki/File:Digital.signal.svg
0
1 (001)
2 (010)
3 (011)
4 (100)
5 (101)
6 (110)
7 (111)

## Slide 10: Amplitude summary of key concepts
A/D converters ALWAYS measure amplitudes as (signed) integers
Velocity=counts*calib where calib is (m/s^2)/count
Calib=sensor gain*ADcalib
http://en.wikipedia.org/wiki/File:Digital.signal.svg
7 counts*820 nm/s/count=5740 nm/s

## Slide 11: Computer abstraction
Time series can be represented by a vector of data
  C: int d[200];
  C++: vector<float> d; d.reserve(200);
  Matlab: d=zeros(200,1);
  FORTRAN: real*8 d(200)
Time variable is implicit: time d(i) = t0+i*dt (C index)
d[i] (or d(i) in matlab or FORTRAN) is amplitude at sample number i
By convention vectors are stored in contiguous memory blocks (important for efficiency)

## Slide 12: Let’s look at some examples
Seismic Unix: SU/src/cwp/lib/xcor.c
SEISPP: AUG/contrib/lib/seismic/libseispp/correlation.cc
Java: http://boole.mines.edu/jtk/trunk/src/edu/mines/jtk/dsp/Recursive2ndOrderFilter.java

## Slide 13: The Rest of the Story
Headers: what does this mean and were did it come from?
Modern terminology: metadata
  Wikepedia: “Metadata (meta data, or sometimes metainformation) is "data about other data", of any sort in any media.”
  Synonym: “In computing, an attribute is a specification that defines a property of an object, element, or file.”
Examples?

## Slide 14: Let’s look at some formats
SEGY: pdf or handout
SAC: http://www.iris.edu/manuals/sac/manual.html
WARNING: segy and sac are “external representations” of seismic data. They are NOT a definition of seismic data. Key concepts independent of these implementations:
  t0 and dt are NOT metadata. They are required components of the data
  Some additional attributes (metadata) are almost always necessary to make data useable
  Formats usually create a fixed namespace of attributes that go with the data
  Databases are an alternative way to link data to other attributes
  SEISPP example of an internal representation: http://geology.indiana.edu/pavlis/software/seispp/html/d7/df8/classSEISPP_1_1TimeSeries.html

## Slide 15: Standard Earthquake Exchange Data (SEED) format
Many have (correctly) noted SEED is a 4-letter word
Much of SEED’s complexity is due to an extended definition of what “metadata” means compared to something like SAC
Miniseed
  Kinder, gentler SEED
  Bare-bones metadata
  Blockettes with compressed sample data

## Slide 16: Data gaps
Continuous data are never really continuous
Gaps occur from
  System failures (usually long)
  Telemetry systems dropping packets (short)
  Improperly corrected time tears (very short)
  Triggered data (mostly gaps)
How are they marked?
  System dependent
  Standard convention is + or – full scale int
Let’s look at an example

## Slide 17
Long data gap
Two shorter gaps

## Slide 18: Let’s look at some Data the hard way
Point your browser back to the SAC format page
Get the SEGY pdf or printed document
Get out “Exercise 1” handout