## Slide 2: What is the Advantage of Seismic Array Processing?
Seismic arrays are geographic distributions of matched seismic sensors whose data can be used to infer certain seismic wavefield properties
The spatial aperture of seismic arrays has traditionally been small in extent
There are a number of these small aperture seismic arrays around the world including two in Australia
Small aperture seismic arrays have been used to estimate the horizontal vector slowness of the impinging wavefield from a seismic event
Estimates of horizontal vector slowness can be used to provide approximate event locations using only data from a single array
Horizontal vector slowness estimates from multiple arrays have been used to refine event location estimates and, more importantly, to provide a means for estimating fault propagation characteristics for large events
Fault propagation models can be used to determine overall energy release and as a starting point for modeling Tsunami propagation
All of this can be done quickly using only the P-arrival part of the waveform, thereby supporting Tsunami Early Warning

## Slide 3: Alice Springs Seismic Array

## Slide 4: Warramunga Seismic Array

## Slide 5: USArray Transportable Array

## Slide 6: Array Processing 101
Consider a seismic wavefield from a P-arrival impinging upon a small aperture array
This seismic wavefield is planar which is a reasonable approximation for a wavefield across a small aperture array from a distant event

## Slide 7: Alice Springs Example

## Slide 8: Alice Springs Example

## Slide 9: Array Processing 101
Consider a seismic wavefield from a P-arrival impinging upon a small aperture array
This seismic wavefield is planar which is a reasonable approximation for a wavefield across a small aperture array from a distant event

## Slide 10
A planar wavefield like this produces a time shift to an otherwise approximately coherent seismogram at each station
If is the horizontal relative position vector between any two stations
And is the horizontal slowness vector of the impinging wavefield in sec/km
Then is the time it takes for the wavefield to propagate between the two stations
If we assume a value of , we can compute for each station relative to some reference station
We can apply the time shift to each station which should time align the waveforms if the value of corresponds to the actual wavefield value
All of the station waveforms can be summed together to produce a “beam”. This process is also known as “stacking”
We can repeat this “beamforming” procedure over a grid of values and look for the beam with the largest power, thereby inferring the value of for the wavefield; this process is known as seismic array processing

## Slide 11: Array Antenna Patterns
Seismic arrays behave in a manner similar to certain electromagnetic (RF) arrays; such electromagnetic arrays are sometimes referred to as “antennas”
RF antennas have directional focusing characteristics; similarly seismic arrays also have directional focusing characteristics
Antenna focusing gain patterns are common for RF antennas and can also be computed for seismic arrays; these antenna patterns show the array resolving power, for seismic arrays the ability to estimate , the wavefield horizontal slowness vector
Consider a periodic seismic wavefield of form
If we define antenna gain as the stack power average over a wave cycle we get
Where is the number of stations in the array and are the station horizontal positions relative to a reference station

## Slide 12: Alice Springs Antenna Pattern (1 hz)

## Slide 13: Warramunga Antenna Pattern (1 hz)

## Slide 14: Array Processing in Antelope
A new Antelope program, orbwfproc, has been developed that will provide real-time array processing capability
A pre-release version of orbwfproc is being tested at Geoscience Australia; the first production version will be available in the next Antelope release scheduled for Spring 2009

## Slide 16: What does orbwfproc do?
Import raw waveform data from real-time ORBs from one or more seismic arrays
Form pre-filtered “gathers” of waveform channels for each array into regularized channel-sample grids
Compute beams (stacks) over grids of horizontal vector slowness values assuming planar wavefield characteristics; this is done for each time sample over a grid of slowness values
Also compute power averages for each beam at each time sample (power of the stack) plus power averages for each of the individual array channels plus an average of the individual array channel powers (stack of the powers)
Also compute “semblance” by dividing the beam power averages by the stack of the individual channel power averages
Scan the semblance grids for the slowness vector that corresponds to maximum semblance for each time sample
Compute azimuth and scalar slowness corresponding to maximum semblance
Export beams as waveforms plus maximum semblance, azimuth and scalar slowness as waveforms plus the semblance grids themselves into ORB output packets

## Slide 17: What is semblance?
Semblance is the power of the stack divided by the stack of the powers
Semblance ranges from 1/n for completely uncorrelated noise across the array channels to 1 for a completely coherent signal across the array channels
Semblance is a normalized measure of array channel coherence
Semblance provides a size-independent single-array event detector

## Slide 20: Alice Springs Antenna Pattern (1 hz)

## Slide 21: Projecting slowness to event location

## Slide 22: Projecting slowness to event location

## Slide 23: Using large aperture arrays
380 LP USArray stations and plane wave stacking

## Slide 24: USArray Transportable Array

## Slide 25: Stacking to geographic grids
Consider defining relative time shifts of array channels using actual travel times to a grid of geographic coordinates
Removes plane wave approximation
Useful for large aperture arrays where the plane wave approximation is invalid
orbwfproc can do geographic grid stacking

## Slide 26: Stacking to geographic grids

## Slide 27: Future developments for orbwfproc
Semblance-based array detector
Grid refinement for more finely determined peak slowness and azimuth
Datascope version
Integration into event associator
Combining grids from multiple arrays in real time to produce forward source imaging in space and time