## Slide 1: Using MATLAB to Process and Analyze Seismograms
Bob Woodward
IRIS
USArray Short Course
Aug 15-19, 2011
Northwestern University

## Slide 2: The Basics
Data acquisition
Data file format
Reading data
Data preprocessing
Analysis
  Speed, speed, speed
The importance of sanity checks
  Use the plotting tools!
Results
  Use the plotting tools!

## Slide 3: Data Files
Data file formats
  SAC files are handy
  Other file formats
    See Chad’s talk tomorrow for info about reading miniSEED format directly
    With time and effort you can read any ASCII / binary file format
Data reading
  Use wildcarding of file names to subset the # of files that needs to be read?
  Typically make a pass to read headers
  Allocate memory for data
  Read data into one matrix
Gotcha
Byte order
Gotcha
S N C L
KNETWK, KCMPNM, KSTNM, KHOLE

## Slide 4: Prepping the Data
Organize data in matrix
  Seismograms down columns
    Fastest for working with single seismograms
    Facilitates using MATLAB functions
Use epochal time for all time-related arithmetic
Decimate as you go
  To minimize total memory required
Time series toolbox contains common filtering and tapering functions
Consider using the MATLAB “save” command to save a pre-processed (e.g., collated, decimated, etc.) copy of the data
  Can save significant time when doing large numbers of runs to explore other parameters or to debug
Gotcha
MATLAB epochal time different from UNIX

## Slide 5: Instrument Response
See Porritt’s routines from last year for some samples
General tips
  Stay below ~0.8 of the Nyquist
    Acausal rippling in the time domain
    Instability for deconvolution
Watch out if you are at very low frequencies
  Response is very small
Consider multiplying synthetic by response, rather than dividing data by response
  Not realistic in some situations
  Skip the full transfer function – just use sensor poles and zeros
    The “filter cascade” can generally be ignored
Gotcha
Response epochs
Gotcha
Matching PZ files to data

## Slide 6: Analysis
Typically, this is all about speed
  See “resources” section at end of slides
Rich built-in function environment
  Build your own functions for code re-use
Learn the IDE for coding efficiency
  M-Lint
  Cells
Use the simple plot commands to sanity check your results
  This is one of the key benefits of developing in MATLAB
  Debugging code
  Debugging algorithm
  Especially useful:
    “hist” to make a histogram of just about anything
    “plot” – time series and other continuous functions
    “scatter” – discrete x – y data points
Gotcha #1
Label those axes

## Slide 7: MATLAB Resources
MATLAB Central
  Functions for all types of calculations
  At the Mathworks web site
MatSeis – Sandia National Lab
  Seismic analysis and display package
  https://na22.nnsa.doe.gov/cgi-bin/prod/nemre/matseis.cgi
The Waveform Suite – Celso Reyes
  Seismic analysis and display
M_Map – R. Pawlowicz
  Mapping tools
  http://www.eos.ubc.ca/~rich/map.html

## Slide 8: MATLAB Resources
Libmseed – IRIS DMC (C. Trabant)
  Comprehensive library of miniSEED manipulation functions
  C code, with a MATLAB interface module
Splitlab – Wustefeld, et al (see web site)
  GUI environment for shear wave splitting measurements
matTaup – a MATLAB version of the TauP toolkit
Ttbox – travel time toolbox – M. Knapmeyer
Function library – Frederik Simons
Octave – Open source MATLAB alternative
Accelerating MATLAB
  Loren Shure’s blog on accelerating MATLAB
    http://blogs.mathworks.com/loren/2008/06/25/speeding-up-matlab-applications/
  Summary / tutorial on accelerating MATLAB
    http://www.math.ucla.edu/~getreuer/matopt.pdf