## Slide 1: Exercise 2
A Quick Look Analysis
Should We Be Interested?
Block
1
Block
5
Block
4
Block
3
Block
2
Block
8
Block
7
Block
6
Somewhereia
Bonanza Basin
Our company thinks the Bonanza Basin has a lot of hydrocarbon (HC) potential
Eight blocks are now available to place bids on
We need to do a quick analysis on this particular opportunity
Notes: Slide poses the question – should we be interested in the 8 blocks that just went up for sale?
The exercise is a quick look or feasibility analysis.
Do we think we have all five play elements in this area?
If one is very likely to be missing, e.g., no evidence for source, then there is no need to work further on this opportunity.

## Slide 2: A Quick-Look Evaluation
Block
1
Block
5
Block
4
Block
3
Block
2
Block
8
Block
7
Block
6
Somewhereia
Bonanza Basin
Exercise 2
  You have been asked to perform a quick ‘back-of-the-envelope’ evaluation of the blocks being offered in the Bonanza Basin, offshore Somewhereia. Is there enough potential that our company should take a serious look at this opportunity?
  Before management agrees to have a team work on the area for several months, they would like a quick look on how profitable these blocks might be. Thus, you have been commissioned to “test the waters.” With only a little time (about a week) and not much data, you are to make a recommendation on whether a more thorough evaluation (more people working for 5 months) is worth the effort.

## Slide 3: In-House & Public Data
Bonanza Basin
Somewhereia
Block
1
Block
5
Block
4
Block
3
Block
2
Block
8
Block
7
Block
6
Well A-1
A check of in-house and available literature reveals:
  A well (A-1) was drilled on the shelf, just updip from the open blocks
  Several seismic lines exist in the company files
Figure 1
Notes: A base map of readily available data. There is one well (A-1) in the area. There are 9 seismic traverses.
Not much data, but we have to work with what we have. Slide 5 will show the seismic line that goes near the well.

## Slide 4: Well A-1
Well information is sparse, but:
  There are good nearshore (beach) sandstones that would form a high- quality reservoir
  A good marine shale above the sandstone can be an adequate seal
  Source rocks that would generate oil lie deeper than the sandstones
  At the well, the source rocks are immature (not buried deeply enough to start generating HCs)
In summary, there is a potential reservoir, source, and seal.
The open blocks hold promise if:
1. The source is more deeply buried,
2. The sandstone unit extends far enough out into the basin, and
3. The sandstones maintain good porosity further out into the basin where
they are deeper
Figure 2
Notes: A synopsis of the well data that we have from a scout.
At the well location:
  A good nearshore (beach) sandstones – a possible reservoir
  A good marine shale above the sandstones – a possible seal
  Source rocks that would generate oil if “cooked” more

## Slide 5: A Seismic Line through the Well
The seismic indicates that for the open blocks:
1. The source (green) is more deeply buried,
2. The sandstones (yellow) may extend far enough out into the basin, and
3. The intervals thicken slightly out into the basin
Figure 3
Notes: The seismic line that goes very close to the A-1 well location
  The potential reservoir unit is colored yellow
  The potential source unit is colored green
  The potential seal unit is colored brown

## Slide 6: Structural Blocks
Figure 4
The well is on continental crust
The open blocks are on thinned continental to oceanic crust
Thus heat flow and temperature gradients should be higher for the open blocks
Well A-1
Notes: A map shows the thoughts about the crustal types and possible major faults (fracture zones) in the area. This interpretation could be based on satellite gravity data, not just the 9 seismic line ship tracts. This is an extensional (pull apart) margin, and we expect large extensional fault blocks that could provide traps.

## Slide 7: Depth to the Top of The Reservoir
Somewhereia
1.0
0.5
1.5
2.0
2.5
3.0
5.0
3.5
4.0
4.5
5.5
5.0
4.0
5.5
3.5
4.5
7.0
6.0
Well A-1
Figure 5
Take note of where the seismic lines and well log data are.
Much of this map is an extrapolation from the 9 seismic lines with depth data.
Notes: A quick map of the depth to the top of the potential reservoir unit. The interpretation is based on the well data (Well A-1) and 9 seismic lines (dashed white lines).
The contouring is based on very few lines (lots of extrapolation), so the confidence in the map is low – but it seems reasonable given the setting and limited data.

## Slide 8: Simple Model Results
Figure 6
If we assume that the source is 400 m below the reservoir everywhere, then where the source is at 3400 m, the top of the reservoir is at 3000 m (3400 m – 400 m)
Notes: Software that models basin subsidence, fill, and physical properties (depth, temperature, HC maturation, sandstone porosity) was used with the Well A-1 data as the source of input.
It has given us two relationships: HC generation as a function of depth and reservoir porosity as a function of depth.
Again, with limited data and time, the model has low confidence, but is good enough for our quick look.

## Slide 9: Tasks
Generate a map showing reservoir quality (porosity) over the open blocks (complete Figure 7)
Generate a map showing source maturity (where oil and gas are generated) over the open blocks (complete Figure 8)
Answer these three questions:
  Are there any blocks that look promising, that might have traps that could hold significant amounts of oil or gas? Which ones?
  Are there any blocks that hold very little potential? Which ones?
  Should our company form a team to do more evaluations?
    YES NO
Notes: This slide has the 3 steps that the exercise instructions take the students through. Refer to the SOLUTION file for answers.

## Slide 10: Exercise 2
Questions?