## Slide 1: Petroleum Geology & Geophysics
2. Introduction To Play Elements
Images Courtesy of ExxonMobil

## Slide 2: Methods for Finding Oil
Prospect based on Lady Luck
      I have this feeling…..
      I’ll drill here!
Which do you think would lead to the most success?
Play a Trend
      3 fields lie along a NE-SW trend
      I’ll drill to the NE of the known fields
Surface Anomalies
      There is a bump on the surface with a hydrocarbon (HC) seep
      I’ll drill on this hill
Subsurface Interpretation
      I’ll gain an understanding of the geology of this area
      Based on my learnings, I’ll drill into this trap
Notes: This lists four (4) possible methods for finding oil from the least to the most scientifically driven. Ask your students what they think the best method for finding oil would be. Hopefully, the students will answer the question that #4 will result in the most success.

## Slide 3: What We Need for Success
A Rube Goldberg View
of a Hydrocarbon System
A “Kitchen”
Where Organic
Material Is
Cooked
A “Container”
From Which
Oil & Gas
Can Be
Produced
“Plumbing” To Connect
the Container to the Kitchen
Correctly
Placed
Wells
Source
Migration
Reservoir
Trap
Seal
Notes: Rube Goldberg drew complicated contraptions to do simple tasks – like the board game Mouse Trap.
If I were to ask Rube “What do we need for success in finding HCs?” he might reply:
First thing you need is a kitchen...
Then you need a container...
Usually the kitchen and container are not connected, so you need plumbing...
Next you need to place the well in the right location
If you miss the container – a dry hole and no money
But if everything ‘works’ – you get oil out of the ground and money in the bank
This is actually anti-Rube Goldberg since it takes a complicated process and highly simplifies it
Being a bit more technical, we need:
  Source – rock rich in organic carbon that has the right temperature & pressure conditions so that the
  chemical kinetics transform organic matter into oil & gas molecules
  Reservoir rock with a trapping geometry capped by a sealing rock
  Migration pathways that allow the oil & gas molecules to move from the source to the trap on a geologic time scale
How many magenta words are on this slide? FIVE. These five (5) are called play elements.

## Slide 4: The Kitchen
Source
  Organic-Rich Rocks, usually shales
  Temperature & Pressure Conditions that Result in Oil & Gas Generation
A “Kitchen”
Where Organic
Material Is
Cooked
Notes: The kitchen is where organic matter dispersed within a source interval has undergone the temperature/pressure history necessary for oil and gas to be generated and expelled. Source intervals are organically rich. They are rated based on their organic content (TOC = total organic carbon) and its richness (HI = hydrogen index which controls oil vs. gas). Most source intervals are shales, the best source rocks were deposited under reducing conditions.

## Slide 5: The Container
Reservoir
  Porous & Permeable Rock Suitable for Production
  Most Commonly Sandstones & Carbonates
Trap
  3-D Configuration that “Pools” the Oil & Gas
  Structural and/or Stratigraphic Traps
Seal
  Rocks that Prevents Leakage from the Trap
  Most Commonly Shales and Evaporites
  Top Seals & Lateral Seals
A “Container”
From Which
Oil & Gas
Can Be
Produced
Notes: A reservoir is a rock with enough porosity (pore space) and permeability (connectiveness) that we can produce (pump) oil and gas out of it. Most reservoirs are in clastic units of sand-size or larger particles (sandstones, conglomerates) or in coarse carbonates (e.g., reefs).
A trap is a 3D configuration in the subsurface that allows oil/gas to pool in significant quantities. Traps resulting from faults or other structural features are called structural traps – they are the easiest to recognize. Traps resulting from the wedging out of a reservoir, either due to depositional thinning or post-depositional erosion, are called stratigraphic traps.
Seals are rock layers that prevent leakage of HCs from the trap. The most common seals are shales and evaporites. Top seal prevents leakage up through the top of a reservoir. To have a trap, we also need lateral seals so that HCs don’t leak out of the sides of a trap.

## Slide 6: The Plumbing
Migration
  From source (shales) to porous reservoirs
  Strata-Parallel Component (sand & silt layers)
  Cross-Strata Component (faults and/or fractures)
“Plumbing” To Connect
the Container to the Kitchen
Notes: Hydrocarbon (HC) migration is the process of moving droplets of oil and gas from the source to the reservoir. Buoyancy is the primary force that causes HC migration – gas is lighter than oil which is lighter than water/brine.
Primary migration is getting the HC out of the source interval. Secondary migration is moving the HC in carrier beds and up faults/fractures to the reservoir. Migration parallel to the depositional units occurs in sand and silt beds that serve as carrier beds.
Migration from one stratigraphic level to another is called cross-stratal migration. It commonly occurs via faults and fractures. Most cross-stratal migration is in an upward direction (buoyancy forces), but depending on pressure gradients HCs can move down into carrier beds.

## Slide 7: Petroleum System Elements
0
2
4
6
8
Depth (km)
Source
Reservoir
Trap & Seal
Migration
?
Gas & Oil
No More
HC Generation
Oil & Gas Generation
Window
Gas
Generation
Window

## Slide 8: Other Important Components
Timing
  Did the Trap form before HC Migration began?
Fill & Spill
  Has HC Generation Exceeded Trap Volume?
  Has there been Spillage from Trap to Trap?
  Where is the Oil?
Preservation
  Has Oil been Degraded in the Reservoir, by thermal cracking or biodegradation?
Notes: There are other elements to consider for the HC System.
Timing – did the trap exist when HC migration occurred? Obviously, if HC migration occurred before the trap existed, the trap will be empty or severely under-filled.
Fill & Spill – if the trap volume is small compared to the volume of generated HC, then the trap has been overfilled and excess HC has spilled. Since free gas displaces oil, an overfilled trap will probably hold gas and spill oil. The spilled oil could be trapped further up the overall migration pathway. We’ll see an example of this in the North Sea.
Preservation – if oil is trapped, there are conditions that can degrade the oil with time. If the reservoir gets too hot, the oil can be cooked (cracked) to gas. If the reservoir is shallow and cool, bacteria can feed off the oil and spoil (degrade) it.

## Slide 9: HC Fill & Spill
Trap A
Trap B
Synclinal
Spill Point
Fault Leak
Spill Point
1. Early Charge: Some Oil, Minor Gas
2. Peak Charge: Significant Oil, Some Gas
Gas Cap
Displaces Oil
Oil Spilled
from Trap A
to Trap B
Oil Spills
Up Fault
3. Late Charge: No Oil, Significant Gas
Notes: This slide illustrates some basic concepts about HC fill and spill.
Trap A is closest to the kitchen and will fill first. It has a synclinal spill point on the right. If Trap A fills down to the level of the synclinal spill point, any extra HC will cause some HCs to spill out of Trap A and continue up the migration pathway to Trap B. Note that Trap B has a fault leak point.
Early charge from an oil-prone source consists of oil with a minor amount of gas. Trap A starts to fill with oil and some dissolved gas.
As time passes, significant oil with a large proportion of gas reaches the trap. If there is more gas than can be dissolved in the oil, then a free gas cap forms. The gas cap will displace oil, so only oil (with some dissolved gas) will spill.
Eventually the source will become over-mature, only generating gas. If enough gas reaches Trap A, it will become entirely filled with gas – all the oil being displaced. Trap B now has a free gas cap and an oil leg, with oil spilling out of Trap B at the fault leak point. Perhaps there is a Trap C further up the migration path where oil spilled from Trap B is collecting.

## Slide 10: Using Play Elements
If we can:
Map where source rocks exist and have/are generating hydrocarbons
Determine where reservoir-quality rocks were deposited
Locate potential traps
Deduce that migration paths, timing, fill & spill and preservation all look favorable
Then we can:
Decide on which basins to focus on
Determine which blocks hold the greatest promise
Position wells to best evaluate prospects, plan the development of a discovery, or effectively deplete a field
Notes: Thus, if we can do the 4 bullet points, then we can (1) Decide… (2) Determine… (3) Position…

## Slide 11: Learn by Doing
Your Task:
  Decide if your company should go to the next stage – assign a team to work for ~5 months
Block
1
Block
5
Block
4
Block
3
Block
2
Block
8
Block
7
Block
6
Somewhereia
Bonanza Basin
Exercise 2
Given:
  Very basic information on the Bonanza Basin
  Initial results from a simple model of the effects of burial on source and reservoir
Notes: We have a homework exercise that illustrates how all of this can work. Let’s consider eight blocks up for bid in a fictitious basin, the Bonanza Basin. You will have a series of maps related to 4 of the play elements. For simplicity, we will say that we have a great seal everywhere.
Your task is to do a QUICK look and see if any of the 8 blocks are worth studying (spending money and people time to evaluate).
I’ll review what you have and what you need to do next, but first, any questions?

## Slide 12
Questions?