## Slide 1: Petroleum Geology & Geophysics
3. Tools of the Trade
Mega-Regional
Present Circulation
Plate Reconstructions
Maps showing Features
Local
Cores
Logs
Outcrops
Well-Seismic Ties
Images Courtesy of ExxonMobil

## Slide 2: Data Types Vary with Scale
From a basin-wide scale analysis to a field-depletion scale study, we want to integrate all available information from as many data sources as possible
Regional Analysis
Basin Analysis
Block Analysis
Prospect Analysis
Field Analysis
Compartment Analysis
Mega-Regional
Fine-Scale
Notes: Analysis in the petroleum industry goes from very broad scale (mega-regional) to very focused scales, like a compartment of a producing reservoir.

## Slide 3: Mega-Regional Data
Cen. to Maastrictian
• Maast. to Present
Open marine
Albian to Cenomanian
Aptian
Late Jurassic to Aptian
G
U
L
F
M
A
R
I
N
E
C
A
R
B
O
N
A
T
E
M
A
R
I
N
E
A
N
O
X
I
C
R
I
F
T
Geologic Maps
Plate Tectonics
Gravity & Magnetics
Regional Seismic Lines
Tectonic Evolution
Stratigraphic Charts
Paleogeographic Maps
Etc.
Mitchum et al., 1977b
AAPG©1977 reprinted with permission of the AAPG whose permission is required for further use.
Most Images Courtesy of ExxonMobil
Notes: Some examples of mega-regional data types.

## Slide 4: Mega-Regional Analysis
Usually mega-regional analyses are performed to:
  Decide which basins hold the highest potential for discovery & production of oil or natural gas
  Determine how much to bid for blocks that are open (or will be open) for lease
  Provide the regional setting of a basin or sub-basin to help understand the characteristics of the region
  To guide step-out wells, i.e. those that extend beyond a known field in search of a similar HC accumulation
Notes: Why does the petroleum industry use mega-regional data? (Note that HC stands for hydrocarbon.)

## Slide 5: Local Data - Surface
Measured
Sections
20 ft
Surface Measurements/Observations
  Topographic/Bathymetric maps
  Surface geology (structure & stratigraphy)
  Nearby outcrops (or analogs)
  Heat flow measurements
  HC seeps
  Etc.
Outcrop Studies
Images Courtesy of ExxonMobil
Notes: Now to more local data. What types of data and measurements can the petroleum industry get at the surface?

## Slide 6: Local Data - Subsurface
Subsurface Measurements/Observations
  Data from Wells
    cores, cuttings, logs
    lithology, ages, geochem, etc.
  Geophysical Data
    Seismic (2D, 3D, 4D)
    Gravity & Magnetics
Vibroseis – Seismic Sources
Logging a Well
Images Courtesy of ExxonMobil
Notes: With more localized data, what can the petroleum industry get from the subsurface? For instance, geological information when we drill wells and get data. Well data can provide subsurface rock data. We can also take measurements inside the well borehole (run a variety of logs).

## Slide 7: Data from Wells
Samples
  Conventional Cores
  Sidewall Cores
  Cuttings
Measurements
  Wire-line Logs
  Pressure
  Temperature
  Fluid samples
  Flow Properties
  Vertical Seismic Profiles (VSP)
We’ll look at well data in more detail in Unit 4
Notes: Three types of rock samples, with details to follow. Six types of measurements we can make in a well bore.

## Slide 8: Well Samples: Conventional Cores
Coring apparatus positioned at the bottom of the drill stem
Often gets intact samples of >1 meter
Good for analyzing lithology, sedimentary features, porosity, permeability, paleontology (ages, environments)
Interval is cored ‘blind,’ i.e., before the interval is logged
Expensive (2 round trips for the drill stem = lots of rig time)
Notes: Some details and a photo of a conventional core

## Slide 9: Well Samples: Sidewall Cores
Small samples (1 x 2.5 inches)
30 samples per run
Sampling based on logs
Stabilizer
Gun Body
Core Barrels
Step 1:
Gun in position
Step 2:
Shot fired
Step 3:
Core retrieved
Notes: This slide illustrates a sidewall core. On the left is the tool we lower in the hole, which shows a series of bullet-like core barrels. On the right, the steps to get a sidewall core sample are shown.

## Slide 10: Well Samples: Cuttings
The ‘rubble’ that comes up the sides of the well bore with the circulating fluid
Can provide samples for certain kinds of analysis, e.g., lithology, paleontology
Not suitable for porosity, permeability, sedimentary structures (rocks are pulverized)
Very inexpensive – no lost rig time
PROBLEM – no control on the depth from which the samples came from; could be from any zone not cased (enclosed by cement)
Notes: Well cuttings can give us some types of information, but not other types. This process is relatively inexpensive, however, the major problem is that there is no control on the depth from which the samples came from, and the samples could be from any zone not cased.

## Slide 11: Well Measurements: Wire-line Logs
A well log is a record of one or more physical measurements as a function of depth in a borehole
Gamma Ray
Density
Resistivity
Depth
Notes: This slide explains the definition a well log. On the left, the drum with wire to lower/raise logging tools is shown. Note that there is also an instrument hut for the operator. On the right is an example of the output – a well log. Three measurements are shown in the well log: 1) Gamma ray which detects natural radiation. For example, shales give higher values than silts or sands; 2) Resistivity, which is high for HC-bearing zones; and 3) Density of the rock formation (e.g., gm/cc).

## Slide 12: Examples of Logging Tools
Notes: A photo showing a variety of logging tools that are available. Each tool can be lowered into a borehole and take different measurements. Several tools will be hocked together to comprise one run – or trip. A drill rig is very expensive, about $1 million per day, so we want to minimize the time the drill rig is “down” during logging.

## Slide 13: What Logs Measure
Lithology/Mineralogy
Porosity
Fluid Type
Fluid Saturation
Permeability
Property
Stratigraphy
Downhole Pressure
Density
Acoustic Velocity
Notes: Here are some of the things a well log can measure, with respect to the properties of the formation(s).

## Slide 14: Geophysical Data
Objective:
Take measurements at the surface that give us an image of the subsurface
Analogy:
A sonogram
We’ll look at seismic data in more detail in Unit 5
Notes: We can also use geophysical methods to provide images of the subsurface without drilling a well. All of the equipment is operated at the surface. An analogy is a sonogram, which doctors use to get images inside the body. Sound energy is used to get the picture, like seeing a baby in the womb or your heart without being cut open.

## Slide 15: Seismic Data
Listening Devices
0 s

An Explosion!
0 s
Energy
Source
.1 s
.2 s
.3 s
Some Energy is Reflected
Most Energy is Transmitted
.4 s
.4 s
.5 s
Some Energy is Reflected
Most Energy is Transmitted
.6 s
.7 s
.8 s
.8 s
Notes: The main geophysical tool that petroleum geologists, geophysicists, and engineers use is seismic data and/or seismic profiles. Sound energy is generated at the surface by a Vibroseis truck for instance, and sound waves move down through the earth. Some energy is reflected off the rock layer boundaries and returns to the surface. We have listening devices to capture the reflected energy waves. The slide animation shows energy propagating down, being partly reflected at the two sediment boundaries.

## Slide 16: Raw Seismic Data
Device
#1
Device
#2
0.0
0.3
0.4
0.5
0.6
0.7
0.8
0.1
0.2
For the explosion we just considered ...
Listening device #1 records a reflection starting at 0.4 seconds
Listening device #2 records a reflection starting at 0.8 seconds
To image the subsurface, we use many shots (explosions)
and many receivers (listening devices) arranged in lines either on land or offshore
Time
Notes: This shows what the two listening devices would “hear” for the reflections illustrated on the previous slide. The two rock boundaries were detected at different times after the shot. This is highly simplified, but shows the basic science. We can build images of the subsurface by using many shots (explosions) and many receivers (listening devices) arranged in lines either on land or offshore.

## Slide 17: From Raw Data to an Image
Subsurface
‘Image’
Data Processing
Stream
Field Record
(marine)
Data Courtesy of TGS
Notes: This slide shows some raw data as obtained in the field (upper left). We process the data using super-computers, and obtain subsurface images that can be interpreted in terms of geology and HC possibilities. (Note that slides 14–17 are a preview of Unit 5.)

## Slide 18: Gravity & Magnetic Data
Instruments measure the local gravity and magnetic fields
Data are processed to highlight local anomalies (residual maps)
Bodies with anomalous density or magnetic susceptibility are modeled/interpreted
Bouguer Gravity Map
Total Magnetic Intensity
Maps Courtesy of ExxonMobil
Notes: Geophysical data can also include gravity and magnetic data. We measure the local gravity and magnetic fields either when we collect the seismic data or independently. These days, we can use gravity data obtained by satellites. The gravity and magnetic data can be processed such that we can get information about the subsurface.

## Slide 19: Back to the Bonanza Basin
Your Task:
  Use the play element maps to determine:
    Which blocks have favorable conditions
    Which blocks don’t have much hope
    Which blocks are in the ‘maybe’ category
Block
1
Block
5
Block
4
Block
3
Block
2
Block
8
Block
7
Block
6
Somewhereia
Bonanza Basin
Exercise 3
Given:
  A set of play element maps
  A piece of tracing paper
Notes: We are going to extend our work on the Bonanza Basin lease sale in Exercise 3. For exercise 3, we return to the fictitious Bonanza Basin. You (the student) will be working on play elements for the eight (8) blocks that are up for bid (an extension of Exercise 2). You will have a series of maps related to four of the five play elements. For simplicity, we will say that we have a great seal everywhere. Your task is to consider which, if any, blocks we should focus our evaluation on and if any blocks can be dropped from further consideration. The Exercise 3 introduction will get you started, but before we look at Exercise 3, any questions?

## Slide 20
Questions?