## Slide 1: Petroleum Geology & Geophysics
4. Well Data
Images Courtesy of ExxonMobil
Notes: This unit is on well log data. We will look at five (5) common logs. Each measures a specific parameter as a function of depth in the well.
We will work through the interpretation of a set of well log curves. Finally, we will talk about correlating surfaces using a series of well logs.

## Slide 2: Types of Well Data
Measurements
  Wire-line Logs
  Pressure
  Temperature
  Fluid samples
  Flow Properties
  Vertical Seismic Profiles (VSP)
Rock Samples from out of the hole
Instruments (tools) are lowered into the hole and record data
Samples
  Conventional Cores
  Sidewall Cores
  Cuttings
Notes: This slide defines the two (2) basic types of data we get from wells. First, we get actual rock (sediment) samples. Later, we will talk about cores and cuttings.
Then, we can get measurements by lowering instruments (referred to as tools) into the borehole and getting a variety of measurements. We’ll discuss five (5) of these tools later in this lecture.

## Slide 3: Well Samples: Conventional Cores
Source
Organic richness (TOC)
Organic quality (type, HI)
Thermal maturity
Age from microfossils
Seal
Lithology
Layering
Vert. Permeability (quality)
Age from microfossils
http://www.mbari.org/news/homepage/2005/sand-channelcores2-350.jpg
Alternating fine sand & silt
Well sorted sand
Clean pebbles & gravel
Reservoir
Lithology
Grain size & sorting
Sedimentary structures
Porosity & permeability
Age from microfossils
Environment of deposition
Notes: Our best data come from conventional cores. At a depth of interest, drilling stops, a core barrel (pipe) is pushed into the rocks at the base of the hole, and sediment is captured.
The figures show portions of three (3) such cores that captured different lithologies. The types of information we can get in terms of reservoir, source rocks, and seals are listed. The worst thing about cores is that it takes a lot of rig time and that means lots of money.

## Slide 4: Well Samples: Sidewall Cores
http://www.offshore-mag.com/content/os/en/articles/2012/04/otc-2012--baker-hughes-rotary-sidewall-coring-service/_jcr_content/leftcolumn/article/footerimage.img.jpg/1335534247106.jpg
Source
Organic richness (TOC)
Organic quality (type, HI)
Thermal maturity
Age from microfossils
Seal
Lithology
Layering
Vert. Permeability (quality)
Age from microfossils
Reservoir
Lithology
Grain size & sorting
Sedimentary structures
Porosity & permeability
Age from microfossils
Environment of deposition
Notes: Sidewall cores are less expensive, but we get very small samples. The process was shown on Slide 9, Lecture 3. You can think of a hollow bullet being fired into the side of a borehole. We recover a small plug of sediment, on the order of an inch in diameter. The impact can shatter the rock, destroying sedimentary structures and layering. We can get much of the data above from conventional cores; however, with some exceptions. The exceptions have been dimmed to a light blue in this slide.

## Slide 5: Well Samples: Cuttings
The rock fragments that come to the surface as a well is drilled
Similar to wood shavings produced by drilling into a piece of wood
http://www.geomore.com/well-samples/
http://phigblog.com/
PROBLEMS
  Rock is pulverized
  Very little control on the depth from which the samples came from
Gives indications of lithology and age
Notes: Cuttings are the “rock shavings” that come to the surface during drilling. An analog is the wood shavings that you get when you drill into a piece of wood.
Cuttings can be used to get indications of the rock type and geologic ages of the rock being cut.
There are two (2) main problems with cutting samples:
The rock is pulverized, so we can’t get many properties.
We don’t know the depth for the rock shavings. We can estimate the time it would take for a shaving to come up from depth (e.g., we might estimate that when we are drilling at 10,124 ft it would take X minutes for the material to get to the surface. Also, rock material can break loose at any depth shallower than the drill bit (cavings).
The good thing about cuttings are that they are very inexpensive to collect (bag) and analyze.

## Slide 6: Common Logs and What They Measure
Gamma Ray
Spontaneous Potential
Sonic
Density
Neutron
Resistivity
Nuclear Mag. Reson.
Photoelectric Effect
Wireline Testing
Well Test
Dipmeter
Borehole Image
Core
Lithology/Mineralogy
Porosity
Fluid Type
Fluid Saturation
Permeability
Stratigraphy
Downhole Pressure
Geophysical Properties
Log
Property
Courtesy of ExxonMobil
Notes: Let’s move on to well log measurements. The top of this chart lists some of the most common well log data, and along the left hand side, the property or use of the data. The red circles indicate major applications, while the smaller green circles represent secondary uses.

## Slide 7: Overview of Five Key Logs
Caliper – measures borehole size
Lithology Logs – differentiate sands
Porosity Logs – porosity & fluid types
Velocity Logs – relate well to seismic data
Resistivity Logs – Identify HC zones
Notes: We will briefly look at these five (5) types of key well logs.

## Slide 8: Borehole Size
Borehole size is set by the drill bit, but it is influenced by:
Changes in stress state
  borehole breakout
  induced fracturing
  creep of salt
Chemical Reactions
  swelling clays in shales
  dissolution of salt
Drilling Process
  spiral borehole
  bit marks
Courtesy of ExxonMobil
Notes: One important parameter to know is the size (diameter) of the well bore as a function of depth. Some logs need the tools to touch or be near the rock formations to get accurate measurements. Thus, if we know a certain portion of the well bore is much larger than average, we may need to correct or delete data from these zones.
The diameter of the drill bit is the primary control on hole size. Other factors that influence the size of the borehole include changes in stress state, borehole breakout, induced fracturing, salt creep, chemical reactions, swelling clays in shales, dissolution of salt, the drilling process itself, spiraling of the borehole, and bit marks.

## Slide 9: Caliper Logs
What Do They Measure?
Size and shape of a recently drilled hole
How Do They Work?
Mechanical arms record hole size
Hydraulic systems with calibrated potentiometers
How Are They Used?
Hole size used to correct other logs
Hole volume for amount of cement
Lithologic information
  washouts indicative of formation properties
Stress field from borehole break-out
Notes: This slide shows a diagram of a caliper log, which measures the size of the borehole. The caliper works by use of two (2) or more “arms” that are pushed out hydraulically so that they touch the sides of the bore hole. The hydraulic systems are calibrated to give us the hole size in inches or centimeters. This information is used to correct logs that are sensitive to hole size, determine how much cement is needed when casing (lining) the well, obtain some lithologic information (e.g., large diameter zones (washouts) indicate unconsolidated (loose) rocks), and determine stress fields from borehole break-outs.

## Slide 10: Lithology Logs
Gamma Ray
  a scintillation detector (similar to a Geiger counter) that measures the natural radiation from a formation
SP (spontaneous potential)
  a measurement vs depth of the potential difference between the voltage in the wellbore as a function of depth and an electrode on the surface
For both logs:
Deflections to the right = Shale
Deflections to the left = Sand
Shale
Sand
Sd
Gamma Ray
Shale
Baseline
Courtesy of ExxonMobil
Notes: We will introduce two logs commonly used to determine lithology: the Gamma Ray log and the spontaneous potential (SP) log. The Gamma Ray log uses a scintillation detector (similar to a Geiger counter) to measure the natural radiation from a formation. Shales have a high level of natural radioactivity, hence the curve (right) shows large numbers, while sands have low levels of natural radioactivity, hence the curve is deflected towards the left (small numbers). Analysts draw a “shale base line” (dotted red) that averages the high values. Where the curve is near this line, the interval is interpreted to be shale/clay, but the further the curve is to the left of the baseline, the more likely it is sand.
The second type of log is the SP (spontaneous potential), which measurements the potential difference between the voltage in the wellbore and an electrode on the surface. This log is displayed so, like the gamma ray log, deflections to the right are usually shale while deflections to the left are sand.

## Slide 11: Porosity Logs
Density porosity (solid black line)
  measure the bulk (average) density of the formation (rock & fluids)
Neutron porosity (dashed red line)
  measures the hydrogen content
Deflections to the left = more porous
Deflections to the right = less porous
  Dashed red left of solid black line = Shale
  Dashed red right of solid black = Gas Sand
  Dashed red over solid black = Wet Sand or Oil Sand
Shale
Gas
Oil or
H2O
Gas
Neutron Porosity
Density Porosity
Courtesy of ExxonMobil
Notes:   This slide introduces two types of porosity logs. The density porosity (shown by a solid black line) measures the average bulk density of the formation (rock & fluids). The neutron porosity (dashed red line) measures the hydrogen content. For both logs, deflections to the left mean the formation is more porous while deflections to the right mean the formation is less porous.
  The way we interpret these logs is to draw them together (i.e., in the same track). If the dashed red line is to the LEFT of the solid black line (shale), while if the dashed red line is to the RIGHT of the solid black line, the formation is likely a gas sand. If the dashed red line approximately overlies the solid black line, then the formation is likely wet sand or oil sand.

## Slide 12: Sonic (Velocity) Log
Sonic (DT)
  Acoustic energy is emitted by a transmitter, travels through the formation/fluids, and then is detected by multiple receivers
  Log displays the interval transit time (Dt) in μsec/ft (the inverse of velocity)
T
T
R1
R2
R1
R2
Delta-T
Units = microseconds/ft
Rock Formation
Rock Formation
Difference between 2 paths
Time
0
0
Notes: The sonic log measures the time it takes for sound energy to travel a specific distance. This measure is of interval transit time, which is often referred to as Delta Time of Dt. The units are microseconds per foot (i.e., μsec/ft). The inverse of Dt is the acoustic velocity, which is very important to the seismic professionals.
The tools have at least one (1) transmitter and at least two (2) detectors (receivers). We measure the time difference in receiving an acoustic pulse at each receiver. As shown by the magenta line, the difference in travel paths is a small distance within the rock formation. Thus Dt gives a measure of the transit time (and hence velocity) within the rock formation.

## Slide 13: Resistivity Logs
Deep resistivity – High Values:
  Hydrocarbons
  Tight streaks (low porosity)
Deep resistivity – Low Values:
  Shale
  Wet sand
Separation between resistivities means:
  The formation fluid is different from the drilling fluid
  The formation is permeable to the drilling fluid
ILD (deep)
MSFL
SFL
Formation Fluid
different from
Drilling Fluid
Formation Fluid
similar to
Drilling Fluid
Courtesy of ExxonMobil
Deep, Medium, and Shallow refers to how far into the formation the resistivity is reading (4 ft, 2 ft, few inches)
Notes: Another common log measures the electrical resistivity of the formation. Tools are designed to investigate different distances into the rocks. The meaning of distance (of penetration) into the rocks for shallow is a few inches into the formation, while medium is about 2 feet into the formation, and deep is about 4 feet into the formation. If the deep resistivity is high, this indicates either the presence of hydrocarbons (HCs) or low porosity tight streaks. If the deep resistivity is low, this indicates shale or water/brine-filled sands. If there is separation between the medium and deep measurements, it means the formation fluid is different from the drilling fluid, and the formation is permeable to the drilling fluid.
On the log that is shown, deep (black) and medium (red). The region boxed in red shows where the curves are separated, hence the formation fluid is different from the drilling fluid. If the drilling fluid is water, then the interval does not have water in the pore space. Alternatively, in the region boxed in green, the curves are NOT separated, hence the formation fluid is the same as the drilling fluid.

## Slide 14: Putting It All Together
We will assume that this well was drilled with an oil-based mud
Gamma Ray
Caliper
ILD (deep)
MSFL
SFL
RHOB)
NPHI
Courtesy of ExxonMobil
Notes: This slide shows a well log with three (3) tracks (or columns of different measurements). Track 1 has the caliper and gamma ray measurements; Track 2 has 3 resistivity logs where shallow is green, medium is red, and deep is black; and Track 3 has two (2) porosity logs where black is density and red is neutron. We will interpret these logs in the next few slides.

## Slide 15: Step 1: Lithology
Using the Gamma Ray log, define a shale base line
Deflections far to the left are sands
Intermediate deflections to the left are silts
ILD (deep)
MSFL
SFL
RHOB)
NPHI
Gamma Ray
Caliper
Sandstone
Sandstone
Sandstone
Siltstone
Shale
Siltstone
Shale
Courtesy of ExxonMobil
Notes: First, we can interpret lithology based on the gamma log, where the red dashed line represents the shale baseline. The depth range is subdivided into 3 litho-types: high gamma (near baseline) is shale (green), low gamma is sandstone (yellow), and intermediate is silt (brown).

## Slide 16: Step 2: Porosity Log Crossovers
ILD (deep)
MSFL
SFL
RHOB)
NPHI
Gamma Ray
Caliper
Sandstone
Sandstone
Sandstone
Siltstone
Shale
Siltstone
Shale
Where is the neutron porosity to the right of the density porosity?
This indicates where gas is in the sand pores
Gas
Courtesy of ExxonMobil
Notes: Next we examine the two (2) porosity logs. Where the red curve is to the right of the black (the lines cross-over), the sands contain gas in the pore space. Note that the top ~80% of the thick sand has gas (red).

## Slide 17: Step 3: Resistivity Logs
ILD (deep)
MSFL
SFL
RHOB)
NPHI
Gas
Gamma Ray
Caliper
Sandstone
Sandstone
Sandstone
Siltstone
Shale
Siltstone
Shale
Where do the resistivity logs give different values?
This indicates where the fluids in the rocks differ from the drilling fluid
This confirms our gas zone
Since we used an oil- based mud, the two green zones are interpreted to be oil
Courtesy of ExxonMobil
Water or Oil
Water or Oil
Formation Fluid
similar to
Drilling Fluid
Water or Oil
Water or Oil
Formation Fluid
different from
Drilling Fluid
Notes:   Now we interpret the resistivity logs. For the bottom of the thick sand and the deeper sand, the medium and deep resistivity have similar values. This indicates that the drilling fluid is the same as the formation fluid. If the drilling fluid was an oil-based mud, then we have oil zones. If the drilling fluid was a water-based mud, then we have wet sands (pores filled with water).
  There is a lot more that a log analyst can do – in fact, this is basic stuff that any experienced geoscientist should be able to do. There are many basic well log interpretation courses people in industry can take that run for three (3) to ten (10) business days.

## Slide 18: Well Log Correlation
Well logs give us detailed information at the location of the borehole
If there are several wells in an area, we can correlate stratigraphic units between them
The correlation is based on ‘characteristics’ of the well log responses – like a fingerprint
Often we select a datum – a correlation horizon that is registered to a common depth (flattened)
There are two main ‘philosophies’ used in well log correlation:
  Correlate based on lithologic units - Lithostratigraphy
  Correlate based on assume time lines – Chronostratigraphy
  Which is Better? A matter of heated debate!!
Notes:   If we have more than one (1) well in an area of interest, then we can work on correlating stratigraphy (rock layers) from one well to another.
  Well log correlation is an important part of understanding both regional stratigraphy and field-scale stratigraphy.
  We use log response patterns somewhat like fingerprints to make interpretations.
  For example, the sand at 10,523 ft in well 1 correlates (is age-equivalent to) the sand at 12,010 ft in well 2.
  To remove post-depositional tilting, people often datum (flatten) the logs from different wells on:
  What is believed to be a time marker, e.g., a bentonite (volcanic) layer,
  A regional unconformity, or
  The top/base of a paleontological zone (e.g., last occurrence of microfossil X).
  There are two main ‘philosophies’ used in well log correlation:
  Correlate based on lithologic units – Lithostratigraphy
  Correlate based on assume time lines – Chronostratigraphy
  Which is Better? A matter of heated debate!!
  There are good aspects to doing lithostratigraphic correlations.
  Similarly, there are good aspects to doing chronostratigraphic correlations.
  Our exercise will illustrate these differences.

## Slide 19: How to Correlate these Logs?
AAPG©1990 reprinted with permission of the AAPG whose permission is required for further use.
Well A
Well D
Well C
Well B
Coastal Plain Sandstones and Mudstones
Shallow Marine Sandstones
Shelf Mudstones
Van Wagoner et al., 1990
Notes:   In this slide, we have four (4) gamma ray logs. Several depositional environments and lithologies have been interpreted for you here. The green represents coastal plain sandstones and mud, the yellow represents the shallow marine sandstones (beach deposits and nearshore sands), and the grey are shelf mudstones (offshore mud/clay). We would like to make some well-to-well correlations in the following slides.

## Slide 20: Lithostratigraphy
Here the correlation is based on common lithologic units
Well A
Well D
Well C
Well B
Datum
Coastal Plain
Nearshore Sands
Shelf Mudstones
Van Wagoner et al., 1990
AAPG©1990 reprinted with permission of the AAPG whose permission is required for further use.
Notes:   One option is to key in on the thicker nearshore sands and correlate their tops. That is want has been done here; the well logs have also been datumed (shifted up/down) to align on the top of the thick sands. This is called a lithostratigraphic correlation, since we are using lithologic type to say what correlates (is depositional time equivalent) with what. When units are given formation and member names, we are usually dealing with lithostratigraphic style of correlation.

## Slide 21: Chronostratigraphy
Here the correlation is based on an interpretation of time-equivalent stratal packages – i.e., parasequences
Well A
Well D
Well C
Well B
Index
Fossil
Coastal Plain
Nearshore Sands
Shelf Mudstones
Van Wagoner et al., 1990
AAPG©1990 reprinted with permission of the AAPG whose permission is required for further use.
Notes: An alternative way to correlate stratigraphic layers is to define units in each well that were deposited at about the same geologic time.
These geologic time lines may come from index fossils, or their first or last appearances. Some units can be easy to define as time correlative – e.g., a bentonite (volcanic) layer associated with a single volcanic eruption.
What can be done in many cases is to look for unique log responses that can be tracked from well to well. This is what you will be doing in Exercise 4.

## Slide 22: Does It Matter?
Chronostratigraphy
Lithostratigraphy
Perhaps not for finding a field
BUT
It can impact:
- estimates of reserves
- development plans
- enhanced recovery
Based on Van Wagoner et al., 1990
Well A
Well D
Well C
Well B
Well A
Well D
Well C
Well B
Notes: Does it matter if we correlate using a lithostratigraphic approach versus a chronostratigraphic style? In an exploration stage, it probably makes little difference. You would probably want to drill the structure (crest) given either interpretation. BUT it can impact details that are important in the development and production stage of a new or old field.
Differences in the two (2) interpretations can lead to differences in estimates of HC reserves (volumes), development plans, and how you might enhance recovery (e.g., drill injection wells).
For example, consider the two (2) deepest sands in well C. In the upper interpretation, these two (2) sands are totally isolated from the younger, thicker sands. In the lower figure, these two (2) sands are correlated with the thick sands in well A. In addition, in the lower figure, we could inject water into the sands in the A well and it could enhance recovery from the two (2) deepest sands in well C, whereas this is not true with the upper figure.
Our experience is that using a chronostratigraphic approach usually leads to better explanations of enhanced recovery efforts than does using the lithostratigraphic approach. The chronostratigraphic style is also more beneficial when using seismic data to predict lithologies and layering – more on this in later units.

## Slide 23: Well Log Correlation: Example 1
Fluvial to Estuarine and Coastal Plain Sandstones and Mudstones
Shallow Marine Sandstones
Shelf Mudstones
200 ft
1 mile
Van Wagoner et al., 1990
AAPG©1990 reprinted with permission of the AAPG whose permission is required for further use.
Notes: Here we have five (5) logs from a US onshore basin. Three environments of deposition/rock types are color-coded. The horizontal lines are what have been interpreted as parasequence boundaries. The question is how to correlate between wells – to fill in the gaps.

## Slide 24: Well Log Correlation: Example 1
Well log correlation can provide detailed stratigraphy for analyzing an oil/gas field
Fluvial to Estuarine and Coastal Plain Sandstones and Mudstones
Shallow Marine Sandstones
Shelf Mudstones
200 ft
1 mile
Van Wagoner et al., 1990
AAPG©1990 reprinted with permission of the AAPG whose permission is required for further use.
Notes: Here is the interpretation as published by Van Wagoner et al., 1990. The lines represent parasequence boundaries – and are taken to be time correlative (time stratigraphic) surfaces.

## Slide 25: Well Log Correlation: Example 2
Well A
Well B
Well C
Well D
OTC©1979 reprinted with permission of the OTC whose permission is required for further use.
based on Ramsayer, 1979
With only a few, widely spaced wells, there are many ways to correlate between wells.

## Slide 26: Well Log Correlation: Example 2
One Possible Correlation
Well A
Well B
Well C
Well D
OTC©1979 reprinted with permission of the OTC whose permission is required for further use.
based on Ramsayer, 1979
With only a few, widely spaced wells, there are many ways to correlate between wells.

## Slide 27: Well Log Correlation: Example 2
With only a few, widely spaced wells, there are many ways to correlate between wells.
Another Possible Correlation
Well A
Well B
Well C
Well D
OTC©1979 reprinted with permission of the OTC whose permission is required for further use.
based on Ramsayer, 1979

## Slide 28: Well Log Correlation: Example 2
Since seismic reflection tend to parallel stratal surfaces, they can give us valuable insights
Well C
Well D
OTC©1979 reprinted with permission of the OTC whose permission is required for further use.
Ramsayer, 1979

## Slide 29: Well Log Correlation: Example 2
400 ft
4000 ft
12,000’
14,000’
13,000’
Austin Chalk
Eagleford Shale
Buda
Limestone
Woodbine Fm
OTC©1979 reprinted with permission of the OTC whose permission is required for further use.
Ramsayer, 1979

## Slide 30: Two East Texas Gas Fields
400 ft
4000 ft
12,000’
14,000’
13,000’
N. Seven
Oaks Field
Hortense
Field
OTC©1979 reprinted with permission of the OTC whose permission is required for further use.
Ramsayer, 1979

## Slide 31
Questions?