## Slide 1: Petroleum Geology & Geophysics
5. The Seismic Method
Mitchum et al., 1977b
AAPG©1977 reprinted with permission of the AAPG whose permission is required for further use.
Most Images Courtesy of ExxonMobil
Notes: Unit 5 gives a very simple introduction into reflection seismology. This lecture covers an introduction into the seismic reflection method, seismic acquisition, and seismic processing. The goal is to obtain subsurface images so that we can interpret geology and hydrocarbon (HC) system elements.

## Slide 2: Basic Exploration Workflow
Drill
Wildcats
Identify
Opportunities
Process
Seismic Data
Capture
Prime Areas
Interpret
Seismic Data
Acquire
Seismic Data
To D/P
Drop
Prospect
Confirmation
Well
Success
Success
Failure
Uneconomic
Economic
Analysis
Assess
Prospects
Notes: This is what staff in exploration do at a very high level:
  They identify opportunities (high potential basins where we might gain access – licenses),
  They capture prime areas – typically through lease sales,
  If they get one (1) or more blocks, they may acquire better seismic data,
  The seismic data has to be processed,
  Then the data are interpreted,
  During interpretation, interesting features/anomalies that might be associated with undiscovered fields are noted
After Step 6, the features/anomalies are Initially called ‘leads.’ If some detailed work indicates that there is a good chance the features hold economic amounts of HCs, they are called prospects. The use of the term ‘prospect’ varies – some say it is used when a lead is good enough to present to a manager as a drilling candidate.
Prospects have to be assessed – to help decide on whether or not to drill it. Questions need answered include: 1) Will it hold oil or gas?; 2) How much (what volume of recoverable oil/gas)?; and 3) What is the quality of the reservoir? An economic analysis would then be performed to answer whether the value of the predicted volume of HCs greater than the costs involved. The information is presented to the manager – he/she decides if it should be drilled, and the first well drilled is called a ‘wildcat’. If the wildcat is a success (i.e. we find evidence for enough HCs that we want to proceed), exploration may need to drill one (1) or more confirmation/delineation wells.
We will illustrate this with a hypothetical example in a few minutes. Once the economic viability is established, the new field is turned over to: 1) the development department/company, if facilities (platform, pipeline, etc.) will be expensive, or 2) the production department/company, if inexpensive (e.g., two (2) land wells and an extension of a pipeline a couple of miles).

## Slide 3: The Seismic Method
Listening Devices
0 s

An Explosion!
0 s
Energy
Source
.1 s
.2 s
.3 s
Some Energy is Reflected
Most Energy is Transmitted
.4 s
.4 s
.5 s
Some Energy is Reflected
Most Energy is Transmitted
.6 s
.7 s
.8 s
.8 s
Notes: This slide illustrates the basics of reflection seismology. We start with an energy source – like an explosion. Acoustic energy radiates down through the Earth (represented by the half-circles and the arcs). For simplicity, geophysicists use rays (lines with arrows) to represent the acoustic energy traveling through the Earth.
At a boundary between one unit and the next deeper unit, some of energy is reflected – most is transmitted (continues to travel down). The reflected energy travels towards the surface where we have set out “listening” devices.
In this cartoon example, some energy is reflected off the top of the orange unit and is “heard” (recorded) at 0.4 seconds at the receiver near the middle of the diagram. Most of the energy is transmitted through the orange layer. At the top of the brown layer, some energy is reflected and is recorded at 0.8 seconds at the receiver on the right side of the diagram.

## Slide 4: Raw Seismic Data
Device
#1
Device
#2
0.0
0.3
0.4
0.5
0.6
0.7
0.8
0.1
0.2
For the explosion we just considered ...
Listening device #1 records a reflection starting at 0.4 seconds
Listening device #2 records a reflection starting at 0.8 seconds
To Image the Subsurface, We Use Many Shots (explosions)
and Many Receivers (listening devices)
Arranged in Lines either on Land or Offshore
Time
Notes: This slide shows what the raw seismic data would look like for the two (2) reflections we just considered.
The seismic energy sent out by the explosion looks like a sine wave. The filled in (blue) portions would be compressions (i.e. material is pushed together), which is usually recorded as positive numbers and displayed to the right of the center (zero) line. The unfilled portion to the left of the center line would be rarefactions (i.e. material is expanding out), which is usually recorded as negative numbers and displayed to the left of the center (zero) line.
In this figure, Device #1 recorded the energy reflected off the top of the orange unit and shows a response at 0.4 seconds, while Device #2 recorded the energy reflected off the top of the brown layer and shows a response at 0.8 seconds. To get a good image of the subsurface, we use hundreds of shots (explosions) and millions of receivers (listening devices) arranged in lines either on land or in the offshore environment.

## Slide 5: Seismic Acquisition
A 3D survey is designed based on:
  Imaging Objectives: image area, target depth, dips, velocity, size/thickness of bodies to be imaged, etc.
  Survey Parameters: survey area, fold, offsets, sampling, shooting direction, etc.
  Balance between Data Quality & $$$$$
Land Operations
Vibrators Generate a Disturbance
Geophones Detect Motion
Marine Operations
Air Guns Generate a Disturbance
Hydrophones Detect Pressure
Images Courtesy of ExxonMobil
Notes: Today, many of our seismic surveys (land and marine) acquire 3D seismic data. However, there still are 2D surveys collected.
To design a seismic survey, we start by asking the ones familiar with the area about what they want to image. For example, an anticline at 9876 ft covers 10 sq miles with sandstone units believed to be 150 feet thick. This determines many of the survey parameters, like the survey area, the fold, shooting direction, etc. Seismic acquisition is always a balance because good quality data is expensive, and the quality level will vary to answer the necessary business questions.
The left picture is of a land seismic acquisition operation in which four vibrator trucks are working in tandem.
The right picture is of a marine seismic acquisition ship. Behind the ship, you can see two (2) airgun arrays and four (4) streamers (cables with hydrophones).

## Slide 6: Raw Data - Marine
Notes: Here is a display of raw seismic data recorded for one (1) shot/explosion in the marine environment. The horizontal scale is receiver number, which can be translated into ft/miles or meters/km. The vertical scale is two-way travel time.
The receiver nearest the boat is on the left; the receiver furthest away on the right. Notice the hyperbolic shape of the reflections. This shape is because near the boat, the energy travels almost straight down and up over very little lateral distance (red arrow on right figure). For receivers far from the boat (perhaps 4 km), the energy not only has a vertical component, but also a horizontal component (blue arrows on right figure). Thus, the distance traveled by the blue rays is longer than the red rays, and therefore takes more travel time. Based on the hyperbolic shape of the reflections, we can calculate the average velocity along the ray paths.

## Slide 7: Seismic Processing
Field Record
(marine)
Data Processing
Stream
Subsurface ‘Image’
Notes: We obtain the raw seismic data for energy that travels from each shot into each receiver. The raw data goes to the seismic data processors.
They have methods to manipulate the raw data so that we get images of the subsurface that can be interpreted. With data processing, the saying “you get what you pay for” is quite true. Simple corrections are fast and relatively cheap (in dollars, manpower and time).
If the subsurface is complex, however, there are very sophisticated algorithms to “focus” the subsurface image, which is very expensive. The applied processing is (hopefully) enough to give images that answer the business questions without spending more money/effort than necessary. As with acquisition, we strive to achieve the correct balance.

## Slide 8: Shot Gather
Source
Receivers
R1
R2
R3
R4
R5
S1
Direct Arrival
Reflections
2 Way Travel Time
Offset (Distance)
R1
R2
R3
R4
R5
Direct Arrival
Reflection
For each shot, reflections are recorded in 5 receivers
There are 5 ‘bounce’ points along interface 3
1
2
3
For Shot 1
Notes: This slide illustrates a marine operation. For simplicity, we will consider one (1) shot (S1) and 5 Receivers (R1, R2, ... R5). The shot record on the right shows two (2) events: 1) the direct arrival, where acoustic energy travels horizontally through the water and is detected by the receivers (red detected energy or reflections) shown by a straight line over the receivers. The slope of the line is controlled by the velocity of sound in sea water.
A reflection off the top of the grey layer is shown by the blue detected energy. This event has a hyperbolic shape, which can be used to estimate the average velocity between the shot and the top of the grey unit.

## Slide 9: Common Midpoint Gather
Sources
Receivers
R1
R2
R3
R4
R5
S1
S2
S3
S4
S5
We sort the shot-receiver pairs so that data from the same ‘bounce’ point (e.g., at ‘A’) is captured
CMP = common midpoint
For Point A
A
CMP Gather
Offset Distance
Notes: The first thing the data processors do is to sort the data. They want to collect all the reflections that “bounce” off the same subsurface point. For example, they want all the information related to the red box “A”. Different combinations of shots and receivers have a “bounce” point at A (e.g., shot 5 into receiver 5).
They display these combinations as a function of lateral distance to get the figure on the right – a common midpoint gather (CMP). It looks like a shot record, but for a shot record, the common feature is the shot, while for a CMP Gather, the common factor is the “bounce” point or midpoint. Whereas on the shot record the traces are evenly spaced, the traces on a CMP gather may not be equally spaced.

## Slide 10: CMP Gather
The travel times differ since the path for a near offset trace
is less than the path for a far offset trace
With the correct velocity, we can correct for the difference in travel time for each trace.
The curvature of this hyperbola is a function of the average velocity down to the depth of the reflection
CMP Gather
Offset Distance
Notes: On the CMP gather, we again have reflections with a hyperbolic shape. The travel times differ since the path for a near offset trace is shorter than the path for a far offset trace. If we know or can estimate the correct velocity, we can correct for the difference in travel time for each trace. From the shape of the hyperbola, we can estimate the average velocity down to the depth of the reflection.

## Slide 11: With Correct Velocity, Gather is Flat
CMP Gather
Offset Distance
Velocity
Correct
Flat
Velocity
Too Slow
Curves
Down
Velocity
Too Fast
Curves
Up
Notes: With the speed of computers, we can iteratively try different velocities and see which value is best. We know the velocity is correct when all the reflections are at the same time valve – or rather, they are FLAT with offset. This is shown in the middle figure on the right. If the velocity is too slow, the reflection curves down – we have not corrected the gather enough (upper right). If the velocity is too fast, the reflection curves up – we have over-corrected the gather (lower right).

## Slide 12: A Stacked Trace
CMP Gather
Moveout Corrected
Midpoint Gather
Stacked
Trace
Offset Distance
We stack several offset traces
(# traces = fold)
The geologic ‘signal’ will be additive
The random ‘noise’ will tend to cancel
Stacking greatly improves S/N
(signal-to-noise)
10 Fold
Notes: The next step is to sum all of the flatten gathers, which are called moveout corrected gathers. In this case, we have ten (10) traces that are from a common midpoint, where each has a different amount of lateral offset. We add the ten (10) traces together. Since it is ten (10) traces, we say that this is ten (10) fold data.
Why do we add the traces? Each individual trace has information about the midpoint (like the red A box in Slide 9) and a certain amount of ‘noise’. The receivers pick up the reflected seismic energy, but also other sound energy. On land, it might be noise from passing cars/trucks, wind, etc. In marine operations, it might be waves, noise on the boat, weather, etc. The geologic information from the midpoint (e.g., Box A) should be about the same on all the traces. Much of the ‘noise’ is random, thus by doing the summation, we enhance the signal and we cancel out the noise. Stacking is one of the best ways we have to improve the signal-to-noise ratio.

## Slide 13: Positioning Problems

Energy
Source

The seismic ray hits an inclined surface at 90º and reflects back
0.2 s down
0.2 s up
0.4 s -
The reflection is displayed beneath the source-receiver midpoint
Bounce
Point
Notes: Thus far, we have kept everything quite simple by assuming the boundaries that generate reflections are horizontal (flat). Problems develop if the boundaries are not flat – they have some dip. When the boundary dips, what we record is the energy that travels from the source and hits the boundary at 90º (normal incidence).
In the figure on the left, we record the energy that follows the dotted black line. In this case, the energy travels 0.2 seconds down to the bounce point and 0.2 seconds up to the receiver for a total of 0.4 seconds. When this is displayed, we would plot the reflection vertically below the shot at 0.4 seconds (the blue peak). Thus we capture the reflected energy, but do not place it in the correct position. This is another thing we have to correct – but, don’t worry, we have methods to apply this correction!

## Slide 14: Preview of the First of Three Exercises
1






2
3
4
6
5
Where would the reflection lie?
90º
Notes: Time for an exercise! Here we have a dipping seafloor. We will consider six (6) shot locations and only the direct down and direct up ray path. That direct down – direct up raypath hits the seafloor where it is 90º – as shown for shot #1. We want to figure out where the reflected energy would be displayed (without corrections).

## Slide 15: Seismic Interpretation
Determine the local geology from the subsurface images
Map faults and other structural features
Map unconformities and other major stratal surfaces
Interpret depositional environments
Infer lithofacies from reflection patterns & velocities
Predict ages of stratal units
Examine elements of the HC systems
Mitchum et al., 1977
AAPG©1977 reprinted with permission of the AAPG whose permission is required for further use.
Notes: After seismic acquisition and processing, we have seismic interpretation. Here is where we take the images and deduce the subsurface geology. This includes:
  Map faults and other structural features,
  Map unconformities and other major stratal surfaces,
  Interpret depositional environments,
  Infer lithofacies from reflection patterns & velocities,
  Predict ages of stratal units, and
  Examine elements of the HC systems.

## Slide 16
Questions?