## Slide 1: Exercise 5a
Dipping Reflections
Where Would the Reflection Lie?
Your Task:
  Construct the CMP representation for this dipping reflection
1






2
3
4
6
5
Notes: Main Task and Objective

## Slide 2: For Shot #1 – The Actual Ray Path
1






2
3
4
6
5
Compass
Where would the reflection lie?
90°
Notes: To figure out where the reflected energy would be displayed, we first trace the raypath. We can use a compass. Place the point on shot point #1. Place the pencil point at the place where the ray path hits the seafloor at 90º - as shown for shot #1.

## Slide 3: For Shot #1 – Where the Response Plots
1






2
3
4
6
5
Where would the reflection lie?
Notes: To figure out where the reflected energy would be displayed, we then swing an arc so that the pencil point is directly below the shot point. This is where the seismic response would plot.
Thus, on the previous slide, we captured the distance (for a seismic section that would be related to the two-way travel time). On this slide, we have determined where it would be displayed – directly beneath the associated shot.
EXERCISE: Now the students should swing arcs for shots 2 through 6 and mark where the seismic response would plot. The “bounce” point is where the ray path is at 90º. Swing an arc to locate where the recorded reflection would be plotted/displayed, which should take about 5 minutes.

## Slide 4: Exercise 5a
Questions?