## Slide 1: Petroleum Geology & Geophysics
6. Seismic Reflections
Shot
Receiver
Layer 1
Layer 2
Layer 3
Layer 4
Impedance = Velocity * Density
Seismic Record
Travel Time (2 way) in msec
0
+
Peak
-
Trough
Layer 1
Layer 2
Layer 3
Layer 4
Layer 2
Layer 3
Impedance
Increase
Impedance
Decrease
Impedance
Increase
Notes: This unit gives a very simple explanation of seismic reflections. The lecture goes through reflection coefficients, pulses and convolution, and then walks through three (3) exercises to reflect on those points.

## Slide 2: The Ideal Seismic Response
Increase in Impedance
Decrease in Impedance
Able to resolve boundaries of beds a few meters thick
1 meter
Notes: The ideal seismic response gives us information about the subsurface stratigraphy at the same scale as an outcrop. Here the beds are about a foot thick – the ideal seismic line would show us this level of detail. However, we do not live in an ideal world. The seismic method does not allow us to “resolve” (be able to distinguish) strata at this fine a scale.

## Slide 3: Stratigraphic Hierarchy
Parasequences
Bed Sets
Parasequence Sets
Sequences
Beds
Lamina Sets
Lamina
Sequence Sets
Thin Units, Limited Extent
Thick Units, Widespread
Core
Logs
Seismic
3rd Order (3-5 MY)
4th Order
2nd Order
5th Order
7th Order
6th Order
9th Order
8th Order
Mid to Lower Order Stratal Units
Notes: There is a hierarchy of layering within sedimentary rocks – the strata. This hierarchy (or scale) is shown on the left. The smallest scale of sedimentary layering is the lamina. Two (2) or more related lamina form a slightly thicker stratal unit are called a lamina set. Several lamina sets form beds, and several beds stack to form bed sets. This continues on to very thick units called depositional sequences and sequence sets.
Seismic data cannot image (resolve) beds or bed sets. However, they are able to image parasequences, parasequence sets, and larger-scale (thicker) stratal units. Thus, seismic data is limited to imaging larger-scale stratal units. However, the advantage of seismic data is the areal coverage it provides. For many sedimentary basins, we have 2D or 3D seismic data covering the entire extent (area) of the basin.

## Slide 4: Scale for Seismic Data
Although seismic data can not image small-scale stratal units, it can image mid- to low-order stratal units
Parasequences
Bed Sets
Parasequence Sets
Sequences
Beds
Lamina Sets
Lamina
Sequence Sets
The big advantage of seismic data is its extensive areal coverage
3rd Order
4th Order
2nd Order
5th Order
7th Order
6th Order
9th Order
8th Order
Notes: There is a hierarchy of layering within sedimentary rocks – the strata. This hierarchy (or scale) is shown on the left.
The smallest scale of sedimentary layering is the lamina. Two (2) or more related lamina form a slightly thicker stratal unit are called a lamina set. Several lamina sets form beds, and several beds stack to form bed sets. This continues on to very thick units called depositional sequences and sequence sets.
Seismic data cannot image (resolve) beds or bed sets. However, they are able to image parasequences, parasequence sets, and larger-scale (thicker) stratal units. Thus, seismic data is limited to imaging larger-scale stratal units. However, the advantage of seismic data is the areal coverage it provides. For many sedimentary basins, we have 2D or 3D seismic data covering the entire extent (area) of the basin.

## Slide 5: Seismic - Units 10s of Meters Thick
5 m
Predominantly
Shale
Predominantly
Shale
Predominantly
Sand
Notes: The resolution of the seismic data (or the thickness of stratal units that can be distinguished) depends on: 1) the time duration of the seismic pulse that was used to acquire the data and, 2) the velocity of the rocks.
Since velocities tend to increase with depth, we can resolve thinner stratal units at shallow depths (e.g., 10 meters) than we can at intermediate depths (e.g., 25 meters). In addition, we can resolve finer stratal units at intermediate depths (e.g., 25 meters) than we can at great depths (e.g., 40 meters).
As shown on this slide, the seismic data tend to “integrate” or average the layering at a scale of 10s of meters. Here the seismic response can tell us that the upper part of this outcrop is predominantly sand, while the lower part of the outcrop is predominantly shale. There are finer-scale layers in the outcrop (beds and bedsets), but we would not be able to distinguish these with seismic data.

## Slide 6: Wave Equation Lingo
Compression
Rarefaction
A
A = Amplitude
λ = Wavelength
length, ft or m
λ
P = Period
time (ms)
Period = Time for the waveform
to travel 1 wavelength
Dp = Pulse
Duration
time (ms)
0
Positive
Numbers
Negative
Numbers
Notes: In this slide, we have some of the most common terms related to seismic data. The black “sine wave” is a simple wavelet, which is a simple approximation of the acoustic wave that travels down through the earth and is reflected back up to receivers on the surface. The wavelet consists of movement that is part compression (positive values as recorded by sensors on the surface, i.e., receivers) and part rarefaction (negative values).
Amplitude (A) is a measure of how big the wavelet is – or the magnitude of the excursion to the right of zero (compression = positive) or to the left of zero (rarefaction = negative). Lambda () is the wavelength of the wavelet – or its length in feet or meters. The Period (P) is the time for the wavelet to travel one wavelength. Lastly, the Pulse Duration (Dp) is the time that it takes for the wavelet to pass a particular reference point. The next slide shows a few simple equations that relate some of these parameters.

## Slide 7: Basic Equations
P = 1 / f (1)
λ = V * P = V / f (2)
d = V * T / 2 (3)
where
P = Period
f = Frequency
λ = Wavelength
V = Velocity
d = distance (depth)
T = two-way time
Notes: Equation 1 tells us that the Period is equal to 1/Frequency.
Equation 2 tells us that the Wavelength is equal to the Velocity times the Period or, with Equation 1, the Wavelength equals the Velocity divided by the Frequency.
Equation 3 tells us that the distance (or the depth) is equal to the velocity times the time divided by 2.
Q: Why the division by 2? A: The acoustic wave travels the distance twice – once down and once up.

## Slide 8: What Causes Reflections?
Any interface between bodies with different acoustic properties
Acoustic properties define Impedance (I), in which:
  I = velocity * density
Shot
Receiver
Layer 1
Layer 2
Boundary
Small change in impedance – small reflection
Large change in impedance – large reflection
Notes: Let’s review what causes a seismic reflection. A seismic reflection is generated at any interface between rock layers with different acoustic properties. These acoustic properties are the velocity and the density of the rock.
Again, geophysicists use the term impedance (I), which equals velocity * density. If the change in impedance across a boundary is small, the amount of reflected energy is small. If the change in impedance across a boundary is large, the amount of reflected energy is large.

## Slide 9: Seismic Interface
Shale
Sand
Reflection
Coefficient
=
=
I below – I above
I below + I above
=
Velocity = 2300 m/s
Density = 1.8 gm/cc
Velocity = 2450 m/s
Density = 1.7 gm/cc
Notes: This slide shows the acoustic properties for rocks above and below an interface – in this case, shale on top of sand. If there is time, let the students perform the calculation. The solution is on the next slide.

## Slide 10: Seismic Interface
Shale
Sand
Velocity = 2300 m/s
Density = 1.8 gm/cc
I = 2300 * 1.8 = 4140
Velocity = 2450 m/s
Density = 1.7 gm/cc
I = 2450 * 1.7 = 4165
Reflection
Coefficient
=
4165 - 4140
4165 + 4140
=
I below – I above
I below + I above
=
0.003
Of the incident energy, 0.3% is reflected, 99.7% is transmitted
Notes: This is the answer for the RC for the previous slide.

## Slide 11: Back to Basics
Seismic energy travels down and
is reflected off acoustic boundaries
Shot
Receiver
Seismic
Record
0.0
0.2
1.2
1.4
1.0
0.4
0.6
0.5
0.3
0.1
0.7
1.1
1.3
0.8
0.9
Increase in
impedance
Increase in
impedance
Notes: In review, the essence of the seismic method is that: geoscientists generate energy at the surface through Vibroseis trucks and/or through dynamite. The energy travels down through the earth, and at a boundary between one rock unit and another, there can be a change in either the velocity of the rocks, the densities of the rocks, or both.
The acoustic properties of a rock layer are described by a parameter called impedance.
Impedance = velocity times density ( z = V * ). A change in impedance (e.g., top of the yellow layer), a fraction of the energy “bounces” or is reflected. Most of the energy continues down, or is transmitted through the layer. At the next change in impedance (top of the brown layer) some of the energy “bounces” or is reflected.
Let’s say that the acoustic energy corresponds to a compression (positive numbers) followed by a rarefaction (negative numbers). In this case, at a boundary where the impedance increases (lower layer has a higher impedance than the upper layer) the reflected energy will be a compression followed by a rarefaction – on the seismic section a black peak followed by a white trough. If there is a decrease in impedance at a boundary, the reflected energy will be a rarefaction followed by a compression – on the seismic section a white trough followed by a black peak.
On this slide there is an increase in impedance at both boundaries – hence both events on the seismic trace are a black peak followed by a white trough. On the first slide, there is an example on the right where there are two (2) boundaries with an increase in impedance (between layers 1 and 2, and also between layers 3 and 4) and one boundary where there is a decrease in impedance (between layers 2 and 3).

## Slide 12: Acoustic Structure of the Earth
Shot
Receiver
I1 = 1 * V1
I2 =  2 * V2
I4 =  4 * V4
I3 =  3 * V3
Reflection
Coefficients
Pulse
C
O
N
V
O
L
U
T
I
O
N
Seismic
Trace
Imped
Low
High
Notes: This is a simplification of the previous slide. At a certain location, we have various layers with different impedance values. We can calculate the impedance of each layer by multiplying the velocity by the density.
On the far left, we show the impedance as a log curve. The amount of energy that is reflected is a function of the magnitude of the impedance change across a boundary. A small change in impedance results in a small amount of reflected energy, while a large change in impedance results in a larger amount of reflected energy.
We can calculate a parameter called the Reflection Coefficient (RC) using a formula that is given in the associate exercise, which we will introduce in a few minutes. Note that an increase in impedance results in a positive RC, while a decrease in impedance results in a negative RC.
We display the RCs as a log of spikes where positive RCs are plotted to the right of zero, and negative RCs are plotted to the left of zero. The length of the spike is proportional to the value of the RC (small spike = small change in impedance; large spike = large change in impedance). The shallowest spike on this slide indicates a positive RC (to the right of zero) of a moderate change in impedance (a bigger change in impedance at the boundary between layers 1 and 2 then between layers 2 and 3; but not as big a change as between layers 4 and 5).
If we know or an can assume the shape of the acoustic pulse (waveform), then we can use a mathematical process called convolution to model the seismic response for each of the boundaries individually. The actual seismic pulse is the sum total of all the individual responses.
As we will discuss further, there can be constructive or destructive interference between the individual responses, something that complicates the life of a seismic interpreter!

## Slide 13: That ‘Pesky’ Pulse
Reflection
Coefficients
Ideal
Pulse
Seismic
Trace
If the frequency content (bandwidth)
is very large, then the pulse
approaches a spike and we can
resolve fine-scale stratigraphy
Typical
Pulse
Seismic
Trace
Typically the frequency
content is limited to about
10 to 50 Hz (BW = 40),
which greatly limits our
vertical resolution
Notes: If the frequency content (bandwidth; BW) is very large, then the pulse approaches a spike and we can resolve fine-scale stratigraphy. This ideal pulse goes back to what was described in slide 2. Unfortunately, the frequency of the pulses we are able to generate are limited, typically from about 10 to 50 Hz (BW = 50 – 10 = 40 Hz). Thus, our ability to resolve thin beds on seismic data is controlled by the limited bandwidth of our pulse. A high-resolution survey would have pulse frequencies from about 5 to 60 Hz, or a bandwidth of 55 Hz – much better than 40 Hz.

## Slide 14: Types of Pulses
Causal (real – no motion before wave arrives)
Front loaded
Peak arrival time is frequency dependent
RC is at the first displacement; maximum displacement (peak or trough) is delayed by ¼ λ
Minimum Phase
Reflection
Coefficients
Notes: Let’s consider the pulse for a few minutes. There are two end-member types of pulses. The first end-member is a minimum phase pulse, which is the type of pulse that you would get from an explosion or an earthquake. There is no particle motion before the explosion occurs. Immediately after the explosion, particle motion will build to a compressional maximum, then decrease, build to a rarefaction maximum (most negative value) and then go back to zero. Minimum phase pulses are causal (real – no motion before wave arrives), front loaded, the peak arrival time is frequency dependent, and the RC is at the first displacement. The maximum displacement (peak or trough) is delayed relative to where the RC is by ¼ λ.

## Slide 15: Types of Pulses
Not causal (not real, since there is motion before the wave arrives)
Symmetric about RC
Peak arrival time is not frequency dependant
Maximum peak-to-side lobe ratio
RC is at the maximum displacement (peak or trough)
Reflection
Coefficients
Zero Phase
Notes: The second end-member type of pulse is called zero phase. The shape of a zero phase pulse relative to the RC is shown on this slide. A zero phase pulse is not causal (not real, since there is motion before the wave arrives), is symmetric about the RC, the peak arrival time is not frequency dependent, has the maximum peak-to-side lobe ratio, and the RC is at the maximum displacement (peak or trough).

## Slide 16: Polarity – Minimum Phase
SEG Normal Convention
A compression is:
Negative # on the tape
Displayed as a Trough
Reflection
Coefficients
- +
SEG = Society of Exploration Geophysics
Polarity = How will an increase in impedance be displayed?
Notes: Next, we will explain seismic polarity – i.e., the mathematical sign convention. SEG stands for the Society of Exploration Geophysics. They have set an industry standard for the definition of polarity for both minimum phase and zero phase pulses. For a minimum phase pulse and a positive RC (increase in impedance), the first numbers recorded on the tape should be negative and the first motion should be displayed as a trough. If a minimum phase dataset is said to be SEG reverse polarity, that would mean for a positive RC the first motion would be displayed as a peak.

## Slide 17: Polarity – Zero Phase
SEG Normal Convention
A compression is:
Positive # on the tape
Displayed as a Peak
Reflection
Coefficients
- +
SEG = Society of Exploration Geophysics
Polarity = How will an increase in impedance be displayed?
Notes: As this slide shows, for SEG normal, zero phase pulse and a positive RC (increase in impedance), the numbers recorded on the tape for where the RC is located should be positive, and the motion centered on the RC should be displayed as a peak. If a zero phase dataset is said to be SEG reverse polarity, a positive RC means that motion centered on the RC would be displayed as a trough.

## Slide 18: Seismic Reflection – Single Interface
Shale
Sand
Impedance
R.C.
Response
The mathematical operation to model the interaction of a pulse with a reflection coefficient is called CONVOLUTION
Notes: This is the same interface shown on slides 15 and 16. The RC is shown as a positive spike at the depth of the interface, a zero phase pulse (SEG reverse) as the response. (In addition, you could ask the students the phase & polarity of the assumed pulse.)

## Slide 19: Seismic Reflections – Thick Interval
Shale
Sand
Impedance
R.C.
Response
Shale
A thick interval is one in which the response from the top interface finishes before the response from the base interface begins
NOTE: The response “flips” for a negative R.C.
Notes: The upper interface is the same as on slides 15 and 16. The lower interface has the same impedance change (RC) times -1. This means that the lower shale has the same impedance (velocity * density) as the upper shale.
The upper +RC has a zero phase pulse with a peak centered on it, while the lower -RC has a zero phase pulse with a trough centered on it. The sand is thick enough that the response for the upper interface finishes before the response for the lower interface begins. Thus, the two responses are clear, and there are no interference effects.
For a seismic interpreter, a thick unit is one that is greater than the pulse duration time. This is true for both a zero phase pulse and a minimum phase pulse.

## Slide 20: QUESTION:
What would happen if an interval is thin, i.e., the response from the top interface does not finish before the response from the base interface begins?
ANSWER:
At depths (two-way times) where the two responses co-exist, the two values would add together. The receiver would “hear” both responses simultaneously with no way to “know” it is “hearing” the tail end of the response from the top and the start up of the response from the base.
Notes: You can pose this question to get the students thinking about what happens if a unit thins to less than the pulse duration time. The answer is revealed with an animation. You can have a mini-discussion before revealing the answer. The next slide shows an example for a “thin” unit, one that results in wavelet interference.

## Slide 21: Interference Effects
Wavelets
Composite
Constructive Interference
R.C.
1
1
1
2
Wavelets
Composite
Destructive Interference
R.C.
1
2
2
2
Notes: This slide shows a case of: (1) constructive and (2) destructive interference. On the left, two RC of opposite signs are spaced less that the pulse duration. Wavelet 1 for RC 1 and wavelet 2 for RC 2 are shown. The net (composite) response is shown, where the first peak is larger than either individual wavelet peak due to constructive interference (summation). The second trough is larger (more negative) than the individual troughs.
On the right, two RC of the same sign (both +RCs) are spaced less that the pulse duration. Wavelet 1 for RC 1 and wavelet 2 for RC 2 are shown, along with the net (composite) response. The first peak is smaller and of longer time duration than either individual wavelet peak due to destructive interference (subtraction). The second trough is larger (more negative) than the individual troughs.

## Slide 22: Seismic Data & Stratal Surfaces
Unconformities
Facies Changes
Foreshore/Upper Shoreface
Submarine Fan
Lower Shoreface - Offshore
Fluvial Incised Valley Fill
Estuarine
Coastal Plain
Slope - Basin
Condensed Interval
Seismic reflections parallel mid to low order stratal surfaces
Reflection terminations mark unconformities
Changes in reflection character indicate facies changes
Stratal Surfaces
Notes: We will talk about this in greater detail in a later unit, but seismic reflections tend to parallel stratigraphic surfaces. We can use reflection terminations to identify and mark unconformities. Changes in the characteristics of a reflection (e.g., amplitude, frequency, continuity) indicate changes in depositional facies.

## Slide 23: Why Stratal Surfaces?
Recall: Reflections are generated where there is a change in acoustic properties (I = rv)
SB
SB
SB
SSB
Brushy Canyon Formation, West Texas
Very Gradational Lateral
Changes in Physical Properties
Can Have Abrupt Vertical
Changes in Physical Properties
Especially at PS Boundaries
Consider: Where can there be sharp changes in impedance?
    horizontally as lithofacies change?
    vertically across stratal boundaries?
Notes: Why do reflections parallel stratigraphic surfaces? Recall that reflections are generated where there is a change in acoustic properties, so either the velocity of the rocks change, the densities of the rocks change, or both change.
Let’s look at a thick outcrop in West Texas, which is 1200 ft or 365 meters in relief. From the bottom to top, there are four (4) formations - the Pipeline Shale (guess what the lithology is?), the Lower Brushy Canyon, the Middle Brushy Canyon, and the Upper Brushy Canyon. Each member of the Brushy Canyon consists of shale with silt and sand layers – sand content increases Lower to Middle, and Middle to Upper.
Now consider where there would be sharp changes in impedance. Note some white, ledge-forming layers (e.g., just below the Middle Brushy Canyon label). This is a relatively sand-rich layer, and we could walk out on this layer for several miles. If we sampled this layer, say every ¼ mile, we would find that the first sample might be 75% sand, the next 73%, then 72%, 70%, 71%, 68%, 65%, 66%, 64%, 62%, 60%, etc. The point is that the sand content is changing, and also the acoustic properties, but these changes are very gradational. There are not sharp physical surfaces laterally across which the acoustic properties change significantly.
Now consider if someone repelled down the cliff and took sediment samples every 2 meters. The first sample might be a shale, next a shale, then a silt, a sand, a shale, a shale a sand, a shale, a silt, a shale, a sand, a silt, etc. The point is that there would be more abrupt changes in acoustic properties vertically. Some significant changes would occur at the layer-scale stratigraphic packages, i.e. at boundaries between parasequences, and between parasequence sets, and between depositional sequences.
Thus, it is reasonable to conclude that the reflections we see on seismic sections are generated at parasequence boundaries, and at parasequence set boundaries, and at sequence boundaries. You may be thinking, ‘Is there NOT a seismic response as we pass from one environment of deposition (EOD) to another EOD?’ YES, there is.
For instance, a reflection will follow a boundary between one parasequence and the next parasequence. The characteristics (attributes) of the reflection (say a peak) will change as the sedimentary facies above and below the parasequence boundary changes. For example, a shale on top of fluvial rocks might result in a moderate reflection amplitude, changing to a higher amplitude reflection where there is shale on top of nearshore sands, changing to moderate amplitude where there is shale on top of offshore silts, and changing to low amplitude where there is shale on top of offshore shale.

## Slide 24: Not Every Reflection is Strata!
There are other seismic reflections out there that may not be stratigraphic in origin
Facies Changes
Fluid Contacts
Fault Planes
Multiples
Others
Unconformities
O
W
G
Stratal Surfaces
Notes: A word of caution: there are other seismic reflections out there that may not be stratigraphic in origin. Some examples include: fluid contacts, fault planes, and multiples.

## Slide 25
Questions?
Notes: It is time to introduce 3 new exercises, but first, any questions.