## Slide 1: Exercise 6a: Dipping Reflector
What Percentage of the Energy is Reflected?
Your Task:
  Use the velocity and density for two layers to calculate the associated reflection coefficient at the interface between the two layers
Notes: This review, which I would do at the start of class 7, is short. Basically reveal the answer.

## Slide 2: Interface 1
I = 2000 * 1.7 = 3400
I = 2400 * 1.8 = 4320
= 0.12
4320 - 3400
4320 + 3400
RC =
920
7720
=
Notes:   Solution for interface #1.

## Slide 3: Interface 2
I = 2000 * 1.7 = 3400
I = 2400 * 1.8 = 4320
= -0.12
3400 - 4320
3400 + 4320
RC =
-920
7720
=
Notes:   Solution for interface #2.

## Slide 4: Interface 2
7 | You should have gotten a negative number in step 6. What is the significance of a negative reflection coefficient?
8 | If a positive RC produces a zero phase trough, what do you anticipate the difference in response will be for interface 1 and interface 2?
The impedance decreases from above to below the interface.
The response will be “flipped” relative to the pulse.
Interface 1 – a trough followed by a peak.
Interface 2 – a peak followed by a trough.
Notes:   Solution for steps 7 and 8.

## Slide 5: Interface 3
I = 2000 * 1.7 = 3400
I = 2600 * 2.1 = 5460
= 0.23
5460 - 3400
5460 + 3400
RC =
2060
8860
=
Notes:   Solution for Interface #3.

## Slide 6: Interface 3
12 | Why is the RC you calculated in step 10 so much bigger that the RCs you calculated in steps 3 and 6?
13 | If a positive RC produces a zero phase trough, what do you anticipate the difference in response will be for interface 1 and interface 3?
Both the velocity and the density of the carbonate is much larger than those for the sand. The bigger the impedance contrast, the more energy is reflected.
Interface 1 – a moderate trough followed by a peak.
Interface 2 – a larger trough followed by a peak.
Notes:   Solution for steps 12 and 13

## Slide 7: Exercise 6a
Questions?