## Slide 1: Petroleum Geology & Geophysics
7. Source Rocks
A “Kitchen”
Where Organic
Material Is
Cooked
“Plumbing” To Connect the Container to the Kitchen
Source
Migration
Reservoir
Trap
Seal
Where HCs Accumulate
Notes: This unit focuses on one (1) play element – source (white oval). Please see ‘Introduction to Play Elements’ lesson for more information about the rest of the play elements.

## Slide 2: Petroleum System
What is a Petroleum System?
A Petroleum System includes where the petroleum originates, where and how it accumulates, and how it got from its source to its trap.
There are four essential elements and two major processes.
Notes: A definition of play elements. The four (4) elements and two (2) processes are given on the next slide.

## Slide 3: Elements and Processes
Essential Elements
Source rocks
Reservoir rocks
Seal rocks
Overburden rocks
Major Processes
Trap formation
Hydrocarbon
  Generation
  Migration
  Accumulation
Source
Migration
Reservoir
Trap
Seal
Notes: This is a slightly different way to describe play elements. Here we split out two required processes: (1) Trap formation, and (2) hydrocarbon (HC) generation, migration and accumulation. Overburden rocks are an essential element. These rocks, which are younger than our target interval, are what buries the source and compacts the sealing rocks.
Overburden is good for source generation and seal strength. Overburden is bad for a reservoir as more compaction (and diagenesis, such as cementation) reduces porosity & permeability.

## Slide 4: Source of Oil & Gas
Plant or
Animal
Remains
sugar
C6H22O11
Time
Burial
Temperature
Oil & Gas
Molecules
Methane Gas
CH4
ORGANIC MATERIAL
REACTION
CONDITIONS
OIL - GAS GENERATION
Image Courtesy of ExxonMobil
Notes: Oil and gas molecules come from organic matter – plant or animal remains. The hydrocarbon (HC) generation process needs the right conditions for the chemical changes to occur. This primarily depends on temperature, which requires time for the organic matter to be buried and reactions to occur. We’ll give some more details in the next few slides.

## Slide 5: Organic Matter
Organic Productivity
  Plants or Critters
  Nutrients
  Growing Conditions
Areas of Upwelling
Clear Water
Photic Zone
Swamps
http://nicholas.duke.edu/people/faculty/cassar/images/biological_pump.png
Notes: We need organic matter to be produced and preserved within the sediments. Organic productivity can be in the form of plant matter or “critters”. This requires nutrients and other favorable growing conditions (shown in purple).

## Slide 6: Two More Factors
Organic Concentration
  Organic content >1% by weight (TOC)
  Areas with low terrigenous sediment input
Organic Preservation
  Not heavily oxidized (decomposed)
  Low oxygen environments
Away from Rivers
Stagnant Waters
Oxygen Minimum
Notes: Besides organic productivity, we need organic concentration and organic preservation. A source rock has a minimum of 1% by weight of organic material – it can get above 20% by weight. Normally this means areas where terrigenous input (sand, silt, clay/shale) is low.
If organic material is exposed to oxygen for very long, the material will oxidize and lose its potential to generate hydrocarbons (HCs). The best source rocks are deposited where oxygen levels are low, for example in a stagnant lake or swamp. We’ll look at important low-oxygen environments on the next slide.

## Slide 7: Anoxic Environments
Oxygen Minimum in a Water Column
https://uwaterloo.ca/wat-on-earth/sites/ca.wat-on-earth/files/uploads/
images/figure%202.png
http://earthguide.ucsd.edu/virtualmuseum/
images/raw/CCC_Fig4_6_1.jpg
Where oxygen levels are reduced so that oxidation (decomposition) is reduced
Oxygen Minimum on a Continental Slope
ANOXIC ZONE
Continental
Crust
Rivers
Nutrients
Sunlight
Photosynthesis
CO2
CH2O
O2
H2O
+
+

Atmosphere
Organic-rich
Sediments
Notes: In certain places, a large body of water (e.g., an ocean) can develop a water layer with anoxic conditions. Organic production is high in the photic zone. As organic matter dies and sinks, some is decomposed and this lowers the oxygen content just below the base of the photic zone. This can go to the point that an anoxic zone develops. Since decomposition does not proceed under anoxic conditions, the seafloor sediments can be organic rich. For certain geologic periods, some oceans were especially starved of oxygen. Sediments deposited at these times can become world-class source rocks (>15% total organic carbon).

## Slide 8: Favorable Geologic Periods
http://www.csus.edu/indiv/l/loom/wk%2015/mass%20extinctions.jpg
Notes: This chart shows geologic time across the top, and the colored bars represent the number of living families. There were mass extinction events at certain periods of time, which can be linked to some very rich source rock intervals.

## Slide 9: Organic Matter Types
Type I
  Algal remains deposited under anoxic conditions
  Deep lakes
  Generate waxy crude oils
Type II
  Planktonic & bacterial remains
  Marine anoxic conditions
  Generate both oil and gas
Type III
  Terrestrial plant matter
  Decomposed by bacteria and fungi, sub-oxic
  Generate gas with some light oil
Notes: Geochemists have developed a means to classify the organic material in a source rock. They speak of Type I, Type II and Type III. You can see that each type is associated with different types of remains, environments and decomposition characteristics. For me, it is very important that each type generates a different type of hydrocarbon (HC). If I had the chance to explore in one of two basins, and I knew there was Type III organic matter in the first basin and Type I organic matter in the second basin, I’d be more interested in the second basin (Type 1) since it is more likely to have oil as opposed to gas, all other factors being equal.

## Slide 10: Source Rock Properties
Total Organic Content (TOC)
  Weight % organic carbon
  Greater than 1% TOC considered a source rock
  If exceeds 15% TOC - world class source rock
Hydrogen Index (HI)
  The density of hydrogen in the rock relative to that of water (# H atoms per unit volume/# H atoms/vol in water)
  HI is the key factor in the response of a neutron porosity log
Notes: Geochemists also address two other properties of source rocks (in addition to organic matter type). We’ve talked about the first – TOC = total organic carbon (by weight %). Any rock with >1% TOC would be considered a potential source rock. About 1-5% would be a poor or lean source rock, 5-10% would be a good source rock, 10-15% would be an excellent source, and anything >15% would be a world-class source rock.
The other property is HI = Hydrogen Index. This is a measure of the hydrogen content of the source material.

## Slide 11: We Need More than High TOC
We need the raw material (organic matter) to generate oil and gas molecules
We also need the chemical reaction that converts plant & animal remains into HCs
Temperature is a primary control on the chemical reaction that we need
Temperature is controlled by the temperature gradient and depth of burial
Geochemists can model the the reactions using the Arrhenius equation
http://www.chemguide.co.uk/physical/basicrates/arrhenius.html
Notes: Thus far, I’ve talked about “potential” source rocks. High Total Organic Carbon (TOC) is great, but we need the organic matter to go through the chemical transformation that results in oil and gas. Temperature is a primary control on the chemical reaction that we need, and temperature is controlled by the temperature gradient and depth of burial. Geochemists understand the transformation process well enough that they can model it using the Arrhenius equation. For our purpose, we can leave the equation for others to study.

## Slide 12: From Organic Matter to HCs
http://www.ems.psu.edu/~pisupati/ACSOutreach/ Petroleum_2.html
  Compaction under mild temperature and pressure converts the organic material into kerogen, a dewatered waxy material
Diagenesis
  Proteins, lipids & carbohydrates are deposited with sediment
Deposition
Catagenesis
  The thermal degradation of kerogen to form HC chains. As burial depth and temperature increases, longer HC chains (oil) is cracked to shorter HC chains (gas)
Metagenesis
  Hydrogen is driven off leaving residual carbon
Diagenesis
Metagenesis
Catagenesis
Living
Organisms
Principal Zone of Oil Formation
Zone of Gas Formation
Kerogen
Lignin
Carbo-
hydrates
Proteins
Lipids
Crude Oil
Nat. Gas
Modified from Tissot and Welte, 1984. Petroleum formation and occurrence, Springer-Verlag, 699 pp.
Summary of the oil formation process
Small to Medium Hydrocarbons
Heavy HCs
And Bitumen
Methane and
Light Hydrocarbons
Notes: This slide highlights the changes that occur for organic matter. After deposition, the organic matter and sediments undergo diagenesis. The sediments are compacted and both temperature and pressure start to increase. Organic matter is transformed into kerogen, a pre-cursor of oil & gas.
Further burial with higher temperatures and pressures results in catagenesis. The hydrocarbon (HC) chains associated with oil and gas start to form. Early catagenesis is when oil forms. As catagenesis continues, the longer oil HC chains break down – it is “cracked” to gas.
The final stage is metagenesis, when hydrogen is driven off. Now we are talking about graphite and diamonds.

## Slide 13: Van Krevelen Diagram
https://geochemist.wordpress.com/2009/01/08/evolusi-termal-material-organik-2/
If we plot the O/C ratio vs. the H/C ratio:
  The three organic matter types (OMTs) can be distinguished
  The degree of diagenesis to catagenesis can be determined
Notes: Here is what is called a Van Krevelen diagram. The X axis is the oxygen/carbon (O/C) ratio, and the Y axis is the hydrogen/carbon (H/C) ratio.
Notice that the three organic matter classes are differentiated. Note also how the ratios decrease as the chemical transformation proceeds. The green zone is where CO2, CH4 and H2O are generated, the blue zone is where oil is generated, and the black zone is where gas is generated.

## Slide 14: Basin Modeling
We can use computer software to model a basin’s history
This modeling can be:
  1-D – modeling a well location (or pseudo-well)
  2-D – model a cross-section (between wells)
  3-D – use a series of grids to model a region
We start with present-day stratigraphy
We back-strip from present to past times (geohistory)
We calibrate with temperature data and current indicators of HC generation states
Then, we can forward model through geologic time to get source and reservoir properties
Notes: How do we use all this geochemical information? We have computer software that will model a basin’s history. This modeling can be done for a single location, like where a well is or is planned. It can also be done for a cross-section (2D model) or with a set of grids (3D model).
We start with the present-day stratigraphy, and back-strip from present to past times (something commonly called geohistory). We then calibrate the model using temperature data and current indicators of HC generation states. Once we have bootstrapped the basin back through time, we can forward model through geologic time to get source and reservoir properties through time.

## Slide 15: Basin Modeling
0 Ma
18 Ma
29 Ma
36 Ma
42 Ma
Back-strip the
Present-day
Strata to
Unravel
the Basin’s
History
Time Steps are
Limited to Mapped Horizons
Model Rock
& Fluid Properties
Forward through Time
Time Steps are
Regular Intervals as Defined by the User
Notes: Here is a simple cross-section with four (4) major depositional units shown by brown, orange, yellow and green. We can back-strip each unit and estimate the basin’s shape – unit by unit. We do need to predict paleo-water depths, and are limited to the ages of the interpreted horizons – here 18 Ma, 29 Ma, 36 Ma and before deposition began at 42 Ma.
After we do the back-stripping, we can estimate the parameters that controlled the basin’s development, such as: subsidence rates through time, sediment supply through time, paleobathymetry, and some estimate of sea level change through time. We can then use basin simulation software to model the basin forward through time. We can use a much smaller time step, e.g., ½ million year. We can also model temperatures, pressures, hydrocarbon (HC) generation, porosity changes, etc.

## Slide 16: Back-Strip for Burial History
165
178
172
198
70
30/0
155
110
145
130
0
1
2
3
4
5
6
7
Present Day
Stratigraphy
Depth (km)
Geologic Ages (MY)
Present Day Sea Level
From an existing well, we can get present day stratigraphy:
  Age-depth pairs (e.g., 198 Ma, 6725 m)
  Lithology of each major interval
  Paleo data for ages and water depths
Software allows us to step back in time by progressively removing the top layer
We datum each time step based on present day sea level or our favorite SL curve
This gives us a model for how the basin subsided and was filled with sediment
We also “de-compact” the sediments as we move back through geologic time
Well A
We can also use seismic-derived stratigraphy to model pseudo-wells
Notes: We will walk through an example of the analyses we can do for a single location (1D model). From a well (or an interpreted seismic line) we can get the present-day stratigraphy. We input the needed data into a software program that does the back-stripping for us. We get a model for how the basin subsided and filled with the sedimentary units (sequences). Most software packages will “de-compact” the sediment back through time.

## Slide 17: Back-Strip for Burial History
165
178
172
198
70
30/0
155
110
145
130
0
1
2
3
4
5
6
7
Depth (km)
Present Day
Stratigraphy
Geologic Ages (MY)
Well A
0
110
100
90
80
70
60
170
190
180
160
150
140
130
120
200
50
40
30
20
10
Present Day Sea Level
Sources of Uncertainty:
  Ages of tops
  Paleowater depth
  Litho (compaction)
  Amount of eroded section
  Injected salt
Notes: This is a geohistory or burial history diagram. At this scale, we assume sea level is constant. The present-day strata are back-stripped and decompacted. Also we include our understanding of how water depths vary throughout time (paleo-bathymetry). For the location of Well A, we have a model for how this point subsided and was filled with sediment (and ocean water).

## Slide 18: Components of Total Subsidence
165
178
172
198
70
30/0
155
110
145
130
110
100
90
80
70
60
170
190
180
160
150
140
130
120
200
50
40
30
20
10
0
Present Day Sea Level
0
1
2
3
4
5
6
7
Depth (km)
Present Day
Stratigraphy
Geologic Ages (MY)
Well A
Continental
Crust
The crust at Well A is extended (thinned) continental crust
Total subsidence is the combined effect of the tectonic-thermal effect of the local extension
and the weight of the deposited sediments
Knowing the stratigraphy, we can estimate the effect of the weight of the sediments
Notes: Our geohistory analysis has given us the total subsidence for our deepest (oldest) horizon. Let’s say for our case this is the subsidence of the continental crust. We can consider that total subsidence consists of two major components: 1) the tectonic (including thermal) forces that gave rise to basin formation, and 2) the weight of the sedimentary column. Since we have information about the sediments, we can estimate the weight component. With both total subsidence and the weight component through time, we can get an estimate of the tectonic-thermal component: (Total – Weight = Tectonic-thermal)

## Slide 19: Extensional Margins
Lithosphere
Continental Crust
Mantle
MOHO
Oceanic Crust
Asthenosphere
Sediments
35 Km
10 Km
Continental Crustal
Extension
50%
100%
0%
Full
Zero
Oceanic Crust
Notes: Extensional or pull-apart continental margins (like both sides of the North and South Atlantic) have yielded many oil and gas fields. We have a good understanding for these extensional margins (here we will keep things simple - modern advanced models are now available). For an Atlantic-type margin, the continental crust is extended (stretched) from a thickness of about 35 km (un-stretched) to fully extended where it meets oceanic crust, which is about 5 km thick. Thus, on a cross-section across this type of margin, extension goes from 0% to 100%, as shown. It turns out that we have some theoretical work on how the crust would subside as a function of its degree of stretching if no sediment weighed it down. The theory also tells us about heat flow as a function of its degree of stretching.

## Slide 20: Theoretical Post-Rift Thermal Subsidence
Royden et al. (1980) used the subsidence of oceanic crust (100% extension) to develop several models of how extended continental crust would subside in the absence of sediment load
These curves are for their dike injection model
Modified from Hardenbol, Vail and Ferrer (1981)
0.1
0.2
0
0.3
0.4
0.5
0.6
0.7
0.8
0.9
1.0
110
100
70
60
170
190
180
160
150
140
130
120
200
50
40
30
20
10
0
90
100
110
120
130
140
30
10
20
40
50
60
70
80
0
150
160
170
180
190
200
0
1
2
3
4
5
6
7
Sea Level
Time since Rifting (MY)
Geologic Time (MY)
90
80
35
32
36
28
26
23
20
17
14
11
0
Oceanic Crust
Continental Crust
Crust Thickness
Fraction of Continental Crust Thinning
Time of Rifting
Notes: The red curves represent how, in theory, continental crust should subside after rifting as a function of crustal stretching. The lowest curve, 100% stretching, was derived from profiles out from mid-ocean ridges. These red curves are tectonic-thermal curves for extensional margins. You see where we are going, don’t you?

## Slide 21: Components of Total Subsidence
165
178
172
198
70
30/0
155
110
145
130
110
100
90
80
70
60
170
190
180
160
150
140
130
120
200
50
40
30
20
10
0
Present Day Sea Level
0
1
2
3
4
5
6
7
Depth (km)
Present Day
Stratigraphy
Geologic Ages (MY)
Well A
Continental
Crust
The subsidence due to the weight of the sediments
The subsidence due to the tectonic-thermal effect of the local extension
70% Thinning
Time of
Sag
Notes: Here is our geohistory diagram that shows only: total subsidence (red line), the sediment weight (tan region) and the remaining tectonic-thermal subsidence (magenta line).
The dashed black line is the thermal subsidence associated with 70% crustal thinning for a rift event that ended about 180 MY ago. Further landward of Well A, thinning would have been less; further basinward it would have been more. This is important information for predicting paleo-heat flow around Well A. We can match the tectonic-thermal subsidence (magenta line) with the dashed black line to estimate the amount of stretching at this location and infer the paleo-heat flow.

## Slide 22: Heat Flow
165
178
172
198
70
30/0
155
110
145
130
110
100
90
80
70
60
170
190
180
160
150
140
130
120
200
50
40
30
20
10
0
Present Day Sea Level
0
1
2
3
4
5
6
7
Depth (km)
Present Day
Stratigraphy
Geologic Ages (MY)
Well A
Time of
Sag
Time of
Rifting
Heat Flow
History
Background (crustal) Heat Flow
Heating and then Cooling due to Rifting
2.2
1.8
1.4
1.0
70% Thinning
Notes: For an extensional margin, heat flow has two components: a background heat flow, and extra heat associated with continental extension and the rising asthenosphere.
For our study location, we assume a background heat flow of 1.2 HFU (heat flow units). To this we add the heat associated with rifting to the point of 70% crustal thinning (from our tectonic-thermal subsidence curve).
Outside our scope: We enter this paleo-heat flow estimate to the basin modeling software, and it predicts temperatures through time. One way to calibrate this temperature history is to check predicted present-day temperatures against measured temperatures. We also have some paleo-temperature methods, but these are

## Slide 23: Temperatures
0
1
2
3
4
5
6
7
Well A
Present Day
Stratigraphy
165
178
172
198
70
30/0
155
110
145
130
Depth (km)
Geologic Ages (MY)
Temperature
120
40
80
160
200
0
Software allows us to model the temperature history of each depositional unit
Present temperatures from well data can be used to calibrate the thermal model
In this case, we have a reasonable match between measured and predicted temperatures
Thus, we can model the HC generation history of our source unit(s)
Present Day
Temperature
Profile
Notes: How good is our temperature model? When Well A was drilled, they obtained temperature data at seven (7) depths (black dots). Our model for today’s temperature profile fits the measured data quite well. Usually several iterations are necessary to get this good a fit. Background heat flow and the stretching factor are adjusted to get a reasonable match. If several wells with temperature data are in an area of interest, then each well is modeled and the goal is to have a spatially consistent model. For example, if two wells are only a couple of miles apart, you would not expect background heat flow to be significantly different for each.
This same methodology can be done for a cross-section (2D model) or for a region (3D model using input grids). 3D models are superior because there are important 3D effects that we can not include in 1D models.

## Slide 24: Vitrinite Reflectance
Organic material from cores or cuttings can be examined under a microscope
Specialists can determine how shiny the vitrinite particles are
Vitrinite reflectance is a measure of how hot the rocks have been – a paleo-thermo- meter
Thus, we can also calibrate our temperature history using this type of data
0
1
2
3
4
5
6
7
Well A
Present Day
Stratigraphy
165
178
172
198
70
30/0
155
110
145
130
Depth (km)
Geologic Ages (MY)
Vitrinite Reflectance (Ro)
0.9
0.5
0.7
1.1
1.3
0.3
Present Day
Ro
Profile
Notes: We have another way to test our temperature model. As organic matter is “cooked” it changes appearance. Geochemists examine samples under a microscope and determine how shiny the vitrinite particles are. They have a scale, called vitrinite reflectance (Ro), that indicates how hot the source rock was. Ro is a subjective scale, so it is not as precise as temperature (error bars on Ro are wide). This slide shows a predicted Ro curve (green line) with measured data. Given the subjective nature of Ro data, this is not a bad fit.

## Slide 25: Hydrocarbon Generation
Ro can be linked to when oil and gas are being generated
The oil window is about Ro values of 0.55 to 0.95
The gas window is about Ro values of 0.95 to 2.2
For each modeled location (real or pseudo-well) we can get a depth for the tops and bases of these windows
If results are fairly consistent, we can use depth maps to outline oil and gas generation areas
0
1
2
3
4
5
6
7
Well A
Present Day
Stratigraphy
165
178
172
198
70
30/0
155
110
145
130
Depth (km)
Geologic Ages (MY)
Vitrinite Reflectance (Ro)
0.9
0.5
0.7
1.1
1.3
0.3
Present Day
Ro
Profile
Top of Oil Window
Top of Gas Window
Notes: Once we have a satisfactorily calibrated temperature model, we can start to work on HC generation. The Ro value for the onset of oil and gas generation varies a little bit based on the organic matter type (I, II or III). For our discussion, we will say that oil generation starts at an Ro value of 0.55 and that gas generation starts at 0.95. Using the diagram on the previous slide (also repeated here), we can predict a depth for the top of the oil window of 3400 m. Similarly, we predict the top of the gas window to be at 5600 m.

## Slide 26: Source & Generation Analysis
Use available data to identify intervals that could be potential source rocks
Collect TOC, HI, temperature and Ro data in and around your area of interest
Select locations to model subsidence, fill and temperature histories
    Actual well locations
    Pseudo-well locations using seismic-derived stratigraphy
Run initial models
Calibrate models using temperature data, Ro data and areal consistency
Develop a depth vs. Ro relationship
Use this relationship and depth maps for the top/base of the source interval(s) to map the oil generation ‘window’ and the gas generation ‘window’
Notes: This slide summarizes the steps in our analysis – reviews what we just did for Well A.

## Slide 27
Questions?

## Slide 28: References
Slide 5: http://nicholas.duke.edu/people/faculty/cassar/images/biological_pump.png
Slide 7: http://earthguide.ucsd.edu/virtualmuseum/images/raw/CCC_Fig4_6_1.jpg
Slide 7: https://uwaterloo.ca/wat-on-earth/sites/ca.wat-on-earth/files/uploads/images/figure%202.png
Slide 8: http://www.csus.edu/indiv/l/loom/wk%2015/mass%20extinctions.jpg From Discovery Biology, 2006, W. W. Norton & Company
Slide 11: http://www.chemguide.co.uk/physical/basicrates/arrhenius.html
Slide 12: http://www.ems.psu.edu/~pisupati/ACSOutreach/Petroleum_2.html Modified from Tissot and Welte, 1984. Petroleum formation and occurrence, Springer-Verlag
Slide 13: https://geochemist.wordpress.com/2009/01/08/evolusi-termal-material-organik-2/
Slide 20: Modified from Hardenbol, Vail and Ferrer (1981) Interpreting paleoenvironments, subsidence history, and sea-level changes on passive margins from seismic biostratigraphy--26th International Geological Congress, Geology of Continental Margins: Oceanologica Acta, Supplement, v. 4, p. 33-44.
Slide 20: Roydon, L., Sclater, J>G> and von Herzen, R.P., 1980. Continental margin subsidence and heat flow: Important parameters in formation of petroleum hydrocarbons. AAPG Bulletin, V. 64, p. 173-187.
Slides 30-42: Schroeder & Sylta, 1993, Modelling the hydrocarbon system of the North Viking Graben: a case study, in Dore et al (ed.), Basin Modelling: Advances and Applications, NPF Special Publication 3, Elsevier, pp. 469-484.

## Slide 29
Supplemental
Notes: The following twelve (12) slides present a case study from the Norwegian North Sea. It was done in 1990, so it is not as sophisticated as what we can do with current technology.
You might not want to show this in class due to time constraints, but you may want to consider having the students review it on their own as they work the exercise.

## Slide 30: Study Area
Study Area was 100 x 250 km
This slide and the ones that follow are from:
Schroeder & Sylta (1993), Modelling the hydrocarbon system of the North Viking Graben: a case study, in Dore et al (ed), Basin Modelling: Advances and Applications, NPF Special Publication 3, Elsevier, pp. 469-484.
Notes: This starts a case study done in 1990 in preparation for a Norwegian lease sale. The area is in the central North Sea to the west of Bergen. Nine (9) oil/gas fields are in the area. The blue circles on the right map are the location of wells that were used to calibrate the basin model.

## Slide 31: North Viking Graben Example
Draupne Shale
Facies
Change
Sognefjord Shale
Heather Shale
Brent Sand with Coals
Schroeder & Sylta [1993]
Main Source: Draupne – Type 1, TOC > 18%, high HI, moderately thick, widespread
Secondary Source: Brent Coals – Type 3, TOC 30%, low HI, thin, patchy
1 km
7 km
Notes: Here is a block diagram for the eastern side of the central North Sea rift. The Brent formation is the oldest rocks we are interested in. Brent sands are our reservoir and migration path rocks. There are some coals within the Brent, which is the secondary source rocks.
On top of the Brent, the Sogenefjord shales and then the Heather shales were deposited. Far to the east (landward) the Heather changes to a nearshore sand facies.
Next to be deposited was the Draupne shale, which is a world-class source at TOC > 18% because anoxic conditions existed during deposition. The equivalent rocks on the English side of the North Sea are called the Kimmeridge clay, much better known (famous) than the name Draupne. After deposition of the Draupne/Kimmeridge clay there was a major unconformity with erosion of paleo-highs (base of Cretaceous unconformity).
The North Sea is a failed rift system, so there are large rotated fault blocks, which form the traps. The seal is either the Draupne shale or Early Cretaceous deep marine shales.

## Slide 32: Four Basic Steps
Schroeder & Sylta [1993]
Notes: There were four (4) major steps in the study. The ultimate goal for the study was to predict HC generation, migration and trap fill as part of the analysis of blocks up for bids.
Step 1 was to compile the available data needed to build the basin model. There was well data and seismic data. Step 2 was to model HC generation.

## Slide 33: Modeling HC Generation – Phase 1
35 wells were selected to model (based on available temperature & Ro data)
35 1-D Geohistory analysis
Basement was unloaded (1-D) to obtain the amount of crustal thinning at each site
Dike injection model was used to predict heat flow through time
The temperature model was calibrated using well temperature and Ro data
HC generation & expulsion was modeled forward through geologic time for 2 source intervals
Areal consistency was obtained by compiling a folio of maps (e.g., crustal thinning, paleo-water depths for each mapped horizon)
Schroeder & Sylta [1993]
Notes: Step 2 was subdivided into two (2) phases. Phase 1 focused on well location and well data. Phase 2 focused on seismic data. We had thirty-five (35) wells with the data we needed, including temperature and vitrinite reflectance information. We worked the 1D geohistory analysis described in the lecture. This included: Subsidence analysis, Estimating the tectonic-thermal component of subsidence, Getting a crustal stretching value for each location, Predicting heat flow through time, Calibrating the model with the temperature and vitrinite reflectance data, and Modeling HC generation and expulsion from the source rocks through time.
We plotted many of our 1D input variables and output values (e.g., crustal thinning) on basemaps to make sure all the data had reasonable spatial variations.
For example, the stretching factor should be lowest to the east and greatest towards the center of the rift (west).

## Slide 34: 1-D Subsidence History
Two phases of rifting that are tied to regional North Sea geology
Ɣ = % crustal thinning
E Jr Rifting
Early K Rifting
Ɣ = .12
Ɣ = .53
Geologic Time (MY)
Depth (m)
Schroeder & Sylta [1993]
Notes: Here is one of the geohistory diagrams. Regional studies suggest two rifting events: a smaller event during the Early Jurassic and a more significant one in the Early Cretaceous. For this well location, we determined a crustal stretching factor of 12% for the first rifting event and 53% for the second.

## Slide 35: 1-D Predicted Heat Flow History
E Jr Rifting
Early K Rifting
Geologic Time (MY)
Depth (m)
Rifting Events
Schroeder & Sylta [1993]
Notes: We used these timings and stretching factors to predict heat flow at this location from the Late Triassic to the present.

## Slide 36: 1D Temperature Calibration
Area Trend is derived from Ro data from 8 other wells in the vicinity of this well
TEMPERATURE DATA
°C
VITRINITE DATA
%
Depth of Interest
Depth (m)
Top of Oil Window at 2550 m
Schroeder & Sylta [1993]
Notes: How good was our model? This shows measured temperature and vitrinite reflectance as a function of depth versus our predicted values. Predicted temperatures are too hot for the Tertiary, but not bad for the depths we are interested in, where the Jurassic source intervals lie.

## Slide 37: Draupne Bed History
Top of interval
Base of interval
Temp
Ro
Temperature (°C)
Vitrinite Reflectance (%)
Geologic Time (MY)
Oil Generation
Schroeder & Sylta [1993]
Notes: The calibration allowed us to predict the timing and amount of HC generation fro the Draupne at this location through time. For the organic matter in the Draupne, oil generation starts at Ro = 0.60, thus oil generation started around 28 MY ago.

## Slide 38: Draupne Cumulative Oil & Gas Yield
Gas
Cumulative Oil Yield
(gm HC/100 gm OTOC)
Geologic Time (MY)
Cumulative Gas Yield
(gm HC/100 gm OTOC)
Oil
Onset of oil generation is Late Oligocene
Onset of gas generation
is Earliest Miocene
Schroeder & Sylta [1993]
Notes: Here is the cumulative yield for oil (left scale bar, green line) and for gas (right scale bar, red line).

## Slide 39: Areal Consistency
35 Data Points from Calibration Wells
Horizon time/depth
Crustal Thinning
Paleo WD
% sand, silt, clay
Paleo HF
OTOC
HI
Eff. Source thick (2)
Organic matter type
Cum. Oil generation
Cum Gas generation
PASS 1
Suite of Maps for end time of each Interval
Horizon time/depth
Crustal thinning
Paleo WD
% sand, silt, clay
Temperature
OTOC
HI
Eff. Source thick (2)
Organic matter type
Cum. Oil generation
Cum Gas generation
Input/Output
Maps
Schroeder & Sylta [1993]
Notes: After examination of the thirty-five (35) well locations, we made maps of the various input and output parameters. In most cases, reasonable map patterns were observed. If something looked anomalous, we iterated so that we had reasonably consistent maps.

## Slide 40: Additional Sites
193 Additional Points were Modeled
Horizon time/depth
Crustal Thinning
Paleo WD
% sand, silt, clay
Paleo HF
OTOC
HI
Eff. Source thick (2)
Organic matter type
Cum. Oil generation
Cum Gas generation
PASS 2
Suite of Maps for end time of each Interval
Horizon time/depth
Crustal thinning
Paleo WD
% sand, silt, clay
Temperature
OTOC
HI
Eff. Source thick (2)
Organic matter type
Cum. Oil generation
Cum Gas generation
Input
Output
Schroeder & Sylta [1993]
Notes: At this point, we had thirty-five (35) 1D models with some imposed spatial consistency. We wanted more control points for our final model, so we selected 193 additional points to generate pseudo-wells, what we would expect if we were to drill at these 193 locations. We used seismic horizons to give us present-day stratigraphy (age-depth pairs), and paleo-bathymetric maps from Phase 1 to set water depths through time. Of course we did not have temperature or vitrinite reflectance data to calibrate our pseudo-well locations.
Why add point? If you think about it, we tend to drill highs (anticlines). Thus there is a bias in our available data. Our “kitchens” are in lows (synclines). So we tend to pick pseuso-well locations in the synclines – where the HC generation action is located.

## Slide 41: Depth Map for a Portion of the Area
Top of Oil Window
Top of Gas Window
Schroeder & Sylta [1993]
Notes: Here is a color-coded depth map to the top of the Brent reservoir. The names are fields: Huldra, Oseberg, etc. For the underlying Draupne source, the oil window starts at the middle of the yellow depth range. The top of the window is in the deep purple depth range.

## Slide 42: Present Day HC Generation Prediction
Remember, this is present-day HC generation. This point went through the oil window before it entered the gas window.
Top of Oil Window
Top of Gas Window
Oil Window
Gas Window
Schroeder & Sylta [1993]
Notes: Here is the same map, but this time color-coded based on HC generation for the Draupne source. Most of the area is in the oil generation region. The deepest area, colored red, is where the Draupne is in the gas only generation stage. Light yellow in the SE is where the Draupne is not generating – it is immature.