## Slide 1: Exercise
Exercise: Shelf Margin Sands
Analyzing Seismic Sequences for Reservoir Sands
Your Task:
  Use data provided to analyze two shelf margin sequences

## Slide 2: Introduction
You have learned about several environments where reservoir-quality sands can be deposited - one of these is near a shelf margin. We will use the terminology of Rich (1951).
We will use eight (8) seismic lines that were acquired and processed in the 1970s. Data quality is poor by today’s standards. In addition, the lines have been compressed to fit a single page. In spite of these two facts, we can still use seismic geometries to make some interpretations.
Shallow
Notes: This exercise focuses on a shelf to slope to basin environment of deposition. This slide shows terminology defined by Rich (1951).
Students will be mapping the extent of the: Undaform, Clinoform, and Fondoform on several 2D seismic lines. These geometries are easy to identify.

## Slide 3: Definitions
The following four (4) slides give abbreviated definitions, with an example from Line C for the BLUE to PINK seismic sequence. More complete definitions are in the instructions.
Notes: Here is Line C with five (5) mapped horizons (orange, blue, pink, red, green). The pink to blue interval (sequence) is highlighted.
This line has been subdivided into 4 units:
Shallow: where the thickness is three or less ½ cycles (a ½ cycle is a black peak or a white trough),
Undaform: where the top is relatively horizontal as the shelf built out,
Clinoform: where the top dips down as a continental slope, and
Fondoform: where the sequence is thin as the top flattens on the abyssal plain.

## Slide 4: Shallow
Shallow: where the sequence is quite thin, and usually has parallel to slightly inclined reflections. This facies tends to thin to below seismic resolution updip; it often thickens in a downdip direction.
Notes: Line C with the criteria for “shallow”.

## Slide 5: Undaform
Undaform: where the sequence thickens considerably as deposition extends beyond the previous shelf edge. It extends downdip to the final shelf edge. The top of the undaform was deposited near wavebase and this high-energy environment often leads to sandy lithofacies.
Notes: Line C with the criteria for “undaform”.

## Slide 6: Clinoform
Clinoform: just downdip from the final shelf edge. The interval thins as the paleobathymetry increases. This is a lower energy environment resulting in mostly silt and shale deposition. The reflections are normally inclined, dipping down in a basinward direction.
Notes: Line C with the criteria for “clinoform.”

## Slide 7: Fondoform
Fondoform: basinward of the final toe (base) of the paleo-slope. Shales and pelagic clays are the expected lithologies. The reflections are parallel to subparallel. The unit is often thin and can get below seismic resolution in a downdip direction.
Notes: Line C with the criteria for “fondoform.”

## Slide 8: Procedure
Select 1 of the 4 sequences to analyze first (e.g., BLUE to PINK)
Complete Table 1 by noting the approximate shot point location where there is a transition from one zone to another
Mark the positions you recorded along each seismic line on the base map. It is helpful to color-code each zone on the base map
Notes: Students can fill out this table for any sequence (e.g., BLUE to PINK). Space is provided for each of the 7 seismic lines. They are to record the shot point (from the seismic line) where the transitions occur. When they fill this out for a sequence, then it is easy to mark each boundary on the map. They will do TWO sequences using Table 1 for their first and Table 2 for their second.

## Slide 9: Procedure, cont.
Can you draw a smooth boundary connecting each of the four (4) seismic facies boundaries on all the lines? If not, can you reinterpret the positions of the boundaries in Table 1 so that there is lateral consistency?
Based on your map, where would you predict the best sands to be located?
Select a second depositional sequence for the same type of analysis. Repeat steps 2 through 5 for your second sequence. Table 2 is provided for recording your observations for your second seismic sequence.
Notes: Part 2 of the procedure (as given on the word document). This has them using the data entered in the table to make a map of environments for the sequence they choose.

## Slide 10: Hint
Sea Level
Depositional
Model
High Energy
Low Energy
Moderate Energy
Notes: This will help them answer the questions about the best reservoir. The high energy environment (yellow) has the best quality reservoir rocks. Waves, tides and storms periodically stir up the sediment. The coarser (bigger and heavier) particles settle quickly so don’t move very far. The finer particles (silt & clay/shale) stay suspended in the sea water longer and move further offshore before settling out (being re-deposited). Thus, the sediment in the high energy environment get “cleaned up” and have better reservoir quality – IF sand was coming down the rivers at the time of deposition. The high energy environment concentrates the coarsest grain size available, which could be pebbles, coarse sand, fine sand, or silt.

## Slide 11
Questions?