## Slide 1: Petroleum Geology & Geophysics
Reservoir Rocks
A “Kitchen”
Where Organic
Material Is
Cooked
“Plumbing” To Connect the Container to the Kitchen
Source
Migration
Where HCs Accumulate
Reservoir
Trap
Seal
Notes: This unit gives a very simple overview of reservoir rocks. This is a huge area of study and information; we’ll discuss only conventional clastic reservoirs, after a brief introduction.

## Slide 2: Elements and Processes
Essential Elements
Source rocks
Reservoir rocks
Seal rocks
Overburden rocks
Major Processes
Trap formation
Hydrocarbon
  Generation
  Migration
  Accumulation
Source
Migration
Reservoir
Trap
Seal
Notes: Hydrocarbon (HC) system elements and processes, with reservoir rocks marked.

## Slide 3: Reservoir Rocks
A Reservoir Rock is one from which oil & gas can be extracted from wells and brought to the surface
It must have:
1. Void space in the rock for HC molecules to occupy
2. Sufficient “plumbing” so the HC molecules can escape from the rock
Porosity
Permeability
Notes: A simple definition of a reservoir rock. A reservoir rock is one from which oil & gas can be extracted from wells and brought to the surface. A reservoir must have two rock properties: 1) space (porosity), and 2) sufficient plumbing (permeability).

## Slide 4: Porosity
Porosity (commonly symbolized as Φ) is a measure of the void (i.e., "empty") spaces in a material, and is a fraction of the volume of voids over the total volume (between 0 and 100%).
From Wikipedia
Influence of structure and texture of a porous medium on porosity:
a) poorly graded uniform granular material in which particles have their own porosity system;
b) well graded granular material with small particles filling the big pores;
c) partially closed discontinuity systems appeared in an intact porous rock due to active water;
d) open discontinuity systems appeared in an intact rock due to mechanic fracturing.
(from Freeze and Cherry, 1979 after Meinzer, 1923)
http://echo2.epfl.ch/VICAIRE/mod_3/chapt_1/main.htm
Notes: Definition of porosity (commonly symbolized as Φ).

## Slide 5: Permeability
Permeability (commonly symbolized as κ) is a measure of the ability of a porous material (often, a rock or an unconsolidated material) to allow fluids to pass through it.
From Wikipedia
http://petroleum101.com/what-is-a-petroleum-reservoir/
Without enough permeability in the rock, the oil and gas would not be able to flow and it would remain trapped in the reservoir rock. Permeability is really an expression about how interconnected the pores and natural fractures in the rock are.
Permeability and porosity are the two most important characteristics of a reservoir, and are studied intensely by asset evaluation teams.
Notes: Definition of permeability (commonly symbolized as κ).

## Slide 6: Types of Reservoirs
Conventional
Reservoirs
Unconventional
Reservoirs
Clastic
Carbonate
Tight Oil/Gas Sands
Shale Oil/Gas
Coal Bed Methane
Traditional methods are used to extract HCs from reservoir-quality rocks within some type of trap
New methods are used to extract HCs from non-reservoir-quality rocks often within source intervals
Notes: This slide categorizes conventional reservoirs and unconventional reservoirs (aka. resource plays). We have clastic reservoirs, where the grains are typically made if quartz. We also have reservoirs in carbonate rocks (limestones, dolomites).
The big exciting development in the last few years are unconventional plays. Rocks with low porosity and permeability are being tapped for their HCs. The development of horizontal drilling and hydraulic fracturing (hydrofracking) has led to this new type of production.

## Slide 7: Clastic Reservoirs
Conventional
Reservoirs
Clastic
Carbonate
Alluvial Fans
Aeolian Dunes
Fluvial
Shoreline
Delta
Deep Water
Notes: We will look briefly at these six (6) common clastic reservoir rocks. This scheme is based on the environment of deposition (EOD) of the sands.

## Slide 8: Alluvial Fans
An alluvial fan is a fan- or cone-shaped deposit of sediment crossed and built up by streams. These flows come from a single point source at the apex of the fan, and over time move to occupy many positions on the fan surface. Fans are typically found where a canyon draining from mountainous terrain emerges out onto a flatter plain, and especially along fault-bounded mountain fronts.
http://imgkid.com/alluvial-fan.shtml
From Wikipedia
http://imgkid.com/alluvial-fan.shtml
Notes: Definition of an alluvial fan. Alluvial fans reflect a high energy EOD, when heavy rains or spring thaws results in a lot of water and sediment being flushed out of mountainous terrain. Coarse rocks are concentrated in alluvial fans, finer sediment is carried downstream. Alluvial fans can be great reservoirs with high porosity and permeability.

## Slide 9: Aeolian Dunes
A dune is a hill of sand built when sand grains interact with either wind or water flow. Most kinds of dunes are longer on the windward side where the sand is pushed up the dune and have a shorter "slip face" in the lee of the wind. A "dune field" is an area covered by extensive sand dunes.
http://www.summitpost.org/mesquite-flat-dunes-highpoint/276799
From Wikipedia
http://geography.howstuffworks.com/terms-and-associations/sand-dune1.htm
Notes: Definition of aeolian dunes. Aeolian deposits are associated with strong winds and water. Coarse grains are moved along the surface, forming sand dunes.

## Slide 10: Fluvial
Fluvial (Rivers)
  Braided Rivers
  Meandering Rivers
http://en.wikipedia.org/wiki/File:Meandering_River_2_Innoko_NWR.jpg
http://en.wikipedia.org/wiki/File:Toklat_River_-_East_Fork_01.jpg
Notes: Fluvial deposits are associated with river systems. There are two end members of fluvial systems: braided rivers and meandering rivers.

## Slide 11: Braided Rivers
A braided river is one that has a channel that consists of a network of small channels separated by small and often temporary islands. Braided streams occur in rivers with high slope and/or large sediment load. They are also typical of environments that dramatically decrease channel depth and channel velocity.
http://intheplaygroundofgiants.com/the-geology-of-sedimentary-rocks/
http://www.tulane.edu/~sanelson/eens1110/streams.htm
From Wikipedia
Notes: Definition of a braided river. Braided rivers are characteristic of higher-gradient surface topography.
Note the ideal facies sequence in the lower right. The sands vary from medium to coarse sands and even gravels.

## Slide 12: Meandering Rivers
A meander, a bend in a sinuous river, forms when moving water erodes the outer banks of a bend and widens its valley. The inner bend has less energy and sands or silts are deposited. A stream of any volume may assume a meandering course, alternately eroding sediments from the outside of a bend and depositing them on the inside.
From Wikipedia
http://intheplaygroundofgiants.com/the-geology-of-sedimentary-rocks/
http://intheplaygroundofgiants.com/the-geology-of-sedimentary-rocks/
Notes: Definition of meandering rivers. A meandering river is one that bends in a sinuous pattern. This is characteristic of low-gradient surface topography.
Note the ideal facies sequence in the lower right. There can be gravel at the base of the deposit and grain size fines upward.

## Slide 13: Shoreline
A shoreline is where an ocean, sea or lake intersects the land. It usually consists of loose particles of rocks. Waves and tides concentrate the coarsest size grains, winnowing out finer size grains. Shoreline deposits are well sorted an can consists of a dominant grain size from fine sand to cobbles.
Swash zone: is alternately covered and exposed by wave run-up.
Beach face: sloping section below berm that is exposed to the swash of the waves.
Wrack line: the highest reach of the daily tide where organic and inorganic debris is deposited by wave action.
Berm: Nearly horizontal portion that stays dry except during extremely high tides and storms. May have sand dunes.
http://en.wikipedia.org/wiki/Beach
Notes: Definition of shoreline sands. Shoreline sands are deposited near where large bodies of water intersects the land (beaches). The photo describes different zones near a shoreline.

## Slide 14: Shoreline Environments
http://3dparks.wr.usgs.gov/nyc/shoreline/beaches.htm
Notes: This diagram shows some typically shoreline environments of deposition (EODs) and sedimentary deposits. The movement of water, waves, tides, storms, rivers, offer a lot of opportunities to stir up sediment, have the coarsest grain size get “cleaned up” while finer sized particles are “winnowed out.”

## Slide 15: Deltas
A river delta is a landform that forms at the mouth of a river, where the river flows into an ocean, sea, estuary, lake, or reservoir. Deltas form from deposition of sediment carried by a river as the flow leaves its mouth. Over long periods, this deposition builds the characteristic geographic pattern of a river delta.
http://en.wikipedia.org/wiki/File:Mississippi_Delta_Lobes.jpg
http://en.wikipedia.org/wiki/File:Mississippi_delta_from_space.jpg
From Wikipedia
Notes: Where a major river intersects the ocean, a delta may form. This slide describes the definition of deltas. The picture on the left is a picture from space of the modern Mississippi River delta. The picture on the right is a map showing how the location of the delta has switched in the last thousand years.

## Slide 16: Types of Deltas
http://echo2.epfl.ch/VICAIRE/mod_3/chapt_3/main.htm
Marine Muds
Paralic muds and peats
Channel and barrier sands
Non-deposition
River Dominated
Tide Dominated
Wave Dominated
Notes: The morphology and sand distribution in a delta varies with the dominant force. The upper left is a sketch of a delta were tides are the dominant force. The upper right represents what we get if the river is the dominant force. The lower sketch is for a wave dominated situation. Which one do you think is appropriate for the Mississippi Delta?

## Slide 17: Delta – Environments of Deposition (EODs)
Delta Plain
Delta Front
Delta Slope
Basinal
http://pixshark.com/nile-delta.htm
Sea Level
Notes: Here is an image of the Nile Delta with an overlay of deltaic EODs. The cross-section uses the same EOD color-codes to show the lateral and vertical succession of deltaic facies. Delta-front sands have the best reservoir characteristics. Waves and storms stir these sediments on occasion, which puts all the sediment into suspension. The coarser (heavier) grains fall to the seafloor first, fast, and without moving too far. The finer sediment particles stay in suspension longer and drift further offshore. Thus, the yellow delta-front EOD is what we want to target – coarser grains and well sorted – good porosity and permeability.

## Slide 18: Seismic Line through a Delta
Delta Front
Delta Plain
Delta Slope
Basinal Shales
Basinal Shales
Deep Water Fans
6
7
5
4
3
2
1
8
Image Courtesy of ExxonMobil
Notes: Here is a color-coded seismic section. The seismic reflections show deltaic progradation geometries. Note the delta plain (brown), delta front (yellow), and delta slope (light green) environments of deposition (EODs). The yellow zones are where we would expect the best reservoir-quality sands.

## Slide 19: Continental Margin Geomorphology
Sea Level
Undaform
Fondoform
Clinoform
Terminology of Rich (1951): Alternate Terminology
Undaform – shallow water deposits of the shelf - - - - - - topset beds
Clinoform – deeper water deposits of the slope - - - - - - foreset beds
Fondoform – deepest water deposits of the basin - - - - - - - - - bottonset beds
Notes: For deltas and continental margins, we often see stratal geometries (and seismic reflection geometries) that indicate sediment has built up (vertical) a little, but has built out (horizontal) a lot. Rich (1951) came up with some terminology for the geometric components:
Undaform (topset beds) – shallow water deposits of the shelf
Clinoform (foreset beds) – deeper water deposits of the slope
Fondoform (bottomset beds) – deepest water deposits of the basin
Other people prefer the terms: topset beds, foreset beds, and bottomset beds. You will use Rich’s terminology in the exercise.

## Slide 20: Submarine Canyon
Monterey Canyon and other features carved by gravity driven turbidity currents
http://geologycafe.com/class/chapter14.html
A submarine canyon is a steep-sided valley cut into the sea floor of the continental slope, sometimes extending well onto the continental shelf. Some submarine canyons are found as extensions to large rivers; however, most of them have no such association.
From Wikipedia
Submarine canyons, cut during times when sea level was low, provide conduits for coarse clastics (sands, gravel) to reach deep water environments and be deposited. Sediment moves down canyons via turbidity and debris flows .
Notes: There are also deep water reservoir rocks – out past the shelf margin. Sediment is funneled down submarine canyons. Information about submarine canyons is shown on the slide.
The picture is seafloor bathymetry off Monterey, CA. Note the canyons that extend westward from shallow water environments (orange) out to very deep water (dark blue).

## Slide 21: Deep Water Sands
A turbidite is the geologic deposit of a turbidity current, which is a type of sediment gravity flow responsible for distributing vast amounts of clastic sediment into the deep ocean.
All from:
http://www.nature.com/scitable/knowledge/library/submarine-fans-and-canyon-channel-systems-a-24178428
From Wikipedia
Ancient submarine fan model of Mutti & Ricci Lucchi (1972) (left), based on vertical stacking of sedimentary rocks (right). Modified from Mutti & Ricci Lucchi (1972) and Mutti (1992).
Notes: Sediment at or near the head of a submarine canyon are stirred up by major storms or earthquakes. Gravity makes the sediment-laddened waters flow down the canyons and get deposited near the base (toe) of the slope on the basin floor. We call this sediment-laddened flows turbidity currents.

## Slide 22: Deep Water Sand Deposition
Low
Density
High
Density
Fine Sand and Mud
Overbanking Flow
Mud
Fraction
Sand
Fraction
°
Loss of Erosional
Confinement
Deposition of
Low-Density Turbidite
Deposition of
High-Density Turbidite
Loss of Erosional Confinement
Adapted from Beaubouef et al, 1999
Reservoir quality sands can be deposited as part of a confined to semi-confined channel system within canyons on the slope and rise
Reservoir quality sands also can be deposited as part of a unconfined sheet sands on the basin floor (abyssal plain)
Notes: The upper diagram shows how sand is concentrated in the axis of deep water channel axes with finer-grained sediments deposited above and to the sides of the coarser sands. Often we are eroding sediment from the shelf and upper part of the canyon while depositing sediment in the lower reaches of the canyon and out on to the basin floor. Turbidity flows are another good mechanism for concentrating the coarsest grains and winnowing out the fine-grained particles.
Note the conceptual model on the right. The upper parts of the canyon are dominated by erosion and sediment bypass. Some deposition (of coarse grains) can occur in the lower part of the canyon. Here the walls of the canyon still exist. They confine deposition laterally between the walls. As the height of the walls of the canyon wall go to zero, deposition begins to spill over the walls. We get semi-confined deposition. Most of the coarsest grained sediment stays within the canyon, but some reservoir-quality sands can breach the low canyon walls and start to spread out laterally. Further down dip, the canyon walls are gone. All the sediment “fans” out – we call this unconfined deposition. Reservoir-quality rocks will form sheets – layers that are relatively thin but laterally extensive.
One last point. At the base of the continental slope there often is a change in seafloor slope (can be several knick points where the seafloor changes slope rather abruptly). A quick change in slope will cause the turbidity current to abruptly slow, since it is gravity driven). We call this a hydraulic jump. An abrupt change in slope results in relative thick layers.

## Slide 23: Making Predictions
Depositional Model
Seismic Observations
are turned into
Stratigraphic Predictions
using Depositional Models
Seismic-Based EOD Map
Predicted Lithologies
Salt
Salt
Notes: This is an example of our process for making stratigraphic predictions using a deep water environment of deposition (EOD). The upper left is a map showing a mini-basin surrounded by salt. This happens in the Gulf of Mexico. A break in the salt wall near the top has allowed sediment to fill this mini-basin from the north. Using seismic data, we mapped a thick, lobate deposit (yellow). 3D seismic even allows us to image distributary channel systems. We want to predict reservoir-quality sands where the two black lines are drawn.
To make predictions, we use a depositional model (center). The northern black line is where we would expect confined to semi-confined deposition. We predict sands within the canyon walls. These sands should extend up and down the canyon, but laterally restricted. We’d also expect cutting and filling with each turbidite flow, some amalgamated sands.
The southern black line is where the canyon walls no longer confine the turbidity flows – unconfined deposition. We anticipate sands that are thin, but widespread (sheets). The prediction of vertical and lateral distribution of reservoir rocks is important in exploration, field development and field production.

## Slide 24: West Texas Outcrop Example
TOE-OF-SLOPE
BASIN FLOOR
Relict
Carbonate
Slope
Slope Siltstones
Slope Siltstones
APPROXIMATE LOCATION
OF OUTCROP BELT
miles
km
0
0
5
5
Proximal Channelized Fan:
Brushy Mesa
Medial Channelized Fan:
Channel to Sheet Transition:
Colleen Canyon
Sheet Complexes:
Cordoniz Canyon
Beaubouef et al, 1999
Notes: Here is an outcrop study from West Texas published by Rick Beaubouef and his colleagues at ExxonMobil. The map is an interpretation for part of the Brushy Canyon Formation based on 10+ detailed outcrop studies. Moving from the NW to the SE, we transition from the paleo-slope to the paleo-basin floor. From NW to SE, we also transition from:
- primarily bypass of sediments in the mid canyon,
- through confined deposition,
- to semi-confined deposition, and finally to unconfined deposition.

## Slide 25: Types of Reservoirs
Conventional
Reservoirs
Unconventional
Reservoirs
Clastic
Carbonate
Tight Oil/Gas Sands
Shale Oil/Gas
Coal Bed Methane
Traditional methods are used to extract HCs from reservoir-quality rocks within some type of trap
New methods are used to extract HCs from non-reservoir-quality rocks often within source intervals
Notes: We have covered several types of conventional clastic reservoirs. We can also have conventional carbonate reservoirs. We don’t have time to go into any detail on carbonate reservoirs, but don’t think this is because carbonate reservoirs are not important. Worldwide, we have about the same amount of production from carbonate reservoirs (e.g., most Middle East fields) as we do from clastic reservoirs.

## Slide 26: Carbonate Depositional Environments
http://geologycafe.com/images/carbonate_environs.jpg
Notes: Carbonate reservoirs result from the breakdown of plants and animals composed of calcium carbonate – like coral. Carbonate “critters” grow in the photic zone where waters are warm and clear (not much sand, silt, clay). In high energy environments, such as beaches and shoals, coarser carbonate grains can be concentrated while the suspension fraction is removed.

## Slide 27: A Modern Example
http://geologycafe.com/images/south_florida.jpg
South Florida is part of a growing carbonate platform with the Florida Keys consisting of a modern barrier reef complex.
Notes: Here is an example of a modern carbonate environment, the southern tip of Florida. Waters are warm and clear and carbonate organisms produce almost all of the sediment. The beach off Miami and all the Florida Keys consist of carbonate sands – future carbonate reservoirs.

## Slide 28: Carbonate Porosity & Permeability
Carbonate reservoirs exist wherever limestones or dolomites have high porosity and permeably
Primary porosity and permeably is that which is associated with initial deposition, like the pore space between ooids
Secondary porosity and permeably is that which is associated with post-depositional diagenetic processes, such as carbonate dissolution
Carbonate reservoirs are more problematic than clastic reservoirs in that the post-depositional processes are more complex
Some carbonate diagenetic processes:
  increase porosity and permeably, but
  other processes decrease porosity and permeably
Notes: Five important facts about carbonate porosity & permeability.

## Slide 29: Types of Reservoirs
Conventional
Reservoirs
Unconventional
Reservoirs
Clastic
Carbonate
Tight Oil/Gas Sands
Shale Oil/Gas
Coal Bed Methane
Traditional methods are used to extract HCs from reservoir-quality rocks within some type of trap
New methods are used to extract HCs from non-reservoir-quality rocks often within source intervals
Notes: New technology has allowed us to produce oil & gas from low porosity & permeability rocks. We have known that there are a lot of HCs in shales and low permeability sands for decades; we just could not extract these HCs and make money. This changed about 10 years ago with the combination of two technological breakthroughs: 1) horizontal drilling and; 2) fracturing “tight” rocks (low permeability) by pressurizing a portion of a well. This has revitalized and revolutionized production in the US (and elsewhere). The added production from unconventionals is part of the big price drop in oil prices in late 2014 – early 2015.

## Slide 30: What is an Unconventional Reservoir?
CONVENTIONAL
UNCONVENTIONAL
Marcellus Shale
High Porosity (20-40%)
High Permeability
Moderate Porosity (10-20%)
Moderate Permeability
Ultra Low Porosity (2-10%)
Ultra Low Permeability
Fluids flow easily
through the rock
(100’s – 1000’s bbls/day)
Fluids flow poorly through the rock
(10’s – 100’s bbls/day)
Fluids will NOT
flow naturally
Fluids will only flow if fracture stimulated
(10’s – 100’s bbls/ day when frac’d)
Courtesy of Noble Energy
Notes: An unconventional reservoir has three characteristics:
- the rocks have very low porosity
- the rocks have very low permeability, and
- fluids will not flow unless the rocks are fracture stimulated.
We have to fracture the rocks so that the trapped oil and gas can escape due to the fracture permeability.

## Slide 31: No Traditional Reservoir, Trap, Seal
Photosynthesis (millions of years ago) creates food for simple organisms.
2) Critters die and collect on seafloor, forming a source rock.
3) Organic goo is buried and heated so that HCs are generated.
Salt
Dome
Conventional fields with reservoir rocks, traps and seals.
Unconventional fields in which HCs are produced from porous streaks after fracking
Courtesy of Noble Energy
Notes: Unconventional fields, also called resource plays, differ from conventional fields in that there is no traditional reservoir, trap, or seal.
We extract HCs from source beds. We still must have organic rich rocks buried and heated to where HC generation will occur. The source beds also need to be somewhat brittle (e.g., have some silica in them) so that they can be fracked.
The dominant import from the platform is muddy sediment, however, the sediment can be grainy depending on source. Grainy, graded layers or rip-ups indicate storm activity. Tidal creeks and channels also can be grainy.
Tidal flats that are dominated by cyanobacteria  stromatolites (layered bio-chemical accretionary structures)
Fauna is generally very restricted depending on environment
In arid climates, evaporites can precipitate in sabkhas (arabic word for ‘salt flat’)

## Slide 32: References - 1
Slide 4: http://echo2.epfl.ch/VICAIRE/mod_3/chapt_1/main.htm Figure 1.13
Slide 5: http://petroleum101.com/what-is-a-petroleum-reservoir/ fourth figure
Slide 8: http://imgkid.com/alluvial-fan.shtml image 8 and image 7
Slide 9: http://geography.howstuffworks.com/terms-and-associations/sand-dune1.htm
Slide 9: http://www.summitpost.org/mesquite-flat-dunes-highpoint/276799 image 3 by Noondueler
Slide 10: http://en.wikipedia.org/wiki/File:Toklat_River_-_East_Fork_01.jpg by Dawn Endico
Slide 10: http://en.wikipedia.org/wiki/File:Meandering_River_2_Innoko_NWR.jpg US Fish & Wildlife
Slide 11: http://www.tulane.edu/~sanelson/eens1110/streams.htm Prof. Stephen A. Nelson
Slide 11: http://intheplaygroundofgiants.com/the-geology-of-sedimentary-rocks/ Figure 18 Kenneth A. Bevis
Slide 12: http://intheplaygroundofgiants.com/the-geology-of-sedimentary-rocks/ Figure 19 Kenneth A. Bevis
Slide 13: http://en.wikipedia.org/wiki/Beach second figure
Slide 14: http://3dparks.wr.usgs.gov/nyc/shoreline/beaches.htm Figure 170
Slide 15: http://en.wikipedia.org/wiki/File:Mississippi_delta_from_space.jpg from NASA
Slide 15: http://en.wikipedia.org/wiki/File:Mississippi_Delta_Lobes.jpg
Notes: Reference Slide

## Slide 33: References - 2
Slide 16: http://echo2.epfl.ch/VICAIRE/mod_3/chapt_3/main.htm Figure 3.10
Slide 17: http://pixshark.com/nile-delta.htm image 13
Slide 20: http://geologycafe.com/class/chapter14.html
Slide 21: http://www.nature.com/scitable/knowledge/library/submarine-fans-and-canyon-channel-systems-a- 24178428 Figure 5, which references:
Mutti, E., and Ricci Lucchi, F., 1972, Le torbiditi dell'Appennino settentrionale: introduzione all'ananisi di facies: Memoirs Soc. Geol. Italiana, v. 11, p. 161-199
Slide 22, 23: Beaubouef, R.T., Rossen, C., Zelt, F.B., Sullivan, M.D., Mohrig, D.C>, & Jennette, D.C. 1999. Deep-water sandstones, Brushy Canyon Formation, West Texas. AAPG Continuing Education Course Note Series #40, The American Association of Petroleum Geologists, Tulsa.
Slide 25: http://geologycafe.com/images/carbonate_environs.jpg
Slide 26: http://geologycafe.com/images/south_florida.jpg
Notes: References (con’t)

## Slide 34
Questions?