## Slide 1: Petroleum Geology & Geophysics
Structure/Traps
A “Kitchen”
Where Organic
Material Is
Cooked
“Plumbing” To Connect the Container to the Kitchen
Source
Migration
Where HCs Accumulate
Reservoir
Trap
Seal
Notes: This lesson introduces structural analysis and HC traps.

## Slide 2: Elements and Processes
Essential Elements
Source rocks
Reservoir rocks
Seal rocks
Overburden rocks
Major Processes
Trap formation
Hydrocarbon
  Generation
  Migration
  Accumulation
Source
Migration
Reservoir
Trap
Seal
Notes: This slide describes the hydrocarbon (HC) system elements and processes, with trap formation marked.

## Slide 3: Outline
The purposes of structural analysis in hydrocarbon (HC) exploration, development, and production
The role of seismic interpretation in structural analysis
Strengths & weaknesses of seismic data for structural analysis
The concept of structural styles
Hydrocarbon (HC) Traps
Notes: Outline for the lecture.

## Slide 4: Structural Analysis - What is it?
The analysis of all of the significant processes that formed a basin and deformed its sedimentary fill from basin-scale processes (e.g., plate tectonics) to centimeter-scale processes (e.g., fracturing)
Some Major Elements:
  Basin Formation
  Fault Network Mapping
  Stratigraphic Deformation
  Present-Day Trap Definition
  Timing of Trap Development
Image Courtesy of ExxonMobil
Notes: What is structural analysis? Ideally, it is the analysis of all of the significant processes that:
- formed a basin and deformed its sedimentary fill
- from basin-scale processes (e.g., plate tectonics) to centimeter-scale processes (e.g., fracturing)
Typically, what we focus on is :
How did the basin form?
Mapping the major fault systems
Looking at sediment deformation for potential traps
Identifying present-day traps and things that may control their fill level (trap size)
In some cases, we may need to work out when the trap formed & its size history.

## Slide 5: Purposes of Structural Analysis
Answer:
  To properly locate wells
  To discover new reserves
  To efficiently produce discovered reserves
But also:
  To define the size of HC reserves (how many barrels)
  To determine trap integrity (e. g., Fault seal)
  To understand basin architecture:
    For thermal modeling of source maturation
    For modeling hydrocarbon migration
Notes: Why do we conduct a structural analysis?

## Slide 6: Role of Seismic Interpretation
Identify and map faults, folds, uplifts, and other structural elements
Interpret structural settings and structural styles
Ensure 3D geometric consistency in an interpretation - is it structurally valid?
Determine timing relationships, especially the timing of trap formation
Check if the interpretation is admissible
Notes: What type of things can we get from seismic data in terms of structural geology?
We can:
  Identify and map faults, folds, uplifts, and other structural elements,
  Interpret structural settings (e.g. divergent, convergent, etc.) and structural styles (described later)
  Ensure 3D geometric consistency in an interpretation - is it structurally valid? (Focus of Exercise)
  Determine timing relationships, especially the timing of trap formation:
    this is especially important if HC migration occurred about the same time as the trap formed
  Check if the interpretation is admissible – have we violated any laws of nature?

## Slide 7: Data Used in Structural Analysis
Seismic reflection data (2D and 3D)
Seismic refraction data
Surface geology data
  from field geology
  from remote sensing data
Well data
Gravity measurements
Magnetic surveys
Images Courtesy of ExxonMobil
Notes: We can use a variety of data for our structural analysis.

## Slide 8: A Caution about Seismic Images
Most seismic data is displayed in 2-way TIME, which can distort geometric relationships
Watch the vertical exaggeration; it changes with depth
V:H is 1:1
At 2500 m/s
V:H is 1.2:1
At 3000 m/s
1 km
V:H is 1.4:1
At 3500 m/s
Image Courtesy of ExxonMobil
Notes: A caution about seismic data. Here is a seismic profile from the area you will work in the next exercise. Most (~90%) seismic data have a vertical scale of two-way travel time. This is the basic unit of measure – how long did it take for the acoustic wave to travel down to and then be reflected up from the subsurface?
Since velocity is not constant – but overall increases with depth, the time scale is not linear with depth. A 10 ms interval at a shallow depth corresponds to less thickness than a 10 ms interval at a great depth. Thus the vertical-to-horizontal ratio (i.e., the vertical exaggeration) changes with depth. Structural geologists prefer to look at profiles with a V:H ratio of 1:1 (no vertical exaggeration).
At 1:1, a dip in the subsurface, say of 10 degrees, will show as a dip of 10 degrees on the seismic section. We can adjust the seismic display – usually we set the zone of interest (main reservoir) to a V:H of 1:1. At deeper depths, the V:H will increase slowly; At shallower depths, it will slowly decrease.

## Slide 9: The STRENGTHS of Seismic Data
Inherently 3-D (even if a 2-D grid)
Able to image trap-scale structures
Able to image stratigraphy, to identify reservoir, seal, and for use as structural markers, e. g. to constrain fault offsets
Provides a 3-D context for understanding other data
  surface geology
  well data
  potential field data
Notes: The strengths of seismic data are listed here: 1) Our interpretation is inherently 3D, even if we only have a 2D seismic grid, we map a fault on several lines and interpolate a 3D fault plane; 2) We are able to image traps that are the same scale as our interest, 3) We are able to image stratigraphy, to identify structural markers that tells us about the sense and magnitude of fault offsets, and, 4) Our structural framework provides a 3-D context for understanding other data, like surface geology, well data, and potential field data (gravity and magnetics).

## Slide 10: The WEAKNESSES of Seismic Data
Limited resolution: can’t resolve “small” features
Steep dips can be difficult to image
Acquisition can be difficult, e. g. in areas of variable topography, variable surface geology, or “hard” water bottom
Vertical axis is typically (migrated) time, not depth
  Velocity variations distort geometries
Display scales are commonly not V:H=1:1, which results in distortions of geometries
Typically we can’t “see” hydrocarbons
Notes: This slide shows the weaknesses of seismic data: 1) Seismic data has limited resolution: we can’t resolve “small” features – like a horst block that is 1 km x 1 km, but we are not interested in such small features; 2) Steep dips (> about 30 degrees) can be very difficult to image, 3) Acquisition can be difficult, e. g. in areas of: variable topography, variable surface geology, or “hard” water bottom, 4) Vertical axis is typically (migrated) with time, not depth, 5) Velocity variations distort geometries, 6) Display scales are commonly not V:H = 1:1, which results in distortions of geometries, and 7) Typically we can’t “see” hydrocarbons directly.

## Slide 11: Structural Information from Seismic
From seismic data, we can determine such structural information as:
Basin subsidence/uplift
Faults: presence & history
Folds: presence & history
Flexural loading
Salt or shale diapirs
Strike & dip of strata
Burial history
Thermal history
Over-pressured zones
Timing when structures grew
Images Courtesy of ExxonMobil
Notes: Seismic data allows us to determine such structural information, like…

## Slide 12: A ‘Synergistic’ Relationship
You can not get all of the structural information without working the stratigraphy
You can not get all of the stratigraphic information without working the structure
Image Courtesy of ExxonMobil
Notes: There is a synergistic relationship between structural analysis and stratigraphic analysis, as shown.
Here is part of the seismic data you will use in the exercise. There is some interpretation – the green fault and the cyan and purple horizon. In your mind, think of this line without any interpretation. The manner in which the reflections (orange and black bands) terminate near the middle of the seismic line indicates the presence of a fault (point out a few examples). We can interpret a fault near the green line – there is room to move it slightly left or right or to change the dip angle – the seismic imaging is OK, but not great.
Is this a normal fault with the right block down relative to the left? Since this is from an extensional basin, there is a good chance that it is a normal fault (as opposed to a reverse fault).
OK – what is the amount of offset – 10 m, 50 m, 300 m?
Without working a little stratigraphy we can not say.
Now, imagine you know the top of a reservoir is where the cyan horizon is marked on the right side of the seismic line.
If you do not know there is a fault, you would correlate it as so (trace the orange band, with a slight drop at the green fault).
On the left your cyan horizon would be too deep, which could have major impact on HC presence and volume.
Working both the structure and stratigraphy together, we get the interpretation as shown.
About 160 ms of offset two-way time = 0.08 seconds one-way time.
If the velocity at this depth is 2400 m/s, then the offset would be about 190 m (2400 m/s * 0.08 s = 192 m).

## Slide 13: Stratigraphy Helps in Structural Analysis
Constraining the magnitude of displacement across faults
  Throw, heave, and stratigraphic separation
  Correlation across faults and piercing points
Defining reservoir, trap, and source geometry
Giving timing information about deposition and deformation
  Uniform thickness before movement
  Variable thickness during & after movement
Indicating the location of detachment surfaces
Enabling us to assess the capacity of faults to seal HC columns
Stratigraphy helps in structural analysis by:
Notes: Stratigraphy helps in structural analysis by…

## Slide 14: Fault Terminology
HEAVE
STRATIGRAPHIC SEPARATION
THROW
Image Courtesy of ExxonMobil
Notes: Here is some common fault terminology:
Throw is the vertical component of the horizon separation from high side to low side.
Heave is the horizontal component of the horizon separation from high side to low side.
The stratigraphic separation is the hypotenuse of the triangle.

## Slide 15: Mapping a Faulted Horizon
1 km
http://archives.aapg.org/europe/newsletters/2008/03mar/jackson3.jpg
Two-Way Time
(ms)
0
250
500
N
Notes: Here are some things to note about showing a faulted horizon on a map.
If we were mapping the magenta horizon from the previous slide:
There would be a gap for the magenta horizon that is equal to the heave.
The magenta horizon would be contoured on the foot wall side (right on the seismic line) to the high-side cutoff,
It would be contoured on the hanging wall side (left on the seismic line) to the low-side cutoff.
Normally we do not show contours between the high-side cutoff and the low-side cutoff; it would be shaded in as a dark color.
This is to represent the stratigraphic separation at the fault.

## Slide 16: Basic Observations: Profile View
We can recognize moderate- to large-scale faults on seismic profiles by:
Termination of reflections
Offset in stratigraphic markers
Abrupt changes in dip
Abrupt changes in seismic patterns
Fault plane reflections
Associated folding or sag
Discontinuities
Image Courtesy of ExxonMobil
Notes: What are some of the clues we look for on seismic data to recognize faults?
They are listed here:
Termination of reflections (point out some),
Offset in stratigraphic markers,
Abrupt changes in dip – NOT on this example,
Abrupt changes in seismic patterns – e.g. a strong, continuous reflection turns into a low amplitude reflection,
Fault plane reflections – ONLY when fault dips less than about 20 degrees,
Associated folding or sag (some of this above the red fault), and
Discontinuities – more about this on the NEXT few slides.

## Slide 17: Fault Identification: Time Slice View
1856 ms
Do you see any evidence for faults?
Image Courtesy of ExxonMobil
Notes: Here is a view of some seismic data, offshore Louisiana. These data are from a 3D seismic volume.
This figure is a MAP view at a two-way travel-time (TWT) of 1.856 seconds or 1856 milliseconds (ms).
Blue represents compression – what would be black on a B&W section? white = zero amplitudes; red = ‘white’ troughs on a paper section. Q: Can anyone see evidence for one (1) or more faults?
A: On the right of the image, a fault is apparent by the offset of the blue & red bands. Other faults can be seen towards the south (bottom). Several small faults are towards the west – small offsets in the red reflection bands. These faults are relatively easy to spot since the ‘bands’ are at a high angle to the fault traces. There is a curvilinear fault that starts just NW of center and curves towards the SE. This one is hard to see because the ‘bands’ and the fault trace are at low angles (almost parallel).
In the early 1980s, people came up with a technique to enhance faults in 3D seismic data. Amoco was smart enough to patent their method – which they called Coherency. Basically, one trace is compared to its neighboring traces over a small time window (or gate).
If the traces are perfectly identical in shape – a value of 1.0 is assigned. As the similarity of the traces decreases, the assigned values also decrease to 0.95, 0.90, 0.88, etc. More technically, we perform a cross correlation between a reference trace and its neighboring traces. We display the cross-correlation value, usually using a grey scale (right side of next slide).

## Slide 18: Coherency Data
Also known as Discontinuity or Variance
A derivative data volume based on trace-to-trace correlation
Data range from 0 to 1 (1 = neighboring traces are identical)
  Amplitude Data
Coherency
1856 ms
1856 ms
Images Courtesy of ExxonMobil
Notes: Coherency is Amoco's name; other companies do similar analyses and call it discontinuity, variance, similarity, etc. Here the display on the left is the reflection amplitude data in red-white-blue (same as on the previous slide). On the right is the cross-correlation data using a grey scale; white is .98 or higher, black is .80 or lower, grey is between .98 and .80.
Q: What do you suppose the black lineations indicate? A: They are potential fault segments (point out a few examples). The display on the right ‘enhances’ fault traces. Where there is a black lineation, one trace is on the high side and its neighbor is on the low side or in the fault zone. Note the black-grey region in the south. This indicates a general lack of similarity of seismic traces in this region – an indication that the data quality is not good. Another thing that can show up on this type of data are major stratigraphic boundaries – like going from inside to outside a major channel system. This example does not show any stratigraphic features.

## Slide 19: Corendering of Data
1856 ms
1. The amplitude data is displayed (red-blue)
2. The coherency data below user-defined thresholds is overlain in black (very low values ) and gray (low values)
Opacity for the Continuity Data
Black
Gray
Transparent
Images Courtesy of ExxonMobil
Notes: Another neat trick is to co-render the amplitude data and the discontinuity data – as shown here. Simply put, we: 1) paint the amplitude data (red-white-blue) on the screen, 2) overlay the discontinuity data, and 3) set the transparency so that very low values are opaque (black), intermediate values are semi-transparent (gray) and high values are fully transparent (invisible). This means that if traces are nearly the same, the reflection amplitude data (red, white, blue) shows through.
You can see in this example some dark lineations – which are candidates for fault traces. In my opinion, this is a very good display to work with while mapping faults.

## Slide 20: Fault Identification: Profile Views
A
B
C
tie
W
E
N
S
A
B
C
For an interpretation to be internally consistent, faults must tie on intersecting lines
Images Courtesy of ExxonMobil
Notes: For both 2D and 3D seismic, we want our fault planes to be consistent in 3D space. A fault plane in the earth will have one depth point at any given location (latitude, longitude), except for a fault that bends back on itself. For our interpretation, this means at any seismic trace our interpreted fault plane should have only one (1) two-way time (TWT) value.
On this slide, the upper left is a map view of a seismic survey area. The seismic is a line that makes a 90 degree turn: A-B runs north to south, and B-C runs west to east. The red fault is consistently interpreted – consistent does not mean correct necessarily, but a correct interpretation must be consistent. The fault plane (red line) on the two (2) perpendicular lines has the same TWT where the two lines join (intersect). We say the fault “ties” at this location.
We would not want to see the fault high on one side and low on the other where two lines intersect – what we call a “mistie”. The yellow line represents a stratigraphic horizon, down-dropped near the line intersection point (B). FYI, the colors on the map view represent the TWT for the yellow horizon. Hot colors are shallow, while cool colors are deep. You can see the fault gaps (grey zones on the map) for the red fault where A-B and B-C are located (down to the south).

## Slide 21: Interpreting Faults
Structural
Observations
Structural
Concepts
Notes: When we are interpreting faults on seismic data, there are two main components:
1) We make observations – evidence based on the seismic for the location, offset, etc. of significant faults, and
2) We have in our mind the various structural concepts that we have learned from basic and advanced structure classes or experiences.
As indicated, there is a lot of back-and-forth between observations and concepts.

## Slide 22: Interpreting Faults
Structural
Observations
Fault segments on seismic lines
Fault plane orientation
Sense of motion
Magnitude of offset
Range of depths
Relative timing
  when faults moved
  when structures grew
Structural
Concepts
Tectonic Setting
  Divergent zones
  Convergent zones
  Strike-slip zones
  Mobil substrate
How Structures Evolve
  Fault-bend folds
  Fault-propagation folds
  Salt movement
  etc.
Notes: Structural Observations and Structural Concepts
With the concepts, think about how some of the structures could have formed and evolved?
Salt movement: how salt diapirs evolve from early to mature

## Slide 23: Structural Styles
What is a “structural style”?
“Important differences in trend arrangements and structural morphologies provide criteria for differentiation of styles. These differences also result in different kinds of hydrocarbon traps.” (Harding and Lowell, 1979)
Notes: Structural style is a tool developed by Todd Harding and James Lowell in the 1970’s. Here we define the tool, and the next slide will help you understand and use this tool (method).

## Slide 24: Structural Styles Matrix
BASEMENT
INVOLVED
BASEMENT
DETACHED
EXTENSION
CONTRAC-
TION
LATERAL
UPLIFT,
SUBSIDENCE
extensional
fault
blocks
detached
normal
faulting
contractional
fault
blocks
fold-and-
thrust belts
strike-slip
or wrench
faulting
tear faults
(detached)
basement
warps
salt, shale
diapirism
2 Rows
4 Columns
Notes: The essence of structural styles is this 2D matrix. Columns are the tectonic setting – extension, contraction, lateral or strike-slip, or regional uplift/subsidence. The rows are the depth of faulting – do faults offset basement rocks (basement involved) or do they detach within the sedimentary section?
What is the value of this matrix? Historically, we know of many types of traps – probably more than 40 (e.g., high-side traps on rotated fault blocks, anticlines with 4-way dip closure). This matrix gives me eight (8) “pigeon-holes”. There are a limited number of trap types associated with each of these pigeon-holes. Thus, if I know I am working in an area characterized by extension and the faults offset basement, I can be on the lookout for perhaps six (6) types of traps instead of 40+ trap types. This tool helps to focus on the trap types that the student should expect to see. We will look at a couple of examples.

## Slide 25: Extensional Faults
basement involved
basement detached
1 mile
Images Courtesy of ExxonMobil
Notes: Both examples here are for basins under extension. On the left, we have basement involved faults - they offset basement (red). One type of trap to look for in this case would be closures along the high side of the faults. The seismic comes from the data set you will look at in the exercise.
On the right, the faults are basement detached. The seismic comes from the US Gulf Coast. These types of faults are commonly called listric normal faults or slump faults. The detachment plane is in “weak” marine shales, thousands of feet above basement. Note how the reflections above the fault curve into the fault plane – these are called “roll-over” structures. A lot of oil & gas have been produced from this type of trap in Texas, Louisiana, Mississippi and Alabama – both onshore and offshore. This is one of a handful of trap types to look out for if we know the study area is in the extension/basement detached pigeon-hole.

## Slide 26: Contractional Faults
basement involved
basement detached
Stone, 1983
Norton, 1983
AAPG©1983 reprinted with permission of the AAPG whose permission is required for further use.
AAPG©1983 reprinted with permission of the AAPG whose permission is required for further use.
Notes: This slide shows two (2) example seismic lines from compressional regions. On the left, the faults offset basement.
On the right, the faults are detached along décollement surfaces within the sedimentary section.

## Slide 27: Diapirs Can Provide Good Traps
Salt and shale layers can become mobile
when subjected to differential loading
Many oil and gas fields have been found associated with salt & shale diapirs
Imaging beneath salt is very difficult, but the rewards can be great!
Notes: Diapirs, both salt and shale, provide large trapping potential. Here the magenta ‘blobs’ are intended to represent salt bodies. In the upper right, there are traps above the salt on the high side of normal faults. The more significant traps are along the flanks of the salt dome where reservoir rocks dip into the salt body. Salt has extremely low permeability – fluids do not flow through them even on a geologic time scale. Oil & gas that get into the sands migrate updip; if there is a top seal, a large to giant hydrocarbon (HC) field can form.
In the lower left, the salt has formed a ledge/sill/canopy. We can drill through 100s to 1000s of feet of salt and tap into super giant fields.
This is the new, big play in the deep Gulf of Mexico. The challenge here is to image the sediments below the salt, which is very difficult since the salt body severely distorts the seismic ray paths.

## Slide 28: Faults & Folds
Contractional
Extensional
Fault Bend Folds
Contractional
Extensional
Fault Propagation Folds
Images Courtesy of ExxonMobil
Notes: Various models have been proposed for how some of our large structures form. Two commonly used models are summarized here, for both extensional and compressional (contractional) basins: 1) fault bend folds, and 2) fault propagation folds. It is beyond the scope of this course to delve any deeper.

## Slide 29: Is the Interpretation Admissible?
We can check
the kinematic admissibility of a
thrust fault interpretation by means of a 2-D sequential restoration
Image Courtesy of ExxonMobil
Notes: Once we have an interpretation, we should ask “is the interpretation admissible – is the implied deformation reasonable?” This example comes from a fold & thrust belt (highly compressive) environment.
The top figure is the interpretation of the present day structuring. This example is rather old – probably from the mid 1980s. At that time, we only had software that could restore 2D cross-sections; now we have 3D restoration software. As we go down through the images, we are seeing the implied structuring back through geologic time. The lowest image is a 2D restoration before the compression began.
There are several “gaps” in the layers and a couple of overlaps. This indicates potential problems with the interpretation (we’ll ignore errors due to not working in 3D). For example, there is a gap on the far left of the restored cross-section. This indicates that either the fault plane in the present-day interpretation is not at the correct angle or the way the layers curve into the fault is not correct.
If we plan to drill the “left” structure, this could mean either larger or smaller volumes of oil. Here is a KEY – if we would still drill the well given the uncertainty in the oil volume, we would not do more refinement of the interpretation. However, if we thought there would not be enough oil in the “left” structure to make a profit if the fault was (say) 5 degrees steeper; then we would test the likelihood that the fault is that steep. That means reinterpreting the fault (making it steeper), doing the restoration, and seeing if the gap is much smaller (interpretation possible closer to the truth) or much larger (less likely to be true).
Work that impacts a business decision is carried out; work that will not significantly change a business decision will not be done – makes dollars & cents?

## Slide 30: Structural Analysis: Products
From our structural analysis, coupled with some basic stratigraphy, we are able to:
Define important geometric relationships
Determine the timing of:
  fault movement
  trap development
Predict the location of detachment surfaces
Evaluate the capacity of faults to seal
Images Courtesy of ExxonMobil
Notes: What do we get from our structural analysis? Here is a short list, though we can get a lot more.

## Slide 31: Getting Timing Information
Yellow Unit
High Side
Low Side
High Side
Low Side
High Side
Low Side
High Side
Low Side
Pink Unit
Lavender Unit
Orange Unit
Bars Represent
Thicknesses
Fault A
Fault B
Fault C
Time of Movement
on the Fault
Fault A
Fault B
Fault C
Notes: This cartoon section illustrates how we can get information on when a fault was active. We examine the thickness of a unit (stratigraphic sequence) on both sides of a fault. If the thickness is fairly constant, then the fault was not active when that sequence was deposited. If the sequence is noticeably thicker on the downthrown side of the fault, it indicates that we fault was active.
For example, look at Fault A. The yellow and pink units are about the same thickness on either side of Fault A. The lavender and orange units thicken across the fault. This can be explained if there was movement on Fault A during lavender and orange deposition. As the block between Fault A and Fault B moved down, there was more accommodation (space for sediments to be deposited) on the downthrown side of Fault A.
Now look at Fault C. This fault was moving when yellow and pink were being deposited. There was some movement during lavender time. Fault C was not active (moving) during orange time (since there is no thickness change).

## Slide 32: Outline
The purposes of structural analysis in hydrocarbon exploration, development, production
The role of seismic interpretation in structural analysis
Strengths & weaknesses of seismic data for structural analysis
The concept of structural styles
HC Traps
Notes: Now we turn our attention to hydrocarbon (HC) traps.

## Slide 33: Identify Traps
Use depth (or time) structure maps, with fault zones, to look for places where significant accumulations of HC might be trapped:
Structural traps e.g., anticlines, high-side fault blocks, low-side roll-overs
Stratigraphic traps e.g., sub-unconformity traps, sand pinch-outs
Combination traps (structure + stratigraphy) e.g., deep-water channel crossing an anticline
Notes: We use depth (or time) structure maps, which include the fault zones, to look for places where significant accumulations of HC might be trapped. Structural traps would be things such as: anticlines, high-side fault blocks, or low-side roll-overs. Stratigraphic traps would be things such as: sub-unconformity traps, or sand pinch-outs. Combination traps (structure + stratigraphy) would be things such as: a deep-water channel that crosses an anticline. We’ll look at some cartoon examples of these in the next few slides.

## Slide 34: Structural Traps – A Simple Anticline
Synclinal Spill Point
Controls HC Level
If HC charge is great
HCs migrate to anticline
Traps progressively fill top-down
When HCs reaching the trap is greater than the trap volume, the trap is filled to a leak point
Here there is a synclinal leak point on the east side of the trap
A
A’
A
A’
Synclinal Spill Point
Low
Low
Notes: Here is an example of a simple structural trap – an anticline. On the left is a map view; on the right is cross-section A-A’. If enough HC has migrated into the trap, it will be filled to a spill or leak point. For this example, the spill point is on the ENE side of the high (anticline). If more HC is added to this trap, the extra HC will spill to the NE, possibly filling another trap further along the migration pathway.

## Slide 35: Structural Traps – A Simple Anticline
HCs migrate to anticline
Traps progressively fill top-down
When HCs reaching the trap is small, the trap is under-filled – it could hold more
Here the trap is ‘charge-limited’ and is not filled to the synclinal leak point
HC Migrating to Trap
Controls HC Level
If HC charge is limited
A
A’
A
A’
Low
Low
A’
Synclinal Spill Point
Notes: If the amount of HC reaching the trap is small (less than the trap could hold), then the trap is said to be under-filled. In this example, the trap is ‘HC charge-limited’ and is not filled to the spill point. The way the cross-section is drawn, both ‘bumps’ have been filled to about the same level. This would be true if HC migration came from the NW or SE, with HC migration pathways reaching both high points.
If HC migration came from the west, it would first fill the western ‘bump’ to the saddle point and then HC would start to fill the eastern ‘bump.’ If HC migration came from the east, how would the two ‘bumps’ fill? Fill east first; then spill to west.

## Slide 36: Structural Traps – Roll-Over Anticline
Leak at Fault
Controls HC Level
Synclinal Leak Point
Controls HC Level
Faulted Anticline – Fault Leaks
Faulted Anticline – Fault Seals
A
A’
A
A’
A
A’
A
A’
Leak Point
Leak Point
Notes: Here is another type of structural trap with two degrees of HC fill. On the left, a cross-section is on the top and a map view is below. Where the reservoir on the down side touches the fault is the leak point. More HC fill would leak across and up the fault plane and move through the high-side sands. On the right, a cross-section is on the top and a map view is below. Here the fault ‘seals’ – does not allow HC to move through it. The reservoir fill level is controlled by a synclinal leak point to the southwest. This illustrates the importance of predicting whether a fault leaks or seals HCs.
It could be that the left case does not hold enough HC to be an economic success, but the right case does hold enough HC to be an economic success. There are methods to predict the sealing potential of faults; we’ll look at some of them in Lesson 10.

## Slide 37: Stratigraphic Traps – Sub-Unconformity
A
A’
Upper Sand
Lower Sand
Upper Sand
Lower Sand
A
A’
Cross-Section View
Map View
Notes: Here in one example of a stratigraphic trap. On the left is a cross-section; on the right is a map view. This represents a sub-unconformity style of trap. Sands below the unconformity have a component of dip and form the reservoir. Above the unconformity is a marine shale that provides the seal. Here the big unknown is how far downdip each sand contains hydrocarbons (HCs).

## Slide 38: Stratigraphic Traps –Reef
Cross-Section View
Map View
B
B’
B
B’
Notes: Here is another example of stratigraphic traps. On the left is a cross-section; on the right is a map view.
This image represents an isolated carbonate reef. Porous and permeable carbonate facies form the reservoir – often in the edges of the reef rather than in the central lagoon facies. Again, there has to be an adequate seal facies capping the reef and along the edges.

## Slide 39: Combo Traps – Channel over an Anticline
A
A
Channel Axis
Channel Margin
Channel Margin
Shale
Shale
Structure
Stratigraphy
Low
Low
High
A
A’
Structure + Stratigraphy
OIL
Water
Water
Cross Section
A
A’
A’
A’
Notes: This slide illustrates a combination trap – one that has both a structural component and a stratigraphic component.
- Top left = structure map with an anticline in the center.
- Top right = depositional facies – a deep water channel system. The axial facies (light yellow) has the best reservoir properties.
- Bottom left = cross-section showing structure, depositional facies, and green is where the oil is trapped.
- Bottom right = map view with structure contours, facies belts and oil within reservoir quality rocks.
The anticline causes oil to migrate towards the high point (crest). The facies belts limit the producible reservoir to the channel axis facies. This trap has both a structural & a stratigraphic component.

## Slide 40: Structural Analysis Process
Perform structural styles analysis
  What is the structural setting & structural style?
  What are the expected faults, folds and trapping geometries?
Construct a structural interpretation that is geometrically consistent in 3-D
Assess the admissibility of the interpretation
  kinematic
  mechanical
Identify potential structural traps
Define the extent of the trap (what controls the HC fill level?)
Analyze the timing of trap development
  Trap volume as a function of time
  Compare trap size/timing to HC generation/migration
Notes: In summary, this is a basic workflow for structural analysis and trap identification.

## Slide 41: References - 1
Slide 15: http://archives.aapg.org/europe/newsletters/2008/03mar/jackson3.jpg
Slide 22: Harding, T.P. and Lowell, J.D., 1979. Structural styles, their plate tectonic habitats, and hydrocarbon traps in petroleum provinces, AAPG Bulletin, V. 63, p. 1016-1058.
Slide 25: Stone, D. S., 1983. Seismic Profile: South Elk Basin. in A. W. Bally (ed.) Seismic Expression of Structural Styles, AAPG Studies in Geology Series # 15.
Slide 25: Norton, M. A., 1983. Kemmerer Area, Lincoln County Wyoming. in A. W. Bally (ed.) Seismic Expression of Structural Styles, AAPG Studies in Geology Series # 15.
Notes: References

## Slide 42
Questions?