## Slide 1: Petroleum Geology & Geophysics
Seal and Migration
A “Kitchen”
Where Organic
Material Is
Cooked
“Plumbing” To Connect the Container to the Kitchen
Source
Migration
Where HCs Accumulate
Reservoir
Trap
Seal
From
Lecture 2
Notes: This unit focuses on two play elements – seal and HC migration.

## Slide 2: Elements and Processes
Essential Elements
Source rocks
Reservoir rocks
Seal rocks
Overburden rocks
Major Processes
Trap formation
Hydrocarbon
  Generation
  Migration
  Accumulation
Source
From
Lecture 7
Reservoir
Trap
Seal
Migration
Notes: In this lesson, we will learn about seal rocks, which is an essential element of a hydrocarbon play, and hydrocarbon migration, which is a major process in finding hydrocarbon traps.

## Slide 3: Hydrocarbon Seal
A Seal (or cap rock) is a unit with low permeability that impedes the escape of hydrocarbons from the reservoir rock.
Common seals include evaporites, chalks and shales.
Analysis of seals involves assessment of their thickness and extent, such that their effective-ness can be quantified.
From Wikipedia
http://www.worldwildlife.org/species/seals
http://www.bing.com/images/search?q=hydrocarbon+seal&FORM=HDRSC2#view=detail&id=0668B0B3CA4D515146258369DD6124D80B9F0633&selectedIndex=54
Seal Rocks
Notes: A hydrocarbon seal can also be call the cap rock. It is a unit with low permeability that impedes the escape of hydrocarbons from the reservoir rock. Common seals include evaporites, chalks and shales. Analysis of seals involves assessment of their thickness and extent, such that their effectiveness can be quantified.

## Slide 4: Some Examples of Traps & Seals
http://www.bing.com/images/search?q=hydrocarbon+seal&FORM=HDRSC2#view=detail&id=7BD59D95C835A73BCA76D82D377228D7BB7B433F&selectedIndex=15
SALT
Gas
Oil
Beneath Salt
Notes: Here are some simple cross-sections that show the seal/cap rock (dark grey) for different types of traps: 1) An anticline, 2) A normal fault trap, 3) A stratigraphic trap, and 4) A thrust fault trap.

## Slide 5: A Critical Question
Given a particular trap, how much oil or gas can it hold?
Another way of expressing this question is: What is the controlling factor for HC fill in this trap?
There are three general controls on the fill level:
A synclinal spill point
A fault leak point
The sealing capacity of the seal rocks
Notes: A critical question for us is how much HC can a given trap hold? To answer this, we have to know or presume what controls the fill level. The three (3) main controls are listed: 1) A synclinal spill point, 2) A fault leak point, and 3) The sealing capacity of the seal rocks. We’ll look briefly at all three.

## Slide 6: Synclinal Spill Point
A synclinal spill point is the structurally lowest point in a hydrocarbon trap that can retain hydrocarbons. Once a trap has been filled to its spill point, further storage or retention of hydrocarbons will not occur for lack of reservoir space within that trap. The hydrocarbons spill and they continue to migrate until they are trapped elsewhere.
From Lesson 2
http://www.glossary.oilfield.slb.com/en/Terms.aspx?LookIn=term%20name&filter=spill%20point
Notes: A synclinal spill point is the structurally lowest point in a hydrocarbon trap that can retain hydrocarbons. Once a trap has been filled to its spill point, further storage or retention of hydrocarbons will not occur for lack of reservoir space within that trap. The hydrocarbons spill and they continue to migrate until they are trapped elsewhere or form a surface HC seep. With a good depth structure map for the top of the reservoir, synclinal spill points are relatively easy to predict. Of course, this prediction is only as good as the accuracy of the map.

## Slide 7: Synclinal Spill: Example
http://www.searchanddiscovery.com/documents/2008/08038putney/images/fig01.htm
Low Point, or
Saddle, or
Synclinal Spill
N
HC
Kitchen
If HC generation and migration were from the west of Tengiz and of infinite quantity, then Tengiz would fill before Korolev.
Tengiz would fill down to the lowest closing contour (medium green).
As more HC migrates into Tengiz, the excess HCs would spill through the synclinal spill point and start to fill Korolev.
Notes: Here is a block diagram for the Tengiz and Korolev fields. If the HC kitchen is to the west, then the Tengiz trap would fill first. If the HC charge reaching Tengiz is greater than the HC volume Tengiz can hold, there is a low point on the east of Tengiz that would be the synclinal spill point. Spilled HCs would then start to fill the Korolev trap.

## Slide 8: Fault Leak Point
Faults can either trap or leak HCs. If a fault is a good seal, it will prevent HCs from flowing out of a trap. Some faults only inhibit HC flow (do not seal on a geologic time scale, but act as a seal on a production time scale). In some cases, a fault will be sealing for oil but not for gas. Non-sealing faults can serve as migration pathways.
The Fault Leaks
The Fault Seals
From Lesson 2
Notes: Faults can either trap or leak HCs. If a fault is a good seal, it will prevent HCs from flowing out of a trap. Some faults only inhibit HC flow (don’t seal on a geologic time scale but act as a seal over a production time scale). In some cases, a fault will be sealing for oil but not for gas (gas is more buoyant). Non-sealing faults can serve as migration pathways. In the cartoon cross-sections, the fault leaks on the left and HC fill level is controlled by the leak point. On the right, the fault seals the oil. HC fill might be controlled by HC generation and migration. Also remember, we are looking at a single cross-section. For the situation on the right, perhaps there is another fault where HC leakage occurs and the fill level is in fact controlled by a fault leak not represented by this cross-section. Another possibility is that there is a synclinal spill point that we don’t see on this cross section. In addition, there can be small offset faults that we cannot map that could control the HC fill level.

## Slide 9: Fault Leak
http://www.pgs.com/Geophysical-Services/Seismic-Techniques/HD3D/Applications/
If All the Faults Seal
If All the Faults Leak
Notes: Here is a structure map of a faulted anticline. The image on the right is a zoom of the crestal area marked by the magenta box on the left. The map on the left is meant to represent the oil fill if all the faults seal; synclinal spill points define the deepest oil level in each fault block. The map on the right is meant to represent the oil fill if all the faults leak; the deepest closing contour defines the oil fill level in each fault block.

## Slide 10: In this Case, Does Fault Q Seal?
http://www.callforbids.cnsopb.ns.ca/2012/01/sites/default/files/images/inline/figure_44.jpg
Gas Show
Interpreted Gas/Water Contact
Someone has interpreted the downdip limit of gas, the gas/water contact. Based on this interpretation, does Fault Q seal?
Fault Q
Notes: Here we have a structure map with someone’s prediction of the gas fill level (gas/water contact). Note the fault named Q. Based on this prediction, did the interpreter think fault Q was sealing or leaking gas on a geologic time scale?
ANSWER: Fault Q was interpreted to seal gas. At the gas/water contact (deepest level of gas) (dashed magenta line) depth contours do run into the fault. The other fault to the SW also is interpreted to seal; it does have less offset. If Fault Q turns out to be leaking, then the gas field would be much smaller. The red line is close to the deepest contour that is not cut off by Fault Q.

## Slide 11: Quality of the Seal
Fields need a top seal and lateral seals – low permeability rocks to keep the HCs in place. HCs want to “escape” due to the upward force of buoyancy. Opposing forces are gravity and the resistance fluids in a rock have to being “replaced.”
Consider a drop of oil in a brine-filled reservoir. Relatively high porosity and permeability allows oil to fill the top of a reservoir, displacing the brine.
Buoyancy
Gravity &
Resistance
Oil
Drop
Reservoir
Rock
Notes: Seals are rocks with low permeability – difficult for fluids to pass through. Reservoir rocks have high to moderate permeability. A drop of oil in a rock with water (or brine) in the pore space will rise because the force of buoyancy is greater than gravity and resistance. Gas has even higher buoyancy, which is why free gas will sit above oil in a field. Now let’s consider changes at the top of a reservoir where we have a seal (cap rock).

## Slide 12: Reservoir – Seal Boundary
Sealing lithologies (shales, evaporates, etc.) have low permeability. HCs at the top of a reservoir still want to “escape.” The smaller pore throats in the seal offer much greater resistance to the “invasion” of oil and gas molecules. This, in very simple terms, is how HCs are held in place.
Buoyancy
Gravity &
Resistance
Oil
Drop
Notes: Here I’ve shown a shale on top of the reservoir. Shales are made of clay particles that tend to lay “flat”. Shales have less pore space (lower porosity) and the pore space is less connected (lower permeability). For the same amount of buoyant force on an oil droplet, the resistance of water in the shales to ‘yield’ space for the oil to get in is much higher. Thus, oil will ‘collect’ in the reservoir giving us a HC column.

## Slide 13: Some Things to Note
Pressure on the seal increases as the thickness of the oil and/or gas increases.
There will be an upper limit to the thickness of a HC column that a seal can hold in place.
If that upper limit is reached, the seal can fracture and leak until the forces are balanced.
Gas is more buoyant than oil (since it has lower density).
It is possible for a seal to leak gas while still holding oil in place.
Notes: As the height of the trapped oil increases, so do the forces of buoyancy. If enough buoyant pressure develops, it can exceed the fracture strength of the sealing rocks. This type of natural fracturing of the seal may limit the column height of the trapped HCs. It is therefore important to predict the fracture strength of the seal rocks. How this is done is beyond the scope of this course. Suffice it to say that some seals can hold back HC columns of 500 meters or more. Evaporities are ‘stronger’ seals than shales.

## Slide 14: Fault Seal Analysis
A particular fault can be either a seal to HC flow or a conduit.
We have seen that the volume of HC in a trap can be controlled by the sealing or leaking properties of a fault.
Thus fault seal analysis is a very important part of our sizing the HC in a prospect or field.
Juxtaposed lithology
Fault smear gouge
We only have time to look at two common methods:
Notes: Let’s talk a little bit about fault seal analysis. A fault zone, which can be razor sharp or rather wide, can have some porosity and permeability.

## Slide 15: Juxtaposed Lithology
A succession of sand and shale units have been offset by a post-depositional fault. HCs can cross-leak when a porous sand is juxtaposed against the same or a different porous sand (as long as the fault zone is not too impermeable).
A
C
B
A
B
Major Fault Offset
Fault
Offset
A
C
B
A
B
C
Minor Fault Offset
Fault
Offset
Notes: One way to analyze a fault seal is to consider what lithologies are currently juxtaposed across a given fault. Where are there porous units, I’ll say sands, juxtaposed against other porous units (sands)? For this analysis, we will assume the worst case scenario – that the faults can leak across the fault zone (cross-leak). On the left we have three (3) sands and a minor amount of fault offset. For all three (3) sands, the offset is less than the sand thicknesses, so any HCs that migrate into the sands on the down-thrown side (left) would leak across the fault to the same sand layer on the up-thrown side (right). On the right we have the same stratigraphy but more fault offset. Considering only cross-fault leak (i.e., not considering up-fault leak): 1) We can trap HC in sand A on the left side of the fault; 2) We can trap HC in the upper part of sand B on the left side of the fault; 3) The depth at which the top of sand C on the right is across from sand B on the left is the cross-fault leak point. HC could be trapped on the low-side of sand B down to the depth of the red arrow – the cross-fault leak point.

## Slide 16: Juxtaposed Lithology
http://en.allexperts.com/q/Geology-1359/2009/12/Petroleum-Geology-4.htm
Possible sand-sand juxtaposition makes cross-fault leak a high risk
Sand-shale juxtaposition makes cross-fault leak a low risk
Fault may NOT control fill level
Fault MAY control fill level
Notes: This further illustrates the diagram on the right side of the previous slide. The seismic backdrop was used to predict the presence of sandier layers, where the amplitude response is moderate to high. In terms of cross-fault leak, the left side of the upper sand would not leak – this sand could hold HC for its entire thickness. For the left side of the second sand, there is a slight overlap of sand on sand. If the fault zone is not impermeable (e.g., contains a lot of shale), then cross-fault leak is possible.

## Slide 17: Cross-Fault Leak Analysis
High Side
Low Side
A
A’
B
B’
C
C’
A
A’
THROW
Dip Section
B
B’
High-Side Section
A
C
C’
Low-Side Section
A
N
Notes: We will now illustrate a simple method for analyzing cross-fault leak, it is called an Allan diagram. The upper left is a map view of a fault, high side is to the NW. Three (3) cross sections are indicated:
(1) A-A’ is west-to-east and shown in the lower left. The offset for the top of the sand is marked.
(2) B-B’ is a cross section along the high-side of the fault. It is shown in the upper right.
(3) C-C’ is a cross section along the low-side of the fault. It is shown in the lower right.
The “yellow bands” on the two cross sections on the right show us the depths of the sands on either side of the fault.

## Slide 18: Allan Diagram
High Side
Low Side
A
A’
B
B’
C
C’
A
Superimpose sands from high-side and low-side sections to check for potential cross-fault leak points
Potential leak point at
sand-to-sand juxtaposition
Allan Diagram
High Side
Low Side
Notes: I have made an Allan on the right side of this slide. It shows the depths of the sand on either side of the fault as they would project onto the fault plane. On the left (south) the sands are separate – there is no sand-sand juxtaposition. On the right (NE) the sands overlap – there is sand-sand juxtaposition across the fault plane. If the fault zone is not impermeable, then we would have a HC leak point as noted. HC migrating in the sand from the east would fill the sand on the high side down to this leak point. If more HC reached the high-side trap than the trap can hold, the “excess” HCs would leak towards the NE along the low-side sands.

## Slide 19: Fault Smear Gouge
As a fault moves, rock material may be pulverized and dragged within the fault zone forming a gouge. If a lot of shale gets incorporated within the fault gouge, it may form a seal.
http://wiki.aapg.org/Fault_seal_quantitative_prediction:_shale_smear_factor,_shale_gouge_ratio,_and_smear_gouge_ratio
Clay (black) smears separating sandstones from a lignite mine in Germany. Note tapering of clay within the fault zone and the compound nature of the clay smear in the fault zone. (No scale on original figure.)
Modified from Weber et al., 1978
A
D
C
B
E
D
F
Notes: I’ve said twice “if the fault zone is not impermeable”. If shale layers are offset by the fault, then there can be some to a lot of shale in the fault gouge – the rock material smeared in the fault zone as the rocks rub each other.
This diagram is a drawing of layers within a mine in Germany. White with speckles represents sand layers; black represents shale layers. Note the fault zone – left side going down relative to the right side. As the layers on either side of the fault zone rub each other, some rock material gets entrained in the fault zone. Shales are more ductile than sandstones and can form continuous elements within the fault zone. It appears that there is a thin, continuous shale between sand C and sand E. So even though we have a sand-sand juxtaposition across the fault zone, there may be enough shale gouge to prevent cross-fault leakage. Between sand B and sand D there may be a small break in the shale where we have sand in the fault gouge. If this is the case, then we probably would have cross-fault leakage.

## Slide 20: Shale Gouge Ratio (SGR)
Layer 1
Layer 7
Layer 6
Layer 5
Layer 4
Layer 3
Layer 2
If we know the amount of fault offset and the lithologies that “rubbed each other,” we can calculate a shale gouge ratio.
For this example,
SGR = (Vsh for Layer 5 * thickness Layer 5) +
(Vsh for Layer 6 * thickness Layer 6) +
(Vsh for Layer 7 * thickness Layer 7)
Vertical Offset
Or
SGR = Σ (Vsh * Δz) / VO
Where Vsh = Volume of Shale
Δz = Layer Thickness
VO = Vertical Offset
The higher the SGR, the more likely the fault will seal HCs
Notes: Cross-fault leak is dependent on the permeability of the fault gouge. If we know the amount of fault offset and the lithologies that “rubbed each other,” we can calculate something called the shale gouge ratio. We need the stratigraphy “pre-fault.” This might come from a nearby well or a “best guess” based on seismic stratigraphic analysis. For illustration purposes, we’ll use the stratigraphy shown on this hypothetical cross section. We need to link a high-side point to the corresponding low-side point. Here we will use the base of sand A as our point of reference. The red arrow shows the amount of vertical offset. As the base of sand A went down, it “rubbed” the entire thickness of layer 7 (sand A) plus layer 6 plus layer 5. The formula for the shale gouge ratio (SGR) is shown. Vsh is the volume of shale in a rock layer as a percent. A pure shale would have a Vsh of 1; a pure sand would have a Vsh of 0. There is no hard and fast rule about what SGR results in sealing faults – it varies by local area. Generally a SGR of 0.7 or higher would be interpreted as a high chance for cross-fault seal.

## Slide 21: Geophysical Evidence
http://www.premierminerals.net/projects.php?proj=12
A sand filled with gas or oil will have a significantly higher reflection coefficient than water sands, silts or shales. In some cases, high seismic amplitudes will indicate the HC fill of a trap. In such cases, we can tell a lot about the sealing capacity of faults.
High Seismic Amplitudes
High seismic amplitude values on the crest of the anticline that conform to a depth contour.
Gas was found west of the fault.
There is a high chance of success for a well to the east of the fault.
Well Found Gas
Undrilled
Fault Block
Proposed Location with High Chance for Success
High seismic amplitudes fit inside a depth contour
Well Was Dry
Notes: When gas or oil fills the pore space in a sand, its impedance is reduced, sometimes significantly. If we map the top of a sand reservoir, we can display the amplitudes along that interpreted horizon. If the presence of HC results in a significant change in the reflection coefficient, seismic amplitudes will show is HC distribution. This is one type of direct HC indicator (DHI) what industry loves to find and use. The map is the seismic amplitude along a reflector at the top of a sand. A well on the west encountered gas in the sands. The ‘hot’ colors indicate very high seismic amplitudes. These high amplitudes are at the crest of the western fault block, added support that high seismic amplitudes indicate the presence of gas. There is also high seismic amplitude to the east of the gas well and at the crest of the eastern fault block. Thus, the seismic data suggest we will find gas to the east of the fault and we also have an indication of the extent of the gas. Note the offset in high amplitudes near the southern tip-out of the N-S fault. This is evidence that this fault is sealing, since the down-dip extent of the gas is offset.

## Slide 22: Elements and Processes
Essential Elements
Source rocks
Reservoir rocks
Seal rocks
Overburden rocks
Major Processes
Trap formation
Hydrocarbon
  Generation
  Migration
  Accumulation
Source
Migration
Reservoir
Trap
Seal
Notes: We have talked about seal a little. This is about all we can cover in this course. Let’s move on to HC migration.

## Slide 23: Hydrocarbon Migration
Hydrocarbon migration is the movement of oil and gas molecules in the subsurface. The primary driving mechanism is pressure-driven buoyancy, lighter molecules moving to lower pressure conditions. Normally this is vertical movement, but over-pressure can result in some non-vertical migration.
http://www.bing.com/images/search?q=hydrocarbon+seal&FORM=HDRSC2#view=detail&id=0668B0B3CA4D515146258369DD6124D80B9F0633&selectedIndex=54
HC migration can be along porous carrier beds or up through fault zones or fracture networks.
Migration
Notes: Hydrocarbon migration is the movement of oil and gas molecules in the subsurface. The primary driving mechanism is pressure-driven buoyancy, lighter molecules moving to lower pressure conditions. Normally this is vertical movement, but over-pressure can result in some non-vertical migration. HC migration can be along porous carrier beds or up through fault zones or fracture networks.
The figure shows HC generation at a relatively deep level. Molecules move up the fault zone until they reach a porous, lower pressure sandstone unit. The HC molecules then travel near the top of the sand to the crest of an anticlinal structure. The layer above the sand is a impermeably shale (cap rock). This shale prevents the HC to escape from the sands at the crest of the anticline.
There is too much gas for all of it to be dissolved in the oil. Thus we have a gas cap (red) (gas is more buoyant than oil so rises higher) and an oil leg (green).

## Slide 24: Two Types of HC Migration
Primary Migration: is the percolation of oil and gas molecules out of the source layers and into a more porous carrier bed. There is a delay time between when the source starts to generate HCs and when oil and gas starts to leave the source layers. This delay is built into most software.
Secondary Migration: is the movement of oil and gas molecules once they leave the source up until they reach the first trap. This movement occurs in silt and sand layers (does not have to be reservoir-quality sands) or up faults and fractures.
Notes: We speak of two types of HC migration:
Primary Migration is the percolation of oil and gas molecules out of the source layers and into a more porous carrier bed.
There is a delay time between when the source starts to generate HCs and when oil and gas starts to leave the source layers.
This delay is built into our HC migration software.
Secondary Migration is the movement of oil and gas molecules once they leave the source and until they reach the first trap.
This movement occurs in silt and sand layers (does not have to be reservoir-quality sands) or up fault zones and/or fracture networks.
Typically we just assume that primary migration will occur.
We do try to understand secondary migrathion pathways in our area of study.

## Slide 25: HC Migration
Let’s consider a drop of oil generated in the source interval and its journey to a trap.
Carrier
Source
Primary Migration out of the source
A drop of oil is generated
The drop moves up to a carrier bed
Travel in a carrier bed to the top of the closest anticline
Notes: Here we consider a drop of oil generated in a source layer. First, the oil has to get out of the source. This is primary migration. It tends to be a very tortuous path that we don’t try to model. Once out of the source interval, the oil molecule will percolate from higher pressure areas to lower pressure areas, which is generally vertically up. If the molecule “finds” a porous and permeable layer (which typically has lower pressure than shales), it will start to travel along the top of this carrier bed. Migration continued until the oil is trapped (structural, stratigraphic or combination) or it gets to the surface (a HC seep).

## Slide 26: Carrier Bed Migration
For basin modeling/predictions, we look for regional sequences that we can map, and that are (or we believe would be) able to handle secondary migration. We generate depth (or time) structure maps for the tops of these sequences. Then we perform a secondary migration analysis.
Carrier
Source
Synclines are Drainage Divide
Trap W
Trap E
Notes: To model and/or understand secondary migration, we look for regional sequences that we can map, and are (or we believe would be) able to handle secondary migration. We generate depth (or time) structure maps for the tops of these sequences. Then we perform a secondary migration drainage analysis.
For example, the drop of oil on the left will percolate up to the top of the carrier bed, then it will move updip (by buoyancy) to Trap W.
The drop of oil on the right will percolate up to the top of the carrier bed, then it will move updip (by buoyancy) to Trap E. The drop of oil near the center will percolate up to the top of the carrier bed. It happens to get to the top of the carrier bed at the center of a syncline. This molecule has a 50% chance to go west to Trap W and a 50% chance to go east to Trap E.
Synclines therefore become HC migration drainage divides. It is similar to drainage divides for water along the crest of the Rockies. For water, the driver is gravity, rain drops want to get low, and the drainage divides are crests. Water reservoirs (lakes, seas, oceans) are lows. For HC molecules, the driver is buoyancy, oil drops want to get high, and the drainage divides are synclines. HC reservoirs are high points.

## Slide 27: Carrier Bed Modeling
Schematic of the surface of a carrier bed showing flow vectors (black arrows), drainage divides (blue lines) and the free gas caps (lt. red) and oil legs (green)of four culminations.
3D
View
Map
View
Schroeder & Sylta, 1993
Notes: Here we have a 3D view of some anticlines and synclines. We’ll assume this surface is the top of a carrier bed with a seal above it. HC molecules percolate up to this surface. We can subdivide this surface into drainage polygons by considering all the synclines as drainage divides. Then any molecules that reach the top of the carrier bed within a particular drainage divide will migrate updip to the anticline within that drainage divide. The black arrows show some modeled migration paths within the different drainage polygons. The structural highs show gas caps (red) and oil legs (green).
Geoscientists love to work with maps. We can represent the 3D surface by a map by projecting the 3D view onto a common depth plane. With depth contours for the top of the carrier bed, we can define the drainage polygons and locate the structural traps. Then we can determine the “fetch area” for each trap. With computer software we can do the same thing, but we can do the bookkeeping to determine the volume of oil and gas that can reach each trap. Wow!

## Slide 28: A Single HC Fetch Area
H = High Point
= Drainage
Divide
= Fetch for
trap H1
H2
H4
H3
H1
Notes: This is meant to represent part of a depth map for the top of a carrier bed. There is a central high (H1) that is surrounded by synclines (dashed red lines). The yellow area is the area that would “feed” HC molecules to trap H1. We call this the fetch area for H1. Any HC molecule generated in the source that percolates to the top of the carrier within this fetch area (yellow) would move updip towards H1. As more HC reaches H1, the trap fills with gas and/or oil.
What if the volume of HC reaching H1 is greater than the volume of HC that trap H1 can hold? Let’s use a simple analogue.

## Slide 29: HC Fill & Spill – An Analogy
Inverted 12 Oz container in an aquarium
Air Pump
Pump in 3 oz
Pump in 6 oz
Pump in 9 oz
Pump in 12 oz
What would happen if we added more air?
Notes: Here is an analogy for trap fill and spill. We have a 21 oz container filled with water in an aquarium. We start the air pump and add air to the bottom of the container. It fills with 3 oz of air, then 6, then 9, then 12 oz. If we add more air, it spills out the bottom of the container and bubbles upward.
The same thing happens with oil and gas. The air pump is HC generation within the source. If the first trap along the HC pathway can’t hold all the HC, the excess spills and migrates further along the migration pathway. If there are more traps, they fill progressively.

## Slide 30: HC Fill & Spill
H
Mini-Basin 3
H
Mini-Basin 2
Mini-Basin 1
Oil Spills from 1 to 2
H
Oil Spills from 2 to 3
Mini-Basin 3
Mini-Basin 2
Mini-Basin 1
Oil
Kitchen
Notes: Here is a simple diagram of an oil migration pathway. Oil is generated in a “kitchen” to the south. Trap 1 is filled to capacity; excess oil spills up to mini-basin 2. If trap 2 fills to capacity, excess oil spills up to mini-basin 3. Trap 3 will start to fill., etc.

## Slide 31: HC Fill & Spill
A huge accounting exercise.
First, define all the drainage polygons.
Second, calculate the volume of all the oil & gas generation within each drainage polygon (local fetch).
Third, calculate the volume of HC each trap can hold.
Then model HC migration:
  Start with the deepest drainage polygon-trap,
  Fill the deepest trap with oil and gas,
  If there is excess HC volume, added it to the drainage polygon it would spill into, and
  Progressively work up to the shallowest polygon-trap.
Notes: This summarizes the steps that we go through. Exercise 10b takes you through some of these steps.

## Slide 32: North Sea Example
Schroeder & Sylta, 1993
An Example Drainage Polygon:
  Has a unique ID number (e.g., 12345).
  Has a trap defined by a culmination depth and a spill/leak depth.
  Has local HC generation (fetch volume).
  Has spillage into it from a deeper drainage polygon.
  Trap pore volume is filled with oil and gas:
    Filled with oil + dissolved gas.
    If excess gas, a gas cap is formed.
    If there is too much gas, oil (with dissolved gas) spills first.
    If all the oil spills and there is still excess gas, then gas will spill.
Notes: The next few slides walk through an example from the North Sea. This shows an example drainage polygon, obtained from a grid for the top of the main reservoir. Each polygon has a structural trap, in the case on the east side and given an ID of 12345. The leak point for this trap is on the east side. This trap is shown to have a gas cap (red) and an oil leg (green). The black arrows show some representative migration paths within the polygon.

## Slide 33: HC Drainage
Schroeder & Sylta, 1993
Local Drainage:
  HC generation
  HC expulsion
  Primary migration
  Secondary migration to local structural culmination
    Paleo-structure of the top of carrier
    Along the steepest gradient
  HC loss during migration
Spillage
Notes: Local drainage is the HC that is generated within the polygon and its migration to the local (within polygon) trap.
We need to model: 1) HC generation, 2) HC expulsion, 3) Primary migration, which is out of the source rock, 4) Secondary migration, which is to the local structural high, which includes the need to know the paleo-structure of the top of carrier beds (reservoir) and that secondary migration is up along the steepest gradient, and 5) Some HC will be lost during the migration process. The software used here, called SEMI, does all the bookkeeping based on user input.

## Slide 34: Drainage and Spillage
HC Spillage:
  HC charge to trap
    Previously stored
    Incremental drainage
    Spill into drainage
  Gas volumetrics
    In-situ gas density
    Gas in solution
    Gas leakage through cap
  Spillage out of trap
    Excess volume
    Spill direction
    Oil flushed by gas
Schroeder & Sylta, 1993
Notes: If more HC reaches trap 12345 than it can hold, the excess spills further up the migration pathway. Gas is lighter and so oil (with some dissolved gas) spills first. Here, excess HC volumes spill from #12345 to #23460. Excess from both #23460 and # 11234 spill into #37301.
Consider trap #23460 for a moment. It has HC generated within its own drainage polygon. It also has spillage of HC from trap #12345. The combination of locally generated and spilled HC volumes are compared to the capacity of trap #23460. As is shown, the combination is greater than the capacity of trap #23460, so oil spills to trap #37301. Thank goodness for software that keeps track of all the volumes!

## Slide 35: Modeled Trap HC Fill
Brage – no local HC drainage, only spilled oil with dissolved gas.
Huldra – post maximum oil content due to excessive gas flushing its oil updip.
Oseberg – near maximum oil content due to local oil drainage and oil spilled from downdip traps.
Traps
DEEPEST
SHALLOWEST
Schroeder & Sylta, 1993
Notes: For this study area, there were three major fields along a main HC migration route. From deepest to shallowest they are Huldra, Oseberg and Brage. On the left are plots through geologic time of (1) oil fill, (2) total gas fill, (3) free gas (gas cap). Huldra (blue line) started to fill with oil and gas. About 30 MY ago excess gas caused oil to spill. Oseberg (orange line) also started to fill with oil and gas. It had a gas cap early, but now all the gas is dissolved in oil (no free gas). Brage (magenta line) received no HC until about 25 MY ago. This all spilled oil and gas from over-filled deeper traps. It is oil with dissolved gas, no gas cap (free gas).

## Slide 36: References
Slide 3, 23: http://www.bing.com/images/search?q=hydrocarbon+seal&FORM=HDRSC2#view=detail&id =0668B0B3CA4D515146258369DD6124D80B9F0633&selectedIndex=54
Slide 4: http://www.bing.com/images/search?q=hydrocarbon+seal&FORM=HDRSC2#view=detail& id=7BD59D95C835A73BCA76D82D377228D7BB7B433F&selectedIndex=15
Slide 6: http://www.glossary.oilfield.slb.com/en/Terms.aspx?LookIn=term%20name&filter=spill%20point
Slide 7: http://www.searchanddiscovery.com/documents/2008/08038putney/images/fig01.htm
Slide 9: http://www.pgs.com/Geophysical-Services/Seismic-Techniques/HD3D/Applications/
Slide 10: http://www.callforbids.cnsopb.ns.ca/2012/01/sites/default/files/images/inline /figure_44.jpg
Slide 16: http://en.allexperts.com/q/Geology-1359/2009/12/Petroleum-Geology-4.htm
Slide 19: http://wiki.aapg.org/Fault_seal_quantitative_prediction:_shale_smear_factor,_shale_gouge _ratio,_and_smear_gouge_ratio
Slide 21: http://www.premierminerals.net/projects.php?proj=12
Slides 27, 32-35: Schroeder & Sylta, 1993, Modelling the hydrocarbon system of the North Viking Graben: a case study, in Dore et al (ed.), Basin Modelling: Advances and Applications, NPF Special Publication 3, Elsevier, pp. 469-484.
Notes: References

## Slide 37
Questions?