## Slide 1
Part B: Hydrocarbon Charge
Using HC Charge and Trap Volumes
Your Task:
  Estimate the HC fill in three traps given in three different models of HC charge

## Slide 2: Frontier Exploration Map
This map shows three traps and their associated drainage polygons.
Oil is assumed to be generating in the shaded area.
You will estimate the volume of generated oil and the HC capacity of the three traps.
You’ll determine the HC fill in each trap for three different cases.
Notes: This map shows three traps and their associated drainage polygons. Oil is assumed to be generating in the shaded area to the SW.
You will estimate the volume of generated oil and the HC capacity of the three traps. You will determine the HC fill in each trap for three different cases.

## Slide 3: Introduction
You are working a frontier exploration area as part of a small team. A geochemist has modeled the amount of oil and gas generated in the “kitchen” that is down-dip of three structural traps that you have mapped. As is normally the case, there is not a single HC generation model.
Your task is to estimate the volume of HC that each trap can hold. Then you will estimate the HC charge. Next you will determine the HC distribution for three different HC charge possibilities.
Trap Volumes – Keep It Simple
Total Volume = 1/3 π Ravg2 (Htop – Hbase)
Notes: We do not expect very precise numbers since we have so much uncertainty. We can use some simplifying assumptions to get trap volumes. The diagrams on the left illustrate how we can get the volume of the trap assuming a simple cone shape. This diagram and the equation are in the instructions.

## Slide 4: Trap Parameters
Table 1. Key Information for the three traps
Notes: Students will estimate the north-south diameter and east-west diameter for each trap (Figure on Slide 1). They can then get an average diameter and an average radius, which is needed for the equation. The maximum height of the top of the reservoir above the spill depth is Htop. The maximum height of the base of the reservoir above the spill depth is Hbase. With the last three (3) rows, the total trap volume can be calculated.

## Slide 5: Trap Volumes
Table 2. Steps to getting the HC capacity for each trap
Notes: Total Trap Volume is the result from the equation on Slide 3. We multiply the total trap volume by the net-to-gross to get reservoir volume. We can multiply the reservoir volume by porosity to get pore volume. We multiply the pore volume by the HC saturation to get the HC volume. We can convert HC volume from units of km3 to HC volume in million barrels (MBO) by multiplying by 6333.

## Slide 6: Oil Yield within the Kitchen
Low Side
Depths
The geochemist on your team has developed a most-likely generation model, what you might call her best educated guess. She assumed a hydrogen index (HI) value of 500, a total organic carbon (TOC) of 5% and a source thickness of 20 meters. With these source parameters, she expects an oil yield of 12.5 MBO per square kilometer.
So you need the area of the kitchen in km2.
Notes: To get the volume of oil reaching Trap A (its charge), the students need the area of the kitchen. They can count the number of gray squares and multiply by 4 to get the area in km2.

## Slide 7: Case 1: Most Likely
Use your estimated oil volume as the amount of HC reaching Trap A to determine the oil distribution in all three traps.
Hint: If there is excess oil reaching Trap A, the excess volume will spill first to Trap B and then to Trap C.
Notes: Case 1 is a charge of 1200 MBO. This is larger than the HC capacity of Trap A, so the excess starts to fill Trap B.

## Slide 8: Case 2: Minimum Oil Case
Use 75% of your estimated oil volume as the amount of HC reaching Trap A to determine the oil distribution in all three traps.
Notes: Case 2 is a charge of 900 MBO. This is larger than the HC capacity of Trap A, so the excess starts to fill Trap B.

## Slide 9: Case 3, Oil and Gas Case
Assuming that 1200 MBO of oil plus the equivalent of 1200 million barrels of gas reached Trap A, determine the oil and gas distribution in all three traps.
Hint: Gas will push oil out of the lower traps causing first oil and then gas to spill updip.
Notes: Case 3 is a charge of 1200 MB of oil plus 1200 MB equivalent of gas. Trap A is filled to capacity with gas (only). Trap B has a gas cap and an oil leg. Trap C has only oil and brine.

## Slide 10
Questions?