## Slide 1
Map a Regional Unconformity
Map a Regional Unconformity
Your Task:
  To map a regional unconformity, called the Top of Latrobe (TOL) unconformity.

## Slide 2: Introduction
We have a regional grid of 14 2D seismic lines. The TOL unconformity has already been interpreted on six (6) of these lines. Your task is to complete the TOL interpretation on the other eight (8) lines by tying loops. You may do this as a part of a team (2-3 people).
Your goal is to locate large anticlines that could be traps holding economic amounts of oil or gas.
Notes: This introduces the data set – five (5) east-west lines and nine (9) north-south lines. They are given the TOL on six (6) of the lines. They want to find large anticlines. You can have them work individually or in teams of 2 or 3 people.

## Slide 3: Data Coverage
Line 1
Line 4
Line 3
Line 2
Line 7
Line 6
Line 5
Line 8
Line 9
Line A
Line B
Line C
Line D
Line E
Block 11
Block 15
Block 14
Block 13
Block 12
Block 21
Block 25
Block 24
Block 23
Block 22
Block 31
Block 35
Block 34
Block 33
Block 32
10 km
Regional-scale 2D seismic grid
Notes: Lines with interpretation are solid. Lines to work are dashed. The yellow circles indicate intersections to be tied.

## Slide 4: Introduction
The TOL unconformity is easy to spot:
  Below the surface there are strong, continuous reflections, with erosional truncation apparent at some locations.
  Above the surface there are low amplitude, less continuous reflections.
Line B
Line 7
Line 8
TOL
Reservoir
Seal
5 km
Notes: Criteria for identifying the TOL unconformity.

## Slide 5: Introduction
The color seismic sections are nice to look at but they are difficult to mark with anything but a marker. You can’t erase marker lines.
I recommend that you mark the TOL with dotted or dashed lines initially. Once you tie some loops and are satisfied with your interpretation, you can make the lines solid.
NOTE: We do not have to be very precise; we are looking for ‘elephants.’ Even if you are off a couple of seismic cycles on the TOL position, the structures will still stand out.
Notes: The color lines are hard to mark with pencils. I suggest they use a color marker (e.g., green). However, markers can’t be erased. The good thing is that given the task of finding highs, we don’t have to be precise (more of this on slides 11 and 12). Either than can make initial correlations using dashed lines OR use solid lines and don’t worry about minor misties.

## Slide 6: Complete A Quick Interpretation
Line 1
Line 4
Line 3
Line 2
Line 7
Line 6
Line 5
Line 8
Line 9
Line A
Line B
Line C
Line D
Line E
Block 11
Block 15
Block 14
Block 13
Block 12
Block 21
Block 25
Block 24
Block 23
Block 22
Block 31
Block 35
Block 34
Block 33
Block 32
Work as a team – Divide the work
10 km
Notes: If they work in teams of 2 or 3, they need to work at the same time/place but can divide the work e.g., one person work Line C while another works Line 7.

## Slide 7: Evidence for Faulting
Significant offset in the reflection patterns.
Terminations of reflections along the fault plane.
There can be a change in reflector dip across the fault plane.
Near-vertical zones of poor imaging.
Line C
Line B
2000
1800
1600
1400
1000
1500
1000
1500
Line 3
TOL
TOL
5 km
Notes: The students don’t have to map faults – as in tie them or have fault symbols on their maps. They can mark the faults on their seismic lines if they want.

## Slide 8: Evidence for Erosion
Irregular surface separating the reflection patterns.
Terminations of reflections below the TOL surface.
Onlap of reflection above the TOL surface (fill).
Change in the dip of the reflections across the TOL boundary.
4600
4400
5200
4800
5000
1000
1800
1500
Line 7
Line B
TOL
TOL
5 km
Notes: Part of Line B shows evidence of erosion below the TOL unconformity.
NB. Line B is not interpreted, so they can use this slide to mark this part of Line B.

## Slide 9: Erosion at the TOL Surface
There was a lot of tectonic movement as this rift zone died.
TOL surface is faulted and has lots of relief.
High blocks were subject to major erosion.
Younger sediments filled in the paleo-topography.
Photo of F. Schroeder near the TOL surface prior to the deposition above the TOL
Notes: The photo provides a modern example of the type of relief there was before the deposition of the sediments above the TOL unconformity. Photo is from Canyonlands National Park, Utah, USA.

## Slide 10: Look for Anticlines
Line A
Line
3
Line
4
Line
5
Line
6
Line
7
2200
2000
2600
2400
3200
2800
3000
3800
3600
3400
4000
1800
1600
500
0.0
1000
1800
1500
500
0.0
1000
1800
1500
LaTrope
Lake Entrance
Shot Points 2625 - 3100
0 km 10
Notes: Once the students have an anticline (that could be a hydrocarbon trap), they should note its position on the line. The students can use the shot points, as shown here. They can also say the high is from Line A’s intersection with Line 5 to ¾ of the way to Line 6. Any way for them to associate the high with a position on the basemap.

## Slide 11: Speed – Not Precision
The TOL horizon does NOT have to be very precise for our current need. We just want to locate major anticlines.
AQUA Option
LIME Option
Whether you marked the AQUA option or the LIME option, a major anticline would still be found
0 km 4
Notes: We are simulating a quick look for possible structural traps. We don’t need precision – just so we can mark anticlines. The driver here is speed. Later, we will be worried about stratigraphic precision.

## Slide 12: Don’t Fret the Synclines
In terms of locating anticlines, it does not matter if you choose the shallow or deep option.
Shallow
Option
Deep
Option
0 km 4
Notes: Again, we are focused on anticlines. We are not concerned YET with how deep the anticlines are. That comes later.

## Slide 13: Post Extent of Anticlines
Line 1
Line 4
Line 3
Line 2
Line 7
Line 6
Line 5
Line 8
Line 9
Line A
Line B
Line C
Line D
Line E
Block 11
Block 15
Block 14
Block 13
Block 12
Block 21
Block 25
Block 24
Block 23
Block 22
Block 31
Block 35
Block 34
Block 33
Block 32
0 km 20
Notes: The students can relate the position of anticlines seen on the lines to locations on the basemap. They can use a pencil or highlighter to mark the anticlines on the basemap.

## Slide 14: Draw Polygons around Anticlines
14
Line 1
Line 4
Line 3
Line 2
Line 7
Line 6
Line 5
Line 8
Line 9
Line A
Line B
Line C
Line D
Line E
Block 11
Block 15
Block 14
Block 13
Block 12
Block 21
Block 25
Block 24
Block 23
Block 22
Block 31
Block 35
Block 34
Block 33
Block 32
Just an Example
More Realistic?
0 km 20
Notes: After marking the anticlines seen on each line, they can look for patterns and draw ovals on the map. They are to represent possible structural traps.
NOTE: There is NO SOLUTION for this exercise since their map is input for the next exercise.

## Slide 15
Questions?