## Slide 1: Petroleum Geology & Geophysics
Basics of Seismic Interpretation
Notes: This unit gives a very simple introduction to seismic interpretation. It’s the view from 10,000 ft. The remainder of the course will explore basic steps in more detail.

## Slide 2: Acoustic Structure of the Earth
Shot
Receiver
I1 = 1 * V1
I2 =  2 * V2
I4 =  4 * V4
I3 =  3 * V3
Reflection
Coefficients
Pulse
C
O
N
V
O
L
U
T
I
O
N
Seismic
Trace
Imped
Low
High
Notes: This slide is a recap of the seismic method. A good seismic interpreter needs at least a basic understanding of what the seismic wiggles are caused by.

## Slide 3: Marking Faults and Horizons
We have looked at the basic theory behind reflection seismology in earlier lessons.
Now we are ready to start marking seismic sections.
Our first goal is to get a geologic framework:
  Most of the significant fault planes,
  Most of the significant stratigraphic surfaces, and
  Proper horizon-fault and fault-fault intersections.
Notes: Again, basic theory is an important foundation for good seismic interpretation. Now we can start to actually mark seismic data – with color pencils on paper copies or by using a computer mouse. Our first goal …….

## Slide 4: Interpretation Process
Theory behind Reflection Seismology
Geologic Framework
Interpret Faults
Interpret Horizons
Iterate
Notes: This is a simple diagram of the interpretation process. Given an understanding of the theory, we interpret faults and horizons (sequence boundaries) on seismic data. An experienced interpreter works faults and horizons iteratively. Some interpreters are stronger in structural analysis; others are stronger in stratigraphic analysis. After a few years of interpretation experience, interpreters should be competent in both structural and stratigraphic analysis. Our first goal is to build a geologic framework, which will be explained on the next slides.

## Slide 5: Geologic Framework
Structural Interpretation
    Faults & Folds
    Subsidence & Uplift
    Structural Trends
    Structural Features
Stratigraphic Interpretation
    Unconformities
    Stratal Packages
    Environments / Facies / Lithologies
    Ages
Using all available data (wells, seismic, outcrop, regional studies, gravity, magnetics, etc.) build a framework of present-day structure and stratigraphy
Notes: What do I mean by a geologic framework? It is using all available data to build a framework of present-day structure and stratigraphy. This slide shows what is included in a structural analysis, and a stratigraphic analysis, respectively.

## Slide 6: Geologic Framework: Structural Analysis
Faults
Detached Faults
Diapirs
Folds
Salt
Notes: During a structural analysis, we would be interpreting and mapping: faults, folds, salt or shale diapirs, detached faults, and other types of structural elements. We also want to know the type of basin we are dealing with: extensional, compressional, strike-slip (wrench).
We want to define present-day structure, especially as it relates to present-day traps.
We will also want to understand how the basin and traps formed over geologic time.

## Slide 7: Interpreting Structure
Structural
Observations
Structural
Concepts
Notes: When interpreting structure, we make observations and use structural concepts to guide our thoughts and analyses.

## Slide 8: Geologic Framework: Stratigraphic Analysis
Terminations Mark Unconformities and define Seismic Sequences
Erosional Terminations
Onlap Terminations
Reflection Geometries
Horizon Amplitude
Individual Seismic Sequences Are Analyzed
High
Low
Notes: During a stratigraphic analysis, we would be interpreting and mapping: erosional unconformities, packages of onlaping sediments, the geometries of reflections, the seismic attributes, such as horizon reflection amplitude, and other types of stratigraphic signatures. We also want to know the depositional environments for key sedimentary units.
We want to define present-day stratigraphy, especially as it relates to present-day reservoirs, seals, source intervals and traps.
We will also want to understand how the basin filled with sediment over geologic time.

## Slide 9: Interpreting Stratigraphy
Stratigraphic
Observations
Stratigraphic
Concepts
Notes: When interpreting stratigraphy, we make observations and use stratigraphic concepts to guide our thoughts and analyses.

## Slide 10: Structure Maps
1 mile
Shallow
Deep
4 Major Faults
Can be depth structure (ft or m) or two-way time structure (ms)
Represents the 3D shape of a mapped horizon with fault offsets
Can be a 3D visualization or a contour map
Notes: 10
Our combined structural and stratigraphic analysis results in a series of horizon structure maps. These maps may be depth structure maps, which have units of feet or meters, or time structure maps, which have units of milliseconds. These structure maps represent the 3D shape of a mapped horizon with fault offsets. We can display these maps as simple contour maps or, as shown here, a 3D visualization of the shape using color to represent depth.
This image is a map view of a mapped seismic horizon that has fault offsets as illuminated from the southwest. It is a time structure map (red is high, blue is low). There are four (4) major faults and many small-offset faults.

## Slide 11: Remainder of this Course
Seismic Interpretation and Beyond …
  Develop a Geologic Framework
  Use the Geologic Framework to Prospecting (Exploration)
Given the scope and time constraints for this course, we will only be able to look at a subset of the concepts, procedures and tools that geologist and geophysicists use in the exploration phase of the oil & gas industry
Notes: The remainder of this course will cover seismic interpretation and beyond. These two main goals (development of a geologic framework, and exploration) may not seem like a lot, but petroleum scientists employ a lot of science to do this - more science than we can even introduce in this course. Hopefully the remaining lessons will give you an appreciation for what geoscientists do to help their company to make some money.

## Slide 12: Exploration Workflow: Overview
1. Geologic Framework
2. Data Analysis
3. Prospect Elements
4. Prospect Assessment
We can subdivide the exploration work process from seismic interpretation forward into four (4) major elements
Notes: This slide shows four (4) steps in the exploration process. We will study each step.

## Slide 13: Tying Loops
To get consistent 3D horizons and fault planes from seismic data, we use a process called loop tying.
This process started when we only had 2D seismic lines. It carries over to some degree with 3D seismic volumes.
Line 1
Line 2
Line 3
Line A
Line B
Line C
Loop 1
Loop 4
Loop 3
Loop 2
N
Interpret faults and/or horizons on one section (e.g., Line 1)
Transfer your interpretation to another line at a line intersection (e.g., from Line 1 to Line B)
Progressively “tie” loops to branch out onto all the lines
Use a base map to mark lines interpreted and intersections checked to monitor progress
Notes: The most basic step in seismic interpretation is to map faults and horizons (sequence boundaries). We need our interpreted fault planes and horizons to be consistent in three (3) dimensions. What we do when we are mapping faults or horizons is called tying loops. This was the only way to interpret when all we had was a series of 2D seismic lines. With 3D seismic surveys, we have some other interpretation options. Even so, most 3D seismic interpreters get started by tying some loops.
What I mean by a loop in this context is a set of intersecting lines that form a closed loop (polygon). The map diagram shows four (4) loops. Let’s discuss mapping a horizon that is colored yellow around loop 1. My discussion will be for working paper seismic lines.
First, I would interpret the yellow horizon on Line 1. I would fold Line 1 where it is intersected by Line B and lay it on top of Line B at the common x,y point. I’d transfer the position of the yellow horizon from Line 1 to Line B by putting a yellow dash on Line B. Then, I’d use the yellow dash on Line B to interpret the yellow horizon on all or part of Line B. Next I’d fold Line B where it intersects Line 2, and transfer the yellow horizon from Line B to Line 2. Finally, I’d interpret the yellow horizon on all or part of Line 2, and transfer the yellow horizon to Line A and interpret Line A. Check that the yellow horizon on Line A agrees with where I interpreted it on Line 1 at the intersection point.
If the loop “closes,” i.e., the yellow horizon is consistently positioned at all four (4) intersection points, I’m ready to proceed to another loop. If the loop does not “close,” then I have to figure out what part(s) of the loop have to be corrected so it is areally consistent. Can you see how this develops an interpretation that is areally consistent? Areal consistency is a necessary characteristic of a correct interpretation, but areal consistency does not guarantee a correct interpretation.

## Slide 14: Tying a Fault
Line 103
100
200
101
102
103
104
205
204
203
202
201
Line 103 (see map)
Disrupted reflections are evidence for a major fault plane
Fault A is drawn in red
Fault A
Notes: The next few slides show how we tie a fault. We’ll use Fault A, drawn in red. This is line 103, which runs east-west (magenta on map).

## Slide 15: Fault A on Line 102
Line 102 (see map)
Disrupted reflections are evidence for a major fault plane
Line 102
Fault A
100
200
101
102
103
104
205
204
203
202
201
Notes: Line 102 is the next east-west line, which is about 1.25 km north of the initial line. Fault A is interpreted. We have independent interpretations on two (2) parallel seismic lines. We can check for areal consistency by using one or more of the north-south lines. I’ll illustrate using only Line 201.

## Slide 16: Intersection of Lines 103 & 201
Line 103
Line
203
Line
204
Line
202
Line
200
Line
201
W
E
S
N
Line
100
Line
103
Line
102
Line
101
Line
104
Line
106
Line
105
Line 201
Fault A
100
200
101
102
103
104
205
204
203
202
201
Notes: Here I have east-west Line 103 with the interpreted fault on the left. On the right, I have north-south Line 201, which has no interpretation. NOTE on the basemap that these two (2) lines intersect. At that intersection point, Fault A can have only one depth, or in our case, one two-way time.

## Slide 17: Mark Tie Point on Line 201
S
N
Line
100
Line
103
Line
102
Line
101
Line
104
Line
105
Line 201
Line
200
W
Line 103
Line
201
100
200
101
102
103
104
205
204
203
202
201
Notes: I fold Line 103 at the point where it is intersected by Line 201. Then, I slide the folded line on top of Line 201, so the crease is at the intersection point. I transfer the interpreted position of Fault A at the intersection point by placing a red dot on the uninterpreted line (201). Next, I do the same thing for the intersection of Line 201 with another line.

## Slide 18: Intersection of 102 & 201
Line 102
Line
203
Line
204
Line
202
Line
200
Line
201
W
E
S
N
Line
100
Line
103
Line
102
Line
101
Line
104
Line
106
Line
105
Line 201
Fault A
100
200
101
102
103
104
205
204
203
202
201
Notes: I will use the interpretation of Fault A on Line 102 to get its position on the intersecting Line 201.

## Slide 19: Mark Tie Point on Line 201
S
N
Line
100
Line
103
Line
102
Line
101
Line
104
Line
105
Line 201
Line 102
Line
200
Line
201
W
100
200
101
102
103
104
205
204
203
202
201
Notes: I fold Line 102 at the appropriate intersection point, and slide it over on top of Line 201. Mark Line 201 based on the interpretation marked on Line 102. This gives me a consistent interpretation at this second intersection point on Line 201.

## Slide 20: Interpret Line 201
S
N
Line
103
Line
102
Line
101
Line
104
Line
105
Line 201
Line
100
Fault A
100
200
101
102
103
104
205
204
203
202
201
Notes: Given the two tie points (red dots), I see if I can get a full interpretation of Fault A on Line 201. In this case, I can get a fault interpretation of the fault based on the reflection terminations that also honor the two (2) tie points. I may find that I can’t honor the tie points. Then, I have to decide how to tweak the interpretation on ONE of the three (3) lines to get spatial consistency.
Tying a series of faults over a study area takes a lot of iterations (mark, erase, re-mark, check, etc.).

## Slide 21: Keep Track on the Basemap
For Fault A
Interpreted on three (3) lines
Tied at two (2) line intersections
Continue to map Fault A and check for areal consistency at other line intersections
100
200
101
102
103
104
205
204
203
202
201
Notes: Either on paper or on a computer station, an interpreter will mark a basemap to show which lines have been interpreted and which tie points have been checked and are consistent.

## Slide 22: Two-Monitor Computer
When interpreting on a computer, most interpreters use at least 2 monitors
  One to display the seismic lines
  The second to display a basemap
Seismic Displays
Basemap
Notes: Here is a typical computer station for seismic interpretation. NOTE: an old picture before flat screen monitors. The monitor on the left has seismic lines displayed with faults and horizons. The right monitor has a basemap, on which most people will display one horizon to indicate which lines have been interpreted. The basemap indicates which seismic line(s) is/are displayed. It updates automatically as the displayed horizon is interpreted more and more.

## Slide 23: Tying a Horizon
Line 103
100
200
101
102
103
104
205
204
203
202
201
Line 103 (see map)
There is a change of reflection dip about ¼ of the way down, indicating an unconformity
The reflections below the unconformity rise and terminate
Fault A
Notes: The next few slides show how we use the same basic procedure to map a horizon so that it is areally consistent. Here is the east-west Line 103 with Fault A. There is a major unconformity that we want to map. Notice the reflections change dip above/below the yellow horizon. Also note that I have added a dashed blue line on the basemap to indicate Line 103 has been interpreted. The reflections below the yellow horizon dip up to the right and terminate (an indication of significant erosion). I have mapped this unconformity with a yellow line. Now, I want to map this unconformity on other lines and get an areally consistent surface, with fault offsets.

## Slide 24: Intersection 103 & 204
Line 103
Line
203
Line
204
Line
202
Line
200
Line
201
W
E
S
N
Line
100
Line
103
Line
102
Line
101
Line
104
Line
106
Line
105
Line 204
100
200
101
102
103
104
205
204
203
202
201
Fault A
Fault A
Notes: Again, I have an interpreted east-west line (103) that I will tie to an uninterpreted north-south line (204). I’ll do this by folding the interpreted line and using it to mark the yellow horizon on the uninterpreted horizon (next slide).

## Slide 25: Intersection Lines 103 & 204
Fault A
S
N
Line
100
Line
103
Line
102
Line
101
Line
104
Line
106
Line
105
Line 204
Line 103
Line
203
Line
204
Line
202
Line
200
Line
201
W
Fault A
100
200
101
102
103
104
205
204
203
202
201
Notes: As expected, Line 103 is folded, slid across, and used to get a start point for the yellow horizon on Line 204. The basemap shows the right-angle bend I am considering. The yellow horizon is mapped along the north end of Line 204 (shown on basemap).

## Slide 26: Interpretation of Line 204
S
N
Line
100
Line
103
Line
102
Line
101
Line
104
Line
106
Line
105
Line 204
100
200
101
102
103
104
205
204
203
202
201
Fault A
Notes: Now I can interpret the south half of Line 204. The basemap is updated showing that yellow is interpreted for the entire line.

## Slide 27: Intersection of Lines 204 & 102
S
N
Line
100
Line
103
Line
102
Line
101
Line
104
Line
106
Line
105
Line 204
Line 102
Line
203
Line
204
Line
202
Line
200
Line
201
W
E
100
200
101
102
103
104
205
204
203
202
201
Fault A
Fault A
Notes: Next I can use Line 204 for get the yellow horizon on Line 102. The basemap shows these two lines.

## Slide 28: Intersection of Lines 204 & 102
S
N
Line
100
Line
103
Line
102
Line
101
Line
104
Line
106
Line
105
Line 204
100
200
101
102
103
104
205
204
203
202
201
Line 102
Line
203
Line
204
Line
202
Line
200
Line
201
W
Fault A
Notes: Now I use Line 204 to interpret the west end of Line 102. Basemap updates.

## Slide 29: Interpretation of Line 102
Line 102
Line
203
Line
204
Line
202
Line
200
Line
201
W
E
100
200
101
102
103
104
205
204
203
202
201
Fault A
Notes: The east end of Line 102 is interpreted. The basemap is updated.

## Slide 30: Intersection of Lines 102 & 201
Line 102
Line
203
Line
204
Line
202
Line
200
Line
201
W
E
100
200
101
102
103
104
205
204
203
202
201
Fault A
S
N
Line
100
Line
103
Line
102
Line
101
Line
104
Line
106
Line
105
Line 201
Notes: Now I use Line 102 to start my interpretation of Line 201.

## Slide 31: Intersection of Lines 102 & 201
W
E
100
200
101
102
103
104
205
204
203
202
201
S
N
Line
100
Line
103
Line
102
Line
101
Line
104
Line
106
Line
105
Line 201
Line 102
Line
200
Line
201
Notes: The north end of Line 201 is interpreted.

## Slide 32: Interpret Lines 201
100
200
101
102
103
104
205
204
203
202
201
S
N
Line
100
Line
103
Line
102
Line
101
Line
104
Line
106
Line
105
Line 201
Notes: The south end of Line 201 is interpreted.

## Slide 33: Does the Loop Close?
S
N
Line
100
Line
103
Line
102
Line
101
Line
104
Line
106
Line
105
Line 201
Line 103
Line
203
Line
204
Line
202
Line
200
Line
201
W
E
Fault A
100
200
101
102
103
104
205
204
203
202
201
Does the yellow horizon tie where Line 201 intersects with Line 103?
Notes: I have mapped around a closed loop. Now for the test: does the yellow horizon on Line 201 and on Line 103 at their intersection point have the same depth (two-way time) value? If my interpretation is consistent, they will have the same value.

## Slide 34: Does the Loop Close?
S
N
Line
100
Line
103
Line
102
Line
101
Line
104
Line
106
Line
105
Line 201
W
100
200
101
102
103
104
205
204
203
202
201
Line 103
Line
200
Line
201
Does the yellow horizon tie where Line 201 intersects with Line 103?
Yes
Notes: I fold and slide Line 103 and YES the yellow horizon has the same value at their intersection point. Now I can continue my interpretation by closing more loops. If they had different values, it would indicate a problem – we say we have a bust. In such a case, which is common, I have to figure out where I went wrong. I could have correlated the yellow horizon too high or too long on anyone of the four (4) lines. I need to consider where I have high confidence in my correlation and where I had a decision point. For example, perhaps on Line 201 I had a decision point where I choose to carry the yellow horizon on the high side of a “fork.” Perhaps if I choose the lower branch at the fork, I would not have a bust.

## Slide 35: Remember Our Goal
Build a Geologic Framework
    Structural Framework
    Stratigraphic Framework
Identify Prospect Elements
    Source, Migration, Reservoir, Trap, Seal
    Where are all elements favorable
Assess Highest-Potential Prospects
    How much oil/gas do we expect?
    How certain are we?
Economic Analysis
    Value of the HCs minus the total costs
Notes: Just as a reminder, correlating faults and horizons is part of building a geologic framework. It is a key and time-consuming step in our overall process.

## Slide 36
Questions?