## Slide 1
Prepare for a Lease Sale
Prepare for a Lease Sale
Your Task:
  Synthesize the five (5) play elements (at a minimum) for the blocks you want to bid on.
Block 11
Block 15
Block 14
Block 13
Block 12
Block 21
Block 25
Block 24
Block 23
Block 22
Block 31
Block 35
Block 34
Block 33
Block 32
Approximate location of structural highs

## Slide 2: Our Lease Sale
All fifteen (15) blocks will be up for bid at the beginning of the next lecture period.
Each team has the same amount of money, $50 million.
Each team can split their money to bid on blocks.
Your team has to bid on at least three (3) blocks.
The minimum bid for a block is $1 million.
Keep bids in whole numbers – no fraction of $1 million.
Notes: The ultimate goal for the last exercise and this one (Exercises 11 and 12) is a mock lease sale. The fifteen (15) blocks on the base map will be open for bids during the start of the next class period. Teams (or individuals) have $50 million for the sale.
Each team must bid on at least three (3) blocks, they can bid on more than three (3). The minimum bid per block is $1 million. The bids should be in $1 million increments, i.e., no decimals ($23.5 is not allowed). This should not be announced, but placing serious money on a couple of blocks and then bidding $1 million on all the others is a reasonable strategy.

## Slide 3
Objective
In this exercise, you will briefly consider the play elements other than structural traps, which you mapped in the last exercise (Exercise 11).
Final Product
Synthesis of the five (5) play elements (at least) for the blocks you want to bid on. You will place bids on three (3) or more blocks in the next class period.
Notes: The intent during the exercise is for each team to spend NO MORE than 40 minutes working the exercise. This is more than enough time to evaluate their leads, if they work efficiently.

## Slide 4: Introduction
Thus far you have identified some large structural traps.
Now you will consider the other play elements:
source seal
reservoir migration
Notes: They have already recognized several large anticlinal traps (Exercise 11). Each team will have different interpretations depending on how they interpret the sparse grid of seismic lines. Exercise 12 will have them look at source (type and maturity), reservoir, seal and migration.

## Slide 5: Introduction
Your team should not spend more than 40 minutes on this exercise. You may not have enough time to analyze everything in the included maps. Keep your objective in mind – which three (3) or more blocks to bid on and how to split your $50 million license acquisition budget.
You will use tracing paper to help determine which blocks with large structures have other favorable hydrocarbon (HC) system elements.
Notes: They will need a sheet of tracing paper that is 11x17 inches – or two 8.5x11 sheets.

## Slide 6: Figures
Figure 1 – migration drainage divides
Figure 2 – source rock facies (likely HC type)
Figure 3 – present-day source maturity
Figure 4 – depositional environments for the Upper Latrobe
Figure 5 – seal quality for the Lakes Entrance formation
Notes: This slide is simply a list of the five (5) maps they have to work with, which come on 11x17 inch sheets. These five (5) maps and the basemap from the previous exercise (Exercise 11) should be the same scale.

## Slide 7: Suggestion
Examine Figure 1, which has migration drainage divides and the approximate location of highs.
This map may help you refine your anticline ‘ovals’.
Sketch the anticlines your team is considering on the tracing paper.
Then use the tracing paper to evaluate the other play elements for the anticlines you are interested in.
Notes: A suggestion…. If a block has no interpreted high (trap), they do not have to include it in the evaluation – a time saver.

## Slide 8: Uppermost Latrobe Divides
Block 11
Block 15
Block 14
Block 13
Block 12
Block 21
Block 25
Block 24
Block 23
Block 22
Block 31
Block 35
Block 34
Block 33
Block 32
Approximate location of structural highs
0 km 20
Notes: This is Figure 1, shown as an example. The blue circles are “place holders,” they are not where structural highs are located. Students should ignore the blue circles – use the anticlines they developed in the previous exercise (Exercise 11). The red drainage divides are accurate – based on more than the fourteen (14) lines from the previous exercise (Exercise 11). In theory, the students should have an anticline inside each red polygon, but because of the sparse line coverage, they may not. The high in Block 35 is deeper than the seismic coverage on their lines – a hidden treasure.

## Slide 9: Uppermost Latrobe Divides
Block 11
Block 15
Block 14
Block 13
Block 12
Block 21
Block 25
Block 24
Block 23
Block 22
Block 31
Block 35
Block 34
Block 33
Block 32
Approximate location of structural highs
Oil Source
Oil Window
Nearshore Sand
Excellent Seal
Large Drain Area
0 km 20
Notes: A FICTICIOUS example of an assessment of an anticline in Block 3 (conclusions not supported by the data and maps). Given the five (5) bullets, Block 3 has everything going for it and should be considered for a high bid.

## Slide 10: Bidding Strategy
Your team will compete against the other N teams.
You all have the same data and money.
Your team will have to develop your bidding strategy:
  You can go after the best block with most of your money
  You can forego the best and try to get 2 or 3 mid-size structures
  You could try to pick up 4 smaller structures.
NOTE: If there is a tie for high bid on any block, it will be equally divided.
Notes: A bit about bid strategy. For a tie, if 3 teams bid $40 million on Block 32, each would get 1/3 of the oil and gas. NO teams can combine to pool their money. Do not mention the strategy of placing a minimum bid on each block. The highest possible bid = $48 million, with $1 million placed on two other blocks (for the 3 block minimum). Don’t mention this either.

## Slide 11
Questions?
Notes: Slide Ex-12.10