## Slide 1: Petroleum Geology & Geophysics
New Ventures & Gippsland
New
Ventures
Notes: This unit explains what a new venture is, which is the starting point for a field. We cover how companies work towards placing bids on license areas (blocks).
After the main lecture, regional information on the Gippsland basin is presented. This lesson and the following lesson build up towards a mock lease sale of fifteen (15) blocks in the Gippsland basin. It’s the view from 10,000 feet. The remainder of the course will explore basic steps in more detail.

## Slide 2: New Ventures
By New Ventures we mean a geographic area where the energy industry as a whole, or our company in particular, has not been active but has some current interest.
This might be a totally new basin or sub-basin.
It might be a newly accessible area.
It might be a new play in an old area.
It is an area where OUR company hopes to start finding large reserves that will maintain or expand our future production.
Definition
Notes: Definition of a new venture.

## Slide 3: Some Examples
Some new ventures that I (Fred) worked on:
  Initial blocks offered Madagascar (2007) – a new basin.
  First opportunity off mainland China (1980) – new access.
  Ultra deep abyssal plain in the of the Gulf of Mexico (2013) – new play downdip from a major HC province.
  Submarine fans north of the Makenzie delta (1978) - new play downdip from a major HC province.
1
2
3
4
Notes: Four (4) new ventures that I worked on, as examples. You might replace this with some current new ventures. A good source is the seismic advertisements in publications such as AAPG’s Explorer.

## Slide 4: Geoscience Work Process
The Geoscience Work Process can be divided into 4 main stages that are related to the business cycle of an asset
Deplete HC Fields
Stage 4
Initiate Production from Discoveries
Stage 3
Discover HC Reserves
Stage 2
Capture Areas of Highest Potential
Stage 1
Time
Early in the
Business Cycle
Late in the
Business Cycle
Notes: Here is the work process for a field from before discovery through depletion. I like to summarize this with four (4) words: Capture; Discover; Initiate; and Deplete.

## Slide 5: Changes with Business Stage
Time
Early in the
Business Cycle
Late in the
Business Cycle
Exploration
Development
Production
Regional
Compartment-Scale
Reservoir-Scale
Prospect-Scale
Block-Wide
Scales of Analysis
1. Capture
3. Initiate
4. Deplete
2. Discover
Abandon/Sell
Geoscience
Reservoir
Engineering
Information & Effort
Info
Effort
Notes: This shows the changes in emphasis through a field’s lifecycle. The business stage goes from Exploration to field Development to field Production. The scale of analysis continually zooms in from regional to the individual compartments of the field. The need for accuracy and precision also goes up with time (not shown). The bottom display shows the change from almost exclusive work by geoscientists, to a balance between geos and reservoir engineers, to more engineers. Towards the end of the lifecycle, geoscience info increases slowly and the role of geoscientists dwindles.

## Slide 6: Stage 1: Capture Opportunities
Of the 700+ sedimentary basins on the planet, which offer the highest potential for undiscovered HCs?
Which high potential areas can we hope to operate within in the near future?
Is the land holder (e.g., government) for these accessible areas likely to offering up some licenses?
What can we do to get ready to enter this area?
Key Questions
Notes: This slide covers some key questions companies ask and try to answer as they look to identify and capture new opportunities. If a company does not capture enough new opportunities, then its future (10+ years out) is at risk.

## Slide 7: Stage 1: Capture Opportunities
Regional Studies -> Focus Areas
Our company places bids on
Blocks 7 & 8
Lease Sale in a
Focus Area
Play Elements
e.g. Reservoir
Adequacy
Block
2
Block
1
Block
5
Block
6
Block
8
Block
7
Block
4
Block
3
Interesting Leads
Block
8
Block
7
Lead
A
Lead
B
Lead
C
Blocks Up for Bid
Block
1
Block
5
Block
4
Block
3
Block
2
Block
8
Block
7
Block
6
Profit
Analysis
Notes: A graphic to summarize Stage 1 – capturing opportunities.
A company does regional analyses to identify regions with high potential for discovering significant volumes of oil and gas.
Some acreage in a high potential region is opened for bidding on lease blocks.
In this example, eight (8) blocks are available for us to bid on (like Exercise 3).
A set of play element maps are built; sweat spots are identified were all elements are favorable.
Potential traps in the sweat spots are investigated.
We do a rough profit analysis (an example follows).
We decide to place bids on Blocks 7 and 8.

## Slide 8: Regional Studies
Cen. to Maastrictian
• Maast. to Present
Open marine
Albian to Cenomanian
Aptian
Late Jurassic to Aptian
G
U
L
F
M
A
R
I
N
E
C
A
R
B
O
N
A
T
E
M
A
R
I
N
E
A
N
O
X
I
C
R
I
F
T
Geologic Maps
Plate Tectonics
Gravity & Magnetics
Regional Seismic Lines
Tectonic Evolution
Stratigraphic Charts
Paleogeographic Maps
Etc.
Mitchum et al., 1977b
AAPG©1977 reprinted with permission of the AAPG whose permission is required for further use.
Images Courtesy of ExxonMobil
From Lecture 3
Notes: Repeat from Lecture 3. Some examples of regional data we would collect and analyze. We need to put together a geologic story for the area. Then we need to consider the HC likelihood based on that geologic story.

## Slide 9: Regional Studies
Regional studies are performed to:
  Provide the regional setting of a basin or sub-basin so that we can understand the characteristics of the region.
  Turn those characteristics into a set of play element and play adequacy maps.
  Decide which basins on sub-basins have high potential AND low risk for discovering & producing oil or gas.
  Determine how much to bid for blocks that are open to be leased.
From Lecture 3
Notes: Slight change from a slide in Lecture 3. Four reasons for performing a regional analysis.

## Slide 10: Licensing Round
The government of Somewhereia has announced a new lease sale of 8 blocks on April 1.
Energy companies are invited to submit bids to the government on October 1.
Information of terms are available upon request.
  Length of lease will be 15 years
  Monetary and additional commitments
  Government take - % of production, taxes
  Other terms
For Example
Notes: An example of a lease sale announcement. One thing to note is that typically there is about six (6) months between when the license round and its details are announced and when the bids are due. Mega-companies have teams that work regional studies full time – trying to stay ahead of the action. Smaller companies pull staff off their “normal assignments” to form a team to evaluate open blocks.

## Slide 11: Within the Licensing Area
Collect and work available data.
Build individual play elements maps.
Consider the combination of play elements maps.
Identify traps with reservoir, seal, nearby kitchen.
Look for geophysical support for HCs.
Exercise 3
Notes: There is a lot of work to be done over the sale area. Available data has to be collected, perhaps purchased. There is not enough time to gather new data. The team has to build play element maps (what students were provided in exercise 3). They look for sweat spots – where all the play elements are positive. They look for possible traps in the sweat spots.
They look for geophysical support for the presence of HCs – e.g., bright spots or fluid contacts.

## Slide 12: Identify Leads
Block
8
Block
7
Lead
A
Lead
B
Lead
C
A Lead is a geologic feature that looks very promising as it is considered as a possible future field.
It has a convergence of all the play elements.
It has an acceptable level of risk.
The next test is its chance to make the company money.
Definition
Notes: Definition of a lead.

## Slide 13: Economic Minimum
An Economic Minimum is the quantity (volume) of oil or gas that a lead would have to produce so that our company would get a 12% rate of return on our investors’ dollars.
Definition
Value of Produced Oil or Gas
Profit
Total Costs
=
-
e.g., We would have to find 75 mmbbls of oil to get enough profit to yield a 12% rate of return on the money.
Notes: Discussion of an economic minimum – the minimum volume of oil or gas so that we make a decent rate of return (typically 12%). Mmbbls = millions of barrels.

## Slide 14: Estimate Recovery
We estimate Lead B can hold 40 mmbbls of oil.
Recovery should be 20% (8 mmbls).
When 8 mmbls are brought to the surface, it would expand 10 times (80 mmbbls). This is an unrisked volume.
We think Lead B has a 25% chance for everything to work
The risked volume is 25% of the unrisked volume, in this case the risked volume is 20 mmbbls.
Block
8
Lead
B
Notes: We need the value of the oil or gas. To get this, we need the volume at the surface and a future price. So we need an estimate of how much HC, say oil, we think is in the trap, how much we can recover, and what the volume of oil would be at the surface. We’ll consider Lead B in Block 8. We estimate it could hold 40 mmbbls of oil. We guess that only 20% of that can be recovered (moved out of the reservoir rock). As the oil moved up from the pressure in the reservoir to surface pressure, it will expand. We’ll assume the expansion factor is 50 times. For this example, we come up with an estimate of 400 mmbbls. This is what we call an unrisked volume – it assumes all the play elements work as well as they can.
We also do a risk analysis for Lead B. We decide that there is only a 1 out of 4 chance that everything will work out (25% risk). We multiply the unrisked volume by the risk factor (0.25) to get the risked volume, in this case 100 mmbbls. Companies always work economics based on risked volumes.

## Slide 15: First-Pass Profit Analysis
The risked volume is 20 mmbbls.
We project $95/barrel for the future.
Value for Lead B is $1.9 billion
Costs for E/D/P is estimated to be $1 billion
This would result in $900 million profit
Block
8
Lead
B
Notes: Next we need a price for oil 10, 20, 30 years into the future. Our experts in price forecasting tell us that oil will be worth $95 per barrel in todays dollars for the life of the field (25 years). So the value of the oil is 100 mmbls * $95/bbl = $9.5 billion – WOW! We also need an estimate of the total costs to get the blocks, do our exploration, find a field(s), develop the fields and produce oil for 25 years. We work with engineers and others to come up with a likely total cost of $6 billion – another WOW!
Now can do our rough profit analysis. Profit = value minus costs = 9.5 billion – 6 billion = $3.5 billion over 25 years.
In other words, should we invest $6 billion, most of which is spent in about 10 years to get a likely pay out of $3.5 billion, with the pay out starting about 15 years in the future and going until about 40 years in the future? Sounds like a good deal to me, but how does this compare with our company’s other investment options? Its questions like this that senior management have to consider and act upon. That’s why they make BIG bucks.

## Slide 16: Bidding Strategy
We estimate a $900 million profit for Lead B over a 25 yr period.
How does this compare with our company’s other opportunities?
If we want to capture Block 8, how much should we bid?
  Have other companies appreciated it’s value?
  How much might other companies bid?
  We want to be high bidder without leaving to much money “on the table.”
Block
8
Lead
B
Ours
Notes: Let’s say we want to take this chance for a potential payout of $3.5 billion. How much should we bid on Block 8? Other companies will be bidding. Will they also be interested in Block 8? We want to bid enough to win Block 8. But we don’t want to overbid – called leaving money on the table.
For example. Let’s say we bid $1.75 million on the block. If someone bids $1.8 million, we lose.
Let’s say our bid of $1.75 million is the highest bid. The next highest bid was $1.2 million. This means we could have won the block for $1.25 million. We would say that we overbid by $1/2 million or we left $1/2 million on the table.

## Slide 17
Questions?

## Slide 18: Petroleum Geology & Geophysics
The Gippsland Basin
http://www.energyandresources.vic.gov.au/earth-resources/victorias-earth-resources/oil-gas/prospectivity-and-reserves
Notes: Left – continent of Australia with a white box around the Gippsland basin.
Right – map showing oil (green) and gas (red) fields in the Gippsland basin.

## Slide 19: Gippsland Basin – Regional Geology
Location
Plate Tectonic Setting
Basin Evolution
Stratigraphy
Australia’s most prolific HC province with over 4 Billion barrels of oil 4.4 Trillion cubic feet of gas
Notes: This is a quick review of the regional geology of the Gippsland basin, which is off the SE coast of Australia. We will briefly cover the four (4) points listed.
The map on the right shows Australia. The white rectangle to the SE is the location of the Gippsland Basin.
About 1/3 of the basin is onshore; 2/3 offshore. What we will be working in a number of subsequent exercises is data from the offshore portion of this basin.

## Slide 20: Gippsland Basin – Regional Geology
Location
Plate Tectonic Setting
Basin Evolution
Stratigraphy
Australia
East Antarctica
New
Zealand
Subduction
Zone
Volcanic
Arc
Spreading
Center
Courtesy of ExxonMobil
Notes: The next five (5) slides look at the setting of the basin in terms of its plate tectonic history. The magenta oval marks the location of the Gippsland Basin. The map is a reconstruction back to Early Cretaceous time. It is enlarged on the next slide with more information.

## Slide 21: E. Cretaceous, 145 to 98 MY
Subduction along east coast of Australia
Onset of rifting between Australia & Antarctica
Early syn-rift volcano- clastic sediments were deposited (the Strzelecki Group)
Rifting starts in the Gippsland Basin
WNW-ESE fault trend established
Australia
East Antarctica
New
Zealand
Subduction
Zone
Volcanic
Arc
Spreading
Center
Gippsland Basin
Strzelecki Group Deposition
Courtesy of ExxonMobil
Notes: A representation of Early K time. There was a subduction zone and associated volcanism way to the east (around New Zealand). Rifting started between Australia, Antarctica and what is called Zeelandia (New Zealand, Tasmania, Lord Howe Rise). Note there is a triple junction a little west of Gippsland. Australia and Tasmania started to separate, so Gippsland was a pull-apart basin in its youth. You might think of portions of the East Africa Rift as a modern analog for this geologic time. We will look at the stratigraphy in a couple of minutes, but this is the time that the Strzlecki Group was deposited.

## Slide 22: Late Cretaceous, 98 to 78 MY
Rifting commences in the Tasman Sea
Middle syn-rift sediments deposited (the Golden Beach Group)
Existing WSW-ENE faults are utilized
First marine incursion
Australia
East Antarctica
New
Zealand
Golden Beach Group Deposition
Courtesy of ExxonMobil
Notes: Late K time. Extension and rifting continued; the basin got deeper. Syn-rift sediments continued to infill the basin (Golden Beach Group). The basin deepened faster than sediments were able to infill it, so ocean waters got into the eastern part of the basin.

## Slide 23: L. Cret. – E. Oligocene, 78 to 30 MY
Late rift phase clastic sediments (the Latrobe Group)
Declining clastic sediment input
As rifting ceases in Gippsland (~30 MY ), the region collapses rapidly, faults are active and a major transgression occurs
Australia
East Antarctica
New
Zealand
Latrobe Group Deposition
Courtesy of ExxonMobil
Notes: Late K to Early Oligocene interval. Late stage syn-rift sediments – the Latrobe Group. Accommodation space continued to outpace sediment input, so there was a major transgression (shoreline moving landward). The part of the triple junction that formed Gippsland failed (died) – an aulacogen. Tasmania and Australia stopped moving apart. Rifting and seafloor spreading continued further to the south and to the east (green regions with red mid ocean ridges and transforms). The heating associated with rifting ceases in Gippsland and the basin sinks rapidly. The shoreline shifted far updip leaving our study area in deep water. This rapid flooding event caused coupled with basin collapse resulted in a major unconformity at the top of the Latrobe formation (TOL = Top Of Latrobe).

## Slide 24: L. Oligocene to Recent, 30 to 18 MY
Circum-Antarctic current starts
Deep marine shales
Episodic compression results in structural inversion
Far field stresses are accommodated by weak crust under Gippsland Basin
Australia
East Antarctica
New
Zealand
Lord
Howe
Rise
Lakes Entrance Fm Deposition
Courtesy of ExxonMobil
Notes: In Late Oligocene to Early Miocene the Lake Entrance Formation was deposited. It is a deep marine shale which overlies fluvial to nearshore Latrobe sediments (sand-rich). In the Middle to Late Miocene, the area had some carbonate deposition. The Plio-Pleisteocene had clastic deposition. During the Miocene there was some compression as the “platelets” jostled due to far field stresses. Some normal faults were reactivated with reverse motion.

## Slide 25: Gippsland Basin – Regional Geology
Location
Plate Tectonic Setting
Basin Evolution
Stratigraphy
Notes: We’ll look at the basin history using a different point of view.

## Slide 26: Basin Formation
Mantle
Continental
Crust
35 km
Pre-Rifting
Jurassic
Mantle
Continental Crust
35 km
Early Rifting
E. Cretaceous
35 km
Mantle
Continental Crust
End of Rifting
L. Cretaceous
35 km
Continental Crust
Continental Crust
Mantle
Drift/Sag
L. Cenozoic
Notes: Here we will consider the crust and mantle beneath the Gippsland Basin. This shows an old-school style of rift basin evolution; some newer theories would represent the crustal structure a bit differently.
We start in the Jurassic before the onset of rifting. The continental crust (CC) was on the order of 35 km thick. In the Cretaceous through Early Oligocene, the CC was thinned due to extension (pull-apart) between Australia and Tasmania. As the CC “necks,” a basin is formed and sediments are deposited. Rotated normal fault blocks develop. These form today’s traps.
Around the middle of the Oligocene, this arm of the triple junction ceased to be active. Convection in the mantle stopped, and so did crustal heating. This led to a rapid collapse of the basin, which results in a major unconformity surface (TOL – Top Of Latrobe) and a major flooding (transgression).
The top diagram shows what would have happened if some oceanic crust was emplaced along the central rift zone. There is debate as to whether or not a small amount of oceanic crust exists in this basin.

## Slide 27: Gippsland Basin – Regional Geology
Location
Plate Tectonic Setting
Basin Evolution
Stratigraphy
Notes: Now let’s talk a bit more about the stratigraphy.

## Slide 28: Stratigraphy
Strzelecki
Group
Golden Beach Fm
Gurnard Fm
Latrobe
Group
Seaspray
Group
Lakes Entrance Fm
Late Rift
Sag
Mid Rift
Early Rift
Collapse
Compression
http://pubs.usgs.gov/of/1999/ofr-99-0050/OF99-50Q/fig2.html#TOP
Notes: This is a stratigraphic chart for the Gippsland basin. This was put together by the USGS. http://pubs.usgs.gov/of/1999/ofr-99-0050/OF99-50Q/fig2.html#TOP
We’ll start at the bottom of the chart and work our way up in geologic time on the next 6 slides.

## Slide 29: Stratigraphy – E. Cretaceous
Strzelecki Group:
145 to 98 MY
Early rifting phase of deposition
Non-marine clastics with coals
Volcanics
Secondary Source Interval
Continental Crust
Strzelecki Group
-2
0
-4
-6
100
-2
0
-4
-6
0
-8
Kilometers
40
30
20
90
80
60
70
50
Kilometers
Notes: During the early stages of rifting in the Early K, the Strzelecki Group was deposited. It is non-marine, fluvial clastics with some coal seams. These coals are a secondary source rock in the Gippsland Basin. There are also some volcanic rocks associated with rift volcanoes.

## Slide 30: Stratigraphy – L. Cretaceous
Golden Beach SubGroup:
98 to 78 MY
Mid rifting syn-rift deposits
Fluvial/lacustrine to marine clastics
Some coals
Primary Source Interval
Continental Crust
Strzelecki Group
Golden Beach
-2
0
-4
-6
100
-2
0
-4
-6
0
-8
Kilometers
40
30
20
90
80
60
70
50
Kilometers
Notes: More syn-rift sediments were deposited in the Late K – the Golden Beach Sub-Group. Depositional environments included rivers (fluvial), lakes (lacustrine), swamps and sea or ocean shorelines and offshore. More coals were deposited. These coals are the primary source rocks in this basin.

## Slide 31: Stratigraphy – Early Cenozoic
Upper Latrobe Group:
75 to 30 MY
Late rift phase of deposition
Wave dominated shorelines
Transgression – back-stepping shorelines
Primary Reservoir Interval
Continental Crust
Latrobe Group
-2
0
-4
-6
100
-2
0
-4
-6
0
-8
Kilometers
40
30
20
90
80
60
70
50
Kilometers
Notes: The Latest K to Early Oligocene consists of late-stage rift deposits. Sediments transitioned from fluvial updip (west) to delta plain/delta front wave-dominated shorelines, to slopes and ocean basin downdip (east). The primary reservoirs are sandstones deposited where waves and storms clean up the sands (winnow out silts and clays).
During this time, basin subsidence was faster than the sediment supply could keep pace with. Thus with time the shorelines moved landward (to the west). Back-stepping shorelines means it was in what we call a transgressive phase.

## Slide 32: Stratigraphy – L. Oligocene
Lakes Entrance Fm:
30 to 18 MY
Post basin collapse
Subsidence > sediment supply
Marine shales
World class top Seal
Kilometers
-2
0
-4
-6
-2
0
-4
-6
40
30
10
20
0
90
80
60
70
50
100
Continental Crust
Lakes Entrance Fm
-8
Kilometers
Notes: Around mid-Oligocene is when rifting and crustal heating ceased and the basin foundered (deepened rapidly). There was also a lot of motion on the normal faults, which enhanced the elevation changes on individual fault blocks. All this resulted in the major TOL unconformity.
The shoreline was shifted way updip as the basin foundered leaving our area of interest in deep water. Sands and silts were trapped way updip; our area had deepwater shales deposited, which covered the fault blocks. These shales, called the Lakes Entrance Formation, give us a world-class seal.

## Slide 33: Stratigraphy – Miocene
Gippsland Limestone:
24 to 5 MY
Slower subsidence, regression
Marine carbonate deposition
Continental Crust
Gippsland Limestone
40
30
10
20
0
90
80
60
70
50
100
-8
Kilometers
-2
0
-4
-6
Kilometers
-2
0
-4
-6
Notes: Completing our story, during the Miocene the Gippsland Limestone was deposited.

## Slide 34: Stratigraphy – Plio-Pleistocene
Tambo River Fm:
5 to 0 MY
Clastic deposition
Major channels erosion & infill
Causes time-to-depth complications
Tambo River
-2
0
-4
-6
-8
-2
0
-4
-6
Kilometers
40
30
10
20
0
90
80
60
70
50
100
Notes: And in the Pliocene – Pleistocene, more clastics were deposited – the Tambo River Formation.

## Slide 35: Summary: HC System
Source Rock
  Coals and coastal plain coaly shales in the Golden Beach subgroup. Dominantly terrestrial plant origin with high total organic carbon.
Reservoir
The Latrobe Group fluvial to nearshore sandstones are the primary reservoirs.
Seal
Mostly marine shales and marls of the Lakes Entrance Fm. Some shales within the Latrobe Group act as intra-Latrobe seals
Trap
Extensional fault blocks associated with Cretaceous rifting. Later compression enhanced anticlines and fault traps.
Maturation and Migration
The major generation and expulsion was initiated in the Miocene. Peak generation at depths of 4-5 km for oil and 5-6 km for gas.
Notes: This slide forms a summary of the play elements (aka hydrocarbon system elements) for the Gippsland Basin.

## Slide 36: Summary: HC System
Strzelecki
Golden Beach
Upper Latrobe
Lakes Entrance Fm
Gippsland Lms
Tambo River
SOURCE
RESERVOIR
SEAL
TRAPS Form
Overburden
HC Gen/Mig
http://pubs.usgs.gov/of/1999/ofr-99-0050/OF99-50Q/fig6.html
http://pubs.usgs.gov/of/1999/ofr-99-0050/OF99-50Q/fig2.html#TOP
Notes: This is a common way we show play element (HC system) information in a management review. The strat column on the left shows geologic time and the main rock units. On the right, we have the same geologic time scale with some columns. The source column highlights the time source rocks were deposited. The same for reservoir and seal. Overburden is the rocks that buried our intervals of interest to present-day depths. The traps column show when the main fraps formed. The HC generation/migration column indicates when the source intervals were “cooked enough” to yield oil/gas molecules. This helps understand timing issues, such as “were the traps in place when HCs were percolating through the basin?”
http://pubs.usgs.gov/of/1999/ofr-99-0050/OF99-50Q/fig6.html

## Slide 37: References
Slide 18: http://www.energyandresources.vic.gov.au/earth-resources/victorias-earth-resources/oil-gas/prospectivity-and-reserves
Slide 28-34, 36: http://pubs.usgs.gov/of/1999/ofr-99-0050/OF99-50Q/fig2.html#TOP
Slide 36: http://pubs.usgs.gov/of/1999/ofr-99-0050/OF99-50Q/fig6.html

## Slide 38
Questions?
Notes: Slide 12.38