## Slide 1
Prospect Mapping
Prospect Mapping
Your Task:
  Generate a time structure map for the Top of Latrobe on a 2D seismic grid.
Notes: Title slide with main task.

## Slide 2: Exercise
Objective
In this exercise, you will:
Use a grid of 2D seismic lines to map the TOL
Generate a time-structure map
Start considering where to locate a wildcat well (objective of the next exercise).
Final Product
A time-structure map for the TOL surface, our reservoir unit.

## Slide 3: Introduction
Again you will map the TOL unconformity. This time, however, you will be working a much smaller area at a much higher level of detail. Interpretation is provided on five (5) of the eleven (11) lines. You should mark fault offsets (use the pencil), but do not worry about details just yet. You will work one fault in detail later.
Mark the TOL surface with a color pencil in a “white” half cycle or loop. You can use any color (although the interpreted lines have the TOL horizon marked in red). You should be able to erase your interpretation, if necessary, if you draw your initial TOL horizon faintly.
Notes: Students will map the Top of Latrobe (TOL) unconformity. Five (5) of eleven (11) lines have the TOL interpreted.
Students will use the classic paper interpretation method: Fold the seismic line where 2 lines intersect, and Transfer the horizon from an interpreted line to an uninterpreted line.

## Slide 4: Introduction
Once you have mapped the TOL horizon, you will post two-way time values down to this surface on basemap #2. Then you will contour the two-way time values to get a time-structure map for the TOL surface.
From our quick regional mapping in Blocks 31 and 32, what do you expect?
You don’t buy all the lines BUT want a quality map?
NOTE: Our company did not purchase all the lines in the 2D survey.
Notes: Part 1 of the exercise is mapping the TOL on all the uninterpreted lines. Part 2 is to read TWT values and post them on basemap #2 (map #1 is to keep tract of which lines have been interpreted). Part 3 is to contour the TWT values to get a time structure map for the TOL surface. To not have too many lines, I only give them 5 SW-NE lines and 6 NW-SE lines.

## Slide 5: Basemap #1
Line 10
Line 60
Line 63
Line 22
Line 18
Line 14
Line 26
Line 66
Line 69
Line 72
Line 75
0 km 5
N
Basemap #1 – to mark interpretation progress
Notes: This is the basemap showing the SW-NE lines (lower numbers < 30), and the 6 NW-SE lines (with higher numbers > 60).
Basemap 1 is to mark which lines have interpretation. The solid lines have the TOL already marked. As a student interprets over lines, he/she can use a color pencil to show the lines that they have interpreted.

## Slide 6: Basemap #2
Basemap #2 – for your time-structure map
0 km 5
N
Line 10
Line 60
Line 63
Line 22
Line 18
Line 14
Line 26
Line 66
Line 69
Line 72
Line 75
11
12
13
15
16
17
19
20
21
23
24
25
27
28
74
73
71
70
67
65
64
62
61
68
11
12
13
15
16
17
19
20
21
23
24
25
27
28
11
12
13
15
16
17
19
20
21
23
24
25
27
28
11
12
13
15
16
17
19
20
21
23
24
25
27
28
11
12
13
15
16
17
19
20
21
23
24
25
27
28
11
12
13
15
16
17
19
20
21
23
24
25
27
28
74
73
71
70
67
65
64
62
61
68
74
73
71
70
67
65
64
62
61
68
74
73
71
70
67
65
64
62
61
68
74
73
71
70
67
65
64
62
61
68
Notes: This is basemap 2, which is for the TWT values and TWT contours. Tiny circles show the line numbers. The position of all the intersecting lines are marked by vertical lines on the seismic sections. Students should get a TWT value at every tiny circle on this map.
It works best if two (2) students team up for this exercise. Both can finish the TOL interpretation (Part 1). For Part 2 – one student can read TWT values off each seismic line and the other student writes the values on basemap #2. Both can work on the contours of TWT (Part 3).

## Slide 7: Three Tasks
Complete the TOL interpretation
Read and post (write on map) TWT values
Contour the two-way time values
0 km 5
Line
60
Line
72
Line
69
Line
66
Line
63
Line
75
Line 10
Read two-way time values at these points
Notes: This is Line 10. The red horizon is the TOL unconformity. The students should read and write values of TWT at every solid and dashed vertical line (yellow circles).
They can fold any one of the seismic lines near the left or right edge so that just the TWT scale is visible. This is the “ruler” to measure TWT values.

## Slide 8
Questions?