## Slide 1
Assess Barra
Assess the Barracouta Prospect
Your Task:
  You will briefly assess the largest prospect of the blocks our company recently acquired.

## Slide 2: Where We Stand
Our company acquired several blocks in the recent lease sale (blocks 31, 32, 41).
We purchased a grid of regional 2D seismic lines.
Your team mapped the TOL unconformity, which is believed to be the top of a reservoir interval that is capped by a good marine shale.
There is a large anticlinal structure that we have named Barra (short for Barracouta).
Now you need to:
  Size the trap,
  Estimate the in place oil (assuming an oil only case) and
  Get a risked Estimated Ultimate Recovery (EUR).
Notes: Four (4) bullets review where we are in exploring our offshore Australia blocks. The last bullet is our next step.

## Slide 3: Assumptions 1 and 2
We will have to make a series of assumptions to perform our assessment. We will base these assumptions on local data and analogous conditions and fields.
ASSUMPTION 1 The thickness of the HC column at Barra is 75 m.
ASSUMPTION 2 The interval velocity of the reservoir is 2500 m/s.
Notes: To keep things manageable, we will make a series of assumptions. #1 – the HC column (fill height) at Barra is 75 m. This could come from mapping a leak or spill point or from what we have found in similar situations (world-wide analogues).
#2 INTERVAL VELOCITY = 2500 m/s – from the seismic processing.

## Slide 4: Assumption 3
ASSUMPTION 3
The shallowest time value at the crest of the Barra structure is 840 ms. If the HC column is X ms, then you have a base for the 75 m thick reservoir.
Here is a picture of what
we have in mind.
Notes: Assumption #3 – the shallowest TWT for the crest of the anticline ~840 ms, from my mapping. They should find that 75 m with 2500 m/s = 60 ms TWT.
Thus, the fill is down to the 900 ms contour. (Yes, the time thickness is shown, but that is OK.)

## Slide 5: Volume – Spherical Cap
We can simplify a volume calculation by using an equation for the volume of a spherical cap:
Volume = 1/6 π h (3a2 + h2) [1]
where h = the height (75 m)
and a = the radius at the base of the cap.
Notes: One could say this is assumption #4 – that we can approximate the trap’s volume using this equation. Our numbers have so much uncertainty that we’re only after a first order estimate, so this simplification is OK. With computer software, a more accurate volume can be obtained given the mapped top and a fill level (here 900 ms).

## Slide 6: Get an Average Radius
0 km 5
N
Line 10
Line 60
Line 63
Line 22
Line 18
Line 14
Line 26
Line 66
Line 69
Line 72
Line 75
11
12
13
15
16
17
19
20
21
23
24
25
27
28
74
73
71
70
67
65
64
62
61
68
11
12
13
15
16
17
19
20
21
23
24
25
27
28
11
12
13
15
16
17
19
20
21
23
24
25
27
28
11
12
13
15
16
17
19
20
21
23
24
25
27
28
11
12
13
15
16
17
19
20
21
23
24
25
27
28
11
12
13
15
16
17
19
20
21
23
24
25
27
28
74
73
71
70
67
65
64
62
61
68
74
73
71
70
67
65
64
62
61
68
74
73
71
70
67
65
64
62
61
68
74
73
71
70
67
65
64
62
61
68
900 ms
DiameterLong = _____ km
DiameterShort = _____ km
DiameterAverage = _____ km
RadiusAverage = _____ km
Notes: The students are to use their TWT structure map from the previous exercise (Exercise 13 – Prospect Mapping) to get the “a” term in the volume equation. They can measure the diameter in the long and short directions. Then they get an average diameter, then an average radius. NOTE: The 900 ms contour shown here is NOT based on the data. Has the correct orientation, but is too large. Just for illustration of the procedure.

## Slide 7: Volumes
Total Trap Volume = ____________ km3 (equ. [1])
Reservoir Volume = ____________ km3 (* Net:Gross)
Pore Volume = ____________ km3 (* Porosity)
In-place HC Volume = ____________ km3 (* HC Sat.)
Convert to MBO = ____________ MBO (* 6333)
Unrisked EUR = ____________ MBO (* Rec. * Expansion)
STEP
Notes: Steps 4 through 9 go through the process to get an unrisked EUR. The numbers for steps 5 – 9 are in the write up. The process is the same as what they did in Exercise 10a.
Step 4 uses the volume equation with h = 0.075 km and the average radius they compute.
Step 5 assumes 40% net-to-gross.
Step 6 assumes a porosity of 16%
Step 7 assumes 80% HC saturation (20% residual water).
Step 8 converts from cubic km to millions of barrels of oil (MBO).
Step 9 assumes a 20% recovery efficiency and an oil expansion factor of 10.

## Slide 8: Risking
A risking team was formed and they developed a consensus on the risk values for the nine (9) elements:
Reservoir Presence 0.9
• Reservoir Quality 0.8
• Trap Quality 1
• Seal Adequacy 0.8
• Source Quality 1
• Source Maturation 0.85
• HC Migration 1
• Not Low Gas Saturation 0.8
• Not Biodegraded 1
Notes: I give them this list of risk elements. It is not practical for the students to assign these types of values.

## Slide 9: Chance of Success
Multiply the values for the nine (9) risk elements together to get the COS.
COS = _____________
Notes: When the multiply the nine numbers on the previous slide, they get the chance of success (COS).

## Slide 10: Risked EUR
Multiply your unrisked volume (Step 9) by the chance of success (Step 10). The product is the risked EUR.
Risked EUR = _____________
Notes: They multiply their unrisked volume (Step 9) by the chance of success (Step 10). The product is the risked EUR.

## Slide 11
Questions?