## Slide 1: Petroleum Geology & Geophysics
Prospect Risking
Should
we drill
Alpha?
Should
we drill
Beta?
Alpha
Beta
Notes: This unit explains how we risk a prospect. A manager wants to know what we think is the most likely volume of HC we expect AND the chance that this prospect will actually have that amount of HC. The bigger the possible “prize,” the more risk the manager would be willing to take on.

## Slide 2: Objectives & Relevance
Relevance:
  Demonstrate some of the tasks that go into determining the size of the ‘prize’ and the risk associated with a prospect
Objective:
  Introduce the types of considerations necessary to decide if a prospect is ready to review to management as ready to drill.
Notes: We will introduce some of the considerations. This will give you a feel for the types of questions a manager would ask and how we get our “educated guesses” for answers. NOTE: I’ll speak of some analyses without much in details. We will cover many of the analyses that we do later in this course.

## Slide 3: Overview of Prospect Analysis
Given the geologic framework and the results of our data analysis, our next task is to analyze and assess viable prospects
Analyze prospect elements
    Source, Migration, Reservoir, Trap, Seal
    Consider the most-likely scenario
    Consider other cases - the range of possibilities
Assess the prospect
    What volumes of HCs can we expect?
    Will it be oil or gas?
Risk the Prospect
    What is our level of confidence that all the prospect elements work?
Notes: This slide outlines three (3) main steps. We will quickly walk through these in this lecture.

## Slide 4: Outline
Define prospect elements
Estimating trap volume
HC type
Assess recoverable HC
Assign risk
Prospect
Definition
Prospect
Assessment
}
Geologic
Framework
Data
Analysis
Prospect
Definition
Prospect
Assessment
Notes: The three (3) main steps are expanded a bit here into five (5) components.
By making the series of maps you used in Exercise 12, you will define the prospect elements. We look at source, reservoir, trap, seal and migration. Doing this requires that we have the geologic framework already worked out.
Then we work on the four (4) components related to prospect assessment.
2. We need to estimate the trap volume and the HC it might hold.
3. We need to consider what type of HC is most likely – oil, gas, or both.
4. Assessment is our prediction on how much HC we think we will be able to recover (and sell).
5. Risk is an estimation of the chance that we give this prospect for success.

## Slide 5: Outline
Define prospect elements
Estimate trap volume
HC Type
Assess recoverable HC
Assign risk
A “Kitchen”
Where Organic
Material Is
Cooked
A “Container”
From Which
Oil & Gas
Can Be
Produced
“Plumbing” To Connect
the Container to the Kitchen
Correctly
Placed
Wells
Source
Migration
Reservoir
Trap
Seal
Notes: We have already covered the ‘Big 5’ play elements. No need to go over these 5 again.

## Slide 6: A Simple Example
Alpha
Beta
The Alpha and Beta Prospects
Notes: I’ll illustrate prospect analysis for two (2) neighboring prospects, Alpha and Beta. This is a structure map showing two faulted anticlines.

## Slide 7: Most-Likely Scenario
Alpha
Beta
Reservoir
Seal
Source
Basement
Overburden
18 Ma
Oil
Generation
Oil
Migration
Oil
Fill & Spill
Sea Water
Notes: Based on our analyses - we come up with several scenarios of possible HC generation, migration, entrapment and leak/spill.
Usually we consider at least three (3) cases:
  what we think is most-likely to have occurred,
  a pessimistic case (it could be as small as ...), and
  an optimistic case (it could be as big as ...)
Let’s walk through the most-likely case for Alpha and Beta.
Here is what we think was happening at 18 million years ago. The prospects were small anticlines, but without the fault offsets at this time. Downdip of Alpha, the source interval has just entered the oil window. Oil then migrated into Alpha. Some excess oil may have spilled out of Alpha and migrated updip to the Beta anticline. The structural configuration is now as we saw in the previous slide.

## Slide 8: Most-Likely Scenario
Alpha
Beta
Reservoir
Seal
Source
Basement
Overburden
10 Ma
Oil
Generation
Oil
Migration
Oil
Migration
Sea Water
Notes: Here is what we think was happening 10 million years ago. The structural configuration was as we saw before, except the anticlines have fault offsets.
Oil was being generated both in the deepest portions of the source rock interval to the west of Alpha and in the low just to the east of Alpha. Oil migrated in the sands to the faulted trap at Alpha. Similarly, oil migrated in the sands to the faulted trap at Beta. We assume the faults are sealing. Beta now receives oil just from the central “kitchen.”

## Slide 9: Most-Likely Scenario
Reservoir
Seal
Source
Basement
Overburden
Present
Alpha
Beta
Oil
Generation
Gas
Generation
Oil & Gas
Migration
Oil
Migration
Sea Water
Notes: Here is what we think is happening at present. The structural configuration is as we saw before. Gas is being generated in the deepest portions of the source rock interval to the west of Alpha. Oil is being generated at intermediate depths west of Alpha and in the low just to the east of Alpha. Gas and oil are migrating to the faulted trap at Alpha. Only oil is migrating to the faulted trap at Beta.

## Slide 10: Most-Likely Scenario
Map of the Reservoir Unit
Alpha
Beta
Oil
Oil
18 Ma
Notes: Here is a map of what we think the fluid distribution in the two traps was like at 18 million years ago. We predict a moderate amount of oil trapped at Alpha and a small amount of spilled oil trapped at Beta.

## Slide 11: Most-Likely Scenario
Map of the Reservoir Unit
Beta
Alpha
Oil
Oil
10 Ma
Notes: This is a map of what we think the fluid distribution in the two traps was like at 10 million years ago. The importance of the fault is clear. If the fault can not hold (seal) the HCs, then we would have a major problem. But if the faults do seal and form a trap, then we predict a significant amount of oil trapped at Alpha and a moderate amount of oil trapped at Beta.

## Slide 12: Most-Likely Scenario
Alpha
Beta
Oil
Oil
Gas
Map of the Reservoir Unit
Present
Notes: This is a map of what we think the fluid distribution in the two (2) traps is like today. Again, we are counting on the faults to act as seals to hold the HCs in the traps. If the faults do seal and form traps, then we predict a gas cap with an oil leg at Alpha - it looks large enough to be economic! We’ll have to run some numbers to be sure. Also, we predict a significant amount of oil trapped at Beta.

## Slide 13: Exploration’s Task
Notes: We saw this before - a simple flow chart of the work done in exploration. We’ve gone down the workflow through Interpret Seismic Data. We’ve built a geologic framework based on regional and local data. The next step is to assess the prospects - to estimate its value to the company.

## Slide 14: Outline
Define prospect elements
Estimate trap volumes
HC Type
Assess recoverable HC
Assign risk
How Much Could Be
In Alpha & Beta?
Notes: Our next task is to estimates volumes – of the trap first and then of the recoverable HC. How much oil and/or gas might we get out of each prospect?

## Slide 15: Volume of Half a Cone
Volume of a Cone = 1/3 Π r2 * h
Consider the trap to be
approximately ½ a cone
Alpha
Beta
r
h
r
r
Notes: You worked a similar exercise previously. You used volumes of cones to get an approximate trap volume. The faults at Alpha and Beta make the traps similar to ½ a cone. We estimate for each prospect an average radius for the top and base reservoir surface and appropriate heights. We estimate the volume and divide it by two (2) to get the volume of a half-cone.

## Slide 16: For Our Volumes
We’ll say the traps at Alpha and Beta are something like this
We’ll use ½ a cone to get the volume from the top and base of the reservoir
Base 1
Height 1
Base 2
Height 2
Notes: This illustrates how we first get the volume from the top of the reservoir to where we position the base of the HC. Then we get the volume from the base of the reservoir to the base of the HC. We subtract the two to get an estimate of the reservoir rock volume.

## Slide 17: Similar to Exercise 10b
You know how to do some quick estimates using a series of simplifying assumptions
We will focus on Risk
Notes: As you did in Exercise 10b, we start with the total reservoir volume and work down to HC volume in each trap. We convert from km3 to million barrels of oil (MBO). We apply a recovery efficiency and an expansion factor. This gives us a rough estimate of how much oil (or gas) we hope to produce – the Estimated Ultimate Recovery (EUR).
We have not risked the prospects yet – estimated the chance that everything works favorably. Risking is the fifth step.

## Slide 18: Outline
Define prospect elements
Estimate trap volumes
HC Type
Assess recoverable HC
Assign risk
Notes: Since oil and gas have different values, managers want us to consider:
- what if the prospect holds oil?
- what if the prospect holds gas?
We talk about the HC type – oil, gas, or a combination of the two.
(Sometimes we speak about condensates. This is the case where the HC is in a gaseous phase in the reservoir (high temp and pressure), but liquid at the surface. Condensates are less valuable than oil, but more valuable than gas.)

## Slide 19: Oil or Gas???
This early in our study it is difficult to predict fluid type in a particular region/area.
We can use our basin modeling & HC systems analysis to predict the most likely fluid type.
Typically we would consider an oil case and a gas case.
Notes: We are very early in the life of a possible field. The nearest well or outcrop might be 100+ kilometers away. So it is hard to know if we have a source and if it is the type that generates mostly oil or gas. We also may not have a lot of data to calibrate the HC maturation model. So it is difficult to predict if the prospect is likely to be oil or gas, if it in facts has HCs.
The value of the prospect is quite different for oil versus gas.
What we would do is make two predictions:
- If it holds oil, it is likely to have X barrels of recoverable oil.
- If it holds gas, it is likely to hold Y BCF (billion cubic feet) of recoverable gas.
We would then say something like, given HC in the trap, we give it a 60% chance for oil.

## Slide 20: Questions???
How can we verify this scenario?
To what level are the traps filled with oil & gas?
What would be the value ($) if our scenario is correct?
How much more/less HC could there be?
How risky is this prospect (chance that we are totally wrong)?
Our Most-Likely Scenario
Many times the seismic data
will give us clues!
Notes: Here is our most-likely scenario for Alpha and Beta. We can get rough estimates for the EUR of oil and gas for Alpha and of oil for Beta. These volumes depend on the level of fill in each trap. We may have evidence from our seismic mapping of a spill or leak point. Then we can use the interpreted spill or leak point to constrain the volumes.
Once we have the recoverable HC volumes, we can use a price forecast to get a value in dollars. Managers always want a range of possibilities:
– how much bigger could it be?
– how much smaller could it me?
And what is the risk or chance of success? (1 – chance of success = risk) e.g., we think Alpha has a 30% chance of success (or 70% risk).

## Slide 21: Seismic Line Across ‘Alpha’
Fluid Contact?
Oil over Water?
Fluid Contact?
Gas over Oil?
Alpha
Notes: We may get an indication on seismic lines for the fill level of a trap. We call these (seismically defined) fluid contacts. For example, here is a seismic line across the Alpha prospect. There is good evidence for one fluid contact; there is less convincing evidence for a second (shallower) fluid contact. A fluid contact is a boundary between sand with one type of fluid above a different type of fluid below.
The lower contact (green) might be the boundary between oil above and water below. The seismic evidence is fairly good. The upper contact (red) might be the boundary between gas above and oil below. The seismic evidence for this contact is not as certain.

## Slide 22: Outline
Define prospect elements
Estimate trap volumes
HC Type
Assess recoverable HC
Assign risk
Deterministic
Assessment
Probabilistic
Assessment
Notes: The next step is assessment, using numbers related to a prospect to give management numbers they need to make decisions. For where we are in our look at Gippsland, that decision is on which blocks, if any, to bid on and how much to bid. There are two types a assessment: Deterministic and Probabilistic.

## Slide 23: Types of Assessments
Deterministic Assessment
  One value for each parameter
  One final number, e.g., 200 MBO
Probabilistic Assessment
  A range of values for each parameter
  A range of outcomes, e.g. 200 ± 50 MBO
There are two types of assessment we can perform on a lead:
Notes: For a deterministic assessment, we use a single number for each input parameter (e.g., porosity). The result is a single number (e.g., 200 MBO). For a probabilistic assessment, we use ranges for each input parameter.
We get a range of likely outcomes.

## Slide 24: Scenarios & Probabilities
Gas Cap & Oil Leg
Alpha
40% Chance of Occurrence
Scenario 3
Scenario 1
Scenario 2
Scenario 4
Alpha
Alpha
Alpha
Gas Only
Oil Only
Low Gas Saturation
30% Chance of Occurrence
10% Chance of Occurrence
20% Chance of Occurrence
Notes: We might run an assessment for more than one scenario (cases or model for the prospect). Here we have defined four (4) scenarios for Alpha – four (4) possible cases for fluids in the reservoir. What we think is most-likely is the case where there are two (2) fluid contacts with gas on oil on water. Based on the data and our interpretation & analysis, we assign this case a 40% chance of occurrence. Another possibility is that only the lower fluid contact is real. The reservoir could be filled with gas (20% chance) or with oil (30% chance). A fourth possibility is that the reservoir contains just a small quantity of gas - perhaps 5% gas dissolved in 95% water. We refer to this type of condition as low gas saturation. This would be too little gas to be worth trying to produce. This fourth scenario is assigned a 10% chance of occurrence.

## Slide 25: Deterministic Prospect Assessment
To assess a prospect, we assign numbers to the parameters related to HC volumes
Unrisked means that this is the volume if all the play elements work as well as we can expect!
Using what we think are the best estimates for the necessary input parameters, we get these numbers for the all oil case (scenario 3)
EUR = Estimated Ultimate Recovery
Notes: We have a block with two (2) prospects, Alpha and Beta. What do our managers want to know now? How much oil could there be and how sure are we – is the risk high or low?
First, we assess how much HC there could be – if we think of the trap as a ‘container,’ how much fluid (oil, gas, or water) can it hold?
This slide gives an example for the oil ONLY scenario. The steps are similar to what you did in Exercise 10b.
- get the gross rock volume in Alpha and Beta
- get the reservoir volume
- get the pore volume
- get the in-place volume (reservoir depth, temperature, pressure)
- convert the volume into units of million barrels
- get the EUR, based on a recovery efficiency and a correction for surface temp and pressure.
Going through these steps, I came up with 320 MBO for Alpha and 146 MBO for Beta. WOW! Note that this is called an unrisked EUR – it assumes all the play elements have worked beautifully. Next we have to assign a number to the risk (or chance of success).

## Slide 26: Alpha Prospect Assessment Results
0 MOEB
0 BCF
0 MBO
Scenario 4
Low Gas Saturation
192 MOEB
0 BCF
192 MBO
Scenario 3
Oil Only
52 MOEB
314 BCF
0 MBO
Scenario 2
Gas Only
121 MOEB
95 BCF
112 MBO
Scenario 1
Oil & Gas
Oil
Gas
Oil-Equivalent
Assuming 100 MOEB is needed to make prospect economic
Uneconomic
Million Barrels Oil
Billion Cubic Ft Gas
Million Oil Equivalent Barrels
6 BCF = 1 MBO
Uneconomic
Notes: Here is a table for the deterministic assessments for Alpha and Beta based on the four (4) scenarios we defined earlier. It shows estimated oil and gas for each scenario. Gas is in units BCFs, billion cubic feet. To determine value, we use a formula in which six (6) BCF of gas has the value of 1 MBO (million barrels of oil). The last column is the value of oil AND gas in millions of oil-equivalent barrels (MOEBs).
You can see that scenarios 1 & 3 have a lot more MOEBs than scenarios 2 & 4. Given the location of the prospect and what it would cost to build production facilities, we believe that we need 100 MOEBs to make the Alpha Prospect economical. Thus, scenarios 1 & 3 would be worth going after; scenarios 2 and 4 would economic failures. Of course there is still the possibility that there are NO hydrocarbons at all!

## Slide 27: Probabilistic Assessment
The Goal is to Get A Number and a Range of Possible Outcomes
We Input a Range of Values for Each Assessment Parameter
  usually minimum, most-likely, maximum
Area
20
12
27
ML
Min
Max
HC Sat.
Thickness
Net:Gross
Porosity
FVF
Recovery
Notes: On the previous slide, we gave each assessment parameter, like area, a single value. We don’t know exact values, but we can usually define a range for each parameter.
One way to do this is to define a minimum, a maximum, and a most-likely value.
We use statistical methods and the computer to derive a most-likely hydrocarbon volume and a range of values:
- from the optimistic view (it could be as big as … )
- to the pessimistic view (it could be as small as … )

## Slide 28: Unrisked Results
Million Barrels of Oil
Alpha Prospect – Unrisked
0%
20%
40%
60%
80%
100%
0
100
200
300
400
100
Economic Minimum
50% Chance of finding 200 MBO or more
75% Chance of finding the economic minimum
Exceedance Probability
Notes: This is what we call an exceedance probability – the red line. This is unrisked – there is 100% chance to find a barrel of oil or more. The economic minimum of 100 MBO is shown. You read this and find that there is a 75% chance to find 100 MBO or more. There is a 50% chance to find 200 MBO or more, and a 10% chance to find 290 MBO or more.

## Slide 29: Outline
Define prospect elements
Estimate trap volumes
HC Type
Assess recoverable HC
Assign risk
How Confident Are We?
75% Chance of Success
25% Risk
Notes: We are now ready to perform the final step – risking. How confident are we that all the HC system components have worked together and we will find HCs?
Some people like to talk about chance of success – my prospect has a 75% chance (3 out of 4 to succeed).
Other people prefer to speak in terms of risk - my prospect has a risk of 25% chance (1 out of 4 to fail).

## Slide 30: 9 Key Elements of the HC System
Biodegra-
dation
Not Low Gas
Saturation
HC
Migration
Source
Maturation
Source
Quality
Trap
Quality
Seal
Adequacy
Reservoir
Quality
Reservoir
Presence
A team of experts consider these key elements for each prospect.
They rate the chance of success (COS) for each on a scale of 0 to 1
Notes: Here are nine (9) elements that we would assign chance of success (or risk) to. Different companies might have different elements with different names, but we can use this.
A team of experts would consider source quality, source maturity, etc. They would assign a number between 0 and 1 for each element. For example, we know there is a great oil source in our region so source quality is 1.0, but it may be immature in the prospect’s drainage area so source maturity = 0.7.
Biodegradation is when the reservoir is less than 70° C and bacteria has chomped on oil molecules.

## Slide 31: COS for Alpha
Alpha’s biggest risk is that the fault does not seal.
There is also a chance that the trap is only filled with low saturation gas
Reservoir Presence
Reservoir Quality
Trap Quality
Seal Adequacy
Source Quality
Source Maturation
HC Migration
Not Low Gas Saturation
Biodegradation
- - - - 1.0
- - - - 1.0
- - - - 1.0
- - - - 0.8
- - - - 1.0
- - - - 1.0
- - - - 1.0
- 0.9
- - - - 1.0
}
0.72
chance of success
(COS)
Some Risk
Highest Risk
Notes: For Alpha, the team working the prospect are joined by company experts to assign COS values to the nine (9) elements. Here the most risky element is the trap - do the faults act as a seal? Another risk is that, instead of an oil or gas field, we have only low gas saturation.
The experts decide that the Alpha prospect has a 72% chance of being a success. NOTE: We have to be a bit optimistic. If we assigned all nine (9) elements 0.9, the COS would be 39%. Optimistic, but reasonable.

## Slide 32: Risked Probabilistic Assessment
0.0
0.2
0.4
0.6
0.8
1.0
0
100
200
300
400
500
Million Oil Equivalent Barrels
Alpha Prospect – Main Compartment - Risked
Gas Cap & Oil Leg
Gas Only
72% COS
58% Chance of
finding more
than the
Economic
Minimum
72% Chance to find any hydrocarbons
58% Chance to find 100 MOEB
5% Chance to find 400 MOEB
100
Oil Only
5% Chance of
finding more
than 400 MOEB
Economic Minimum
Notes: What we would show our management is a chart like this. It is a plot of oil-equivalent barrels (volume of HCs) on the x-axis and probability of finding at least that volume on the y-axis. This chart for Alpha indicates that there is a 72% chance of finding at least a small amount of HCs.
There is a 58% chance of finding enough to exceed the economic minimum. For the optimist, there is about a 5% chance of finding 400 MOEB!
We would do the same for Beta and any other prospects within a lease block. Given the quality of these prospects and its chance to make a profit compared to the other opportunities our company has, the managers will decide whether or not to bid on the block with Alpha and Beta.

## Slide 33
Questions?