## Slide 1
Well-Seismic Tie
Well-Seismic Tie
Your Task:
  Tie four (4) horizon tops picked on well logs to the wiggles on a 2D seismic line

## Slide 2: Detailed Synthetic Trace
FOUR ‘TOPS’
Top of Austin Chalk
Top of Eagleford Shale
Top of Woodbine Sand
Top of Buda Limestone
Notes: This is the output from an older software package that generates a synthetic seismic trace – labeled here “composite”. The four (4) formation tops to tie (relate) to specific peaks, troughs or zero crossings are indicated and marked by horizontal lines. Students use this display to decide where each top should be marked on the synthetic seismic trace.

## Slide 3: Exercise
In this exercise, you will look at a blocked sonic log from a well. Four (4) formation tops are provided. You will go through the process of relating these formation tops to a synthetic (modeled) seismic trace.
Notes: Once they have decided where each top should be marked on the synthetic, they are ready to transfer the tops to the real seismic line. This is a 2D seismic line that passes close to the well. Note that the well location has been projected to 3000 ft.

## Slide 4: Well to Seismic Tie
Regional Scale
Notes: The students have the synthetic trace (shown here in red) at the same two-way time (TWT) scale as this line in Figure 4. They should cut the synthetic trace in Figure 4 and place it on Figure 2. They should align 2.0 seconds on the seismic and on the synthetic AS A STARTING POINT, and then move the synthetic trace up or down a little to get a reasonable match. Don’t tell them, but I shifted the synthetic trace up 32 ms to get a good match.

## Slide 5: Well to Seismic Tie
Detailed Scale
Notes: The students have the synthetic trace (shown here in red) at the same TWT scale as this line in Figure 3. They should cut the synthetic trace in Figure 5 and place it on Figure 3. They should align 2.0 seconds on the seismic and on the synthetic AS A STARTING POINT, and then move the synthetic trace up or down a little to get a reasonable match.
They should not finalize the tie at the regional c-scale (Figure 2) until they work the tie at this detailed scale (Figure 3).

## Slide 6: Exercise
Questions?