## Slide 1: Wildcat Well Location
0 km 5
N
Line 10
Line 60
Line 63
Line 22
Line 18
Line 14
Line 26
Line 66
Line 69
Line 72
Line 75
11
12
13
15
16
17
19
20
21
23
24
25
27
28
74
73
71
70
67
65
64
62
61
68
11
12
13
15
16
17
19
20
21
23
24
25
27
28
11
12
13
15
16
17
19
20
21
23
24
25
27
28
11
12
13
15
16
17
19
20
21
23
24
25
27
28
11
12
13
15
16
17
19
20
21
23
24
25
27
28
11
12
13
15
16
17
19
20
21
23
24
25
27
28
74
73
71
70
67
65
64
62
61
68
74
73
71
70
67
65
64
62
61
68
74
73
71
70
67
65
64
62
61
68
74
73
71
70
67
65
64
62
61
68
Notes: Use this IN EDIT MODE so each team can move one of the ten (10) color circles on the right to the location of their first (wildcat) well.

## Slide 2: Wildcat Well Location
See The Solution File
For Exercise 14
Notes: After each team has shown their well location, go through the solution slides for Exercise 14.

## Slide 3: Petroleum Geology & Geophysics
Well-Seismic Ties
Notes: This unit explains what we mean by a well-seismic tie and what purposes it serves. The next slide has a lecture outline.

## Slide 4: Outline
What is a well - seismic tie?
Comparison of well and seismic data
Generating a modeled trace
Well-seismic tie workflow
Tying the modeled trace to real seismic data
What is a good well-seismic tie?
Notes: We will cover these topics.

## Slide 5: What Is A Well-Seismic Tie?
Whenever we have well data and seismic data, we need to relate the two, e.g., how does the top of a sand in the well relate to the seismic?
Two Big Issues
Scale: depth (m or ft) versus time (ms).
Seismic pulse limits resolution.
Well A
Well A
Sand A
Sand A
5,678 m
1124 ms
Notes: SLIDE 15.5
Whenever we have well data and seismic data, we need to relate the two.
For example, in this study area, how does the top of the A sand in the well relate to the wiggles on the seismic line through the well?
There are two big issues:
The well data are in units of depth while the seismic is in units of two-way time
The seismic is a lot lower resolution due to the seismic pulse – we can’t “see” as fine a scale of stratigraphy as we can with log data.

## Slide 6: Goal
We want to be able to relate features from well data (tops, faults, cored intervals) to the ‘peaks and troughs’ on the seismic line that pass through the well location.
Similarly, we may want to relate some features on the seismic to the well data.
To do this, we have to develop a depth-to-time relation.
We also want to model how the individual wavelets caused by the various impedance boundaries around our zone of interest (i.e. reflection coefficients) combine to give us the resultant seismic trace.
Notes: Here are the goals of making a well-seismic tie.

## Slide 7: Well vs. Seismic Data
Seismic Data
Sample areas and volumes
Low frequency (5 - 100 Hz)
Vertical resolution 15 - 100 m
Horiz. resolution 150 - 1000 m
Measures seismic amplitude, phase, continuity, horizontal & vertical velocities
Time measurement
100 ms
Well Data
Sample points along well bore
High freq. (10,000 - 20,000 Hz)
Vertical resolution 2 cm - 2 m
Horiz. resolution 0.5 cm - 6 m
Measures vertical velocity, density, resistivity, and other, rock and fluid properties
Depth measurement
100 m
Notes: This slides compares well data characteristics to seismic data characteristics. The main points are:
1) Samples points vs. samples areas (2D seismic) or volumes (3D seismic)
3) Vertical resolution of ~1 meter vs. ~30 meters
6) Measurements in depth (ft or meters) vs. two-way time (milliseconds).

## Slide 8: Units of Measure
Logs are in Depth Units
They are referenced to the Kelly Bushing (KB)
Seismic is in Time Units
They are referenced to a surface elevation (SL)
Vertical depth
Measured
Depth
Kelly
Bushing
Elevation
Two-way time
Surface Elevation
SHOT
REC’R
Notes: Wells are in units of ft or m along the borehole with zero set at the kb (Kelly Bushing). For pure vertical wells, log depths are vertical depths. For deviated wells, we have to correct measured depths to true vertical depth.
Seismic data are processed to a “seismic reference datum”. All marine surveys are datumed to sea level. Coastal surveys are usually datumed to sea level. Inland surveys are datumed to an elevation higher than the highest topographic point in the survey area (e.g., a survey near Denver might be datumed to 5500 ft).

## Slide 9: Check Shot Data
Seismic Shot
Borehole Geophone
Time
Depth
It certainly would be great to relate well data to seismic times (like Sand A on slide 3).
Seismic velocity data allow us to convert ft or meters to time or time to ft or meters.
We also have to compensate for differences in datums.
We can do this with check shots.
Check shots measure the vertical one-way time from the surface to depths where we position a geophone within the well to:
  Determine the start time for the top of well-log curves.
  Calibrate the relationship between well depths and times calculated from a sonic log.
Notes: It certainly would be great to relate well data to seismic times (like Sand A on Slide 3). Seismic velocity data allow us to convert ft or meters to time or time to ft or meters. We also have to compensate for differences in datums.
One way we can do this is with check shot data (old term is a velocity survey). We lower geophones down the wellbore to certain depths. Then we generate seismic energy at the surface. We measure the time it takes for the seismic energy to go from the surface to the depth of the geophone (one-way time). This gives us a relationship between a depth and a one-way travel time. In a check shot survey, we get measurements at eight (8) or more depths from the bottom of the well to near the surface.
With check shot data, we can:
- Determine the start time for the top of well-log curves.
- Calibrate the relationship between well depths and times calculated from a sonic log.

## Slide 10: Generating a Modeled Trace
The sonic (1/v) and density logs give us impedance at the well location
Density
Velocity
We relate the top of Sand A to the seismic trace
Map Top of
Sand A
at this
trough
Sand A
Well A
We calculate the reflection coefficients: ( I2 - I1) / (I2 + I1)
R. C.
Wavelet
We convolve the reflection coefficients with a seismic pulse
Zero Phase
Pulse
Model
Imped.
We ‘block’ the logs to obtain the major acoustic ‘breaks’
Notes: This slide summaries how we make a modeled (or synthetic) trace from well log data. The two logs we use are:
- the sonic long, which measures transit time, which is the inverse of velocity (microseconds per feet), and
- the density log
We know that impedance is the velocity times the density, so we can calculate an impedance “log”. We “block” the log, filtering out the very high frequency changes and keeping moderate to large changes in impedance. Blocking can be done either by hand or by the computer. In the figure, the original log data (unblocked) is in blue; the blocked log is shown in red.
Wherever there is a jump (increase or decrease) in impedance, we can calculate a reflection coefficient (R.C.). We assume or estimate the wavelet of our seismic data. Then we perform the mathematical operation called convolution to get a modeled seismic trace. Your students may have done this in Exercise 6c.

## Slide 11: Seismic-Well Tie Workflow
Time-Depth
VSP = Vertical Seismic Profile
Check shots
Seismic Stacking Velocities
Data Input
Well Data
  Sonic log
  Density log
  Deviation survey
Seismic Data
  Line through well
  Full or near stack
Log QC/Editing
Data Problems
  Washout
  Casing Shoe
  Cycle Skip
  Fluid Invasion
  Stuck Tool
Log Blocking
Manual
  Capture major RCs
Machine
  Min. bed thickness
  Percent change
Optional Step
Wavelet
Analytical
  Shape
  Central freq. (e.g. Ricker 28 Hz)
Extracted
  From a seismic window
Modeled Trace
Convolve RC series with the wavelet
Multiples
AVO (Amplitude Versus Offset) effects
Notes: This summarizes the workflow. Our input is well data and seismic data. We often have to do some editing of the well data to fix problems like measurements in washout zones. We may choose to block the logs to capture the significant changes in impedance (I always block the logs). We need some velocity data to transform log depths to TWT values:
- A vertical seismic profile (VSP) is a very heavily sampled check shot survey
- We’ve mentioned what check shots are
- In the absence of a VSP or check shots, we use the stacking velocities used by the seismic data processors.
We need a wavelet:
- we can use a standard wavelet shape and a frequency
- we can use a statistical approach to extract a pulse in a user-defined seismic window at the well location.
Finally, the computer does the convolution for us. All the software does the simple, zero offset trace generation. Some software packages allows the user to also model multiples and/or amplitude variations as a function of offset angle.

## Slide 12: The Analytical Wavelet
What is the Phase of the Wavelet?
  Minimum Phase
  Zero Phase
What is the Polarity of the Wavelet?
  What is the Response of a +RC?
What is the wavelet shape?
  E.g., Ricker
What is the Central Frequency?
  E.g., 25 Hz
Impedance
R.C.
Response
Notes: Let’s talk a little about the analytical wavelet. We have to input that we want to use either a minimum phase or a zero phase wavelet. We have to define the polarity: what does a positive RC look like? We select a standard pulse shape - my favorite is the Ricker shape. Lastly, we have to provide a central frequency.
The pulse parameters are refined by trial and error. We set the parameters, generate the synthetic trace, and compare it to the actual seismic trace at the well location. For example, there is a modeled trace on the next slide. I started with a 25 Hz Ricker wavelet. The two (2) zero crossings defining the main trough in my zone of interest were too close together – the trough was to short in time. I changed the frequency to 20 Hz - the trough was too long. I found through trial and error that 22 Hz gave me the best match for several zero crossings in my zone of interest.

## Slide 13: Output
Modeled Trace
Density
Seismic
Real &
Modeled
Refl. Coeff.
Formation
Markers
Scales
Sonic
Calib.
Gamma
Impedance
Wavelet
0.840
0.879
1035
10
6
5
4
3
2
1
9
8
7
Notes: This is an example from a synthetic generation software package (Schlumberger’s IESX). It is for the discovery well at Barracouta. The first track (column) has two scales – two-way time on the left and meters on the right. The Top of Latrobe (TOL) unconformity is at about 0.88 seconds or 1035 m. The second track shows the caliper log (hole size) in blue and the Gamma Ray log (sand:shale ratio) in purple. The third track shows the sonic log in blue such that it indicates lower to higher velocities. The fourth track shows a density log in green. The fifth track shows the calculated impedance curve (velocity * density) in red. The sixth track labels the formation markers picked by the well geologist.
You should recognize the top of the Lakes Entrance Formation (our seal unit) and the Top of Latrobe (TOL) unconformity. Track 7 has the reflection coefficients from the blocked impedance curve. Track 8 shows the pulse as a positive RC would generate. This is an SEG reverse zero phase pulse (Lecture 6). I used a Ricker shaped analytical pulse with a central frequency of 22 Hz. Track 9 shows the modeled trace obtained by simple convolution of the RCs and the pulse. It is repeated 3 times. Track 10 shows eleven (11) tracks from the real seismic line (black) with the modeled trace (red) at the well location. The match between real seismic traces (black) and the modeled trace (red) is OK for our current needs.

## Slide 14: Tying Modeled to Real Seismic
The object of our next exercise is to tie the discovery well to the 2D seismic lines
But one more slide
Notes: We can also post the synthetic trace on a display of the seismic line. In this case, the black peaks on the synthetic trace correspond to red peaks on the seismic line. The students will perform a well-seismic tie in Exercise 15. Before starting the exercise, one more slide.

## Slide 15: What is a “Good” Tie?
Seismic attribute analysis
Inversion
Exploitation
Comparing a lead to nearby wells
Exploration
Mapping and tying a regional flooding surface across a basin
Poor/fair
Within a few cycles
Regional Mapping
Example Application
Seismic Quality Required
Accuracy Required
Business Stage
It depends on your needs!
Wavelet character match
Within ~½ cycle
Good
Very good
Notes: What is a “good” tie between real and a modeled seismic trace? This depends on where you are in the life cycle of a field. If you are in the identify and capture stage (new venture) and doing regional mapping, you want a marker in a well (e.g., TOL) to be accurate only within a few cycles (peaks-troughs). Remember Exercise 11 – mapping the TOL on the regional (color) lines? Later in the exploration phase (where we are currently with Barracouta), we want a marker horizon to be within about ½ a cycle. In the exploitation stage, which is field development and production, you want the marker horizon to be in the correct peak or trough and you want that modeled peak or trough to have the same shape characteristics as the real seismic peak or trough.

## Slide 16
Questions?