## Slide 1: Exercise: Well-Seismic Tie
Well-Seismic Tie
Your Task:
  Tie four (4) horizon tops picked on well logs to the wiggles on a 2D seismic line.
Top of Buda
-/+ zero crossing
Notes: A review of exercise 15.

## Slide 2: Exercise
2.8
2.6
2.4
Top of Buda
-/+ zero crossing
Top of Woodbine
-/+ zero crossing
Top of Eagleford
+/- zero crossing
Top of Austin
-/+ zero crossing
Notes: 2
The synthetic (modeled) seismic trace with which I would mark/map the four (4) formation tops.

## Slide 3: Exercise
2.8
2.6
1.0
0.8
0.6
1.2
1.4
1.6
1.8
2.0
2.2
2.4
About a 32 ms shift up
Notes: The synthetic as I tie it – 32 ms shift up. Move quickly to the next slide which zooms in.

## Slide 4: Exercise
Buda
Eagleford
Woodbine
Austin
About a 32 ms shift up
Notes: A zoomed in portion of the seismic with the synthetic trace (red). Using the part of the waveform shown on Slide 2 (particular zero crossings), I have started to map the formation tops.

## Slide 5: Exercise
Buda
Eagleford
Woodbine
Austin
Notes: A relook at the full 2D line with my mapped horizons. I darkened the seismic (changed the gain) so the color-coded horizons stand out more.

## Slide 6: Let’s Look at Barra-1
0 km 5
N
Line 10
Line 60
Line 63
Line 22
Line 18
Line 14
Line 66
Line 69
Line 72
Line 75
11
12
13
15
16
17
19
20
21
23
24
25
27
28
11
12
13
15
16
17
19
20
21
23
24
25
27
28
11
12
13
15
16
17
19
20
21
23
24
25
27
28
11
12
13
15
16
17
19
20
21
23
24
25
27
28
11
12
13
15
16
17
19
20
21
23
24
25
27
28
11
12
13
15
16
17
19
20
21
23
24
25
27
28
74
73
71
70
67
65
64
62
61
68
74
73
71
70
67
65
64
62
61
68
74
73
71
70
67
65
64
62
61
68
74
73
71
70
67
65
64
62
61
68
74
73
71
70
67
65
64
62
61
68
Barracouta-1
Where They
Drilled the
Wildcat
Notes: Let’s look at the well-seismic tie for the Discovery well at Barracouta. This shows where the first well was drilled – it was on a 2D seismic line available at that time. The magenta line shows where the line we will compare to is located. This is seismic from 2000 – not the time of discovery.

## Slide 7: Barracouta-1
TOL
Notes: We reviewed this display at the end of Lecture 15, what each track shows. The depth of the TOL is marked by the dashed red line. There is only a small negative RC at the unconformity.If this was the only RC, it would result in a very small amplitude peak (flip on the wavelet shown in the last track on the right). Due to interference effects of several small RCs, the TOL coincides with a -/+ zero crossing in this vicinity. The next slide zooms in on the TOL.

## Slide 8: Impedance at the TOL
TOL
Notes: The same display as on the previous slide, but several tracks were clipped and the vertical scale was expanded. Note the small negative RC at the TOL (red dashed line). I would map the TOL at the negative-to-positive zero crossing (green line on the real seismic data).

## Slide 9: Impedance at the TOL
TOL
Top of Coarse Clastics
Peak
Top of Latrobe
-/+ zero crossing
Kingfish
Fm
Gunard
Fm
Lakes
Entrance
Fm
Latrobe
Group
Seaspray
Group
0
20
40
meters
Notes: Zooming in even more, we can use the Gamma Ray (GR) log to learn more. The TOL separates the Latrobe Group below from the Seaspray Group above. We want our TOL seismic horizon to map this unconformity. As discussed on the previous slide, in the vicinity of the well it would be on the -/+ zero crossing.
Look at the GR log. The top of the sand (coarse clastics) is 20 meters below the TOL. At the top of the Latrobe group, we have nearshore sands (Kingfish FM) that is capped by 20 m of offshore shale (Gunard Fm). These are details we could never know without the well data. These details are important for mapping this discovery.
At the next level of detail mapping, we would carry two (2) seismic horizons:
- the TOL at the -/+ zero crossing, and
- the TCC (top of course clastics) at the peak.

## Slide 10: Tie to Seismic Line A
Bar1
North
South
~0.75 s
Notes: This is how I would position the synthetic trace on the actual seismic line. Notice the 0.75 second mark on the synthetic is shifted down just a few milliseconds relative to the seismic line.

## Slide 11: Tie to Seismic Line A
Bar1
~0.75 s
TOL
Notes: Now I know which -/+ zero crossing to map for the TOL.

## Slide 12: Tie to Seismic Line A
Line
60
Line
72
Line
69
Line
66
Line
63
Line
75
Line A
North
South
Notes: The seismic data on the previous slide was from inside the red box. Now I can map the TOL on the entire line.

## Slide 13: Change in Amplitude North to South
North
South
Line
60
Line
72
Line
69
Line
66
Line
63
Line
75
Line A
Notes: There is a change in the amplitude characteristics around the TOL from north to south. There is a relative strong peak that the TOL sits on to the north and west. The amplitude is much lower towards the south and east. Why is this?
At the well, the Gunard Fm is only 20 m thick. The seismic at the TOL level gives a good response to the change from deep water shales to offshore shales to nearshore sands. To the south and east, the Gunard Fm thickens such that the seismic at the TOL level senses only deep water shales on offshore shales. The sands are not as clean and deeper. Hence, the impedance contrast decrases and the seismic amplitudes weaken.

## Slide 14: Exercise
Questions?