## Slide 1: Petroleum Geology & Geophysics
Seismic Acquisition
Notes: This unit gives a brief overview of seismic data acquisition. For those specializing in seismic acquisition, there are week long courses on details we can’t even mention in this course. Surveys are expensive and critical - a lot of science goes into survey design and acquisition.

## Slide 2: Introduction
A seismic image combines both seismic data acquisition and seismic data processing. Each works together to produce the best final image.
The acquisition process includes:
  Generating a signal with an energy source
  Detecting and recording the reflections using receivers
The ultimate goal is to create a 2D line or 3D volume of seismic data that adequately samples the geology being mapped. We want to optimize the data through:
  Signal enhancement
  Noise reduction

## Slide 3: Introduction
Keeping this goal and cost considerations in mind, we have to specify acquisition parameters such as:
  Source and receiver spacing,
  Survey surface area,
  Record length, and
  Noise mitigation methodologies.
Notes: There is always a battle between quality subsurface imaging and cost. This battle is fought when the survey is designed and acquisition parameters are set. This slide lists four (4) key survey parameters. We will talk about these as the lecture progresses.

## Slide 4: Time Sampling
Sample #
Amplitude
1
0.00
2
0.25
3
0.17
4
-0.10
5
-0.34
6
-0.24
7
-0.35
8
-0.60
9
-0.53
10
-0.09
11
0.29
12
0.36
13
0.17
14
-0.09
15
-0.33
16
-0.36
17
-0.09
Sampled Seismic Trace
  The seismic signal is sampled at a discrete time interval, called the sample interval or sample rate.
  The sample rate varies by data set, most commonly it is 4 ms, but can be 2 ms or even 1 ms depending on the business needs and instruments in use.
  In the 1960s, industry changed from recording the continuous, analog signal to recording digital data sampled at a fixed time interval.
  This revolutionized the ability to process seismic data for signal enhancement.
Notes: All seismic data is now recorded digitally. That means values are recorded at a set time interval. The most common sample rate is 4 ms (0.004 s). Some data are recorded at 2 ms or 1 ms.

## Slide 5: Producing the Signal
A surface energy source generates an impulse that propagates as a wave radiating outward in all directions.
Notes: We have to produce energy that propagates down through the earth and reflects off acoustic boundaries (at step changes in impedance). This slide is for a land source. The red arcs represent wavefronts of the acoustic energy radiating out at three (3) successive time steps. The black arrows show a few raypaths.

## Slide 6: Capturing Reflections
Surface receivers detect both reflected energy (our signal) and unwanted noise.
These arrivals are recorded on digital media.
After each shot is recorded, the field equipment is changed to a new location and the experiment is repeated.
Notes: The energy has to be detected and recorded digitally. By receivers, we mean “listening devices” that sense and record energy arriving on them. A survey is completed by sending out energy and recording energy using hundreds of source points and thousands of receiver locations. The equipment is moved around the survey area to get the desired subsurface coverage. We say that the equipment “rolls” from one shot location (with a set of active receivers) to the next shot location.

## Slide 7: Attenuating Noise
By using arrays of sources and receivers, we can reduce unwanted, horizontally-propagating noise in the near surface while reinforcing the vertically traveling seismic energy (down from the source array and up from the subsurface reflections).
Receiver Arrays
Source Arrays
Horizontally Propagating
Noise
Receiver Array
Source Array
Vertically Propagating
Signal
Horizontally Propagating
Noise
Notes: We really are interested in only energy that is reflected off subsurface interfaces. So we want to maximize down-going energy and up-coming reflected energy AND minimize horizontally-propagating energy. We can get closer to the ideal situation by using arrays:
- source arrays where we use several energy sources “firing” in unison.
- receiver arrays (or groups) where the output from several “listening devices” are combined to form a single output.
A lot of science has been developed to cancel horizontally-propagating energy while reinforcing the vertically traveling seismic energy.

## Slide 8: Enhancing the Signal
Sorting the traces from multiple shot records to a common midpoint (CMP) gather, allows reflections generated from the same subsurface point to be summed (stacked).
The benefit of stacking is that it allows the desired reflections (signal) to constructively reinforce while reducing what we do not want (random noise, source-generated noise, unwanted multiples and surface waves.
Receivers
Sources
Midpoint
Common Mid-Point Gather
Notes: There is a lot that we can do to increase our desired “signal” (reflected energy) and cancel “noise” (everything else) in processing. We’ll cover some of this in the next lesson on seismic data processing (at a very elementary level).
This slide highlights a very important method for increasing the signal-to-noise ratio for our data. Here we want information at the red dot on a subsurface interface. I show raypaths for three source-receivers pairs that “sample” the geology at the red dot. The “geologic signal” is almost the same for each raypath. If we sum the response from these three raypaths, we reinforce the “geologic signal”. At the same time, much of the “noise” cancels out because much of the noise is random. More on this in next lesson (Lecture 17).

## Slide 9: Marine Acquisition
Notes: A photo of a seismic acquisition ship.

## Slide 10: Marine Source
Air gun
  Air guns are the industry standard for marine energy sources.
  Compressed air is stored in a chamber sealed by a piston.
  When air guns are fired, the piston is forced to move past vents that let the compressed air out into the water.
  The rapidly venting air expands as a bubble.
  When water pressure collapses the bubble, it generates a pressure wave.
Two Air guns (250 cu. in.) arranged in an array
Notes: For marine surveys, all data are acquired using air gun arrays as the energy source. Air guns use compressed air in a cylinder with a piston. Air pressure builds up while a vent is closed. The gun is “fired” by opening the value at a set time interval. The released air forms a bubble in the seawater. Water pressure causes the bubble to implode. This implosion causes a pressure wave (think of a balloon popping and making a loud pop). The photo shows part of an air gun array – note the two cylinders with wires coming out at the bottom of the heavy chains.

## Slide 11: Air Gun Arrays
Just Fired
Bubbles from Previous Shot
Source Array A
Source Array B
Notes: In this photo, Array B has just fired – the air bubbles are just breaking the surface. Array A fired about 10 seconds before the photo was taken - note the remnants of bubbles at the left edge of the photo.

## Slide 12: Receivers - Marine
Hydrophone
  Marine pressure waves are detected by a hydrophone.
  The outer casing houses pressure sensors and provides a stable connection for the electrical contacts.
  The casing is full of holes to allow its contents to sense minute pressure changes in the water.
  Inside the casing is a small pressure sensitive crystal that produces an electrical output when squeezed.
  Hydrophones are housed in streamers, silicon filled flexible tubes that are neutrally buoyant.
Notes: For marine surveys, our listening devices are hydrophones. They measure pressure changes that are extremely small magnitude, as the instruments are highly sensitive. Several hydrophones are coupled to form a receiver group or array. They are encased in flexible tubes called streamers. Streamers, that are towed behind the ship, are very long - on the order of 2 to 8 kilometers.

## Slide 13: Marine Acquisition
Source
Receivers
Notes: Slides 13 to 23 is a “poor man’s movie” to show how the point with the red dot near the center is recorded as the ship sails left to right. This is scene 1. Raypaths are shown from the source array (3 purple squares) down to the top of the brown layer and reflected up to 5 receiver groups (orange circles). There are NO raypaths that “sample” the position of the red dot. As the ship sails to the right, the interface at the red dot will be sampled. NOTE: the red triangle within the brown layer is meant to represent a gas reservoir.

## Slide 14: Marine Acquisition
Source
Receivers
Notes: This is scene 2. Again, there are NO raypaths that “sample” the position of the red dot.

## Slide 15: Marine Acquisition
Source
Receivers
0
∑ Fold
Notes: This is scene 3. Again, there are NO raypaths that “sample” the position of the red dot. The counter at the bottom will keep track of how many source-receiver pairs has a “bounce point at the red dot. The number of raypaths is also called the fold, hence the summation will update.

## Slide 16: Marine Acquisition
Source
Receivers
1
∑ Fold
Notes: This is scene 4. The first “bounce point” is from the source to the first receiver group. The fold = 1.

## Slide 17: Marine Acquisition
Source
Receivers
2
∑ Fold
Notes: This is scene 5. The second “bounce point” is from the source to the second receiver group. The fold = 2.

## Slide 18: Marine Acquisition
Source
Receivers
3
∑ Fold
Notes: This is scene 6. The third “bounce point” is from the source to the third receiver group. The fold = 3.

## Slide 19: Marine Acquisition
Source
Receivers
4
∑ Fold
Notes: This is scene 7. The fourth “bounce point” is from the source to the fourth receiver group. The fold = 4.

## Slide 20: Marine Acquisition
Source
Receivers
5
∑ Fold
Notes: This is scene 8. The fifth “bounce point” is from the source to the fifth receiver group. The fold = 5.

## Slide 21: Marine Acquisition
Source
Receivers
5
∑ Fold
Notes: This is scene 9. There is no “bounce point” since the streamer is not long enough. The fold stays at 5.

## Slide 22: Marine Acquisition
Source
Receivers
5
∑ Fold
Notes: This is scene 10. There is no “bounce point” since the streamer is not long enough. The fold stays at 5.

## Slide 23: Marine Acquisition
Fold
Common-Depth-Point Gather
The collection of traces having reflected from the same subsurface illumination point
5-FOLD GATHER
Near Offset
Far Offset
5
Common Depth Point
Notes: In data processing, we “gather” all the shot-receiver pairs for a “common depth point”, as shown here by the dashed green lines. Note how the angle of incident (and the angle of reflection) is small for the nearest offset and larger for the farthest offset. The data processor would sum (stack) the output from these traces to improve the data quality (increase signal-to-noise ratio). Since five (5) traces are stacked (summed), we say this is five (5) fold data. These days, for a 2D survey, it is common to have 40+ fold.

## Slide 24: 2D Marine Streamer Shot Record
Refractions
Reflections
Noise from Depth Controller
Notes: This is a shot record from a marine survey. The trace from the receiver closest to the boat is on the extreme left. Receiver distance behind the boat increases left to right.
Note how full fold is only reached for deep reflectors. Shallow reflections merge into refracted waves towards the right.

## Slide 25: 3D Marine Acquisition
TWO source arrays and EIGHT streamers (receiver lines)
Notes: Marine 3D looks a lot like 2D, except that multiple source arrays and streamers are towed at once. Boats like the one in the picture, which are basically 2D boats refitted for 3D, tow 2 sources and 6-8 streamers. New boats specially designed for 3D have a triangular shape (think cheese wedge) that allows them to tow more streamers from their wide back deck. Twelve streamers is typical, but some vessels tow as many as 24.

## Slide 26: 3D Marine Acquisition
Receiver Arrays
Gun Arrays
Midpoints
Blue Gun Firers
100 m Streamer Separation
50 m Gun Separation
25 m Receiver Group Separation
Notes: When there is more than one source array, the source arrays are not fired together, but are fired in sequence at about 10 second intervals. Each air gun array therefore generates a unique set of midpoints that are half way between the fired source array and the receivers. For this diagram, the gun array on the left side of the boat has been fired. The gun array and the subsequent midpoints are colored in blue.

## Slide 27: 3D Marine Acquisition
Receiver Arrays
Gun Arrays
Midpoints
100 m Streamer Separation
50 m Gun Separation
25 m Receiver Group Separation
Red Gun Firers
12.5 X 25 m Coverage
Notes: For this diagram, the gun array on the right side of the boat (red) has been fired. The associated midpoints are colored in red. With the survey parameters indicated in the upper right, we get midpoints (traces) spaced of a 12.5 x 25 m grid.

## Slide 28: Land Acquisition
Notes: Let’s switch to land acquisition.

## Slide 29: Land Source – Option 1
Dynamite
  Placed in shallow shot holes, typically 5 to 30 m deep.
  The depth of the hole is chosen to get the best coupling.
  It is expensive, labor intensive and there are safety issues.
  It is used in areas where other surface sources, like vibroseis, cannot be used.
  It may be used when the surface is covered by a thick layer of gravel or sand, has mountainous terrain, or is a swamp or dense jungle.
Notes: One energy source for land surveys is dynamite. Shallow holes are drilled and a charge is lowered into the “shot hole” and ignited. Dynamite is not preferred due to safety and cost issues. However, it is still used in certain areas (last bullet item).

## Slide 30: Land Source – Option 2
Vibroseis
  A large plate is vibrated up and down to send a seismic wave into the ground.
  The truck’s entire weight is placed on the base plate to get good coupling with the ground.
  In general, there is minor surface impact.
  It is less expensive than dynamite.
  The vibrator sweeps through a range of frequencies.
  This “sweep” is later compressed into a compact wavelet through a process called “correlation”.
Notes: The preferred land source is vibrator trucks – referred to as Vibroseis. Large trucks (3 to 5) roll into position, they lower a massive plate to the ground, and then the plate is vibrated. The frequency of the vibration “sweeps” through a range of frequencies. This type of source is safer and less expensive, as long as huge trucks can access the area.

## Slide 31: Land Receivers
Moving
Coil
Metal
Casing
Electrical
Contacts
Geophone
  Ground motion is usually detected by a “moving coil” geophone.
  A strong magnet is surrounded by a wire coil, and the coil is attached to the base of the casing.
  Ground motion moves the magnet and this induces a measurable electrical voltage that is proportional to the speed of the ground movement.
  Geophones must be rugged and accurately detect a wide range of large to small ground motions.
  Geophones are housed in a variety of cases depending on the terrain and the survey environment.
Notes: Land receivers are called geophones. They detect very small ground movements. Until a few years ago, all geophones used magnets and wire coils to convert ground motion into electric signals. Modern technology is replacing magnets and coils with new, smaller, more sensitive micro-devices.

## Slide 32
Vibroseis
Unit
Receivers
Receivers
1
∑ Fold
Land Acquisition
5
4
3
2
1
Notes: Another “poor man’s movie” for land acquisition. We will keep trace of source-receiver pairs that give us information at the red dot. This is scene 1.
A raypath is shown from the source array down to red dot and then reflected up to receiver group 1. The fold counter goes from 0 to 1.

## Slide 33
2
Vibroseis
Unit
Receivers
Receivers
Land Acquisition
∑ Fold
6
5
4
3
2
1
Notes: This is scene 2. A raypath is shown from the source array down to red dot and then reflected up to receiver group 2. The fold counter goes to 2.

## Slide 34
3
Vibroseis
Unit
Receivers
Receivers
Land Acquisition
∑ Fold
6
5
4
3
2
1
Notes: This is scene 3. A raypath is shown from the source array down to red dot and then reflected up to receiver group 3. The fold counter goes to 3.

## Slide 35
4
Vibroseis
Unit
Receivers
Receivers
Land Acquisition
∑ Fold
6
5
4
3
2
1
Notes: This is scene 4. A raypath is shown from the source array down to red dot and then reflected up to receiver group 4. The fold counter goes to 4.

## Slide 36
5
Vibroseis
Unit
Receivers
Receivers
Land Acquisition
∑ Fold
6
5
4
3
2
1
Notes: This is scene 5. A raypath is shown from the source array down to red dot and then reflected up to receiver group 5. The fold counter goes to 5.

## Slide 37
6
Vibroseis
Unit
Receivers
Receivers
Land Acquisition
∑ Fold
6
5
4
3
2
1
Notes: This is scene 6. A raypath is shown from the source array down to red dot and then reflected up to receiver group 6. The fold counter goes to 6.

## Slide 38
6
Common Mid Point gather,
6 fold data
Vibroseis
Unit
Receivers
Receivers
Land Acquisition
∑ Fold
6
5
4
3
2
Notes: This is scene 7. There are no raypaths from the source array down to red dot and then reflected up to a receiver group. Thus, the fold counter stays at 6.

## Slide 39: Land Shot Record
Ground Roll
Refractions
Reflections
0 s
1 s
2 s
Split Spread Geometry
Notes: This is a shot record from a land survey. Unlike a marine survey, we can have receivers in front of and behind the source arrays (e.g., 3 vibrator trucks). So land shot records are somewhat symmetric about the source point.
The cone of high amplitude noise spreading out from the source is "ground roll" - Rayleigh waves excited by the source. Rayleigh waves require an elastic medium, so they don't appear on marine records. They are one of the main reasons (but not the only one) why land data is usually lower data quality than marine.

## Slide 40: 3D Land Acquisition
Notes: This photo is from a 3D land survey operation. Looks like four (4) vibrator tracks acting in sync to cancel horizontal motions.

## Slide 41
x
x
x
x
x
x
x
x
x
x
x
x
x
x
x
x
x
x
x
x
x
x
x
x
x
x
x
x
x
x
x
x
x
x
x
x
x
x
x
x
x
x
x
x
x
x
x
x
x
x
x
Recording Truck
Vibrators
Receiver Groups
50 Meter Receiver Spacing
50 Meter Source Spacing
3D Land Acquisition
Notes: This shows one type of equipment geometry that can be used to acquire a land 3D survey. In general, the source lines (where the vibrators drive) are perpendicular to the receiver (geophone) lines. The guiding principle here is the location of the midpoints half way between the source and receiver locations.
Since the cable linking the receiver arrays conveys a digital signal entirely analogous to a telephone line, the recording truck is able to record the arrivals at a very large number of receiver locations. The receivers are laid out as a series of parallel lines that are all connected to the recording truck. For this diagram, the receivers (green circles) are spaced 50 meters apart and the receiver lines are spaced 400 meters apart. The perpendicular source lines have a 50 meter source spacing (red Xs) and the receiver lines are spaced 400 meters apart.

## Slide 42
x
Recording Truck
Midpoints
Vibrators
Receiver Groups
3D Land Acquisition
1 Vibration Point
3 Active Receiver Lines
Notes: Here we consider one vibration point (white X) with all the receivers (green circles) active. The red diamonds are all the midpoints between the vibration (shot) and all the active receivers. One could say that the red diamonds are the “bounce points” for a horizontal interface in the subsurface.

## Slide 43
Recording Truck
Midpoints
Vibrators
Receiver Groups
250 Meter Midpoint Spacing
3D Land Acquisition
4 Vibration Point
3 Active Receiver Lines
x
x
x
x
Notes: Here we consider the source-receiver midpoints after four (4) vibration points have been activated. You can start to see that a 3D “patch” of subsurface points is being recorded. At this point, the 3D patch is still one (1) fold (single fold), but as the vibrators proceed down the source lines, a larger fold results. The total fold is a direct function of the receiver spacing, receiver line spacing, source spacing, and the source line spacing. Since the patch is only half as wide as the spread of the receivers, when the total patch is acquired, the field layout is picked up and moved over to generate an adjoining patch. When the patches are put together, the product is a full 3D survey.

## Slide 44: Acquisition “Footprint”
Amplitude artifacts oriented in the acquisition direction.
Processing assumptions are not consistent with the actual acquisition geometry.
Artifacts will decrease in magnitude with reflector depth.
Possible mitigation techniques:
  Acquisition (by infill shooting)
  Preprocessing (by flex binning or trace interpolation)
  Appropriate processing
  Post-processing (by map filtering)
Seismic Amplitude along the WB
Notes: With 3D surveys, we get some artifacts (effects that distort the geology) in shallow zones. These artifacts diminish at depth – usually insignificant below about 3000 ft. This is due to some locations not having enough midpoints at shallow depth. The artifacts due to survey geometry are call the acquisition “footprint”.
Both seismic images are from the same marine 3D survey. The image in the upper right is a crossline – perpendicular to the boat paths. The dotted cyan line is the water bottom reflection. Note how jumbled it is. This is due in part to the acquisition geometry. The lower image is the reflection amplitude along the cyan (water bottom). Notice the color striations left-to-right (west-to-east). These striations tell me that the boat sailed east-west rather than north-south. The high-frequency color variations (striations) are NOT due to geology – are an artifact of the acquisition geometry.
There are some methods we can use to mitigate these artifacts. Good solutions are costly. Data processors can cosmetically reduce these artifacts, but cosmetic “tricks” can cause more problems than they solve. Beware!

## Slide 45: Summary
Land Seismic
The source produces ground motion that is reflected in the subsurface and then recorded by geophones. Typically, the source of ground motion is Vibroseis and occasionally dynamite.
Marine Seismic
The source is usually compressed air, producing a pressure wave that is reflected in the subsurface and recorded by hydrophones that are pressure detectors. The efficiency in acquiring a marine 3-D survey is produced by the boat towing multiple source arrays and multiple streamers.
Notes: Summary

## Slide 46
Questions?