## Slide 1: Petroleum Geology & Geophysics
Seismic Data Processing
Velocity
Semblance
Flattened
Gather
Common Midpoint
Gather
Notes: This unit is an overview of seismic data processing, yet there is too much material here for a single class period. If you are emphasizing geophysical aspects, then you might want to cover most of this material in two (2) sessions. If you are emphasizing geological aspects, then you might want to trim this back to about 25 slides (or leave it out).
The next slide has a lecture outline.

## Slide 2: Outline
Introduction to Processing
Basics of a Stacked Seismic Section
Pre-Stack Processing Steps
Seismic Migration

## Slide 3: Processing Objectives
Seismic data acquisition and seismic data processing work together to produce the best earth image.
Ideally, processed seismic data should represent the true earth response. In practice, the processed data will only be an approximation.
The image to the right shows a well processed, interpretable subsurface image.
Obtain an accurate, interpretable subsurface image
Subsurface ‘Image’
Notes: The overall objective of seismic processing is to obtain…

## Slide 4: Seismic Processing - Basics
Field Record
(marine)
Data Processing
Stream
Subsurface ‘Image’
Input
Output
Notes: The input to seismic processing is field records (raw data) – although some processing steps are started in the field. On the right is a shot record from a marine survey. We’ll talk about what goes on in the yellow box to remove a bit of the mystery.
The output is a seismic data set that can be used to interpret subsurface geology. In the image in the lower right, a fault has been marked (black line). Also, a major erosional unconformity has been marked (dashed yellow).

## Slide 5: Processing Challenge
Estimate and remove the effects of non-geologic signals, without impacting the amplitude and phase of the primary reflections.
If we understand how waves propagate, can we develop and apply corrections to generate a more accurate image of the subsurface?
Notes: Here is the big challenge, to estimate and remove…

## Slide 6: Elements of Good Processing
Accurate Geometry
  reflection travel times free from distortion for true trap definition
2. Compact Wavelets
correct reflection amplitude and pulse shape for reservoir lithology and fluid property prediction
3. Reduced Noise
good signal to noise for mapping reflections of interest
Good Processing
Great Processing

## Slide 7: Generic Processing Flow
Processing generally proceeds in several stages
  Signal – steps to:
      Control and shape the wavelet.
      Preserve the relationship of amplitude to the RCs.
      Improve the signal-to-noise ratio (SNR).
  Imaging – steps to:
      Focus the subsurface image.
      Correct for positioning errors.
  Signal Processing – steps involving:
      Application of pre- and post-stack enhancements.
Imaging
Signal Processing
Signal Processing
Migration
Notes: Here is a generic seismic data processing flow. First, we use some signal processing steps preserve the amplitude and shape of the wavelets while improving SNR. Then we work on focusing the image to correctly position the wavelets in 3D space. Note that a process call seismic migration is the main process. Finally, we do more signal processing to fine tune the data.

## Slide 8: Generic Processing Flow (post-stack migration)
Signal Processing
Imaging
Signal Processing
Post-Migration Processing
Front End /Geometry
Noise Mitigation
Amplitude/Phase Control
Velocity Analysis
Migration
Stack
Post-Stack Processing
*
Migration
Notes: We talked a little about stacking the data – summing information from several source-receiver pairs from common reflection points. In the old days (prior to ~1990), stacking was always done before migration. We say the data had post-stack migration (stack first, migration after).

## Slide 9: Generic Processing Flow (pre-stack migration)
Signal Processing
Imaging
Signal Processing
Post-Migration Processing
Front End /Geometry
Noise Mitigation
Amplitude/Phase Control
Velocity Analysis
Migration
Stack
Post-Stack Processing
*
Migration
Notes: With faster, cheaper computers, and more data storage capacity, we can now migrate the data before stacking the data. The good news – this gives us far superior imaging of complex subsurface geology. The bad news – it takes much more money, people and TIME. We will return to the pros and cons of pre-stack migration in a few minutes.

## Slide 10: Developing a Stacked Section
To establish some basics, we’ll begin our discussion with the process called stacking.
Other processing steps precede stacking, which we will cover later in the lecture.
A review of stacking lays a good foundation for our other discussions about seismic processing.
Stacking = summing appropriate traces to enhance the geologic signal and reduce the random noise.
Notes: To get into more detail, we will review the concept of stacking first. We will skip the steps before stacking for now, but we’ll return to some of the steps after discussing stacking. Remember, ‘stacking’ is our code word for summing appropriate traces to enhance the geologic signal and reduce the random noise.

## Slide 11: Repeated Measurements
The seismic method is plagued with noise – both random noise and coherent (systematic) noise.
To reduce random noise, we get repeated measurements for each individual subsurface point.
We can get four (4) independent measures of the geology in the red box by using a series of different shot points and receiver locations
We discussed fold and how we get repeated measurements in the acquisition lecture.

## Slide 12: A Marine Shot Record
Source
Receivers
R1
R2
R3
R4
R5
S1
Direct Arrival
Reflections
Two-Way Travel Time
Offset (Distance)
R1
R2
R3
R4
R5
Direct Arrival
Reflection
A shot record shows all the traces (with different offsets) for a single shot
This is what we collect in the field during acquisition
1
2
3
Shot Record
3
Notes: This is a diagram to explain TWO seismic waves for a marine survey. The first wave we’ll consider is the direct arrival – energy that travels horizontally through seawater directly from the shot array to each receiver group. It is color-coded red. On the shot record on the right (receiver number = distance vs. TWT), the direct arrival is a dipping line. The slope of the straight line is the velocity of sound in water (1500 m/s or 5000 ft/s).
The second wave we’ll consider is the reflected energy off interface 3. It is color-coded blue. It shows up on the shot record as a half hyperbola. The shape of the hyperbola is related to the average sonic velocity down to the interface. The shot records are the raw data we collect in the field.

## Slide 13: A CMP Gather
Sources
Receivers
R1
R2
R3
R4
R5
S1
S2
S3
S4
S5
For Point A
A
CMP Gather
Offset Distance
In processing, we sort the shot-receiver pairs so that data from the same ‘bounce’ point is captured.
This gives us a CMP gather.
CMP = common mid point
1
2
3
3
Notes: One of the main steps in data processing is stacking the data. First, we need to re-sort the individual traces (recorded data) from source-receiver pairs for a common midpoint (CMP). Computer, go find all the source-receiver pairs that has a CMP at position A, please! We display all the CMP traces for position A on a display called a CMP gather (right). The scales are the same as for a shot record - receiver number (which relates to offset distance vs. TWT).
It is important to understand the difference between a shot record and a CMP gather:
- a shot record = one shot and all the recorded traces associated with that shot – what we collect in the field.
- a CMP gather = one location (e.g., A) with all the source-receiver pairs that have A as their mid point – what we sort field data to obtain.

## Slide 14: CMP Gather
Travel times differ with offset since the path for a near offset trace is less than the path for a far offset trace.
With the correct velocity, we can correct for the difference in travel time for each trace.
The curvature of this hyperbola is a function of the average velocity down to the depth of the reflector
CMP Gather
Offset Distance
Notes: Reflected energy has a hyperbolic shape on both a shot record and a CMP gather.
Why is this?
- For a trace with small offset (near the boat), the horizontal component of wave travel is very small.
- For a trace with large offset (far from the boat), the horizontal component of wave travel is much larger.
Thus, TWT increases with offset as the horizontal component of travel increases.
If you like analogies, consider a jet flying from NY to LA. If there are no severe storms, the plane can fly a straight line and arrive on time. However, if there are severe storms in the mid west, the plane may fly south towards Atlanta to miss the bad weather and then turn west, arriving in LA a hour late.

## Slide 15: With Correct Velocity, the Gather is Flattened
CMP Gather
Offset Distance
Velocity
Too Slow
Curves
Down
Velocity
Correct
Flat
Velocity
Too Fast
Curves
Up
Notes: We can estimate the average velocity down to a reflecting interface using the shape of the hyperbola (the tighter the hyperbola, the faster the velocity). Once we have a velocity estimate, we can “correct” for the delay in reflection hyperbola with offset. If after correction the reflection still curves down a little, then the velocity is too slow (not corrected enough). If after correction the reflection is flat (horizontal), then the velocity is “just right” (corrected properly). If after correction the reflection curves up a little, then the velocity is too fast (over corrected).
By “flattening the gathers” during processing, we get a good (but not great) model of velocity as a function of depth at each X,Y where we do the flattening.
This analysis might be done on a grid of 1 km x 1 km and then the velocities are interpolated for an entire 2D line or 3D volume.

## Slide 16: A Stacked Trace
CMP Gather
Moveout Corrected
Midpoint Gather
Stacked
Trace
Offset Distance
We stack several offset traces
(# traces = fold)
The geologic ‘signal’ will be additive
The random ‘noise’ will cancel
Stacking greatly improves SNR
(signal-to-noise)
10 Fold
Notes: With the interpolated velocities, we can “flatten all the gathers” to correct for the time delay with offset. We commonly refer to this as a “moveout correction”. Now each trace has the reflections as if all the offset distances = zero – as if the shot and receiver were in the same X,Y location. Neat!
The next step would be to sum (stack) all these moveout corrected traces for every X,Y location. By summing/stacking the traces, we enhance the geologic ‘signal’ since it is additive. At the same time, we reduce random ‘noise’ (e.g., wave or boat noise) since it tends to cancel with stacking. The more traces we stack, the more we improve the SNR. Fold is the term we use to indicate how many traces we have added (stacked) together. In this diagram, there are ten (10) traces in the center panel, so the fold is 10.

## Slide 17: How the Full Stack is Created
A full stack trace is composed of many traces recorded with different reflection angles but with a common subsurface reflection point.
CMP Gather
Stacked
Section
Depth
NMO Correction
Mute Applied
S5 S4 S3 S2 S1 R1 R2 R3 R4 R5
This gives us ONE trace
Notes: Usually, we flatten and stack (sum) all the available traces for each X,Y location. This would be full fold data.
To summarize the process:
- we start with shot records (recorder in the field) (not shown),
- then we sort the data to get a common midpoint (CMP) gather,
- Next we work velocity as a function of depth (TWT) to get a normal moveout correct gather,
- We apply a mute to zero out undesired effects, and
- Then we stack the NMO & muted gather to get a single trace at a specific X,Y location (magenta line on the 2D line on the far right.
Then we repeat the same process for the next X, Y and the next, and the next, and the next… Thank goodness for modern computers!

## Slide 18: Full Stack – Characteristics
Summation (stacking) decreases random noise and increases signal.
Often the best dataset for structural interpretation.
Cleanest dataset to interpret in areas with low SNR.
Summation (stacking) of all angles (near to far) angles will decrease the overall bandwidth.
May not be the best dataset for stratigraphic detail.
May not be the best dataset to investigate DHIs.
DHI = Direct Hydrocarbon Indicator
Notes: In the last bullet – a DHI is a direct hydrocarbon indicator. A useful DHI is amplitude variation with offset (AVO), which requires partial stacks (e.g., near stack and far stack).

## Slide 19: Partial Stacks
Traces within a specific angle range of a CMP gather are summed to make angle stacks
  e.g. as near, mid, and fars
Nature of seismic acquisition results in offset limited data
Note that with increasing depth, the emergent angle is limited by the offset of the acquisition
A
B
25°
20°
Notes: One thing that changes with different offset distance and with depth is the reflection angle (angle of incidence). Given a velocity model, perhaps from flattening gathers, we can calculate the reflection angle for each pre-stack trace. As shown above, for a shot into the farthest receiver, the reflection angle changes from 25° for the shallow interface to 20° for the deeper interface (remember there is vertical exaggeration).
In processing, I can filter by reflection angle before I stack (sum) the data. For example, I could filter so that I only keep traces where the reflection angle is from 5° to 15°. This would be called a near stack. Then, I could filter, so that I only keep traces where the reflection angle is from 25° to 35°. This would be called a far stack. Typically at our depths of interest, the range of angles will be from about 1° to about 35°. The maximum angle depends on depth and the length of the streamers.

## Slide 20: Angle Stacks – How They are Created
Raypaths – Identical Angle
Near
stack
mutes
Far
stack
mutes
Contours of Reflection Angle
A velocity model must be available to create these contours
Constant Angle Contours
Nears
Mids
Fars
Notes: This slide shows different raypaths that have the same midpoint and the same reflection angle at each interface. We need a velocity model to calculate raypaths and reflection angles.
On the right is a CMP plot on which reflection angles as a function of depth and offset distance are displayed. The red pair of lines might be the data I want to stack for a near-stack data set. The green pair of lines might be the data I want to stack for a far-stack data set. Note the angle filters (pairs of color lines below about 4800 ms are straight-lines). Once the depth (expressed in TWT) is greater than the streamer length, we have to go to the vertical lines to get enough data to stack.

## Slide 21: Near and Far Angle Stacks
Near Mute
Far Mute
NMO corrected CMP Gather
Near Angle Mute
Far Angle Mute
Notes: We have a full NMO corrected CMP gather in the top, center. The pair of red lines is our near angle mute. It is applied in the image on the lower left. This is the data I would stack (sum) to get a near angle stack. The pair of green lines is our far angle mute. It is applied in the image on the lower right. This is the data I would stack (sum) to get a far angle stack.

## Slide 22: Pre-Stack Processing
There are a number of processing steps that are done before stacking.
These are done to:
  Correct for amplitude loss with depth (time).
  Correct for elevation changes for land acquisition.
  Minimize the effect of the wavelet (deconvolution).
  Determine the optimum velocity function for stacking.
Notes: We have covered the concept and process for stacking seismic data. Now let’s step back to some of the thing we do prior to stacking the data.
Pre-stack processing steps might include the following:
- Correct for amplitude loss with depth (time).
- Correct for elevation changes for land acquisition.
- Minimize the effect of the wavelet (deconvolution).
- Determine the optimum velocity function for stacking.
There are other processing steps that can be applied, but more than these is too much detail for this course.

## Slide 23: Amplitude Loss with Time
Loss of energy through time/depth/distance traveled.
Energy decays by the inverse square of the distance traveled.
Energy varies as 1/radius2
or 1/time2
Spherical Divergence
Since we know how signal strength is lost by geometric spreading from the surface source location, we are able to apply a correction factor.
Notes: As the radius of the wave front increases, the energy is spread out over more space. Think of the letters on a balloon as it is blown up. The letters are small and the ink is dark when the balloon is small. As the balloon expands, the letters get bigger, the ink is spread out and the letters get fainter.
We know the energy varies ad a function of 1/radius2 Since we know how signal strength is lost by geometric spreading from the surface source location, we are able to apply a correction factor.

## Slide 24: Amplitude Loss with Time
Energy is partitioned at each acoustic interface.
At a reflecting interface, normal incidence energy is converted into two waves:
  reflected P waves, and
  transmitted P waves.
The incident energy at layer N has been reduced by all of the overlying reflected energy.
Amplitude varies as
T = R (1 - R ) (1 - R ) … (1 - R )
Total
N
N - 1
N - 2
1
2
2
2
Transmission Loss
N = 4
N = 3
N = 2
N = 1
Notes: Transmission loss means that as the energy travels down, a small fraction is reflected every time an acoustic boundary (a change in impedance) is crossed. We can do an “energy balance” to know how the energy is split at an interface. The transmitted energy at a given interface is less than the incident energy. The transmitted energy below interface N is the incident energy at interface N+1.
Again, if we know how amplitude is decaling due to transmission losses, we can compensate (correct) for it.

## Slide 25: Amplitude Loss with Time
Seismic energy is converted to heat.
This is frequency dependent.
The higher the frequency, the greater the loss of signal.
Absorption is referred to as Q.
Q varies by rock type.
Amplitude varies as Ao e-X/Q
Absorption
Attenuation
Q = 50, F = 5 Hz
Attenuation
Q = 50, F = 50 Hz
Low Frequency
High Frequency
Notes: Absorption is the loss of some energy due to heat conversion. This loss is different as a function of frequency. High frequencies decay more rapidly than low frequencies.
Analogy – As a car that has loud music playing drives away from you, you start to lose the treble and only hear the bass.
The absorption of energy as a function of frequency is called the Q factor, or simple Q. If we can figure out Q, we use it in our data processing.

## Slide 26: Gain Compensation
Automatic Gain Control
Programmed Gain Control
Boosting signal strength to a preset level over a specified time interval
Controlling signal strength to preserve proportionality with bedding reflectivity
Original
Trace
15 sample
AGC applied
Gain
Function
Original
Trace
PGC
applied
Gain
Function
Notes: Going back to the car radio analogy for a moment, you can change the settings for treble and bass. These settings change the gain for different frequency ranges. For example, one can decrease the treble and boost the gain to get more of the ba-boom sound.
Automatic gain control (AGC) was commonly applied in the “old days.” A “window length” of samples (e.g., 15 samples) would be specified by the processor. Then the average amplitude over this sliding window was calculated. The amplitude was adjusted so that the average amplitude stayed within a tolerance level. This means the amplitudes were reduced in regions of above average amplitude, and increased in areas of below average amplitude. Note on the left display the zone of low amplitude on the top trace (original) has been boosted in the middle trace (after AGC was applied).
The left, bottom shows the gain function – how amplitudes were adjusted.
On the right is a programmed gain control.
This would be based on spherical divergence and transmission losses.
Note the gain function is a slow increase, which preserves the relative amplitude strength more than an AGC.
AGC is OK for structural interpretation, not good for stratigraphic interpretation.

## Slide 27: Elevation Correction
Time
Origin
Gathers are not flat after Moveout Correction due to Elevation Artifacts
R
R
R
R
R
R
R
R
R
R
R
R
R
R
Shot Layout Variable Surface Elevations
Receivers
Source
Receivers
Source and receivers may be located at different surface elevations.
Travel time to any reflector (a flat one in the figure) will vary as the length of the travel path changes.
This effect must be removed from the data if the traces are to be successfully flattened and then stacked.
Statics
Distorted Hyperbolas
Notes: For land data, we usually have topographic (elevation) changes for all the source and receiver locations. If we do not correct for elevation changes, then all the reflection hyperbolas will have “jitter”. In processing, we can select a specific elevation to be our reference (datum) elevation (e.g., 5300 ft in the Denver Basin). We measure or assume the near-surface velocity. Then we can correct the source locations and the receiver locations to what they would be had they been at our reference elevation.

## Slide 28: Elevation Correction
Time
Origin
Shot Record:
Corrected Moveout Curve
Shot Layout Variable Surface Elevations
Seismic Reference Datum
R
R
R
R
R
R
R
R
R
R
R
R
Receivers
Source
Receivers
After applying this time shift, the data appears as if it has all been recorded on the seismic reference datum.
This is referred to as a static shift.
All the samples for each individual trace are moved by the same amount.
Seismic Reference Datum
‘Clean’ Hyperbolas
Notes: The processor specifies the seismic reference datum. For each trace, a time shift is calculated so that zero time is registered at the seismic reference datum. If this correct is done properly, the hyperbola on the shot records or CMP gathers will look “clean”.

## Slide 29: Static Correction
A time correction was applied to datum traces to a common reference elevation.
Before
After
‘Cleaner’ Hyperbolas
Distorted Hyperbolas
Notes: Here is a before and after comparison. On the left, a CMP gather before applying a static correction. On the right, the same CMP gather after applying the elevation corrections.

## Slide 30: Trace Muting
Removing shallow portions of traces that are dominated by direct arrivals and refractions.
Notes: Muting means setting parts of the data to zero. A data processor will mute any signal that occurs in the water column of a marine survey. He/she will also mute the direct arrivals and refraction energy, since we are only interested in reflected energy. There is some good information in both the direct arrivals and the refraction energy. Other types of analyses are performed with these data, beyond the scope of this course.

## Slide 31: Removing the Wavelet Shape
Wavelet shaping to improve recognition and resolution of reflected events.
Deconvolution
After Decon
Before Decon
Ringing
Notes: Deconvolution (decon) is a process that helps to remove the effects of the shape of the wavelet. It removes the some short-period multiples. The wavelet is made sharper (short time duration), which improves vertical resolution.
Decon is a statistical estimation process, using the data to estimate what the wavelet would be if it had not been corrupted. In this example, some of the “ringininess” in the records on the left has been diminished by applying decon (on the right).

## Slide 32: Multiple Removal
Water Bottom Multiple
Subsurface Multiple
Peg-leg Multiple
Multiples: Seismic energy that has been reflected more than once.
  Multiple removal steps are often applied several times, especially in areas with strong multiples.
    A “peel the onion” approach.
    Pre-Stack and Post-Stack migration steps.
Notes: Next we will talk a little about multiples. A multiple is seismic energy that has been reflected more than once. The water bottom multiple (top, left) is easiest to picture and understand. For this, the water bottom multiples are recorded at two (2) times the water bottom TWT. There are two (2) down-going paths and two (2) up-going paths. On the upper right is shown a double water bottom multiple. There are three (3) down-going paths and three (3) up-going pates – it would be recorded at three (3) times the water bottom TWT.
The middle diagram shows two examples of subsurface multiples. The lower diagram shows two examples of peg-leg multiples.

## Slide 33: Velocity Analysis
Reflections on a CMP Stack
Velocity Semblance Diagram
Used to determine the velocity function that best flattens the gathers
Two-Way Time
Velocity
Values that indicate the degree of ‘flatness’
Notes: We can use the shape of the hyperbolas to estimate seismic velocities. Gathers are flattened using a range of velocities. As the correct velocity at a depth (TWT) is used, the “flatness” reaches a maximum. On the right is a display that shows a measure of flatness as a function of velocity and depth. This is called a semblance diagram. The computer uses a set of rules to pick velocity vs. TWT points. A human will check the machine picks on a course grid of CMP gathers. This combination of machine and human picks on a semblance display results in a 2D or 3D velocity model.

## Slide 34: Velocity Segregation of Multiples
Semblance
Gather
Energy from Multiples
Energy from Multiples
Muted
Notes: Here is an example of picking velocities using a color semblance display (left). The shallow picks are easy – the deeper ones require a bit of experience.
The water bottom here is at about 1200 ms. There are some high semblance patterns starting at about 2400 and 3600 ms – these are water bottom multiples. Semblance diagrams help us recognize multiples.

## Slide 35: Normal Moveout (NMO) Corrected Gather
What happens to the energy from multiples when traces are stacked?
What is the difference in multiple removal for near vs. far angle stacks?
Energy from Multiples
About
400 fold
Notes: This is an NMO display for the same area as used for the last slide. The NMO correction was based on the white line velocity picks on the previous slide. Note the dotted yellow line. This is energy from the first water bottom multiple. It still has downward curvature since it is a slower velocity than the reflections at the same TWT.
If we stack this NMO gather, the primary reflections are flat and will add (constructively interfere). The yellow multiple will cancel out due to destructive interference. Although a multiple is not random but coherent noise, it will be reduced by stacking the traces.
You should be able to understand why the water bottom multiple might be bigger (less canceled out) for a near stack then it would be for a far stack. (Close to flat on the left side = less destructive interference – dipping observed on the right, so more destructive interference).

## Slide 36: Normal Moveout (NMO) Corrected Gather
Energy from Multiples
About
400 fold
The gently dipping multiple will not be canceled during stacking
Near Stack
The strongly dipping multiple will be canceled by destructive interference during stacking
Far Stack
Notes: 36
This illustrates why multiples will not be canceled as much or a near stack than on a far stack.

## Slide 37: Multiple Removal
Approach:
  Marine: technique is determined by water depth
    Deep water – velocity separation (Radon)
    Shallow Water - deconvolution
  Land: uses velocity separation (Radon) and/or deconvolution
In “velocity space” the multiples can be recognized and filtered out
Radon
Notes: We have shown how stacking can reduce water bottom multiples. The data processors have other tools to remove multiples. For marine surveys, the tools they use are determined by water depth:
- Deep water – velocity separation (Radon)
- Shallow Water - deconvolution
For land surveys:
- Radon filtering and/or
- Decon.

## Slide 38: Radon Applied to Remove Multiples
Before Radon
After Radon
Conflicting dip due to primaries and multiples
Multiples effectively removed with Radon
Notes: This slide serves as an example of the benefits of radon filtering. Notice the areas of conflicting dip on the left image. The data processor worked with the project interpreters to confirm the correct dip and the multiples. Radon filtering was then used to effectively attenuate the multiples, as you can see in the image on the right.

## Slide 39: Pre-Stack Processing
There are other advanced processing steps that can be done before stack.
These additional pre-stack processes are beyond the scope of this class.
They are quite expensive is terms of money, time and resources.
We will move on to the principle imaging technique – migration.

## Slide 40: Non-Layer Cake Geology
Thus far my diagrams, by intention, have had nearly horizontal layering.
Things get more complicated with dipping strata.
The ‘bounce’ point is not simply the midpoint.
Angle of Incidence = Angle of Reflection
Midpoint

## Slide 41: Positioning Problems

Energy
Source
The seismic ray hits an inclined surface at 90º and reflects back
0.2 s down
0.2 s up
True Path
A
Posted
Position
B

0.4 s -
The reflection is displayed beneath the source-receiver midpoint
B
Notes: The next five (5) slides show a simple model for a dipping sea floor. On this slide, we have one shot and want to construct a zero-offset raypath. Then, we consider where the sea floor reflection would be posted on a seismic line. The energy wave goes down to where the path is perpendicular to the sea floor (A), some is reflected and the reflected energy returns to the shot point location and is detected. Here it takes 0.2 s to go down and 0.2 s to go up - a total TWT of 0.4 seconds. We know the TWT, but we don’t know how much the reflecting interface dips, if at all. So all we can do is post this reflected energy at 0.4 s below the source-receiver midpoint (in this case at B). Our zero offset response is shown on the right. We know this is positioned correctly ONLY if the seafloor is horizontal. We know that if the sea floor is NOT flat, then there is a mispositioning problem/error.

## Slide 42: Where Would the Reflection Lie?
1






2
3
4
6
5
90º
Notes: We can use the concept illustrated on the last slide as a means to construct a dipping reflector’s response. We will walk through this construction for the first shot point. We will only consider zero offset rays (source and receiver at the same location).

## Slide 43: Where Would the Reflection Lie?
1






2
3
4
6
5
Where would the reflection lie?
Compass
Notes: We can use an old fashioned compass to get the travel distance to the “bounce point”, which is where the radiating energy hits the interface at 90°.

## Slide 44: Where Would the Reflection Lie?
1






2
3
4
6
5
Where would the reflection lie?
Notes: Then we swing an arc from the bounce point (black circle) to the point directly below the source-receiver (red circle). The red circle is where the reflection would be positioned on a seismic line.

## Slide 45: Where Would the Reflection Lie?
1






2
3
4
6
5
The reflection is positioned downdip
and has less dip than the interface
Notes: We repeat the process for shot locations 2 through 6. The black line is where the reflector is in true 3D space. The red line is where the reflector would be posted on a seismic line. Note the error in the reflection’s position. The reflection is positioned downdip from the true position of the reflection interface and it has less dip than the interface. We don’t want reflections to be misplaced in the subsurface, do we? Of course not, but seismic processors will come to our rescue.

## Slide 46: Imaging – Correcting the Position
Unless we do something, we get a distorted image of the subsurface.
Dipping reflectors will be out of position.
Fortunately, our data processors have a solution.
They can correct this mispositioning problem through
Seismic Migration

## Slide 47
Time
Unmigrated Image
Migrating the Stacked Image
Unmigrated Impulse Response
This energy (peak/ trough) could have come from anywhere along this arc.
The shape of this arc is controlled by the velocity field.
Notes: Migration is the process that fixes a lot of our reflection mispositioning problems. So we refer to the seismic data that has not been migrated as unmigrated data. An unmigrated seismic line would be like the red line for the sea floor that we constructed in the two (2) previous slides.
The red wavelet shown here could be the sea floor reflection that we modeled for shot #1 of our dipping sea floor model. The real position of the bounce point could be anywhere along the blue arc (half circle). The shape of this arc is controlled by the velocity field. In the migration process, every sample in every trace is swept out along a circular arc as this single peak-trough is shown here.

## Slide 48
Unmigrated Image
Migrating the Stacked Image
Constructive
Interference
Destructive
Interference
Sweeping Arcs for Three Wavelets
Time
We get constructive interference where the true reflector is located.
Notes: Here we have added two more wavelets from the same reflector (e.g., the dipping water bottom). At the correct position, we get constructive interference – in this case the peak-trough is multiplied by 3. At other (incorrect) locations, there is destructive interference. The positive (peak) values are canceled by the negative (trough) values. The migrated data will significantly reduce the mispositioning problems.

## Slide 49
Migrating the Stacked Image
Poststack Migration
Sweeps Out Arcs
(Kirchoff Summation)
When Many Arcs are Swept
Time
Notes: When we see the circle sweeps for all of the reflectors, the circles conspire to show where the migrated reflector is actually located. Kirchoff summation (a common type of migration) relies on constructive interference to build the migrated image and destructive interference to cancel the irrelevant portion of each one of the circles.

## Slide 50
Time Display
Location
Reflection
Surface
Unmigrated
Image
In Red
Migrated
Image
In Blue
Migrating the Stacked Image
Seismic Migration
Time
Notes: When every sample of every trace has been migrated, and all of the sweeps have been summed, the image seen here in blue is produced by constructive interference. In other words, the image was not formed by knowledge of the subsurface reflectors but by knowledge of where all possible reflectors could be for every sample.
Note that for 3D migration, we have a data cube rather than a profile so the sweep is actually on a sphere in three dimensions rather than a circle. In summary, the key elements of basic seismic processing is: Gather, NMO correct, Stack, and Migrate.

## Slide 51
Seismic Migration
Red lines mark the unmigrated position of two reflections
Notes: The next two (2) diagrams show the process of Kirchoff Summation as a large sum of ellipses. This diagram shows two (2) dipping reflections on unmigrated data.

## Slide 52
Migrated Model
Edge effect from
the model
Migration noise
Seismic Migration
Red lines mark the unmigrated position of two reflectors
Notes: This is after the data have been migrated. The red marks the unmigrated positions. The black peaks show the data after migration. Constructive interference has indeed built an image of the dipping reflectors that are more properly positioned.
With the rather coarse trace spacing used here for the migration, we see that destructive interference has not really worked perfectly resulting in migration noise. We also see events curling up from the ends of each migrated layer. This is a legacy of the ellipse sweep on a model that had abrupt terminations rather than diffractions at the ends of each layer.

## Slide 53: Stacked – Unmigrated Line
Reflections are not properly located in the subsurface
It is difficult to interpret the structure
Notes: A 2D line from Wyoming. Stacked data, but before migration. You can see crossing energy and diffractions.

## Slide 54: Stacked – Migrated Line
Reflections are mare accurately located in the subsurface
Now a thrust fault can be interpreted
Notes: The same 2D line, but after migration. The anticline has been defined (and made smaller). Crossing energy is now moved to the correct locations. The red dotted line is an interpreted thrust fault.

## Slide 55: Migration Options
There are many methods/algorithms for seismic migration.
Each has advantages and disadvantages as we go from simple, quick methods to more rigorous, expensive methods.
“You get what you are willing to pay for”
Post-Stack
Time
Good to Poor
Imaging
$
Pre-Stack
Time
Great to Fair
Imaging
$$$$
Pre-Stack
Depth
Excellent to
Good Imaging
$$$$
$$$$
Notes: There are many options available for seismic migration. The old adage “you get what you pay for” is certainly valid.
Migration can be done after stacking the data or before. If the data are 40 fold, then pre-stack migration has to swing arcs for 40 traces at each X, Y rather than for 1 trace.
So it takes 40 times the compute and wall clock time, which means more money and people. Migration can be done in the time domain or the data can be converted to depth (ft or meters) and then migrated.

## Slide 56: Migration Types
Velocity Variation
Geologic Complexity
Very smooth
Highly Variable
Layer
cake
Highly
Structured
Prestack Depth
With multi-path
Beam WEM RTM
Prestack Depth
Kirchhoff
Prestack Time
Kirchhoff
Post-stack Time
Which type of migration to use is based on velocity variability, geologic complexity, timing, budget, and business need
WEM = Wave Equation Migration
RTM = Reverse Time Migration
Notes: The type of migration one needs depends on two factors:
- the geologic complexity (simple layering to highly structured), and
- the amount of lateral velocity variation.

## Slide 57: Migration Velocity Considerations
Seismic Spread
Length
Sloping Water Bottom
(smooth to moderate)
Simple Salt
(smooth - moderate)
Complex Salt
(moderate-extreme)
Faults
(moderate to extreme)
Smooth => much longer than spread length
Moderate => close to seismic spread length
Extreme => less than a seismic spread length
Time migration
Depth migration
Notes: Time migration is adequate as long as the velocities vary only a little on the scale of the spread length (length of the streamers). Rapid changes in lateral velocity are not handled well with time migration. This can happen if water depth varies rapidly or a high (or low) velocity body (e.g., salt) has a lot of thickness changes.

## Slide 58: When is Time Migration Preferred?
Turn around time is critical.
No velocity control (wells, VSPs or check shots)
Business phase
  Exploration – mostly uses time migration
    Discovery wells usually aim for the middle of the target
    “If it’s so small we can’t hit it with this data, it’s too small”
  Development – may be able to get by
    Depth migration is better
    One side-track will pay for a depth migration project
  Production – depth migration should be used in almost every case
Notes: Time migration is used:
- When turn around time is so critical that waiting for depth migration is not feasible.
- When there is insufficient velocity information to constrain the velocity model
In the business phase, the exploration needs are usually adequately served by time migration. In discovery and assessment, wells can aim for the fat part of the target “If it’s so small we can’t hit with this data, it’s too small”. Development may be able to get by, but if accurate position next to faults or hitting the exact toe of the target is critical, then depth migration is better. One side-track will pay for a depth migration project.
Production – to work well at the production scale, depth migration is usually required.

## Slide 59: When is Depth Migration a Must?
Positioning Accuracy is Paramount, e.g. in the Production stage
Strong Lateral Velocity Changes, e.g. irregular salt bodies
Severe Anisotropy (>5%) – velocity varies by direction, e.g. fractured reservoirs
Always remember to budget enough
Time and Money!
Notes: Depth migration is necessary when:
- Positioning accuracy is paramount – e.g. Production stage.
- When there are strong lateral velocity contrasts and time migration fails to give acceptable images.
  Salt – GoM, West Africa, Deep Water Brazil.
  Volcanics (usually Basalt) – North of Ireland, Faroe Islands, Greenland, Several parts of the North Sea.
  Granite reservoirs - offshore Vietnam.
  Carbonates – North Sea and Middle East.
  Overthrust or other large throw faults that juxtapose very different velocities against each other.
  Gas charged zones (aka gas chimneys).
  Even if your doing exploration you probably need 3D PreSDM.
- When strong anisotropy is present
Just remember committing to the Depth Migration Path means that you are willing to wait and spend lots of money (including interpreter time DURING data processing).

## Slide 60: Land vs. Marine Seismic Data
Marine Data
Land Data
Same wavelet for each shot
Simple geometry
Long lines
Large volume of data
Only need horizontal locations
No statics
Variable wavelet
Complex geometry
Short lines
Small volume
Need vertical locations
Static problems
Notes: A bit of a summary for Marine data (left) and Land data (right).

## Slide 61
Questions?