## Slide 1: Exercise
Part A: Imaging an Anticline
An Anticline
Your Task:
  You will consider how the top of an anticline would appear on a seismic line prior to performing a seismic migration processing step.

## Slide 2: Shot 1
3
4
2
1
7
8
6
5
Subsurface
Interface
Notes: This animation shows what happens at shot point 1. The energy goes down, some is reflected and recorded. Since the raypath that hits the interface at 90° is purely vertical, the reflection (black peak) plots directly below shot point 1.

## Slide 3: Shot 2
3
4
2
1
7
8
6
5
Subsurface
Interface
Notes: This animation shows what happens at shot point 2. The energy goes down, some is reflected and recorded. Since the raypath that hits the interface at 90° is not vertical, the reflection (black peak) plots at the time for the red + blue path but is plotted directly below shot point 2.

## Slide 4: Position of the Reflection
3
4
2
1
7
8
6
5
Subsurface
Interface
Notes: The reflection position is obtained by connecting the 8 reflection locations. I have started to mark the position of the reflection for shots 1 and 2. The students task is to work shots 3 through 8 and “connect the dots.”

## Slide 5: Exercise
Questions?