## Slide 1: Exercise
Determining Survey Area
Subsurface Area to be Imaged
Your Task:
  You will go through some simple calculations to determine the surface area for seismic survey required to fully image the subsurface target area.
24 km
20 km
C.I. = 5 ft

## Slide 2: Introduction
 | When we define a portion of the subsurface that we want to image, we have to acquire a larger surface area than our target. There are two (2) main factors to consider: (1) the surface area needed to capture diffractions around the edge of the image area, and (2) the surface area for a fold to build up (drop off) as we start (finish) each seismic line. You will look at these two (2) factors for a hypothetical 3D survey.
Notes: This slide outlines the need to get more surface coverage than the subsurface area that we want to image. There are two (2) considerations. In the exercise, the students will start with a subsurface area and have to calculate these two (2) factors that increase the surface coverage area.

## Slide 3: Key Information
Depth of target | 3050 m – 3350 m
Two-Way Time | 1000 ms - 1120 ms
Subsurface Image Area | 20 x 24 km
Table I. Key Information for the Target
Notes: Here is a table with the input parameters that the students need. This table is in the written instructions.

## Slide 4: “Cookbook” Instructions
Step | Action
1 | The maximum offset (the distance behind the boat for the last receiver) equals 1.5 times the maximum target depth. Offset Max = 1.5 * Depth Max = __________
Notes: The exercise instructions will lead the students through the calculations – cookbook style. This is the first step – as an example.

## Slide 5: Final Product
0 2
24 km
20 km
C.I. = 5 ft
??? km
??? km
Surface Area
Notes: This is what we want to image in the subsurface, about 18,000 ft down. The east-west distance is 24 km. The north-south distance is 20 km. The final product for this exercise is the surface area coverage for the survey in kilometers.

## Slide 6
Questions?