## Slide 1: Petroleum Geology & Geophysics
3D Seismic Data
N
Notes: This unit describes 3D seismic data.

## Slide 2: Outline
2
What is 3D Seismic Data?
Advantages of 3D Seismic Data
Planning a 3D Seismic Survey
Notes: Lecture outline with three (3) main objectives for the lecture.

## Slide 3: Thus Far…
In the past, we have described and used 2D seismic data
A 2D seismic survey is a series of single lines acquired in a geographic area, usually at the same time
The subsurface is sampled densely along the shot lines
There is one source array and one line of receivers
Distance between individual lines can be between one (1) mile and tens (10s) of miles
0 km 20
0 km 5
N
Line 60
Line 63
Line 66
Line 69
Line 72
Line 75
Line 10
Line 22
Line 18
Line 14
Line 26
Notes: Thus far in this course, we have been working with 2D seismic data. Here are some facts about 2D lines and 2D surveys.

## Slide 4: What is 3D Seismic Data?
A 3D seismic survey is one in which the seismic data is acquired so densely that the data are processed and interpreted as a volume of data
N
Modern 3D surveys have traces spaced about every 12.5 meters (12.5 m x 12.5 m)
People refer to 3D data sets as seismic volumes or seismic cubes
Notes: A few facts about 3D seismic surveys.

## Slide 5: Advantages of 3D Seismic
The dense spatial sampling of 3D seismic data allows us to:
Utilize true 3D processing technology so that we can obtain greatly improved images of the subsurface
Provide new views of the subsurface (time slices)
Derive new types of specialized data (e.g., coherency)
Employ new 3D interpretation tools (e.g., auto-trackers)
Quickly define ‘geobodies’ – connected samples with a specified range of attribute values (e.g., amplitude anomalies)
Visualize the data and the interpretation in 3D space
Communicate better with peers & management
Notes: The key difference between 2D and 3D data is the much denser spatial sampling of 3D seismic data. This list describes seven (7) important advantages of 3D seismic over 2D seismic.
Slide 6 talks about new views (advantage #2).
Slide 7 talks about new types of data (advantage #3)
Slide 10 shows some visualization that helps with communication (advantage #7)

## Slide 6: 3D Seismic Displays
3D Seismic Volume
Inline 1500
Inline 1500
Crossline 3300
Crossline 3300
Time Slice 1000
Time Slice 1000
Traverse A
Traverse A
Notes: We can view vertical lines IN the direction the survey was shot – an Inline. We can also view vertical lines perpendicular to the direction the survey was shot – a crossline. We can cut horizontally through the data volume to see a slice with a constant TWT (two-way time) value – a time slice. We can define a vertical line with an arbitrary path through the volume – a zigzag line, which I am used to calling a traverse. We can make a seismic traverse that goes through several well locations.

## Slide 7: New Types of Data
Given a volume of 3D seismic data, we can do mathematical operations on the standard reflection amplitude data to generate new types of 3D data volumes
Cross
Correlation
Frequency
Filter
Coherency
3D Volume
Low Frequency
3D Volume
Reflection
Amplitude
Input
Notes: We can use different mathematical operations on the standard reflection amplitude data volume to generate new types of 3D data volumes. Perhaps we apply a frequency filter to the original data to eliminate high-frequency “noise” in the data. We can cross-correlate each trace with its neighboring trace and get a volume of cross-correlation values. This is a common practice that produces a new data volume often called coherency. More on coherency in the next two slides.

## Slide 8: Coherency: A New Type of Data
We can measure how similar one trace is compared to its neighbor within a small time window
Mathematically, we perform a cross-correlation to quantify how similar two or more traces are
Trace
123
Trace
124
Trace
125
Trace
126
Trace
127
Trace
128
Trace
129
Trace
130
Correlation Window
X-Cor
0.99
X-Cor
0.95
X-Cor
0.97
X-Cor
0.64
X-Cor
0.98
X-Cor
0.94
X-Cor
0.96
HIGH (LARGE) Correlation
Not likely for a fault offset
LOW (SMALL) Correlation
More likely for a fault offset
Notes: Coherency is a seismic attribute that indicates how similar neighboring traces are. Mathematically, it is a cross-correlation of the two traces over a small time window (on order of 40 ms). Here we have several traces and a correlation window (light yellow). The first three (3) pairs of traces are quite similar, and cross-correlation values are above 0.9. The cross-correlation of traces 126 and 127 is low within the window – the red trough appears shifted down. The cross-correlation of the other trace pairs is high (traces 127-130). Thus, where the traces are not disrupted, the cross-correlation coefficient is large. Where the traces may be disrupted, the cross-correlation is low.
Here is a view of some seismic data, offshore LA. The data is part of a 3D seismic volume. It is a MAP view at a time depth of 1.856 seconds two-way time; or 1856 milliseconds (ms). The blue lines identify compressions, and would be black on B&W section. Can anyone see evidence for one (1) or more faults? A fault is apparent (black line) because of the offset in the red bands (compressions) that are marked in blue. Other faults can be seen as small offsets in the red reflection bands. These faults are relatively easy to spot since the ‘bands’ are at a high angle to the fault traces. There is a curvilinear fault that starts just NW of center and curves towards the SE. This one is hard to see because the ‘bands’ and the fault trace are at low angles (almost parallel). In the early 1980s, researchers and staff came up with a technique to enhance faults in 3D seismic data, and Amoco patented this method called coherency. Coherency is basically one trace compared to its neighboring traces over a small time period. If the traces are perfectly identical in shape, a value of 1.0 is assigned. As the similarity of the traces decrease, the assigned values also decrease (are <1). More technically, we perform a cross correlation between a reference trace and its neighboring traces, and the value of the correlation is called the cross-correlation coefficient.

## Slide 9: Coherency-Type Data
Do you see evidence for faults?
Time Slice: Coherency-Type Data
1856 ms
Notes: Here is a display of a time slice from a coherency volume in a grey scale. The highest cross-correlation values are shown in white, while the lowest cross-correlation values are shown in black. Intermediate values are in shades of grey. What do you suppose the black lineations indicate? They are potential fault segments. Where there is a black lineation, one trace is on the high side and its neighbor is on the low side or in the fault zone.
Note the black-grey region to the south. This indicates a general lack of similarity of traces in this region – an indication of poor data quality. Another thing that can show up on this type of data are major stratigraphic boundaries – like going from inside to outside a major channel system. This example does not show any stratigraphic features.

## Slide 10: Visualization
Specialized interpretation software can takes advantage of the 3D nature of the data
  Used to speed up interpretation time
  Facilitates QC of horizon and fault interpretations
  Great displays to communicate to peers/managers
Notes: Another advantage of 3D data is that we can use volume visualization tools and techniques. There are some volume tools that speed up the interpretation process. There are a lot of tools for displaying the data and one’s interpretation. Here a major unconformity over an anticline was mapped. The shape of the interpreted horizon can be displayed as if a light source was positioned at different locations. On the right, the light is high above and just to the right of center. On the left, the light is at a low angle to the left (west). Shadows reveal different fine-scale features (e.g., minor offset faults).

## Slide 11: Planning a 3D Seismic Survey
Imaging Objectives
Target at 4500 m
Subsurface area 8 x 12 km
Anticline trap
Dips up to 8°
50 m resolution
Etc.
Business Needs
Field Parameters
Survey area
Fold
Bin size
Source array
Streamer length
Etc.
Notes: Now we’ll shift to the topic of designing and acquiring a 3D seismic survey. The driver is one or more business needs – such as where to locate an exploration or production well. The business needs set the imaging objectives. The imaging objectives determine the field parameters for seismic acquisition.

## Slide 12: Image Area and Survey Area
Subsurface area to be imaged
Depth of the target
Maximum structural dip
Required lateral resolution
Area of a 3D Survey depends on:
Survey Length
4.5 km
4 km
Survey Width
Survey Area
Image
Area
Target Depth
Notes: The area covered by a 3D survey always has to be bigger than the area that you need to map. The first step is to define what you need to image (e.g., the crest of the anticline shown on slide 10). Then, you have to know the depth of your target and its maximum structural dip.
Given these, we can figure out the surface area so that we: (1) record arrivals from dipping reflectors, and (2) maintain lateral resolution near the map edges. For small surveys, this extra recording area can mean that the survey has to occupy double the area that you intend to map.

## Slide 13: Determining Surface Area
Ground Surface
KEY EFFECTS
  DIPPING LAYERS
  INCREASING DEPTH
  INCREASING DIP
  DIFFRACTIONS
Desired Image Area
Notes: Here is a cross-section showing three (3) HC levels that we want to image. To determine the surface area for a 3D survey, we have to consider:
  the fact that the layers dip
  the targets have different depths
  the structural dip increases with depth
  we can have diffractions generated, especially near the edges of the image area.

## Slide 14: Determining Surface Area
Desired Image Area
APERTURE
Angle of Incidence = Angle of Reflection
(just like shooting pool)
Ground Surface
KEY EFFECTS
  DIPPING BEDS
  INCREASING DEPTH
  INCREASING DIP
  DIFFRACTIONS
Notes: When there are dipping beds near the edge of the image area, we need to extend the surface coverage so that we capture the reflected energy. This extra region on the surface is referred to as the aperture.

## Slide 15: Determining Surface Area
Desired Image Area
Ground Surface
KEY EFFECTS
  DIPPING BEDS
  INCREASING DEPTH
  INCREASING DIP
  DIFFRACTIONS
DEEPER TARGETS REQUIRE MORE APERTURE
APERTURE
Notes: As our target gets deeper, even if the dip remains constant, the aperture gets bigger.

## Slide 16: Determining Surface Area
STEEPER DIPS REQUIRE MORE APERTURE
Desired Image Area
Ground Surface
KEY EFFECTS
  DIPPING BEDS
  INCREASING DEPTH
  INCREASING DIP
  DIFFRACTIONS
APERTURE
Notes: As the structural dip gets larger, so does the extra surface coverage. More dip means more aperture.

## Slide 17: Determining Surface Area
We need to record diffraction energy
Desired Image Area
Ground Surface
KEY EFFECTS
  DIPPING BEDS
  INCREASING DEPTH
  INCREASING DIP
  DIFFRACTIONS
APERTURE
Notes: We can also have a structural or stratigraphic ‘disruption’ near the edge of our image area that generates a diffraction hyperbola. A small fault is shown on the left. We have to have enough surface coverage to capture diffraction energy out to about 30°. Thus, our aperture has to satisfy this requirement as well.

## Slide 18: Impact of Aperture
Aperture Included in Processing
NO Aperture Included in Processing
Desired Image Area
Notes: This slide shows the impact of having proper aperture. We want good data for the entire length of the seismic line. If our surface coverage was limited to the length of the image area, we would not get good imaging at either end. This is because the data needed for good imaging at the ends was not acquired. However, if the survey area was enlarged to include the required aperture, we get the line on the bottom. Note how the geology is more clearly represented on the lower line.

## Slide 19: Extra Line Length for Fold Build-Up
Desired Image Area
Ground Surface
EDGE OF IMAGE
EDGE OF APERTURE
EDGE OF SURFACE COVERAGE
APERTURE
FOLD BUILD-UP
FOLD
Full
Notes: There is one (1) more factor to consider. We want full fold (maximum number of traces to sum) at the edge of the aperture region. Thus, we have to add surface area to account for fold build-up at the start of a line AND fold drop-off at the end of a line. The term used for this extra surface coverage is TAPER.
Aperture has to be added to all sides of a survey. Taper is only added where fold builds-up or drops-off.

## Slide 20: What is the Proper Balance?
Excellence
in Data
Quality
$$$
$$$
$$$
$$$
$$$
Boosting
Data Quality
Is Very Costly
Saving Money
Compromises
Data Quality
Notes: The challenge in survey design and acquisition is obtaining the proper balance between cost and data quality. Often, we can get excellent data quality, but it would cost too much. Thus, the survey designer has to compromise data quality to stay within budget. We want to have enough data quality to be able to answer the current business needs and needs that may come up for about 8 years (the typical shelf life for a survey). The “accountants” don’t want us spending more than we have to. There is no sense in spending money for seismic data if those data are not going to be good enough to help us.

## Slide 21: Field Operations
5 km
C.I. = 50 m
1700
1600
1400
1350
1500
1600
1650
Subsurface
Area to Image
How would we acquire this offshore survey?
Notes: Let’s say we have an offshore anticline that we want to image. Given the subsurface area we want to image, we can use a set of equations to get the surface area (done in exercise). How exactly we would have a survey boat acquire the data?

## Slide 22: Field Operations
5 km
C.I. = 50 m
1700
1600
1400
1350
1500
1600
1650
Think Zamboni Machine
Notes: Think of a Zamboni machine – the machine used to recondition ice at ice hockey games. The Zamboni does not make tight turns, like you might make moving grass with a push lawn mower. The Zamboni’s first pass is down the center ice, then returns along the side board. Then, the Zamboni goes just off its path near the center pass, etc. A seismic vessel does similar loops to cover the survey area.

## Slide 23: Summary
Land Seismic
The source produces ground motion that is reflected in the subsurface and then recorded by geophones. Typically, the source of ground motion is vibroseis and occasionally dynamite.
Notes: Summary of a land seismic survey

## Slide 24: Summary
Marine Seismic
The source is usually compressed air, producing a pressure wave that is reflected in the subsurface and recorded by hydrophones that are pressure detectors. The efficiency acquiring a marine 3-D survey is produced by the boat towing multiple source arrays and multiple streamers.
Notes: Summary of a Marine Seismic survey

## Slide 25: Summary
Survey Design
  To properly image and migrate dipping reflectors, the acquisition layout must be designed to record the data over a large enough area that reflections from the zone of interest are properly represented in the data.
  This also includes recording enough reflection time that the unmigrated image is captured. Dipping reflectors must have sufficient horizontal sampling that they can be properly migrated.
  In noise-problem areas, the design must attenuate as much noise as possible, enhance signal, and properly sample remaining noise for removal by processing.
Notes: Summary

## Slide 26
Questions?
Notes: SLIDE 18.25