## Slide 1: Determining Survey Area
Subsurface Area to be Imaged
Your Task:
  You will go through some simple calculations to determine the surface area required for a seismic survey that will fully image the subsurface target area.
24 km
20 km
C.I. = 5 ft
Notes: A review of exercise 18.

## Slide 2: 3D Seismic Survey Area
Step | Action
1 | The maximum offset (the distance behind the boat for the last receiver) equals 1.5 times the maximum target depth. OffsetMax = 1.5 * DepthMax = __________
2 | Fold taper is the distance we have to acquire so that we can build up to the maximum fold. This is one factor that makes the surface area larger than the image area at depth. The fold taper distance has to be added when the boat is beginning a swath of lines and when it is ending a swath of lines. Taper = 0.5 * OffsetMax where: Taper = the survey taper in meters OffsetMax = maximum offset distance (step 1) Taper = ___________________
1.5 * 3350 = 5025 m
0.5 * 5025 = 2512 m = 2.5 km
Notes: Steps 1 and 2 with my answers.

## Slide 3: 3D Seismic Survey Area
Step | Action
3 | Aperture = DepthMax * Tan θ where: Aperture = the survey aperture in meters DepthMax = maximum target depth (in meters) Θ = 30° (or the steepest stratigraphic dip) Hint: Tan 30° = 0.577 Aperture = ___________________
4 | We get better imaging in regions of steep dip by shooting in the direction of maximum structural dip. Based only on this factor, we should shoot the survey (check one): [ ] North – South [ ] East – West
3350 * 0.577 = 1933 m = 2 km
X
Notes: Steps 3 and 4 with my answers.

## Slide 4: 3D Seismic Survey Area
0 2
East-West = 28 km
2 + 24 + 2
North-South = 29 km
2.5 + 2 + 20 + 2 + 2.5
Surface Coverage
Aperture
Taper
Aperture
Taper
2
km
2
km
2
km
2
km
2
km
2
km
2
km
2
km
2.5
km
2.5
km
2.5
km
2.5
km
24 km
20 km
Notes: My answer for the surface coverage – 28 km by 29 km.

## Slide 5
Questions?
Notes: Slide SOLU Ex-18.5