## Slide 1: Petroleum Geology & Geophysics
3D Seismic Interpretation
Notes: This unit takes us through a 3D seismic interpretation workflow.

## Slide 2: Outline
Workflow for a Faulted Framework
  Performing a Reconnaissance
  Mapping Major-Offset Faults
  Mapping Horizons
  Mapping Small-Offset Faults
2
Notes: We will walk through a seven (7) step workflow (diagramed on slide 1 and the next slide). The four (4) main steps are listed here.

## Slide 3: Workflow for a Geologic Framework
Quick Recon
1
Recon
2
Interpret Major Faults
3
Generate Fault Planes
4
Interpret Major
Horizons
7
Utilize the Faulted Framework
6
Interpret Small-Offset Faults
Faulted
Framework
Small-Offset Faults
Extract
Horizon
Attributes
5
Horizons
Large-Offset faults
Notes: This is a possible workflow for interpreting 3D data so as to build a geologic framework. Note the four (4) main parts in the seven (7) steps:
Recon – Step 1
Interpret large faults – Steps 2 and 3
Interpret major horizons – Steps 4 and 5
Interpret small-offset faults – Step 6
Use the faulted framework – Step 7

## Slide 4: Step 1: Reconnaissance
Quick Recon
1
Recon
2
Interpret Major Faults
3
Generate Fault Planes
4
Interpret Major
Horizons
7
Utilize the Faulted Framework
6
Interpret Small-Offset Faults
Faulted
Framework
Small-Offset Faults
Extract
Horizon
Attributes
5
Horizons
Large-Offset faults
Notes: Step 1 is to perform a data reconnaissance.

## Slide 5: Survey Coverage
Crossline 9297
Crossline 801
N
Inlines run N-S
Inline numbers increase west to east
Crosslines run E-W
Crossline numbers increase south to north
Inline1481
Inline 4901
Data
NO
Data
NO
Data
Notes: Here is the survey we will use as an example. It is a very large survey from offshore Australia. On this map view, data exists where yellow is displayed. Inlines run approximately north-south, and inline numbers increase west to east. Crosslines run approximately east-west, and crossline numbers increase south to north.

## Slide 6: Displayed Amplitudes
Positive number on tape = RED
Gain can be adjusted
Spike at zero due to many traces with no data
Are these settings OK?
Polarity (positives = red)?
Gain (range in shades)?
Histogram of Amplitude Values
+
-
Notes: The histogram shows the amplitude distribution for the entire survey. There are a lot of zero (0) values due to all the missing traces (black areas on the previous slide). The color scale is such that positive numbers on the tapes are colored shades of red; negative numbers are blue. The representative line shows the results for these settings. For my taste, the gain is too high – too much deep red and deep blue.

## Slide 7: A Shallow Time Slice
What do you observe?
Time Slice 200 ms
N
A cut through the 3D data volume at a constant time value of 200 ms
Notes: This is a display of a shallow time slice – 0.2 seconds TWT or 200 ms below sea level. There is a blow-up of the region within the yellow rectangle. Notice the north-south stripes (lineations)? These are artifacts in the data (something not geologic) – in this case due to seismic acquisition. The north-south stripes indicate that the seismic vessel sailed north-south. Deeper in depth (or TWT) these stripes “heal” – diminish to the point of not being significant.

## Slide 8: Water Bottom Response
Inline 4301
Water Bottom
Reflection?
Polarity is such that an increase in impedance = BLUE, which is a negative number on tape
Poor shallow imaging due to acquisition artifacts
Water bottom can only be mapped where the water depth is greater than 40 meters {1500 m/s * (0.05/2)}
50 ms
Notes: Here is an inline, with south to the right. The water bottom reflection can be seen where the water depth is greater than about 50 ms. It is marked with the aqua line in the center of a trough (blue). Since the water bottom reflection (where detectable) is ALWAYS an increase in impedance, I know that the way the data are displayed that an increase in impedance is blue and a decrease in impedance is red.
The water bottom can be mapped where the water depth is >40 m (since the seismic velocity through water is 1500 m/s, and the water depth is .05 ms (TWT)).

## Slide 9: Visual Inspection: 4 Major Intervals
High Amplitude
Semi-Continuous
Hummocky
Low Amplitude
Sub-parallel
High Amplitude
Continuous
Low Amplitude
Sub-parallel
Inline 3001
Seal??
Reservoir??
1
2
3
4
Notes: The reconnaissance (or recon) is also a quick look at the geology. On this line, it appears that the stratigraphic section can be divided into four (4) gross packages – each with different reflection characteristics. Package 3, with low reflection amplitude, would have only small internal changes in velocity and density – hence a fairly homogeneous lithology. From outcrop studies, we link this to a massive marine shale that could be a good sealing lithology. Package 4 has high amplitude, continuous reflections, which suggests more inter-fingering of different lithologies. Again from outcrop studies, we associate this to marginal marine sands, silts, clay and coals. There may be reservoir-quality sands within this gross package.

## Slide 10: Visual Inspection
High Amplitude Structures Anticlines or Synclines?
Shallow
Deep
High Amp,
Continuous,
Faulted
Low Amp,
Subparallel,
Fill
Time 1200
3
4
Notes: Here is a time slice view at 1200 ms (1.2 seconds TWT). The dark red-black regions are loosely tied to package 4 – our possible reservoir rock. The paler regions are low seismic amplitude, more homogeneous and thought to be marine shales that could form seals. For now this is our initial working hypothesis that will need a lot of detailed examination.
Question: Where the #4 is displayed (left), is it on an anticline or within a syncline? We can quickly answer this if we shift up or down a few time slices. If the high amplitude region expands as we go deeper (higher TWT values like 1220 ms), then it is an anticline. This is what the cartoon figure to the right is meant to indicate. If the high amplitude region shrinks as we go deeper (higher TWT values), then it is an syncline.
For this study area, the feature where #4 is displayed is an anticline. It is a huge anticline, perhaps a great structural trap.
Sure there is a lot of uncertainty and “might be” or “perhaps,” but we have formulated some ideas in just a few minutes. It will take weeks of careful mapping and analysis to “mature” this anticline into something we present to management as a drilling target (prospect), but we have made a start.

## Slide 11: Step 2: Interpret Major Faults
Quick Recon
1
Recon
2
Interpret Major Faults
3
Generate Fault Planes
4
Interpret Major
Horizons
7
Utilize the Faulted Framework
6
Interpret Small-Offset Faults
Faulted
Framework
Small-Offset Faults
Extract
Horizon
Attributes
5
Horizons
Large-Offset faults
Notes: Let’s move on to Step 2. We want to start by interpreting large-offset faults. I’ll define large-offset in a minute. Step 2 is to interpret fault “sticks” on a several dozen vertical lines and time slices. Then, Step 3 will take the sparse fault “sticks” (2D lines) and turn them into continuous fault planes (3D surfaces).

## Slide 12: Large- to Moderate-Offset Faults
Seismic interpreters speak of fault offset in terms of a seismic peak or trough time duration
  Offset of more than one (1) peak or trough = Large-offset
Moderate-Offset Fault
½ of a peak or trough (or more)
Large-Offset Fault
One (1) peak or trough or more
  Offset of more than ½ of a peak or trough = Moderate-offset
Notes: As a seismic interpreter, I consider fault offset as compared to the time duration of a peak or trough. If the offset is between ½ to one (1) peak or trough, I consider it a moderate-offset. If the offset is one (1) peak or trough or more, I consider it a large-offset. If the offset is less than ½ a peak or trough, it would be difficult to identify with seismic data – difficult, but not impossible.

## Slide 13: Major Faults
Profile (Vertical) View
  Consistent breaks in reflections along a dipping plane
  Boundary between zones of different reflection dips
2D or 3D
3D only
Time Slice View
  Boundaries between different reflection packages
  Zones of low continuity seen on coherency-type data
Notes: For 2D or 3D seismic, we can view and interpret on vertical profiles. For 2D data, we have individual lines to work with. For 3D data, we can view and interpret on inlines, crosslines or arbitrary (zig-zag) traverses through the data volume. For 3D, you can use lines that are oriented along structural dip or strike - you are not limited to the acquisition line geometry.
For 3D data, one can also cut the data volume horizontally to view and interpret the data. If the seismic has a vertical scale of TWT, then we can view TIME slices, e.g., 1000 ms. If the seismic has a vertical scale of feet or meters, then we can view DEPTH slices, e.g., 5000 ft.

## Slide 14: Another Benefit of 3D Data
We can generate a new data volume based on the cross-correlation of one trace with its neighboring traces
This process was originally patented by Amoco with the name ‘coherency data’
White means a trace and its neighbor trace are very similar
1100 ms
Dark means a trace and its neighbor trace are NOT similar
Notes: In the previous lecture (Lecture 18), we talked about generating new data volumes, such as coherency (cross-correlation values). For interpreting faults, looking at time (or depth) slices in the coherency volume is very beneficial. Linear bands of low coherency are possible fault traces. Faults can be picked in a coherency volume in the same way that they are picked in the reflection amplitude volume.

## Slide 15: Coherency-Type Data
White = High Correlation
Black = Low Correlation
1160 ms
Faults
Poor Data, Low Amp, or Complex Structure/
Stratigraphy
Notes: Here is the 1160 ms time slice from the coherency volume in our Australian data set. Several dark lineations indicate the presence of fault traces. Regions with a lot of dark shades, such as where the green arrow is pointing, tell me that neighboring traces are not similar. This could be due to poor seismic imaging (poor acquisition or processing) or stratigraphic complexities. One (1) stratigraphic cause of low coherency is that these are relative thin zones (<500 m), and so will appear and disappear quickly as ones moves shallower or deeper on time slices. Major faults have significant depth ranges – they persist as you pan time slices. Fault lineation will “walk” slightly as you pan time slices since most faults are not perfectly vertical.
The faults at the top of this time slice dip down to the southeast. Thus, if we panned to deeper time slices, the black lineation would “walk” to the southeast.

## Slide 16: Fault Mapping Process
Start by manually interpreting the approximate position of faults on a few vertical sections
Post the generation 1 picks on a time slice and correlate individual fault traces on the time slice views of the data
Post the generation 2 picks on the vertical lines and refine the faults
Generation
1
Generation
2
Generation
3
Notes: Different interpreters have different methodologies. My method is to make three (3) passes at interpreting major faults – I use the term “generations.” The words here describe my method – the next series of slides illustrate my technique.

## Slide 17: Gen. 1: Manually Interpret some Lines
  Consistent breaks in reflections along a dipping plane
  Boundary between zones of different reflection dips
Inline 1800
Notes: For generation 1 (first pass), I use a single fault and mark candidate fault planes on several vertical profiles. I’ll give this fault a name of Gen-1. In marking fault Gen-1, speed rather than accuracy is my goal – I’ll be concerned about accuracy in generation 2 and 3. I look for: (1) Consistent breaks in reflections along a dipping plane, and (2) the boundary between zones of different reflection dips. Here on inline 1800, I have marked three (3) faults. I’d work several other inlines, perhaps jumping 100 inlines at a time (e.g., 1900, 2000, 2100).

## Slide 18: Gen. 1: Manually Interpret some Lines
  Four (4) Inlines were interpreted with a ‘generic’ fault
  Four (4) Crosslines were interpreted with a ‘generic’ fault
Xline 4600
Notes: Here is a crossline. I’ve marked two (2) candidate Gen-1 fault planes. The one on the right looks to be a normal fault, while the one on the left appears to be a reverse fault.
I interpret a total of four (4) inlines and four (4) crosslines (for this demo). Normally I would interpret more lines, including several traverses along structural dip.

## Slide 19: Generation 1 Faults
Perhaps there are some fault patterns starting to emerge?
Seismic ‘wiggles’ turned off
Notes: Here is my status after Generation one. This shows the boundaries of the seismic cube and my Gen-1 fault sticks - the seismic wiggles are turned off. So I can see the fault sticks in 3D space – neat! Don’t feel bad if you don’t see much of a pattern – I don’t at this stage – but wait…

## Slide 20: Gen. 2: Interpret on Time Slices
  Optimize the display
Reflection Amplitude
Coherency
Co-Rendered Amplitude + Coherency
1160 ms
Notes: I am ready to start Generation 2 (second pass interpretation). I’ll use time slices for my generation 2 fault interpretation. The software I use (VoxelGeo by Paradigm Geophysical) allows me to co-render two (2) data volumes. The display on the right is generated in the following way: (1) First, the reflection amplitude slice (upper left) is “painted” on the screen; (2) then the coherency slice (lower left) is over-posted on the screen – but using a transparency function. If the coherency is high, the coherency data is made transparent so the amplitude data is seen. If the coherency is quite low, the coherency is made opaque so that black is displayed. The user can adjust the transparency for intermediate coherency values, getting light shades of grey. I find that the time slice displayed on the right is a great way to combine the strengths of both data volumes and facilitate fault interpretation.

## Slide 21: Gen. 2: Interpret on Time Slices
  Post first generation fault intersections
  Boundaries between different reflection packages
  Start mapping individual faults (yellow, aqua, etc.)
1160 ms
Notes: On a time slice, I post the Gen-1 fault – it shows up as small green squares. These are where my quick-pick Gen-1 fault sticks intersect the time slice – here the 1160 time slice. Now, I’ll define a number of faults (like 12) and assign each a different color.
See the three (3) green square close to black lineations? The one near the top-center has very strong evidence for being a significant fault; I’ll make this my yellow fault. Similarly, I will mark a cyan fault, an orange fault and a magenta fault. Remember – these are still only candidates – I’m not finished with them. I’m more interested in positioning my color lines as accurately as possible, but some fine-tuning is yet to take place. At this point, I’m ready to move the faults up or down, perhaps by 100 ms.

## Slide 22: A Deeper Time Slice (60 ms deeper)
1220 ms
1220 ms
First Generation Picks (green)
Second Generation Picks
Notes: Here is the 1220 ms co-rendered time slice – 60 ms deeper. If the interval velocity at this depth averages 3000 m/s, then this would be about 90 m deeper.
On the left, only the Gen-1 fault (green squares) are displayed. On the right, the color-coded generation 2 faults are shown.

## Slide 23: Generation 2 Faults
Fault patterns are becoming much clearer and cleaner
A
D
C
B
E
Green “posts” = First Gen
“Fence rails” = Second Gen
Notes: Now I have displayed the Gen-1 fault sticks (green posts) and the generation 2 faults picked on six (6) time slices (the fence rails). I’ve labeled the faults A through E. Now the pattern is more obvious – correct? This would be about two (2) hours of work.

## Slide 24: Gen. 3: Refined Faults on Vertical Sections
Now we can correlate individual faults with confidence
D
C
B
Notes: Now I’m ready for generation 3 interpretation. I do this on vertical profiles – inlines, crosslines and traverses oriented along structural dip and strike. I turn off the Gen-1 fault sticks – they are not accurate and are no longer needed. I display the generation 2 fault traces, which show up as color-coded squares on vertical profiles. I define another set of faults using the same colors as my generation 2 faults. These will be my most accurate fault sticks, so I’ll keep these and (eventually) trash the gen 1 and gen 2 faults.
Note the magenta square (D) marks a fault plane that can be easily interpreted, with confidence, on this profile. Similarly there is an orange square (C) and cyan square (B) that allow me to pick faults on this profile.
NOTE: Since coherency data uses a correlation window (around 40 ms), there is some spatial smearing. Also resolution limitations make fault zones more smeared on slices than profiles in the reflection amplitude data. FINAL FAULT STICKS SHOULD ALWAYS BE INTERPRETED ON VERTICAL PROFILES.

## Slide 25: Generation 3 Fault ‘Sticks’
Now fault patterns are readily identifiable
“Fence rails” = Second Gen
Colored “posts” = Third Gen
Notes: This is a view of the data volume with only one time slice displayed, along with the generation 2 (rails) and generation 3 (posts) displayed. One can pan the display slice up and down to QC the generation 3 fault sticks. One can also display and pan vertical profiles to QC the generation 3 fault sticks.

## Slide 26: Step 3: Generate Fault Planes
Quick Recon
1
Recon
2
Interpret Major Faults
3
Generate Fault Planes
4
Interpret Major
Horizons
7
Utilize the Faulted Framework
6
Interpret Small-Offset Faults
Faulted
Framework
Small-Offset Faults
Extract
Horizon
Attributes
5
Horizons
Large-Offset faults
Notes: Once I am satisfied with my generation 3 fault sticks (the final product for Step 2), I move on to Step 3. I want continuous fault planes in 3D space – not just “fence posts” on a fraction of the possible lines. Fortunately, this step is quite easy using tools in all 3D seismic interpretation systems.

## Slide 27: From Fault Sticks to Fault Planes
There are software tools for going from individual fault ‘sticks’ to continuous fault planes
Time 1500
Fault ‘Sticks’
Time 1500
Fault Planes
Notes: All the interpretation software packages can convert sparse fault sticks into continuous fault planes. Some packages use a simple interpolation method. Some packages have “smart” interpolators that use something like a coherency volume to “condition” the interpolation. Usually there is a “confidence” parameter that the user can set for the “smart” interpolator.
In this image, the sparse generation 3 fault sticks are displayed on the left. The results of a “smart” interpolator with a 90% confidence factor is shown on the right. Note that the fault planes on the right have some gaps (easiest to see on the magenta fault). After doing some fault quality control (QC), I would use the interpolator with a much lower confidence number to infill the gaps. If important, I’d work on the fault tip-out points updip, downdip and laterally.

## Slide 28: Step 4: Interpret Major Horizons
Quick Recon
1
Recon
2
Interpret Major Faults
3
Generate Fault Planes
4
7
Utilize the Faulted Framework
6
Interpret Small-Offset Faults
Faulted
Framework
Small-Offset Faults
Extract
Horizon
Attributes
5
Horizons
Large-Offset faults
Interpret Major
Horizons
Notes: Now I’m ready to start working major horizons (sequence boundaries). I’ll be using an automatic horizon tracker, similar in many ways to a “smart” fault interpolator. I don’t want the tracker to correlate a horizon across a major fault – obviously. THAT IS WHY WE ALWAYS WORK THE MAJOR FAULTS FIRST.
As indicated, horizon interpretation has two steps (step 4 and 5). Step 4 is to generate the horizons using manual interpretation plus a horizon tracker. Step 5 is to extract attributes on the interpreted horizon surfaces – the reason for this will become clear.

## Slide 29: Major Horizons
We identify major horizons by:
  The termination of reflections (onlap, downlap, erosional truncation, toplap)
  Changes in ‘seismic facies’ (texture)
Inline 1500
Notes: We identify major horizons by: (1) the termination of reflections (onlap, downlap, erosional truncation, toplap); and (2) changes in ‘seismic facies’ (texture).
For this demo, I will map the strong red peak at about 400 ms on the left of this view of Inline 1500. This green horizon separates a lower amplitude seismic facies above from a higher amplitude seismic facies below.
Here I have marked the peak (red) for about 1/3 of the displayed line. I “click” near the appropriate red. The horizon has been defined to be on a peak (red). The software takes my picks and “snaps” it to the local maximum (peak) automatically (unless I override the snap feature). Thus, I can click several points along the red peak and the software will: (1) interpolate between picks, and then (2) snap the green horizon to the local maximum. This allows for both speed and accuracy.

## Slide 30: From Inline to Crossline
Horizon Pick from Inline 1500
Xline 2000
The horizon pick on inline 1500 shows where the horizon should be on an intersecting crossline
Notes: This is crossline 2000. My pick on inline 1500 shows up as a green square where the two (2) lines intersect. This confirms which red peak I want to map on crossline 2000. I’ve manually picked the green horizon on the left 1/3 of this line. The red “splits” into a doublet and I’m not sure (yet) if I should correlate to the upper or lower local maximum in this doublet. I’ll worry that a little later.

## Slide 31: Initial Pick on Six Xlines
The horizon was interpreted on a total of six (6) crosslines using the picks on inline 1500 as starting points
Xline 2500
Notes: In this view, which shows crossline 2500, you can see that I mapped the green horizon on one (1) inline and six (6) crosslines. The spacing between interpreted crosslines is 100 (2000, 2100, etc.). Let’s see how well the computer can do tracking this peak – rather than me over-working the mapping.

## Slide 32: Initial Auto-Tracking
Given the seven (7) manually interpreted lines, an auto-tracker, set to a confidence level of 90%, has done a lot of correlation
Xline 2500
Notes: I used an auto-tracker set at a 90% confidence level. The green surface is what the computer picked in less than a second given my manual interpretation. The surface is color-coded by the horizon color – in this case green.

## Slide 33: Auto-Tracked Time-Structure
Crossline 2500
  Auto-tracked horizon with TWT color-coded
  Manual interpretation = green lines
Notes: Now I have color-coded the horizon surface by TWT (a proxy for depth). Highs are ‘hot’ colors while lows are ‘cool’ colors. I can QC the auto-picked horizon by looking for “step-changes” in color. Such step-changes could be fault offsets or a mis-correlation (horizon “bust”).

## Slide 34: ALWAYS – QC Auto-Tracking
Xline 2185
  Look at lines NOT manually interpreted
  Identify and correct ‘problem regions’
  Various editing tools exist
Region to Clean-Up?
Notes: The other horizon QC is to look at the green horizon on lines that were not manually interpreted. These can be any type of profile – inlines, crosslines or traverses. Here, most of the horizon looks reasonable, except in the center of the line. There is a doublet and sometimes the tracker has picked the upper local max and sometimes the lower local max. I would need to delete this area of “tracker indecision,” and manually pick more lines in this vicinity. Now is when I have to make the decision as to whether it is best to correlate the upper local max or the lower local max. By viewing the initial auto-tracked horizon on this and neighboring lines, I think I should correlate the upper local max.

## Slide 35: More Complex Horizons
View 17
  The green horizon on the last few slides was quite simple to interpret
  For complex horizons, the process is similar but performed in ‘patches’
    Manual + auto-pick each fault block
    Manual + auto-pick each stratigraphic feature
    ‘Stitch’ the ‘patches’ together
Patch #1
Patch #2
Patch #3
Notes: This green horizon is relatively shallow and not broken by many faults. Where horizons are more complex with many fault offsets, we work individual fault blocks one by one.
For the TWT color-coded horizon surface shown here, I would divide the region into three (3) patches. I’d work the fault block labeled patch 1 first: (1) Manually pick the horizon on several lines, (2) Run the auto-tracker within a polygon I define based on the fault surfaces, and then (3) I would work patch 2 and follow that by working patch 3.
This is another reason for interpreting the major faults first, so I know where individual fault blocks exist.

## Slide 36: Base Reservoir Horizon
  Base of reservoir horizon color-coded by TWT
  About twelve (12) fault planes
  What about small-scale faults?
Xline 5100
Notes: Here is a display of a horizon mapped at the base of the main reservoir zone in our Australian data set. About twelve (12) fault planes can be seen rising above the horizon surface. The hot colors indicate a major anticline – the one I noticed during the recon Step 1 (slide 10). The size and position of this possible structural trap is well represented. Of course, I also mapped the top of the reservoir zone.

## Slide 37: Step 5: Extract Horizon Attributes
Quick Recon
1
Recon
2
Interpret Major Faults
3
Generate Fault Planes
4
Interpret Major
Horizons
7
Utilize the Faulted Framework
6
Interpret Small-Offset Faults
Faulted
Framework
Small-Offset Faults
Extract
Horizon
Attributes
5
Horizons
Large-Offset faults
Notes: Once we have several/many major horizons mapped, we can prepare to work on small-offset faults. Step 5 has us extract some horizon surface attributes – measurable characteristics of the surface. These attributes, such as horizon dip, help us to QC the horizon interpretation. They will also set us up for Step 6 where we work smaller-offset faults.

## Slide 38: Base Reservoir Horizon Dip
Crossline 5100
Dip
  Derive surface attributes from an interpreted horizon
  For example: interpreted horizon dip, azimuth, or curvature
  Units of dip = ms/trace
HORIZON DIP
White = low dip
Dark = high dip
Notes: What is displayed here is the local dip on the base reservoir interpreted horizon. Dip is calculated by having the TWT at a reference trace and then looking at the TWT difference for the neighboring eight (8) traces. The maximum absolute dip is written to a new surface at the reference trace X,Y location. This calculation is done for every trace where the horizon has been mapped. The units of horizon dip are milliseconds per trace spacing.
On this display, low dip is white. As dip increases, the color varies towards darker shades of grey. Fault offsets will show up as dark lineations. The advantage of horizon dip is that faults with rather small offsets can be detected (less than ½ of a peak or trough). Surface attributes can also be used to check for errors in mapping each horizon – stair-step changes due to a mis-correlation rather than a fault offset.

## Slide 39: Step 6: Interpret Small-Offset Faults
Quick Recon
1
Recon
2
Interpret Major Faults
3
Generate Fault Planes
4
Interpret Major
Horizons
7
Utilize the Faulted Framework
6
Interpret Small-Offset Faults
Faulted
Framework
Small-Offset Faults
Extract
Horizon
Attributes
5
Horizons
Large-Offset faults
Notes: Step 6 uses surface attributes extracted in Step 5 to map moderate- to small-offset faults.

## Slide 40: Near the Discovery
Xline 3500
Dip
  Some faults can be extended
  Additional (small-offset) faults can be mapped
Fault Can Be Extended
Fault Can Be Added
Correlation “Bust”
Notes: This is a portion of the base reservoir horizon dip map, as shown in slide 38. The larger-offset faults mapped in Steps 2 and 3 are the color-coded near-vertical planes. Note how the hot pink fault surface probably extends further to the right, as indicated by the relatively high surface dip (black) (green arrow). There is a possible unmapped fault further to the right (magenta arrow). The two (2) segments of the yellow fault should be connected. The black zig-zag to the south of the yellow fault (pink arrow) is probably due to a horizon correlation “bust” – as shown in slide 43.
Let’s look at the possible unmapped fault (magenta arrow).

## Slide 41: A Small-Offset Fault
Xline 2553
Xline 2553
Xline 2553
  Horizon dip suggests the presence of a small-offset fault
Notes: Here is crossline 2553, which cuts E-W across the unmapped fault. It does appear that the mapped horizon and the reflections have a slight offset that is hard to identify without the interpretation. This line is more along a strike orientation relative to the possible fault trend.

## Slide 42: A Small-Offset Fault
Inline 1851
Inline 1851
  Horizon dip suggests the presence of a small-offset fault
Notes: Here is inline 1851, which cuts N-S across the unmapped fault. This profile has better evidence for a small offset in both the mapped horizon and the reflections. This line is more along a dip orientation relative to the possible fault trend.

## Slide 43: Correlation “Bust”
Xline 2241
Auto-tracker has “jumped” one cycle
  Horizon dip suggests the presence of an interpretation error, here a jump one peak too deep
Notes: On the inset map of horizon dip there is a dark band that is oriented approximately along and inline and then swings to the left at a right angle. This has the characteristics of a correlation bust. Xline 2241 is where the green dotted line is shown on the map. This line shows the mapped horizon, and the horizon “jumps” one cycle too low at the right side (east). This error can now be corrected by deleting the auto-picked horizon in this region, adding some extra manually interpretation, and the re-running the auto-tracker.

## Slide 44: Step 7: Utilize the Faulted Framework
Quick Recon
1
Recon
2
Interpret Major Faults
3
Generate Fault Planes
4
Interpret Major
Horizons
7
Utilize the Faulted Framework
6
Interpret Small-Offset Faults
Faulted
Framework
Small-Offset Faults
Extract
Horizon
Attributes
5
Horizons
Large-Offset faults
Notes: Going through these seven (7) steps results in a fairly accurate faulted framework (or geologic framework). Of course there can be a lot of iteration and going back to correct fault or horizon interpretation. As you see, we have some nice tools to help us get quality products in a reasonable amount of time. The quality is insured by QC-ing the interpretation as it is being done. Speed and accuracy increase as a person does more and more interpretation and gains experience with the various tools.

## Slide 45: Generate a Geologic Framework
Proper mapping of all major horizons and faults
Horizon-fault intersections are correctly handled
Fault-fault intersections are correctly handled
Intervals between horizons that can be analyzed
Horizon A
Horizon B
Horizon C
Horizon D
Red
Fault
TOL
Base
Notes: Here is a display of some of the final results for part of the Australian data set. The red fault is very important for a producing field on the crest of the anticline. The green horizon, labeled TOL, is the top of the reservoir zone. It is the boundary between our gross package 3 (low amplitude - seal) above and package 4 (high amplitude – reservoir) below from our data recon (slides 9 and 10).
A good seismic interpreter will end up with: (1) Proper mapping of all major horizons and faults; (2) Horizon-fault intersections are correctly handled; (3) Fault-fault intersections are correctly handled, and (4) Intervals between horizons that can be analyzed.

## Slide 46
Questions?