## Slide 1: Petroleum Geology & Geophysics
20. Stratigraphic Hierarchy
Lamina
Lamina sets
Beds
Bed Sets
Parasequences
Parasequence Sets
Sequences
Sequence Sets
Thin Units, Limited Extent
Thick Units, Widespread
Core
Logs
Seismic

## Slide 2: Stratigraphy: Outcrops & Modern Deposits
The fundamentals of stratigraphy come from the study of modern deposits and sedimentary outcrops
Ireland
Grand Canyon
Modern Deposits
Measured
Sections
Notes: The fundamentals of stratigraphy come from the study of modern deposits: 1) looking at delta systems, beaches, rivers, deep marine deposits, and, 2) Sedimentary outcrops – where deposits from the geologic past can be viewed and analyzed.

## Slide 3: Stratigraphy: Well Data
Wells allow us to study subsurface stratigraphy using cores and logs, at single or multiple locations
AAPG©1990 reprinted with permission of the AAPG whose permission is required for further use.
Well Log Correlation
Well Logs
Core
Van Wagoner et al., 1990
Notes: Another source of stratigraphic data comes from wells. We can cut cores during the drilling process. Also, we can lower measuring devices down well bores and collect data as a function of depth – logs. If we have several wells in an area (like within a field), we can correlate the well logs – break the stratigraphy into units based on rock type (formations) or geologic time (chronozones).

## Slide 4: Stratigraphy: Seismic Data
Delta Front
Delta Plain
Delta Slope
Basinal Shales
Basinal Shales
Deep Water Fans
6
7
5
4
3
2
1
8
We can also analyze subsurface geology using seismic reflection data.
Notes: We can also study the stratigraphy within a basin using seismic data. This interpreted line shows a major deltaic system with: delta plain deposits (brown), delta front deposits (yellow), delta slope deposits (light green), basinal shales (dark green), and deep-water fans (orange). The stratigraphic interpretation of seismic data is the focus of the next several lessons in this course.

## Slide 5: Stratigraphic Analysis
Depositional Model
Seismic Observations
are turned into
Stratigraphic Predictions
using Depositional Models
Seismic-Based EOD Map
Predicted Lithologies
Notes: Our basic procedure is like what we did for structural analysis. We make observations – upper left is a seismic-based map from Gulf of Mexico (pink = salt walls). The sediment from updip gets funneled through the gap, and the yellow depositional bodies are interpreted to be distributary deep water fans. Given these observations, we think of an appropriate depositional model (center). The model is based on outcrops, flume experiments, drilling similar features, etc. Given the depositional model, we predict the vertical and lateral distribution of sands. Thus, we infer the lithofacies for the two (2) black lines on the Seismic-Based EOD (Environment Of Deposition) Map.

## Slide 6: A Caution about Seismic Images
Seismic data has a resolution that is not as fine as most stratigraphers are use to working
Units are often 10s to 100s of meters thick
0
500
meters
Notes: Do not forget that seismic data has lower resolution than stratigraphers are use to working with. Units are often 10s to 100s of meters thick.

## Slide 7: Scale of Stratigraphic Correlation
Using Outcrops or Cores
  Visually correlate laminae and beds
  Units are centimeters thick
Resolution
High
Low
Areal Extent
Very
Local
Basin-
wide
Using Well Logs
  Pattern correlation of log markers
  Units are meters thick
Using Seismic Data
  Seismic correlation of bedsets and larger units
  Units are tens to hundreds of meters thick
20
40
0
cm
60
Well A
Well B
Well C
3
6
0
9
12
meters
100
200
0
meters
300
Notes: The scale of our stratigraphic analysis depends on the tool that we are using. Working with outcrops or cores, we can: visually correlate laminae and beds, and units are centimeters thick. Working with well logs, we can: 1) Use log pattern characteristics to correlate log markers; and 2) Units are meters thick.
  Working with seismic data, we can: 1) Generate seismic correlations of bedsets and larger units, and 2) Units are tens to hundreds of meters thick.
  Outcrops and cores have high resolution, but limited areal extent. Seismic data has low resolution, but can have basin-wide areal extent.

## Slide 8: The STRENGTHS of Seismic Data
Good areal coverage
Able to image major depositional units
Able to identify potential source, reservoir, and seal units
Provides a stratigraphic framework within which other data can be understood
  Well data
  Basin fill history
  HC systems
Vail et al., 1977a
AAPG©1977 reprinted with permission of the AAPG whose permission is required for further use.
Notes: A list of some of the strengths of seismic data for stratigaphic analysis.

## Slide 9: The WEAKNESSES of Seismic Data
Limited vertical and lateral resolution: can’t resolve “small” features
Stratigraphic interpretation is limited by the quality of the seismic data/imaging
Seismic responses are non-unique – e.g., low amplitude could be a massive sand or a thick shale
In new areas, we often have to ‘jump’ correlate from adjacent outcrops or basins
Post-depositional erosion and/or structuring can hamper stratigraphic correlations and paleo-depositional reconstructions
Typically we can’t “see” hydrocarbons
Notes: A list of some of the weaknesses of seismic data for stratigaphic analysis.

## Slide 10: Our Methodology
OTC©1979 reprinted with permission of the OTC whose permission is required for further use.
General
Observations
Modern Examples
Outcrop Studies
Subsurface
Learnings
Process Analysis
Local Data
Cores
Logs
Seismic
Seismic-Based
Interpretation
Conceptual
Models
Mass
Transport
Complex
*
*
* Ramsayer, 1979
Notes: This slides shows our basic methodology for stratigraphic analysis. First, we make general observations from modern deposits, outcrop studies, laboratory flumes, and subsurface data. From these observations, we develop models of deposition. We obtain data in the location we are interested in, and we make seismic-based stratigraphic predictions.

## Slide 11: Stratigraphic Hierarchy
There is a hierarchy of stratal units (packages) that extends from local, thin lamina to regional, thick depositional sequences and sequence sets
Lamina
Lamina sets
Beds
Bed Sets
Parasequences
Parasequence Sets
Sequences
Sequence Sets
Thin Units, Limited Extent
Thick Units, Widespread
Core
Logs
Seismic
Our focus
for now
Notes: An important concept for us is that there is a hierarchy of stratal units. These units extend from local, thin lamina to regional, thick depositional sequences and sequence sets. These units are at different scales in terms of thickness, geologic time duration, and 3-D lateral extent. The smallest unit is a lamina.
Several lamina form the next scale unit – the lamina set
Several lamina sets form the next scale unit – the bed
Several beds form the next scale unit – the bed set
and so forth up to several depositional sequences forming a depositional sequence set.
Cores give us local information on the lamina to bed scale of deposits. Well logs give us information on bed to sequence scale of deposits, and seismic data gives us information on parasequence to sequence set scale of deposits.

## Slide 12: Stratigraphic Hierarchy
Each stratal unit, with the exception of lamina, is a genetically related succession of strata bounded by chronostratigraphically (time) significant surfaces.
Each surface is a single, physical boundary that everywhere separates all of the strata above from all of the strata below. The strata below the boundary are, for the most part, older than the strata above.
These hierarchical units share two (2) fundamental properties:
Beds
Bed Sets
Lamina Sets
Notes: The photo with the insert shows deposition from the lamina set to the bed set scale. All the hierarchical units share two (2) fundamental properties: 1) Each stratal unit, with the exception of lamina, is a genetically related succession of strata bounded by chronostratigraphically (time) significant surfaces, and 2) Each surface is a single, physical boundary that everywhere separates all of the strata above from all of the strata below. For the most part, the strata below the boundary are older than the strata above.

## Slide 13: Beds Are Bounded by Bedding Surfaces
Bedding
Surfaces
Mark a Break
Or Change in
Deposition
Bed 1
Bed 4
Bed 3
Bed 2
Bed 6
Bed 5
Notes: This photo illustrates stratal surfaces at the scale of bed boundaries. Each bed is bounded at its top and base by bedding surfaces. Here, the bedding surfaces are easy to identify. These bedding surfaces can mark: 1) a break or gap in deposition - i.e., a time of non-deposition, perhaps an interval between storms, OR 2) they can mark a change in deposition - i.e., a shift in a channel or a change in flow velocity.

## Slide 14: Beds Stack to Form Bed Sets
Bed Set 1
Bed Set 2
Bed Set Boundaries
Bed Set 1
Bed Set 2
Bed Set 4
Bed Set 3
Bed Set 5
Notes: Going up the hierarchy (up in scale), several genetically related beds form a bed set. There are bed set surfaces or boundaries that separate one bed set from the next.

## Slide 15: Bedsets Stack to Form Parasequences
The parasequence is the basic unit of cyclic deposition.
Foreshore
Upper Shoreface
Lower
Shoreface
Offshore/Lower
Shoreface
Offshore
Lower Cozzette
Palisade Section
20 ft
Shoaling
Upward
Pattern
Abrupt
Deepening
Abrupt
Deepening
GR Log
200
0
Parasequence
Boundary
Parasequence
Boundary
Notes: The next unit going up the hierarchy is the parasequence. For a parasequence, the surfaces of importance are flooding surfaces rather than surfaces of non-deposition or erosion. The parasequence is the basic unit of cyclic deposition. Lower order stratal units are usually attributed to episodic events (e.g., storms), but for parasequences and larger units, they are related to cyclic events (e.g., delta shifts or sea level oscillations).
The illustration is the summary of a measured section from a marginal marine setting. The base of the parasequence is placed where there is evidence for an abrupt deepening (change in paleobathymetry from relatively shallow to relatively deeper). Moving up within a single parasequence we see evidence for a shoaling upward pattern, here from offshore near the base of the parasequence to foreshore near the top. The top of this parasequence is marked by another abrupt deepening, in this case, from foreshore below to offshore above.

## Slide 16: A Parasequence
Prodelta
Stream mouth bar
Delta front
PSB
Shoaling
Upward
Pattern
Abrupt
Deepening
Outcrop Analog
Delta plain
Delta front
Definition:
A parasequence is a relatively conformable succession of genetically related beds or bedsets bounded by marine flooding surfaces or their correlative surfaces
Characteristics:
Shoaling succession of lithofacies in vertical section
Grain size increases upward
Parasequence boundaries or flooding surfaces represent surfaces above which there has been an abrupt shift to deeper-water facies
Parasequence boundaries approximate time lines and thus can be used to create a high-resolution sequence stratigraphic framework
Notes: This slide gives the definition and characteristics of a parasequence.

## Slide 17: Parasequences Stack into Parasequence Sets
Coastal Plain
Sandstones
and Mudstones
Shelf
Mudstones
Shallow Marine
Sandstones
Parasequence 4
Parasequence 3
Parasequence 1
Parasequence 2
Parasequence
Set
Marginal Marine Parasequences
Van Wagoner et al., 1990
AAPG©1990 reprinted with permission of the AAPG whose permission is required for further use.
Notes: This diagram is for marginal marine parasequences. Each individual parasequence shows progradation (building out) and aggradation (building up). A series of parasequences will show one of three stacking patterns:
(1) Progradational - where the shallow marine portion of each PS steps further basinward than
its predecessor - a regression;
(2) Retrogradational - where the shallow marine portion of each PS does not extend as far basinward
as its predecessor - a transgression;
(3) Aggradational - where the shallow marine portion of each PS extends about the same distance
into the basin as its predecessor - a somewhat static situation (still stand).

## Slide 18: Marginal Marine Parasequence Stacking
Location of Schematic
Log Response
SP Gamma
Progradational
Retrogradational
Aggradational
Sediment supply outpaces accommodation
Accommodation outpaces sediment supply
Balance between accommodation & sediments
Van Wagoner et al., 1990
AAPG©1990 reprinted with permission of the AAPG whose permission is required for further use.
Notes: Here the three types of parasequence stacking patterns are shown in cross-sectional view. On the far right is the log signature for the position of the red rectangle (sands are color-coded in the SP track):
- For a progradational stacking pattern sediment supply outpaces accommodation (space available to be filled with sediment)
- For a retrogradational stacking pattern sediment supply can not keep pace with accommodation (space is created too fast for the sediment supply to keep filed)
- For the aggradational stacking pattern sediment supply and accommodation are close to being in balance in which the amount of space being created is “just right” in terms of the sediment coming in.
More on accommodation in a later lesson.

## Slide 19: Depositional Sequence
Definition:
  A depositional sequence is a relatively conformable succession of
  genetically related strata bounded at its top and base by
  unconformities or their correlative conformities.
  (Vail and others, 1977; Mitchum, 1977)
Definition:
  A seismic sequence is a depositional sequence identified on a seismic section
  (Mitchum, 1977)
Characteristics:
  Parasequences and parasequence sets are the building blocks of sequences
  The sequence is the fundamental stratal unit for sequence-stratigraphic analysis
  (Mitchum, 1977)
Notes: Here is the definition for a depositional sequence, its characteristics, and the definition of a seismic sequence.

## Slide 20: Stratigraphic Hierarchy
Blackhawk and Castlegate Fms. (Campanian), Book Cliffs, Utah
PS = Parasequence
PSB = Parasequence Boundary
Fluvial
PS
PS
PS
PSB
SB
PSSB
SB
PSSB
Marginal
Marine
Marginal Marine
Fluvial
Sequence
PSSB = Parasequence Set Boundary
SB = Sequence Boundary
Notes: Here is a photo of the Blackhawk and Castlegate Fms. (Campanian) in the Book Cliffs of Utah. A sequence stratigrapher has interpreted stratal packages from parasequence scale up to sequence scale. He has also indicated the EOD – environment of deposition:
    - Parasequences (PS): light gray triangles on the right
    - Parasequence Boundaries (PSB): dotted light gray lines (also red & yellow lines)
    - Parasequence sets: yellow triangles on the left
    - Parasequence set boundaries (PSSB): short dashed yellow lines (also red lines)
    Sequences: dotted red lines near the center mark the sequence boundaries (SB)
    The sequences are from bottom to top:
    the top of one sequence
    a complete sequence (long dashed red line to long dashed red line)
    the start of a third sequence
Looking at the EODs, there are two abrupt shallowings (purple circles) e.g. fluvial on top of marginal marine at the sequence boundaries, and one abrupt deepening (green circle) e.g., fluvial on top of marginal marine, in this case about midway up the middle sequence.

## Slide 21
Questions?
Notes: Slide 20.21