## Slide 1: Exercise 20b
Mapping Top/Base of Reservoir
Generate Two Time Structure Maps
Your Task:
  Use the seismic lines from Exercise 19 to complete an interpretation of the top and base of the main reservoir zone in the Barracouta area.
Time 1100 ms
Amp + Coherency

## Slide 2: Introduction
In Exercise 19, you started a structural interpretation of the 3D seismic data. Now you are to map the top and base of the main reservoir. For now, we will use the TOL horizon as the top of the reservoir. The base reservoir horizon has been marked on several of the 3D lines given to you in Exercise 19.
The top and base horizons have also been marked on the 1100 ms time slice. Your task is to complete the mapping of both horizons and then generate two (2) time structure maps. These horizons will be used in Exercise 22 to get the thickness of the reservoir (in TWT thickness).
Notes: Setting up the exercise:
Same seismic as in Exercise 19
Goal for Exer 20b is to map two (2) horizons representing the top and base of the reservoir. This means using interpretation on several interpreted lines to complete the interpretation, and generating two (2) time structure maps.

## Slide 3: Two Approaches
3
Map the Top and Base simultaneously
Read/post the Top TWT
Contour the Top TWT
Read/post the Base TWT
Contour the Base TWT
Plan A
Plan B
More Time
Efficient
Map the Top completely
Map the Base completely
Read/post the Top TWT
Contour the Top TWT
Read/post the Base TWT
Contour the Base TWT
1a. Map the Top completely
1b. Map the Base completely
Notes: There are two (2) ways (plans of attack) to get this done. Plan A is to focus on each horizon in series – finish the Top before stating the Base, and then finish the Base horizon. Plan B is to work both horizons in parallel – at the same time. Since it takes time to find and fold the seismic lines, it is more time efficient to mark both horizons at the same time. Thus, Plan B should require less time to complete.
The steps once the two (2) horizons are the same:
2. Read TWT values for the Top horizon and post (write) them on basemap #2
3. Contour the TWT values for the Top horizon
4. Read TWT values for the Base horizon and post (write) them on basemap #2
5. Contour the TWT values for the Base horizon

## Slide 4: A Tie – Inline 1600 to Crossline 2800
Notes: The process for completing the horizon interpretation is the same as we used for fault mapping. We use a line intersection where one line has the interpretation and the other does not. We fold one line and place it on the other at the intersection point. Then, we transfer the interpreted horizon to the line without interpretation.
The slide shows Inline 1600 with both the Top horizon (cyan) and Base horizon (yellow) interpreted. We will work the intersection of this line with crossline 2800. Crossline 2800 is folded where it is intersected by Inline 1600 and aligned at the intersection point. This gives us a starting point for interpreting Crossline 2800. The animation shows the interpretation of the Top horizon for the eastern part of Crossline 2800. Not shown – but to be efficient, I would also mark and interpret the Base horizon (yellow).

## Slide 5: A Tie – Slice 1100 to Crossline 3400
Notes: This illustrates another way to extend an interpreted horizon. Time slice 1100 has the Top (cyan) and Base (yellow) horizons interpreted. We can use this interpreted time slice to mark the horizon on intersecting inlines (N-S) or Crosslines (W-E).
The animation shows Crossline 3400 folded and registered where its vertical plane intersects 100 ms. The cyan horizon is correlated on the Crossline from the west flank, to the crest of the anticline, and down the east flank. There is also a portion of the cyan horizon to the far west. The yellow horizon is also mapped on the crossline. The same method can be used for an Inline.

## Slide 6: Reading TWT Values
1000
940
920
950
1060
1310
Notes: Next you have to get TWT values for the Top (and Base) horizons at several locations along the vertical lines. Use the scale at the left or right edge of a line to measure the times. You can use EITHER the inlines or the crosslines – no need to use both, since the horizons have been tied. It is sufficient to read TWT values at each black vertical line that marks intersecting lines. The animation shows the first four (4) values along Xline 2500. As shown on the next slide, you write these values on basemap #2.

## Slide 7: Correlating Parasequences
1000
940
920
950
1060
1000
1000
Notes: Write the TWT values at the proper locations on basemap #2. This slide has them too large. After you get TWT for all the inlines OR crosslines, you can contour the values. Use a 100 ms contour interval.

## Slide 8: Exercise 20b
Steps:
  1. Complete the interpretation of the two horizons.
  Read/Post the TWT values for the Top Reservoir horizon
  Contour the TWT values for the Top Reservoir horizon
  Read/Post the TWT values for the Base Reservoir horizon
  Contour the TWT values for the Base Reservoir horizon
Notes: Here are the five steps for your reference.

## Slide 9: Exercise 20b
Questions?
Notes: Slide Ex-20b.7