## Slide 1: Petroleum Geology & Geophysics
21. Seismic Sequences
Beaubouef et al., 2003
AAPG©2003 reprinted with permission of the AAPG whose permission is required for further use.
From Vail et al., 1977
AAPG©1977 reprinted with permission of the AAPG whose permission is required for further use.

## Slide 2: Importance of Stratigraphic Info
Source rocks are typically organic-rich shales
Reservoir rocks are usually:
  sandstones or coarser clastics, or
  coarse-grained carbonates
Seals are commonly fine-grained shales or evaporites
Lateral HC migration can occur through sedimentary units with minimal porosity and permeability (sub-reservoir quality)
We need to understand the sedimentary fill within our area of interest
Sedimentary rocks are critical to oil & gas:
Notes: Sedimentary rocks are critical to our exploration for and exploitation of oil and gas. If we are to unravel details about the source, reservoir, seal, and migration pathways, we need to understand the sedimentary fill within our area of interest.

## Slide 3: Goal of Seismic Stratigraphy
Given seismic data we need to predict:
The location of rocks that will serve as sources, reservoirs, seals, and migration pathways, and
The rock properties associated with these
stratigraphic units
We need to:
Break out major depositional sequences
Predict their environments of deposition
Infer lithologies (rock types), and
Model how rock properties have changed from initial deposition to present-day burial depths
Notes: Focusing in on seismic data, we want to understand the stratigraphy within our area. We may have local well data, but sometimes we don’t have local wells. We often want to predict the location and rock properties.

## Slide 4: Depositional Sequence
Definition:
  A depositional sequence is a relatively conformable succession of genetically related strata bounded at its top and base by unconformities or their correlative conformities.
  (Vail and others, 1977; Mitchum, 1977; Van Wagoner, 1991)
AAPG©1977 reprinted with permission of the AAPG whose permission is required for further use.
Notes: The definition of a depositional sequence.

## Slide 5: Depositional Sequence
AAPG©1977 reprinted with permission of the AAPG whose permission is required for further use.
Relatively conformable succession of genetically related strata
Bounded at its base by an unconformity
Bounded at its top by an unconformity
Or their correlative conformities
Notes: This slide “unpacks” the definition using some animation.

## Slide 6: Seismic Sequence
Definition:
  A seismic sequence is a depositional sequence identified on a seismic section
  (Mitchum, 1977)
Or its correlative conformities
Bounded at its top by unconformities
Bounded at its base by unconformities
Or its correlative conformities
Notes: The definition of a seismic sequence. The animation applies to the interval that is shaded yellow.

## Slide 7: The Key
How do we recognize depositional sequences or seismic sequences?
By definition, they are bounded at least in part, by unconformities
Thus, we look for evidence for unconformities and use these surfaces to identify the boundaries between depositional sequences or seismic sequences
Notes: How do we recognize depositional sequences or seismic sequences? They are bounded in places by unconformities, so we look for evidence for unconformities and use these surfaces to identify the boundaries between depositional sequences or seismic sequences.

## Slide 8: Consider Working from a Photo
Pre-Cambrian
Paleozoic
The angular discordance between the Pre-Cambrian rocks and the Paleozoic rocks marks an unconformity that separates an older stratigraphic package from a younger stratigraphic package
Earlier phase of deposition
Later phase of deposition
Notes: Let’s consider how we might identify an unconformity using this photo. This is the north wall of the Grand Canyon. We can see evidence for major stratigraphic packages on the wall. Near the bottom of the North Wall, stratal packages are dipping down to the right (east). Towards the top of the North Wall, stratal packages are approximately horizontal. Around the magenta line, there is a significant angular discordance that is the evidence for a major unconformity. There was an earlier phase of deposition (Pre-Cambrian). Then, tectonics caused major tilting (down to east; up to west) and erosion. Next, there was a second phase of deposition (Paleozoic). The Paleozoics were deposited near sea level, but now are 6,000 to 8,000 ft above sea level, so there had to be a major uplift after the Paleozoic, which was the Colorado Plateau Uplift.

## Slide 9: Unconformity on Seismic Data
Notes: Here is a seismic section - but not from the Grand Canyon. Notice the change in dip of the reflections. Let’s mark where the more steeply inclined refectors terminate – green lines with arrow heads. Let’s mark where the shallower refectors terminate – dark green lines with arrow heads. Now let’s mark a boundary that separates the reflectors dipping steeply up to the left from those that are gently dipping up to the right - our convention for these boundaries is a yellow line.
What do you suppose this yellow line represents? An angular unconformity. The termination of reflections indicate a termination of stratal units, here probably parasequence (PS) or parasequence set (PSS) boundaries. As such, it is also satisfies our definition of a sequence boundary.

## Slide 10: Stratal Patterns: Base of a Sequence
Terminations at the Base of a Sequence
Older
Beds
Onlap
Onlap: Younger strata
terminate against more
inclined older strata
Older
Beds
Downlap
Downlap: Younger strata
terminate against less
inclined older strata
Sequence Boundary Lies Just Beneath
the Onlaps and Downlaps
Notes: There are two (2) types of terminations at the base of a sequence: onlap is where younger strata terminate against more inclined older strata, i.e., the younger strata have lower dip than the older strata, and downlap is where younger strata terminate against less inclined older strata , i.e., the younger strata have higher dip than the older strata. We mark the sequence boundary just beneath the onlaps and downlaps.

## Slide 11: Stratal Patterns: Top of a Sequence
Terminations at the Top of a Sequence
Younger
Beds
Erosional
Erosional Truncation: The
lateral termination of
strata by erosion
Toplap
Toplap: The lateral
termination of inclined
strata (updip direction)
Younger
Beds
Sequence Boundary Lies Just Above
the Erosional Truncations and Toplaps
Post-Depositional
Syn-Depositional
Notes: There are two (2) types of terminations at the top of a sequence: erosional truncation is where older strata terminate due to the post-depositional removal of some sediment, and toplap is where older strata terminate against an overlying surface mainly as a result of non-deposition (sediment bypass). This commonly occurs in coastal/shelfal depositional environments where base-level controls sediment bypass. Note that TE is post-depositional while Tp is syndepositional.
We mark the sequence boundary above the TE and Tp, as much as 1/2 cycle above. On seismic data, the response of the unconformity surface and the response of the terminating stratal units may interfere - thus we have a reason for marking the unconformity as much as 1/2 cycle higher than the terminations.

## Slide 12: Outcrop Example of Stratal Terminations
Clastics
Onlap
Carbonates
Erosion
Notes: Here is an outcrop from West Texas, just below center on the left are some carbonate stratal packages. At the right, center, are some younger clastic stratal packages. I’ve marked some stratal surfaces with red lines. We have the left edge of a major erosional channel in which: carbonates were eroded post-deposition, and clastics subsequently infilled the channel.

## Slide 13: Seismic Example of Onlap
Onlaps
Beaubouef et al., 2003
AAPG©2003reprinted with permission of the AAPG whose permission is required for further use.
Notes: Here is a beautiful example of onlap on a seismic section. There is a salt diapir further to the left; another diapir further to the right. Older sediments (mostly basinal shales) were deposited nearly horizontal and then tilted as the diapir rose. After the diapir stopped moving, the younger sediments infilled the low between two salt diapirs. The infilling sediments have a significant sand content, which result in higher seismic amplitudes.

## Slide 14: Outcrop Example of Downlap
Downlap
Notes: Another photo from West Texas. The upper part of the cliff is a prograding carbonate shelf (El Capitan), while the lower part of the cliff consists of deep water shales. There is an angular discordance (hidden by talus) marking a significant stratal surface separating: older, more horizontal basinal shales below, from younger, dipping basinward carbonate slope deposits above.

## Slide 15: Seismic Example of Downlap
Downlaps
Notes: Here is an old seismic line, but you can see about six (6) reflections (peaks/black) that terminate by downlap.

## Slide 16: Outcrop Example of Toplap
Toplap
Notes: This is an outcrop from Utah. The blue lines mark some (younger) stratal surfaces, and the red lines mark deeper (older) stratal surfaces. The geometry of the terminating red lines is what we call toplap.

## Slide 17: Seismic Example of Toplap
Toplaps
Toplaps
Notes: An old seismic line, but you can see two (2) sets of terminating reflections (peaks/black) that have toplap geometries.

## Slide 18: Sequences via Terminations
Sequence Boundaries are Identified by:
  Truncations or Toplaps at their tops
  Onlaps or Downlaps at their bases
Correlative
Conformities
Notes: Thus, we use a series of reflection terminations to identify unconformities. These unconformity surfaces, and their correlative conformities, break the seismic section into
a series of seismic sequences.

## Slide 19: Several Seismic Sequences
Purple SB to Orange SB = Orange Sequence
Orange SB to Blue SB = Blue Sequence
Blue SB to Green SB = Green Sequence
Green SB to Yellow SB = Yellow Sequence
Yellow Seq
Orange
Seq
Blue Seq
Green Seq
Notes: Here is an old seismic line on which five (5) seismic sequence boundaries (SB) and been marked. These five (5) boundaries define four (4) stratigraphic intervals – for four (4) seismic sequences. The Exxon convention is to refer to a seismic sequence by the color at the BASE of the sequence. Thus, the oldest sequence shown goes from the green SB to the yellow SB and is referred to as the Yellow Sequence.

## Slide 20: Lecture 21
Questions?