## Slide 1: Exercise 22
Generating an Isochron Map
Generating an Isochron Map
Your Task:
  Use the top and base of the reservoir that you mapped in Exercise 20b to generate a time-thickness (isochron) map.
Inline 1800

## Slide 2: Exercise 22
Objective
Using the top and base of the reservoir that you mapped in exercise 20b, you will generate an isochron (time-thickness) map. Such a map gives you the thickness of the reservoir interval and may help you determine the environment of deposition for this depositional sequence and then infer the lithologies.
Final Product
An isochron map used too define reservoir thickness.
Notes: Slide Ex-22.2
The exercise objective and final product.

## Slide 3: Introduction
You have defined the top and base of the primary reservoir. We will now start to analyze this depositional sequence.
Given the two (2) horizons, it is relatively simple to get the thickness of our reservoir interval using a manual approach. The steps are simple:
(1) measure the time thickness of the interval at a reasonable number of map locations,
(2) post the values on a basemap, and
(3) contour these values
Notes: Words that introduce the exercise. The students mapped the top and base of the reservoir in exercise 20b. They can generate an isochron map manually by going through the three (3) steps.
With software, generating an isochron map is even easier.
1 – the top horizon is gridded
2 – the base horizon is gridded
3 – a grid operation is used to subtract the two grids
4 – this difference grid is the time thickness; we would generate contours from this grid.

## Slide 4: Introduction
Your map will give the true vertical thickness in units of milliseconds. We can get an average interval velocity for this depositional sequence from the sonic log and thus estimate of the thickness in meters (or feet).
The thickness is important for calculating reservoir volume. It can also help in understanding the environment of deposition and how lithologies might vary away from the well location over the extent of the field.
Notes: The isochron is thickness in units of TWT (ms). We can easily convert time thickness to thickness in units of meters or feet if we have an interval velocity for the sequence. In this case, we have a discovery well and a sonic log. We can get one average interval velocity from the sonic log. This allows us to get an estimate of the thickness in meters. The result is as good as the single interval velocity is representative of the true interval velocities that can vary over the mapped area.

## Slide 5: Measuring Time Thickness
0
100
200
0
100
200
0
100
200
0
100
200
Inline 1400
150
160
160
160
Notes: An illustration of how to measure time thickness along Inline 1400. The scale is in milliseconds; each arrow is 20 ms apart. Align ZERO on the scale to the top horizon (green). Then read the number of ms (to the nearest 10 ms) for the base horizon

## Slide 6: Your Basemap
1500
1600
2200
1800
1900
2000
2100
2200
2200
2500
3100
2800
4000
3700
3400
4300
0 km 5
North
Reservoir Isochron
1400
150
160
160
160
Notes: The students have a clean basemap on which to post time thickness values. NOTE: They should contour the time thickness values lightly with a “lead” pencil. They can complete a table to convert time thickness to thickness in meters. Then they can use a color pencil to sketch contours of thickness in units of meters.

## Slide 7: Exercise 22
Questions?