## Slide 1: Petroleum Geology & Geophysics
Thickness Maps
THIN
THICK
THIN
0
10
15
5
MILES
Shelf Margin
Sand Fairway
TVT
TVT
TST
TST
True Stratigraphic Thickness (TST)
True Vertical Thickness (TVT)

## Slide 2: Outline
Why generate a thickness map?
Types of thickness maps
Generating time-thickness maps
Notes: Outline of the three (3) main points for this lecture.

## Slide 3: Thickness Maps
With our geologic framework, we have mapped the significant horizons and faults
We are especially interested in the depositional sequences (between sequence boundaries) that are potential reservoirs, sources, or seals
We want to know how thick certain depositional sequences are, what environments they were deposited in (EODs), and the types of lithologies they contain within our area of interest
Thickness maps, of course, give us the thickness
Thickness can also help us determine how EODs and lithologies vary across the area
Notes: Given the geologic framework, we can make thickness maps for any interval between two mapped horizons. Key intervals to generate thickness maps are potential reservoirs, sources, or seals. A thickness map can be useful in determining EODs and lithologies in our area of interest.

## Slide 4: For Example
Let’s say we are looking at a deposition sequence that was deposited as part of a major delta system
A reservoir may exist where delta front sands were deposited
Looking at cross-sectional views of this depositional sequence AND a thickness map can greatly facilitate our interpretation
Notes: We’ll consider an area where a major delta was deposited. Cross-sectional views and a thickness map can greatly facilitate our interpretation.

## Slide 5: A Case Study
Green SB
Magenta SB
An area with a major deltaic system
Seismic reflections show a progradational geometry
There was post-depositional tilting and erosion
Notes: A window of seismic data showing reflections with a progradational geometry. This area had post-depositional tilting and erosion. We must be aware of differences between geometries associated with deposition from current-day geometries.

## Slide 6: Deltaic Sequence
The dip of the seismic reflections within the two highlighted depositional sequences suggests that they were deposited as deltas
Green Sequence
Magenta Sequence
Notes: The same seismic window highlighting the Green Sequence and the Magenta Sequence. We’ll focus on the Green Sequence on the next slide.

## Slide 7: Delta Terminology
Undaform
Clinoform
Fondoform
Thin
Thick
Thin
Thick
Thin
Thin
Undaform
Clinoform
Fondoform
Notes: Terminology of Rich (1950), updip to downdip:
- Undaform where upper portion was deposited near sea level – delta plain & delta front.
- Clinoform where upper portion is a paleo-slope – water depth increasing – prodelta.
- Fondoform where upper portion is basinal deposits – abyssal plain.
Note how the interval is thin updip and downdip - it is thick where the unit infilled the margin of the basin where the delta’s depocenter was located.

## Slide 8: 2D Seismic Mapping
H
A
E
C
F
D
B
601
801
1001
1201
1401
201
401
1
401
201
601
801
1001
1201
1401
1601
1
201
401
601
1001
801
1201
1401
1
201
601
401
1801
2001
2201
1601
1401
1201
1001
801
1
601
201
401
801
1001
1201
1401
1201
801
1001
601
401
1
201
1601
1801
1001
1201
1401
801
2001
601
A
G
H
C
B
D
E
F
G
Shelf Margin
Undaform
Clinoform to SM
Clinoform beyond SM
Fondoform
Sequence absent or below resolution
0
10
15
5
MILES
Notes: Seismic lines A through H (8 lines) were interpreted for the Green Sequence using Rich’s terminology:
- Orange = undaform
- Yellow = clinoform out to Shelf margin at end time of the Green Sequence
- Brown = clinoform basinward of the final shelf margin
- Green = fondoform
- Dk Blue = interval thin or absent (below seismic resolution)

## Slide 9: Interpreted EODs
H
A
E
C
F
D
B
601
801
1001
1201
1401
201
401
1
401
201
601
801
1001
1201
1401
1601
1
201
401
601
1001
801
1201
1401
1
201
601
401
1801
2001
2201
1601
1401
1201
1001
801
1
601
201
401
801
1001
1201
1401
1201
801
1001
601
401
1
201
1601
1801
1001
1201
1401
801
2001
601
A
G
H
C
B
D
E
F
G
Undaform
Clinoform to SM
Clinoform beyond SM
Fondoform
Sequence absent or below resolution
Shelf Margin
0
10
15
5
MILES
Fluvial/Coastal Plain
Delta Plain/Delta Front
Delta Slope
Basinal Shales
Notes: Here is the interpretation of environments of deposition (EODs).

## Slide 10: Thickness Map
Isochron
(msec)
THIN
THICK
THIN
0
10
15
5
MILES
Shelf Margin
Sand Fairway
Zero
Thick
Notes: Here is the TWT thickness map in units of msec – an isochron map. The red region (thick) is where the shelf margin built out during deposition of the Green Sequence delta. The best reservoir quality is in the delta front EOD, where waves, tides and storms stir up the sediments and fine-grained particles are winnowed out. The yellow bars are seismic lines associated with the depositional thick.

## Slide 11: Types of Thickness Maps
There are two basic types of thickness maps, depending on how the thickness measurements are made:
A true stratigraphic thickness (TST) map, where thickness is measured perpendicular to the layering
A true vertical thickness (TVT or isochore) map, where thickness is measured vertically with respect to current bed attitudes
As shown on the next slide, the two are only the same if the strata are horizontal
Notes: This slide explains the difference between true stratigraphic thickness (TST) and true vertical thickness (TVT).

## Slide 12: TST versus TVT
For Horizontal Strata
TST = TVT
True Stratigraphic Thickness (TST)
True Vertical Thickness (TVT)
TVT
TST
TVT
TST
Non-Horizontal Strata
TST = TVT
TST = TVT * cos Θ
Notes: If strata are approximately horizontal, then TST equals TVT. If the strata are not horizontal, TST is less than TVT. If stratal dip equals Θ, then TST = TVT * cos Θ.

## Slide 13: Units of Thickness Maps
There are two basic units of thickness maps, depending on the type of data used:
A thickness map in linear units of meters or feet, based on measured sections, vertical wells, or deviated wells that have been corrected to true vertical depth
A thickness map in two-way time units of msec, based on measured seismic sections
If you are using unmigrated seismic data, then time thickness is close to TST
If you are using migrated seismic data,
then time thickness is close to TVT
Notes: If we are in the field or using logs, we measure thickness in units of meters or feet. If we are using seismic data with a vertical scale of TWT, then we measure thickness in units of msec. The name we use for time-thickness maps is ISOCHRON maps.
If you are using unmigrated seismic data, then time thickness is close to TST. If you are using migrated seismic data, then time thickness is close to TVT.

## Slide 14: Generating an Isochron Map
Given two horizons:
At individual locations,
  Isochron = TWTdeeper – TWTshallower
Post individual values on a basemap and contour the values
Grid the TWT values of the deeper horizon
Grid the TWT values of the shallower horizon
Perform a grid operation
  (grid of TWTdeeper) – (grid of TWTshallower)
Generate contours from the isochron grid
Manual
Computer
Notes: We can generate an isochron map in two ways. We can manually calculate the time thickness between two horizons at a number of locations and contour the time thickness values. If we are using computer software, we can have the computer do all the work (given two interpreted horizons):
- Grid the TWT values of the deeper horizon
- Grid the TWT values of the shallower horizon
- Perform a grid operation Isochron grid = (grid of TWTdeeper) – (grid of TWTshallower)
- Generate contours from the isochron grid.

## Slide 15: For Your Exercise
15
Inline 1800
Notes: The students will use their interpreted lines from exercises 19 and 20 to generate an isochron map for the reservoir.
They can:
- Use the two times and subtract them, OR
- Measure the TWT between the top horizon and the base horizon.

## Slide 16: Post and Contour Values
1500
1600
1700
1800
1900
2000
2100
2200
2200
2500
3100
2800
4000
3700
3400
4300
0 km 5
North
Fictitious values for illustration purposes only
Notes: They post the time thickness values on a clean basemap and then contour the values. NOTE: the contours shown here are fictitious.

## Slide 17: Lecture 22
Questions?