## Slide 1: Petroleum Geology & Geophysics
Seismic Facies
Sea Level
Lithologic
Prediction
Depositional
Model
Seismic
Observations

## Slide 2: Objectives
Given a Set of Sequence Boundaries, we want to:
  To predict lithologies within each sequence using seismically-derived information:
    Reflection terminations and geometries
    Seismic attributes (amplitude, continuity, etc.)
    Interpret EODs (environments of deposition)
    Infer lithologic content
  To begin considering where potential reservoir rocks offer us a drilling target (E/D/P)
Notes: Assuming that we have already mapped the significant sequence boundaries, here are the next objectives:
1. Predict lithologies based on seismic info
2. Consider where we have reservoir (and other play element) rocks that we can drill,
in E – exploration phase
in D – development phase
in P – production phase.

## Slide 3: What Is Seismic Facies Analysis?
Input: Seismic Data (2D or 3D)
Product: Prediction of Rock Types
      Sand within reservoir intervals
      Shale in overlying seal intervals & source intervals
Seismic Sequence Analysis
  To define our basic stratal packages - our seismic sequences
Seismic Facies Analysis
  To predict the distribution of lithologies within key sequences
Seismic Stratigraphic Analysis
Notes: We start we either 2D or 3D seismic data. We perform seismic sequence analysis – defining our basic stratal packages. Then we perform what is referred to as seismic facies analysis.
Our goal is to predict where we have potential reservoirs capped by potential seals. We may also want to identify regions that have good source rock potential.

## Slide 4: Some Definitions
Depositional Sequence
  a stratigraphic unit composed of a relatively conformable succession of genetically related strata and bounded at its top and base by unconformities or their correlative conformities
Seismic Facies Unit
  a mappable, three dimensional seismic unit composed of groups of reflections whose parameters differ from those of adjacent facies units
Seismic Facies Analysis
  the description and then geologic interpretation (EOD, lithofacies, etc.) based on seismic reflection parameters
  R. M. Mitchum, 1977
Review
Notes: Some definitions, from AAPG Memoir 26 (1977).

## Slide 5: Seismic Facies Components
Seismic Sequence Analysis
Seismic Facies Analysis
Break Out Key Stratigraphic Units
Interpretation/Prediction
Interpret EODs from patterns
Predict distribution of lithologies
Reflection
Geometries
Non-Geometric Seismic Attributes
Notes: This slide shows the components, a ‘road map,’ for stratigraphic analysis. First, we map sequence boundaries using reflection terminations. This subdivides the sediment fill into genetically related units – depositional sequences. Second, we do seismic facies analysis, which has two elements:
- We use a technique to capture geometric information
- We can also extract seismic attributes, any of a variety of measures of the seismic reflections.
A commonly used seismic attribute is reflection amplitude, another is reflection continuity.
We combine the geometric information with the seismic attributes to predict the environments of deposition (EODs) that influence the types of deposits, e.g., a beach where clean sands may have been deposited.

## Slide 6: Reflection Features Used in Mapping
Feature Significance
Reflection
Geometry
Depositional Processes
Bed Thickness
Fluid Content
Wavelet
Frequency
Lateral Stratal Continuity
Depositional Processes
Reflection
Continuity
Impedance Contrasts
(significant stratal surfaces)
Bed Spacing/Tuning
Fluid Content
Seismic
Amplitude
1
Environment of Deposition
Notes: This slide lists four (4) types of features that we can use in our mapping: seismic geometry, reflection amplitude, reflection continuity, and wavelet frequency. For this lecture, we’ll concentrate on reflection geometry. Sometimes reflection geometry can tell us something about depositional processes and EODs.

## Slide 7: Posting Geometric Observation
The ABC Method
A - B
C
A = Termination Pattern at the Upper Sequence Boundary
B = Termination Pattern at the Lower Sequence Boundary
C = Internal Reflection Pattern
Tr = Truncation
Tp = Toplap
C = Concordant
On = Onlap
Dn = Downlap
C = Concordant
p = parallel m = mounded ob = oblique progradation
sub = subparallel w = wavy sig = sigmoid progradation
div = divergent rf = reflection free sh = shingled
Notes: To capture geometric information, we use what is referred to as the ABC method. The slide shows what at first glance looks like an equation: subtract B from A and divide the remainder by C.
BUT… This is a TEMPLATE that we use to capture observations in a consistent manner.
- A is the type of reflection termination pattern we see at the top of the sequence of interest
the three possibilities are erosional truncation, toplap or concordance (no angular discordance).
- B is the type of reflection termination pattern we see at the base of the sequence of interest
the three possibilities are onlap, downlap or concordance (no angular discordance).
- C is the internal reflection geometry we see, such as parallel reflections.
In the next few slides, we’ll look at sketches for some of the key internal reflection geometries.
NOTE: A trick to remember the TEMPLATE is the think Above, Below, and Center.

## Slide 8: Termination Patterns
Younger
Beds
Erosional
Toplap
Younger
Beds
At the Top of a Sequence
Review
Onlap
Older
Beds
Older
Beds
Downlap
At the Base of a Sequence
Notes: This slide reviews the types of reflection terminations we can observe at the top of a sequence.
These are what we would record for the A term of the template, along with concordance.
It also reviews the types of reflection terminations we can observe at the base of a sequence.
These are what we would record for the B term of the template, along with concordance.

## Slide 9: Internal Reflection Patterns
Parallel
Subparallel
Divergent
Complex
For examples, see AAPG Memoir 26
Stratified
Progradational
Simple
Unstratified
Sigmoid
Oblique
Combination
Shingled
Mounded
Hummocky
Deformed
Chaotic
Reflection
  Free
Notes: This slide shows a hierarchical method to classify internal reflection patterns. First, do you think the reflections indicate stratification patterns? If they do, is the stratification simple, progradational, or complex in appearance? If not, the internal reflection pattern may be chaotic – due to complex structure/stratigraphy or it may be reflection free –a nearly homogenous interval (massive sand, salt, etc.) or it could be a seismic imaging problem. The next slides illustrate the terms on the lower half of this diagram.

## Slide 10: Simple Stratified Internal Configurations
Subparallel
Divergent
Parallel - Even
Complex
Stratified
Progradational
Simple
Notes: Simple stratified means the seismic reflections are parallel, sub-parallel or divergent. The spacing (thickness) between reflections are relatively uniform. A few words on the divergent pattern:
- In the diagram, there are more reflections on the left side than the right.
- The shorter reflections terminate internally, not at the top or base.
- This is probably due to seismic resolution issues.
- The internal layers are thick enough on the right that tops and bases are imaged.
- But moving to the left, units thin and some get too thin for the seismic data to fully resolve.
- Thus, the reflections terminate internally as the total sequence thins right to left.

## Slide 11: Progradational Internal Configurations
Oblique
Sigmoid
Upbuilding (Aggradation)
Outbuilding
(Progradation)
Complex
Stratified
Progradational
Simple
Shingled
Notes: This slide focuses in on progradational internal patterns. This is commonly associated with deltaic-types of deposits that build out a shelf. Sigmoid and oblique are two variations:
- Sigmoid exhibits a combination of upbuilding (or aggradation) and outbuilding (or progradation).
- Oblique exhibits outbuilding without upbuilding. Oblique is characterized by toplap terminations at the top of the sequence.
Sigmoid and oblique represent outbuilding into relatively deep water; 200 meters of water depth or more. Shingled is a progradational pattern in a shallower basin or on a relic shelf. There is not enough paleotopography for progradation to develop at a scale obvious on typical seismic data.

## Slide 12: Complex Internal Configurations
Mounded
Hummocky
Deformed
Complex
Stratified
Progradational
Simple
Notes: Complex internal configurations show significant thickening and thinning. Mounded shows thinning in at least two directions from a central thick. Mounds are common in carbonate environments and in association with deep sea fans. Hummocky shows a complex pattern of thickening/thinning. Deformed indicates that there has been some post-depositional forces that have partially
disrupted the layering. The example shown in the lower right is what might exist where some down-slope creep has occurred.

## Slide 13: The Classic Method - An Example
Line B
Each Line is Subdivided into Seismic Facies Units
where Each Unit Differs from its Neighbors.
Here facies units are based on reflection geometries.
C -On
P
T -C
Ob
T -Dn
Ob
C -Dn
P
C -C
P
Notes: We will code this cartoon section (Line B) to illustrate the ABC method. Animation shows the steps.
- Starting on the left, the first code would be – concordant at the top, onlap at the base, and parallel internally.
- This code is good until we start to observe toplap.
- What is the code for the second unit? Toplap, Concordant, Oblique.
- The third zone? Toplap, Downlap, Oblique.
- The fourth zone? Concordant, Downlap, Parallel (or oblique).
Not everyone would code every segment the same, which is not a problem. Once the codes are posted on a map and interpreted – that is what is important.
The last zone? Concordant, Concordant, Parallel.

## Slide 14: ABC Codes Posted on a Map
10
30
10
20
30
40
50
40
10
20
30
40
50
Line B
20
Line C
Line A
T -Dn
Ob
C -On
P
T -C
Ob
C -Dn
P
C -C
P
C -C
P
C -Dn
P
T -Dn
Ob
T -C
Ob
C -On
P
C -C
P
T -C
Div
Notes: We have placed the codes for Line B on the map – we offset the codes to help the illustration. We also have the codes for Line C (similar string of codes) and Line A (different codes). Note where Line B and Line A intersect – see a problem?
- Line B has Oblique while Line A has Parallel.
- This is not necessarily a conflict.
- Progradation has a dip and a strike component.
- Line B is more of a dip orientation while Line A is more of a strike orientation.
With these two codes, we can conclude the progradation is primarily west to east.

## Slide 15: Facies Synthesis
10
20
40
30
Line B
Line C
Line A
10
20
30
40
50
10
20
30
40
50
C -On
P
T -C
Ob
C -Dn
P
C -C
P
T -Dn
Ob
C -C
P
C -Dn
P
T -Dn
Ob
T -C
Ob
C -On
P
C -C
P
T -C
Div
10
20
40
30
10
20
30
40
50
10
20
30
40
50
Zone of
Progradation
Last Shelf Margin
30
10
20
10
Wedge
Sheet
T -Dn
Ob
C -On
P
T -C
Ob
C -Dn
P
C -C
P
C -C
P
C -Dn
P
T -Dn
Ob
T -C
Ob
C -On
P
C -C
P
T -C
Div
Line B
Line C
Line A
Notes: After we post the observations for each line, we have to synthesize the geometric observations. In this example, there is a zone of oblique progradation to the ESE near the center of the area. Landward there is an onlaping wedge. Basinward where is a sheet (C–C/P).

## Slide 16: Depositional Environments
Basin
Slope
Marginal
Marine
Non-Marine
10
20
30
40
50
10
20
30
40
50
10
20
40
30
Line B
Line C
Line A
Notes: We are now ready to interpret the EODs – Environments of Deposition. From left to right we have:
- A fluvial/non-marine wedge that thins by onlap to the west (tan),
- A nearshore/marginal marine zone (characterized by toplap) (yellow),
- The paleo-slope at the end of this depositional period (concordant at top) (green), and
- The basinal deposits out in deep water (grey).

## Slide 17: Inferred Lithology - Prediction
Facies Model
Delta Front Sandstone
Delta Front Siltstone
Pro-Delta Shales
Offshore Clay
Sea Level
Prediction
Crevasse Splay
Channel Fill
Proximal
Distributary
Mouth Bar
Distal
Distributary
Mouth Bar
Prodelta
Delta Front
Notes: Given these interpreted EODs, we can think about the types of depositional bodies we should have. We use depositional models based on modern analogues, ancient outcrops and/or laboratory experiments. If we were to drill in the marginal marine (yellow) area of the map on the last slide, we would expect (from top-down):
- Delta front sands,
- Delta front silts,
- Prodelta shales, and
- Offshore clays.
We can anticipate a vertical (and lateral) facies succession as shown on the right. We can even use geo-statistics to predict, for example, the thickness and lateral extent of channel sands or crevasse splays.

## Slide 18: Time for an Exercise
Where should I
drill a well
in this area
???
H
A
E
C
F
D
B
601
801
1001
1201
1401
201
401
1
401
201
601
801
1001
1201
1401
1601
1
201
401
601
1001
801
1201
1401
1
201
601
401
1801
2001
2201
1601
1401
1201
1001
801
1
601
201
401
801
1001
1201
1401
1201
801
1001
601
401
1
201
1601
1801
1001
1201
1401
801
2001
601
A
G
H
C
B
D
E
F
G
Notes: It is time for an exercise.

## Slide 19: Lecture 23
Questions?