## Slide 1: Exercise 24
Seismic Attribute Analysis
Seismic Attribute Analysis
Your Task:
  Use two (2) seismic attribute maps to identify areas where good-quality seal rocks overlay good-quality reservoir rocks.
Strong Amplitude
Weak Amplitude
Strong Amplitude
Weak Amplitude
Notes: Title slide with main task.

## Slide 2: A Datumed Seismic Line
Orange
Datum
Notes: This shows a representative east-west line that has been datumed (flattened) on the Green horizon. We are interested in the rocks above and below the Orange horizon:
- below the Orange horizon, we are looking for good-quality reservoir
- above the Orange horizon, we are looking for good-quality sealing rocks.
Note the prograding (inclined) reflections. These gently dipping reflections indicate a nearshore to offshore deltaic series of depositional sequences. ALSO NOTE: The seismic has been phase-shifted to quadrature phase (also called relative impedance). A strong reflection coefficient would correspond to a zero crossing. The loop (half cycle) above a zero crossing gives information on the rock properties of the deposits above the zero crossing.
The loop (half cycle) below a zero crossing gives information on the rock properties of the deposits below the zero crossing.

## Slide 3: Conceptual Depositional Model
Stacked, prograding fluvial to nearshore to offshore marine siliciclastic depositional sequences
Orange
Magenta
Marine Shale
(great seal)
Nearshore Sand
(good reservoir)
Fluvial Sand
(fair reservoir)
Notes: This “cartoon” section shows the types of EODs and sedimentary faces we expect. We want to find locations where at the orange horizon we have:
- The Green facies above (marine shale, a great seal), and
- The Yellow facies below (nearshore, reworked sands, a good reservoir).

## Slide 4: Conceptual Depositional Model
Marine Shale (great seal)
Nearshore Sand (good reservoir)
Marine Shale (great seal)
Marine Shale (great seal)
Nearshore Sand (good reservoir)
Fluvial (fair reservoir)
Orange
Magenta
Prograding sands increase in porosity upwards before being capped by a marine shale.
Notes: This is the vertical stacking our conceptual model would have. Note: at the orange horizon we have a great seal above, but only fair reservoir below.

## Slide 5: Modern Analog: Barrier Island
Notes: This is an air photo of a modern analog for our conceptual model. It is a barrier island. There is great reservoir potential along the beach facies.

## Slide 6: Modeled Seismic Responses
Good Seal
Good Reservoir
Good Seal
Poor Reservoir
Poor Seal
Good Reservoir
Poor Seal
Poor Reservoir
Strong Peak
Strong Trough
Strong Peak
Moderate Trough
Moderate Peak
Strong Trough
Moderate Peak
Moderate Trough
Notes: We used appropriate velocities and densities from the three (3) rock faces to model several seismic responses. We are looking for the depositional stacking at the far left – good reservoir capped by good seal. The seismic response for this is a strong peak and a strong trough above/below the orange horizon.
The other three (3) possibilities are also shown in which either the peak or trough or both are moderate to low amplitude. Thus, if we look at the amplitude of the peak above orange and the trough below orange, we can locate what we what to find.

## Slide 7: Peak Above Orange Amplitude
Strong Amplitude
Weak Amplitude
Notes: This is a map of the amplitude of the peak immediately above the Orange horizon.

## Slide 8: Trough Below Orange Amplitude
Strong Amplitude
Weak Amplitude
Notes: This is a map of the amplitude of the trough immediately below the Orange horizon. As you work through the exercise, you will discover where we have the best chance to find good reservoir
capped by good seal.

## Slide 9: Orange Horizon Time Structure
Shallow
Deep
Notes: This is a time structure map for the orange horizon. You can map where the desired stratigraphic stacking (good reservoir capped by good seal) occurs near a structural high.

## Slide 10: Exercise 24
Questions?