## Slide 1: Petroleum Geology & Geophysics
Seismic Attributes
18%
0
porosity
Predicted Porosity Map

## Slide 2: Definition
What are seismic attributes?
Seismic attributes are mathematical descriptions of the shape or other characteristics of a seismic trace over a specified time (depth) interval.
REVIEW
Notes: What are seismic attributes? Seismic attributes are mathematical descriptions of the shape or other characteristics….

## Slide 3: Attributes for Stratigraphic Analysis
Seismic attributes can be used to help in mapping stratigraphic features.
Typically we use:
  Horizon-local attributes
  Interval attributes
  Surface attributes
Frequency Slice: 16 Hz
freeusp.org/RaceCarWebsite/TechTransfer/ OnlineTraining/Spec_Tutorial/SpecDoc.html
18%
0
porosity
Predicted Porosity
Notes: Seismic attributes can be used to help in stratigraphic interpretation. There are three (3) types of attributes we typically use: horizon-local, interval, surface (mapped horizon) attributes.
Lower, left: Several attributes were combined to predict porosity (more on this example later).
Lower, right: A frequency slice that reveals channel geomorphology.

## Slide 4: Horizon Attributes
For an interpreted horizon
Time/Depth
Maximum Dip
Max Dip Azimuth
Xline 2185
Green Horizon
Reflection Amplitude
Curvature
Etc.
Notes: Horizon attributes are associated with an interpreted horizon. For example, for the green horizon we can measure:
- Time (or depth)
- Maximum dip
- Max dip azimuth
- Reflection amplitude
- Curvature
- and about 12 other attributes.

## Slide 5: Horizon Attributes
Gentle
Steep
Faults
Stratigraphic
features
Horizon Dip Map
Notes: This is a display of the DIP attribute calculated along an interpreted horizon
- Low dips are light
- High dips are dark.
Two (2) types of geologic features are revealed:
- linear segments of high dip associated with fault offsets of the horizon
- curvilinear segments of high dip associated with channels and other stratigraphic features.
How do we separate structural and stratigraphic features?
- structural features are consistent over many time slices
- stratigraphic features change rapidly from one time slice to the next (shallower or deeper).

## Slide 6: Applications of Seismic Attributes
Qualitative Applications
Data quality; seismic artifact identification
Seismic facies; depositional environment
Quantitative Applications
Equations relating rock property changes to changes in seismic attributes
  Reservoir thickness
  Lithology
  Porosity
  Type of fluid fill
Notes: Seismic attributes serve two (2) basic purposes:
  Qualitative evaluations
    checking seismic data quality – identifying artifacts (non-geologic features) in the data
    performing seismic facies mapping to predict depositional environments
  Quantitative analyses
    using well data to provide calibration, we find an equation that uses one or more attributes to predict a rock or fluid property, such as:
      Reservior thickness
      Lithology
      Porosity
      Type of fluid fill (water, oil, gas)
The next few slides will show some examples.

## Slide 7: Qualitative Applications
Example: Data Quality (Artifact) Analysis
Inline-parallel acquisition striping ~40 ms below water bottom
Inline
Direction
40 ms
RMS Amplitude
Over a 200 ms window
Notes: Here is an amplitude-based seismic attribute map at a level about 40 ms (10 data samples) below a shallow water bottom.
Note the east-west trending “stripes”. This is an acquisition artifact associated with a multi-streamer boat collecting the data by sailing east-west and west-east. These ”stripes” tend to “heal” with depth; they may not impact our analysis of a deep reservoir interval.

## Slide 8: Qualitative Applications
1000 ms
Example: Data Quality (Artifact) Analysis
Inline-parallel acquisition striping at 1000 ms
Inline
Direction
RMS Amplitude
Over a 200 ms window
Notes: Here is an amplitude-based seismic attribute map at a level at 1000 ms below sea level. Note the east-west trending “stripes” still exist, but they are very subtle. The ”stripes” have “healed” with depth. The ”stripes” would not significantly impact our analysis at this depth.

## Slide 9: Qualitative Applications
Example: Seismic facies; depositional environment
Classification based on seismic wavelet shapes, Gulf of Mexico
Truncated
Meander Loop
Meander Loop
Expansion
Tangential
Meander Loop
Posamentier, H. W. and Kolla, V., 2003, Seismic Geomorphology of Depositional Elements in Deep-Water Settings, Journal of Sedimentary Research, Vol. 73, No. 3, p. 367-388.
Notes: Here is an example of another qualitative method. In this case, the computer was asked to look at the waveform (reflection shape) over a certain interval and derive 8 “classes.” Then each trace was compared to the eight (8) classes and assigned a color based on the most dominant class. A major channel system (about a km wide) is apparent based on the color-coded classes.

## Slide 10: Quantitative Applications
Requirements:
  Appropriate data processing (e.g., controlled amplitude and controlled phase)
  Data quality reconnaissance
  Good to excellent well-seismic ties
  Sufficient well control (additional control can be obtained through seismic modeling)
Notes: We can also use attributes in a quantitative manner. There are several requirements to perform a quantitative attribute analysis. Some are related to the seismic data, and others relate to calibration data from wells. In terms of the seismic data, the data processing should be Controlled Amplitude and Controlled Phase:
Data quality should be high and checked by doing some reconnaissance
All wells should be tied to the seismic data (via synthetics) and the results should be high-quality well-seismic ties.
In terms of well calibration:
There should be sufficient well control so that variations in rock or fluid properties can be related to variations in one or more seismic attributes
We can use 1-D models to give more calibration points (e.g., if the well has a 50 m gas zone, we could model the seismic response and attribute characteristics of a similar gas sand that is 100 m or 25 m thick).

## Slide 11: Quantitative Applications
Porosity in the
Upper Smackover
No Porosity in the
Upper Smackover
An Oil Field, Onshore Alabama
Impedance
Smackover
Norphlet
Haynesville
Tight
Smackover
Norphlet
Haynesville
Impedance
Porous
Zone
Notes: Next, we will review an example of a quantitative attribute analysis using real data. This study is for an oil field from onshore Alabama. The reservoir is a carbonate interval called the Smackover formation. In some locations, the upper Smackover is porous and contains oil; elsewhere it is tight (no porosity). We want to use seismic data to predict where the Smackover is porous.

## Slide 12: Quantitative Applications
Representative In-Line
Mapped
Horizon
(trough)
2.84
2.82
2.92
2.84
2.82
2.92
The trough is
lower in amplitude
and loop duration
is longer
The trough is
higher in amplitude
and loop duration
is shorter
Porosity
in the Smackover
No Porosity
in the Smackover
Peak
Trough
Peak
Change Porosity results in a Change in Seismic Response
Notes: Here is a seismic line that connects two (2) well locations. The well on the left has porosity (and oil), and the well on the right has no porosity.
NOTE: the black reflection cycle (a trough) associated with the upper Smackover on the left. It is not as black (not as negative) as it is on the right. Also, on the left there is a thin interval of light grey that dies out to the right.
These are subtle differences that may be related to the presence/absence of porosity. It would be hard to visually use these observations, but seismic attributes make it relatively easy.

## Slide 13: 1-D Seismic Modeling
Smackover
Haynesville
Norphlet
16 ft
Porous
Zone
3 ft
Porous
Zone
10 ft
Porous
Zone
Actual
Well
Changing the porosity in the Upper Smackover in 1-D models confirms there is a seismic signature related to porosity
16 ft
Porous
Zone
3 ft
Porous
Zone
Notes: We can check to see if some attributes are sensitive to the amount of porosity. Here we have a “real” well and two “pseudo-wells.” The real well had a 10 foot thick porous zone.
We edited the well data to give us two “pseudo-wells” (modifications of a real well). On the left is a pseudo well with 16 feet of porosity. On the right is a pseudo well with 3 feet of porosity.
We also show a modeled trace for all three. Notice how the trough varies in amplitude and shape as the thickness of the porous zone changes. Using seismic attributes, we can capitalize on these subtle variations.

## Slide 14: Check Predictions
Porosity for the Smackover
  Predicted based on four (4) attributes
  Calibration based on eight (8) wells
Actual Average Smackover Porosity
0
5
3
2
1
8
9
7
6
4
5
0
6
1
4
3
2
8
7
9
Predicted Average Smackover Porosity
Best Fit
95% C.I.
Notes: Here is a cross-plot in which:
  The horizontal axis is porosity thickness (data points are only from actual wells)
  The vertical axis is our predicted porosity thickness from an equation that uses 4 seismic attributes as terms
  e.g., A * (attribute 1) + B * (attribute 2) + C * (attribute 3) + D * (attribute 4).
A best linear fit was derived (mathematically) and 95% confidence intervals are shown. We could have used several pseudo-wells to add more calibrations points, but that was deemed unnecessary for this case since we have eight (8) wells with a good spread of porosity values.

## Slide 15: Predicted Porosity Map
Applying the derived attribute “equation” to the 3D seismic survey resulted in a Smackover porosity map
18%
0
porosity
Valuable in field development planning
Valuable for exploration, near-field wildcats
Unreliable
Edge Effects
Possible New
Well Location
Notes: We use our equation (based on 4 attributes) to derive a map of predicted feet of porosity throughout the area. Hot colors are where we predict the thickest porous zones exist.
There are some “edge effects” near the boundaries of the survey that have to be ignored. The zoomed-in area gives a high level of detail for a known producing zone. We can use this detail to position additional production wells. This map was also used to identify other drill locations for near-field wildcats.

## Slide 16: Summary
Seismic attributes describe shape or other characteristics of a seismic trace over specific intervals or at specific times
Seismic attributes are important because they enable interpreters to extract more information from seismic data
Seismic attributes can be derived from a single-trace, by comparison of multiple traces, or from interpreted horizons
Three common types of single-trace attributes are loop, interval, and sample-based
Seismic attributes are used for qualitative analysis (e.g., data quality, seismic facies mapping) and quantitative analysis (e.g., net sand, porosity prediction)
Notes: In summary ….

## Slide 17: Lecture 24
Questions?
Notes: Slide 24.17