## Slide 1: Exercise 24: Seismic Attribute Analysis
Seismic Attribute Analysis
Your Task:
  Use two (2) seismic attribute maps to identify areas where good-quality seal rocks overlay good-quality reservoir rocks.
Strong Amplitude
Weak Amplitude
Strong Amplitude
Weak Amplitude
Notes: A review of exercise 24.

## Slide 2: Peak Above Orange Amplitude
Strong Amplitude
Weak Amplitude
Black Polygons enclose areas of strong positive responses.
Notes: Map of the amplitude for the peak above the orange horizon with polygons around regions with strong positive responses. Our model suggests these are regions where the seal would be good to great.

## Slide 3: Trough Below Orange Amplitude
Strong Amplitude
Weak Amplitude
Black Polygons enclose areas of strong negative responses
Notes: Map of the amplitude for the trough below the orange horizon with polygons around regions with strong negative responses. Our model suggests these are regions where the reservoir would be good.

## Slide 4: Orange Horizon Time Structure
Shallow
Deep
Yellow Polygons are Good Reservoir
Red Polygons are Good Seals
Notes: Map of the TWT for the orange horizon (deeps are hot colors; shallows are cool colors). Yellow polygons indicate good reservoir. Red polygons indicate good seal. Orange regions are where there is both good reservoir and good seal.

## Slide 5: Reservoir - Seal Quality Classification
Poor Seal
Poor Reservoir
Good Seal
Poor Reservoir
Poor Seal
Good Reservoir
Good Seal
Good Reservoir
Notes: Using seismic interpretation software, a series of logic statements (If …, Then ..) were used to classify each trace. The four (4) possibilities for good or poor reservoir and seal were classified and color-coded. Green indicates where a strong peak overlies a strong trough – our criteria for good seal over good reservoir.

## Slide 6: “Good Areas” on Time Structure
Shallow
Deep
Notes: Here the “green” class from the previous slide is shown as brown polygons. The background map is TWT to the orange horizon. The three black circles are potential drill locations where we expect good seal over good reservoir near a structural high.

## Slide 7: Exercise 24
Questions?