## Slide 1: Exercise 25
Reservoir Quality
Reservoir Quality
Your Task:
  Use a seismic line that goes through the Barracouda-1 well to analyze reservoir quality in terms of cross-sectional area.

## Slide 2: Introduction
Lecture 25 presented the primary factors that control reservoir quality. You will complete a computation table step-by-step to get an estimate of the in-place HCs for the Crossline that intersects Barracouta-1.
Computer tools available in interpretation software allow you to walk through the same basic procedure to obtain an estimate of in-place HC volume for the field or prospect that you are charged to work.
For this exercise, you will have to fill in only columns I, J, and K on the computation sheet, with a few exceptions.
Notes: Without computers, we will make this a 2D problem – the area rather than the volume of HC. This is a “cookbook” exercise where the instructions take students through the computations step-by-step, and in 12 steps, you can come up with a cross-sectional HC area. In step 13, we will assume a length to the field so as to get a HC volume estimate.

## Slide 3: Seismic Line through Baracouta-1
Notes: The crossline that goes through the Barracouta-1 discovery well. We have added lines to demark columns – from A to T. Each column is 0.5 km wide. Note that the position of the gas-water contact (GWC) is marked on the left side of the section. Step 1 will be to draw the base of the gas where it is BELOW the magenta line (top of reservoir). Our goal is to estimate the amount of oil contained between the magenta line and the flat base of gas line in km2.

## Slide 4: The Computation Sheet
Notes: This is the computation sheet with much of the values filled in. Columns A through T relate to the columns draw on Figure 1. For row 1, students complete values for column I through T. For all the other rows, students only need to fill in columns I, J and K. Note that rows 4, 5 and 6 give the EOD for the upper, middle and lower zones of the reservoirs.
Net-to-Gross (N:G) and porosity (Φ) are assigned based on the EOD.

## Slide 5: Basic Procedure
Draw a flat GWC (gas-water contact) on Figure 1.
Measure the cumulative reservoir width.
Get the reservoir thickness in TWT (in unit of ms).
Convert the TWT thickness to a thickness in meters.
Use EODs to assign the average N:G and Φ.
Determine the reservoir cross-sectional area.
Determine the reservoir rock area.
Determine the reservoir pore area.
Determine the HC pore area.
Sum all the values to get the total HC area in units of square km.
for each column
Notes: This slide summarizes the procedure. Steps 3 through 9 are done column-by-column. Step 10 sums all the values in row 18 to get a total cross-sectional area in square kilometers.

## Slide 6: Exercise 25
Questions?