## Slide 1: Petroleum Geology & Geophysics
Reservoir Quality
Total Rock
Volume
Res Sand
Volume
Non-Res
Non-Net
Non-Res
Net Pore
Volume
Non-Res
Non-Net
Non-Res
Solid
Grains
Pores
Non-Res
Non-Net
Non-Res
Solid
Grains
Gas
Water
HC
Volume

## Slide 2: Outline
Overview
What is included in Reservoir Quality?
Components of Reservoir Quality
  Gross Rock Volume
  Reservoir Volume
  Pore Volume
  HC Volume
Notes: Topics covered in this lecture.

## Slide 3: Reservoir Quality - Overview
At least in exploration, we want to know, as best as we can, if there will be good quality reservoir rock where we propose to drill
This means two (2) things:
  Reservoir rocks are present
  Reservoir properties will be good enough to produce HCs
Our ultimate goal is to know how much HC is in the potential reservoir and what portion we can produce, the estimated ultimate recovery (EUR)
Notes: The reservoir remains the play element that our industry tends to focus on the most. Especially in exploration, we want to know if there will be good quality reservoir rock where we propose to drill. This means two (2) things: (1) Reservoir rocks are present; and (2) Reservoir properties will be good enough to produce HCs.
Our ultimate goal is to know how much HC is in the potential reservoir and what portion we can produce, i.e., to estimate the ultimate recovery (EUR).

## Slide 4: Reservoir Quality - Presence
So the first question is whether or not reservoir rocks are present
Data we use to answer this question include:
  Well data from the region
  Outcrops on the flank of the basin
  Seismic data over the proposed well location
Available well data may allow us to build a log cross section across the prospect or at least in the vicinity
If well data exist, then we will want to develop good well-seismic ties
We will use seismic facies analysis (ABC geometries and attributes) to predict EODs and infer where reservoir quality rocks should be present
Notes: The first question is whether or not reservoir rocks are present. The data we use to answer this question include: (1) well data from the region; (2) outcrops on the flank of the basin; and (3) seismic data over the proposed well location. Available well data may allow us to build a log cross section across the prospect or at least in the vicinity.
If well data exist, then we will want to develop moderate- to good-quality well-seismic ties. We will use seismic facies analysis (ABC geometries and attributes) to predict EODs and then infer where reservoir quality rocks should be present.

## Slide 5: Reservoir Quality - Quality
Reservoir quality relates to the ease with which we can produce oil and/or gas from one or more wells
The two (2) main factors controlling reservoir quality are:
  Porosity – the pore space between rock grains
  Permeability – the “connectedness” of the pores
There are various ways geoscientists predict reservoir quality, from simple to complex:
  Use analogs – find sands of similar EODs, age and depth, then use the porosity and permeability of these sands
  Use local data to plot porosity and permeability as a function of depth and make predictions from best-fit lines
  Use software to model the burial, temperature and pressure history of the reservoir interval and predict porosity and permeability of the sands
Notes: Reservoir quality relates to the ease with which we can produce oil and/or gas from one or more wells. The two (2) main factors controlling reservoir quality are: (1) porosity – the pore space between rock grains; and (2) permeability – the “connectedness” of the pores. There are various ways geoscientists predict reservoir quality, from simple to complex: (1) sse analogs – find sands of similar EODs, age and depth, then use the porosity and permeability of these sands; (2) Use local data to plot porosity and permeability as a function of depth and make predictions from best-fit lines; and (3) Use software to model the burial, temperature and pressure history of the reservoir interval and predict porosity and permeability of the sands.

## Slide 6: Reservoir Quality – HC Amount in Place
We want to gain enough information so that we can estimate the volume of HC in place
Normally we make three predictions:
  The most likely volume, our best-educated guess
  What the minimum volume could be, if any HCs are present
  What the maximum reasonable volume could be
Later on we will have to consider how much of the in place volume we can count on bring up to the surface through N wells, the EUR (estimated ultimate recovery)
So how do we get HC in place?
Notes: We want to gain enough information so that we can estimate the volume of HC in place (down in the reservoir at reservoir conditions). Normally we make three (3) predictions: (1) the most likely volume, our best-educated guess; (2) what the minimum volume could be, if any HCs are present; and (3) what the maximum reasonable volume could be.
Later on (exercise 28) we will have to consider how much of the in place volume we can count on bring up to the surface through N wells, the EUR (estimated ultimate recovery).
So how do we get HC in place?

## Slide 7: Obtaining HC in Place
We start by estimating the total volume of rock
Then we reduce the volume step-by-step until we get an estimate of the volume of HC in the reservoir – gas in the case of Barracouta
Total Rock
Volume
Res Sand
Volume
Non-Res
Non-Net
Non-Res
Net Pore
Volume
Non-Res
Non-Net
Non-Res
Solid
Grains
Pores
Non-Res
Non-Net
Non-Res
Solid
Grains
Gas
Water
HC
Volume
Notes: We start by estimating the total volume of rock in our target interval at our prospect. Then, we reduce the volume step-by-step until we get an estimate of the volume of HC in the reservoir gas in the case of Barracouta. We’ll go through these steps in the next few slides.

## Slide 8: Total Rock Volume
A first approximation:
  Map the areal extent of the trap (using a planimeter)
  Estimate how far down dip the HCs extend (more in Lecture 26)
  Convert the isochron map (in ms) to an isochore map (in m or ft) using velocity data from the well
  Combine the HC extent and an average thickness to get a total rock volume (km3 or acre/ft)
Total Rock
Volume
Field Area
*
Aver. Thickness
Total Rock Vol.
Notes: To get a first approximation, we:
  - Map the areal extent of the trap (using a planimeter)
  - Estimate how far down dip the HCs extend (more in Lecture/Exercise 26)
  - Convert the isochron map (in units of ms) to an isochore map (in units of m or ft) using velocity data from the well
  - Combine the HC extent and an average thickness to get a total rock volume (km3 or acre/ft).

## Slide 9: Reservoir Rock Volume
A first approximation:
  Start with the total rock volume
  Estimate the net-to-gross for the reservoir interval (good sands versus waste rock)
  Net-to-gross often varies by the environments of deposition
  For our field:
    N/G for shoreface EOD = 80%
    N/G for delta plain EOD = 65%
    N/G for fluvial EOD = 50%
Res Sand
Volume
Non-Res
Non-Net
Non-Res
Total Rx Vol.
*
Net-to-Gross
Res. Rock Vol.
Notes: To get a first approximation, we:
  - Start with the total rock volume
  - Estimate the net-to-gross for the reservoir interval (good sands versus waste rock)
  - Net-to-gross often varies by the environments of deposition
For our field:
  - N/G for shoreface EOD = 80%
  - N/G for delta plain EOD = 65%
  - N/G for fluvial EOD = 50%.

## Slide 10: Pore Volume
A first approximation:
  Start with the reservoir sand volume
  Use a porosity value (percentage of volume that represents the pore space)
  Porosity (Φ) often varies by the environments of deposition
  For our field:
    Φ for shoreface = 20%
    Φ for delta plain = 18%
    Φ for fluvial = 16%
Net Pore
Volume
Non-Res
Non-Net
Non-Res
Solid
Grains
Pores
Res. Sand Vol.
*
Porosity
Pore Volume
Notes: To get a first approximation, we: (1) Start with the reservoir sand volume; and (2) Use a porosity value (percentage of volume that represents the pore space).
Porosity (Φ) often varies by the environments of deposition (EOD).
For our field:
  - Φ for shoreface = 20%
  - Φ for delta plain = 18%
  - Φ for fluvial = 16%.

## Slide 11: Hydrocarbon Volume
A first approximation:
  Start with the net pore volume
  Use a HC saturation value (e.g. 80% HC saturation means 80% of the pore space contains HCs, the other 20% has irreducible water)
  For this field, a HC saturation of 90% was found to be correct (after production started)
Non-Res
Non-Net
Non-Res
Solid
Grains
Gas
Water
HC
Volume
Net Pore Vol.
*
HC Saturation
HC Volume
Notes: To get a first approximation, we: (1) Start with the net pore volume; and (2) Use a HC saturation value (e.g. 80% HC saturation means 80% of the pore space contains HCs, the other 20% has irreducible water). For this field, a HC saturation of 90% was found to be correct (as determined after the field had been producing for several years.)

## Slide 12: Recoverable HC
We need a recovery efficiency to go from HC in place to recoverable HC
To get a recoverable gas value, we will assume a 70% recovery efficiency
Many factors go into the recovery efficiency, in particular, how effective the reservoir’s “plumbing” is, which is related to permeability
These factors are beyond the scope of this course
There is also a volumetric expansion as the gas rises in the pipe and goes through drops in both temperature and pressure
In-Place HC
*
Expan. Factor
*
Recovery Eff.
Recoverable V.
Non-Res
Non-Net
Non-Res
Solid
Grains
Gas
Water
HC
Volume
In Place
at Depth
Recovered
at Surface
Gas
Expansion
Notes: We need a recovery efficiency to go from HC in place to recoverable HC (at the surface). To get a recoverable gas value, we will assume a 70% recovery efficiency. Many factors go into the recovery efficiency, in particular, how effective the reservoir’s “plumbing” is, which is related to permeability. These factors are beyond the scope of this course. There is also a volumetric expansion as the gas rises in the pipe and goes through drops in both temperature and pressure.

## Slide 13: Lecture 25
Questions?
Notes: Slide 25.13