## Slide 1: Petroleum Geology & Geophysics
Direct HC Indicators
5
25
15
10
20
10
3
4
5
6
7
8
9
IMPEDANCE x 103
DEPTH x 103 FEET
GAS
SAND
OIL
SAND
WATER SAND
SHALE
Data for Gulf Of Mexico Clastics
Looking for
shallow gas
Looking for
deep oil
Flat Spot
www.geoexpro.com/exploration/westloppa/

## Slide 2: Outline
What is a DHI?
Rock & Fluid Properties
DHI Analysis
DHI Characteristics
Predicting Seismic Responses
DHI Validity
Advanced Methods
Pitfalls
Notes: This is a list of the eight (8) main topics we will cover. The first topic is: What is a DHI?

## Slide 3: What is a DHI?
Seismic DHIs are anomalous seismic responses that are caused by the presence of hydrocarbons
DHIs occur when a change in pore fluids causes a change in the elastic properties of the bulk rock which is seismically detectable (i.e. there is a “fluid effect”)
DHIs display one or more types of characteristics that are consistent with hydrocarbons filling pores in a rock matrix
DHI = Direct Hydrocarbon Indicator
Notes: DHI is an acronym for Direct Hydrocarbon Indicator. There is an anomalous seismic response caused by the presence of HCs. DHIs occur when a change in pore fluids causes a change in rock properties. DHIs display one or more characteristics that are consistent with HCs in pores.

## Slide 4: Rock Property Trends with Depth
shale
brine sand
oil sand
gas sand
Depth
Velocity, Impedance
Sands compact faster than shales
Fluids initially are separated in velocity (gas < oil < water)
These trends are caused by variations in mineralogy, grain size, texture, sorting, fluid properties & pressure
Notes: We need to review a few rock and fluid properties. This chart shows how velocity and impedance vary with increasing depth. Four (4) rock types are shown. This chart is based on data from the US Gulf of Mexico. Other basins have similar trends.

## Slide 5: Reflection Coefficient Trends with Depth
Normal Incidence Reflection Coefficient
Here we consider the RC at a shale/porous sand boundary
Shale is higher impedance than sand where the blue line is left of the zero RC line
Note how oil sands result in a more negative RC than brine sand
Gas sands have even more negative RCs
At some point the differences between fluid types is not seismically detectable (HI floor)
Shale/brine sand
Shale/oil sand
Shale/gas sand
Depth
DHI floor
Negative RCs 0
Notes: Again using Gulf of Mexico data, this shows how a RC will change with depth. The blue line is for shale above a brine-filled sand; very shallow it is a negative RC. The green line is for shale above an oil-filled sand. The red line is for shale above a gas-filled sand.

## Slide 6: Typical Gulf Of Mexico Impedance Trend
5
25
15
10
20
10
3
4
5
6
7
8
9
IMPEDANCE x 103
DEPTH x 103 FEET
GAS
SAND
OIL
SAND
BRINE SAND
SHALE
Data for Gulf Of Mexico Clastics
Looking for
shallow gas
Looking for
deep oil
In general:
  Oil sands are lower impedance than water sands and shales
  Gas sands are lower impedance than oil sands
  The differences in the impedance with fluid type tends to decrease with depth
  The larger the impedance difference between the fluid- filled sand and it’s encasing shale, the greater the seismic amplitude anomaly
Notes: Here is another way to view the data. Now the impedance is shown by rock type as a function of depth. Since RC is related to the difference in impedance, the horizon distance between curves indicates the magnitude of a seismic reflection. If you are exploring at about a depth of 4,000 feet, oil sands will be “bright” and gas sands will be “very bright.” However, if you are exploring at about a depth of 8,000 feet, gas sands should still be high amplitude, but you probably won’t be able to differentiate oil sands from shales or wet sands.

## Slide 7: Fluid Properties
Gas
Brine
Oil
Low API
Low GOR
High API
High GOR
Single
Phase
Acoustic Properties of Reservoir Different Fluids
Bulk Modulus (Gpa)
Density (g/cc)
Notes: In porous sands, the rock matrix (sand grains) will have fairly uniform properties. The fluids in the pores between the sand grains can have different properties, so as long as the rock has porosity greater than about 5%, the impedance of the rock will change as the fluid type changes.

## Slide 8: A Rock’s Acoustic Properties
Seismic waves are sensitive to both the rock & fluid properties of fluid saturated rock
Fluid properties are controlled by:
Pressure, temperature
Gas gravity
GOR, API
Salinity
Saturation
Grain properties are controlled by mineralogy
Rock frame properties are controlled by:
Mineralogy, sorting, texture
Compaction
Cementation
Porosity
Reservoir Rock
Filled with Brine
Notes: Let’s consider a sand where the pore space is filled with brine. Grain properties are controlled by mineralogy.

## Slide 9: A Rock’s Acoustic Properties
A Change in Fluid Type in a Reservoir Results in Different Acoustic Properties
Reference values of:
  Velocity
  Density
Reservoir Rock
Filled with Brine
Reservoir Rock
Filled with Oil
Reservoir Rock
Filled with Gas
Compared to brine sand:
  Lower Velocity
  Lower Density
Compared to brine sand:
  Much Lower Velocity
  Much Lower Density
Notes: A change in fluid type in a reservoir results in different acoustic properties. If we let the brine sand be our reference (standard), then the same sand filled with oil will have a lower velocity, density, and therefore impedance. The same sand filled with gas will have a much lower velocity, much lower density, and therefore much lower impedance.

## Slide 10: A Fluid Contact
Shale
Shale
Lower
Impedance
Higher
Impedance
A Change in RC
Along the Top Reservoir
A Fluid Contact
  GWC
  OWC
  GOC
The presence of oil or gas in the reservoir can lead to certain HC indicators
Notes: Consider a sand in a trapping geometry. Gas has a lower density than brine, so it will fill the top of the trap. So we’ll have a gas cap sitting on top of brine-filled sand, and there will be a flat (horizontal) fluid contact. Along the top of the reservoir, the RC will change (decrease) as we go from shale over gas sand at the top of the trap to shale over brine sand on the flank of the anticline. There is also a change in impedance across the fluid contact since gas sand is lower impedance than brine sand. If the trap is above the DHI floor and the gas sand is thick enough, we would expect two (2) DHI signatures: (1) a high amplitude reflection off the top of the gas sand that decreases significantly at the edge of the field; and (2) a fluid contact reflection.

## Slide 11: Outline
What is a DHI?
Rock & Fluid Properties
DHI Analysis
DHI Characteristics
Predicting Seismic Responses
DHI Validity
Advanced Methods
Pitfalls
Notes: Before we look at these and other DHI characteristics, let’s briefly consider what we do for a DHI analysis.

## Slide 12: DHI Analysis
STOP
No
Yes
Modeling
Compare
Yes
Processing
Theory
Seismic Stack
Response
Seismic AVO
Response
Range of Possible
Geologic Models
Compare
Above DHI
Floor?
Interpretation
and DHI Rating
Rock Properties
Analysis of
Well Log Data
Zero Phase Stack
Q Comp
AVO Stacks
Pre-Stack Migrated
Gathers
Controlled Amplitude
and Phase Processing
of Seismic Data
If well data isn’t available, use analog or theoretical information.
Do I get the response I
expect at the well?
Notes: If we suspect our prospect has a DHI, or we want to make sure that our normal data processing has not obscured one, then we have some work to do. First, we want to understand the depth of the DHI floor relative to our prospect (top central column). If our prospect is above the DHI floor, then we can continue. One part of the work is to reprocess the seismic data in a DHI “friendly” manner (left column). We can also use rock and fluid property data from the basin to make some seismic models (right column). We will want to compare the reprocessed zero phase, full stack response to the modeled zero phase, full stack response (upper compare box; center column in yellow). If a model with oil or gas compares quite well to the reprocessed seismic, then my confidence in HC is increased.
We can then consider AVO – amplitude vs offset (topic of next lesson). If an AVO model with oil or gas compares quite well to partial stacks of the reprocessed seismic, then my confidence in HC has increased.

## Slide 13: Outline
What is a DHI?
Rock & Fluid Properties
DHI Analysis
DHI Characteristics
Predicting Seismic Responses
DHI Validity
Advanced Methods
Pitfalls
Notes: Let’s now look at what characteristics a DHI can have. There are seven (7) main characteristics that we look for. The more our prospect has, the merrier we are!

## Slide 14: DHI Characteristics
Hydrocarbon Indicators
  Amplitude Strength
  Impedance Signature
  AVO Response
  Evidence of Fluid Contact
    Flat Spot
    Polarity Reversal
    Abrupt Down-Dip Termination
    Fit-to-Structure
Other Indicators
  Chimneys
  Sag/Pull-Up
  Attenuation/Frequency
Presence of HC is marked by high reflection amplitudes
Notes: At the top of everyone’s list is Amplitude Strength. We’ve already talked about how HC-filled sands have lower impedance that brine sands or shales. Oil sands can have up to moderate amplitude strength. Gas sands can have very high amplitude strength.
People talk about “bright spots” when referring to anomalously strong amplitudes caused by the presence of HCs. You can also appreciate the need for “DHI friendly” data processing. If a processing step “balances” amplitudes if any way, anomalous values are reduced which could mask a DHI-related amplitude.

## Slide 15: Impedance Signature
Hydrocarbon Indicators
  Amplitude Strength
  Impedance Signature
  AVO Response
  Evidence of Fluid Contact
    Flat Spot
    Polarity Reversal
    Abrupt Down-Dip Termination
    Fit-to-Structure
Other Indicators
  Chimneys
  Sag/Pull-Up
  Attenuation/Frequency
Low-Impedance
Reservoir
Reflection Amplitude
Acoustic Impedance
Impedance
Low
High
Low-Impedance
Reservoir
Notes: If your data have been processed to get relative or true impedance, than you can look for low impedance anomalies. Not many data sets are processed to get impedance sections, so data are needed to check if this signature is rare. High amplitudes can be caused by an anomalously high impedance interval (e.g., a volcanic sill, cemented sandstones, carbonate interval). Thus, some “bright spots” have been drilled only to find high impedance rocks, not HCs. On this slide, there is a bright spot on the reflection amplitude section (upper). The impedance section (lower) confirms there is an anomalously low impedance interval that might indicate HCs.

## Slide 16: AVO Response
Hydrocarbon Indicators
  Amplitude Strength
  Impedance Signature
  AVO Response (Amplitude vs Offset)
  Evidence of Fluid Contact
    Flat Spot
    Polarity Reversal
    Abrupt Down-Dip Termination
    Fit-to-Structure
Other Indicators
  Chimneys
  Sag/Pull-Up
  Attenuation/Frequency
Zero
Offset
Near
Angles
Far
Angles
Top of Reservoir
Base of Reservoir
Reflection Amplitude changes as a function of Offset
The topic of the next lesson
Notes: In basins where the rock and fluid properties are “just right,” we can use the AVO (Amplitude vs Offset) response to evaluate the types of fluids in a prospect. In these “Goldilocks” basins, there are changes in seismic amplitudes as a function of reflection angle. These changes have different relationships for brine-, oil-, and gas-filled reservoirs. We’ll study this in some detail in the next lesson.
On the slide, we show three (3) traces. On the left is a zero offset modeled trace. In the center is a trace modeled for near angles (e.g., 5° to 15°). On the right is a trace modeled for far angles (e.g., 20° to 30°). Notice how the trough at the top of the reservoir and the peak at its base are more negative/positive left-to-right.

## Slide 17: Flat Spot
Hydrocarbon Indicators
  Amplitude Strength
  Impedance Signature
  AVO Response
  Evidence of Fluid Contact
    Flat Spot
    Polarity Reversal
    Abrupt Down-Dip Termination
    Fit-to-Structure
Other Indicators
  Chimneys
  Sag/Pull-Up
  Attenuation/Frequency
A change from a lighter to a denser fluid results in a reflector
A fluid contact will be flat in depth; it may not be perfectly flat in time
Flat Spot
www.geoexpro.com/exploration/westloppa/
Notes: There are four (4) indicators of a possible fluid contact. We have already discussed the possible change in impedance in a reservoir as the fluid type changes (e.g., gas to oil or brine). The first of these four (4) is a flat spot; a seismic reflection due to the impedance changes across the fluid contact. To be seen, the reservoir has to be thick enough given seismic resolution constraints, say 50 meters or more.
The image shows a flat spot at a Norwegian field. Note the black reflection, fairly flat, that cuts across the dipping stratigraphy.

## Slide 18: Polarity Reversal
Hydrocarbon Indicators
  Amplitude Strength
  Impedance Signature
  AVO Response
  Evidence of Fluid Contact
    Flat Spot
    Polarity Reversal
    Abrupt Down-Dip Termination
    Fit-to-Structure
Other Indicators
  Chimneys
  Sag/Pull-Up
  Attenuation/Frequency
Alistair Brown, 2010,
Search and Discovery #40514
Reservoir with HC is low impedance; with brine is high impedance
Top Reservoir
Peak
Trough
Notes: HC-filled sands are always low impedance relative to brine-sands and shales. In some cases, HC-sand is low impedance, but brine-sand has higher impedance than encasing shales. This means that the shale/HC-sand interface (top of reservoir) has a negative RC, but a shale/brine-sand interface has a positive RC.
In the displayed seismic line, a peak represents a –RC, and a trough represents a +RC. Thus, along the top of the reservoir sand there is a ‘polarity reversal’ – the top sand reflection changes from peak to trough. Thus, a likely explanation for a polarity reversal is that there has been a change in fluid type in a porous interval.

## Slide 19: Abrupt Termination
Top
Res.
Base
Res.
Abrupt Term. Amplitude
Hydrocarbon Indicators
  Amplitude Strength
  Impedance Signature
  AVO Response
  Evidence of Fluid Contact
    Flat Spot
    Polarity Reversal
    Abrupt Down-Dip Termination
    Fit-to-Structure
Other Indicators
  Chimneys
  Sag/Pull-Up
  Attenuation/Frequency
Amplitudes abruptly terminate downdip at a change in fluid contact
Notes: Another fluid contact indicator is an abrupt downdip amplitude termination, which is caused when shale and brine-sands have similar impedance, and so generate low amplitude reflections. HCs in the reservoir result in anomalous impedances and high RCs, so amplitudes are high where HCs are present.

## Slide 20: Fit-to-Structure
Hydrocarbon Indicators
  Amplitude Strength
  Impedance Signature
  AVO Response
  Evidence of Fluid Contact
    Flat Spot
    Polarity Reversal
    Abrupt Down-Dip Termination
    Fit-to-Structure
Other Indicators
  Chimneys
  Sag/Pull-Up
  Attenuation/Frequency
Amplitude anomaly conforms to a depth (TWT) contour
Notes: Since a fluid contact is almost always flat in depth, any HC indicator should conform to a specific depth contour. This amplitude map for the top of a sandy interval has some high amplitudes. The downdip extent of the amplitudes “fit” a particular depth contour.
If the seismic data is in units of TWT instead of depth, the “fit” to a TWT contour may not be so good. This is because some lateral velocity changes in the rocks above the reservoir (overburden) can distort the TWT representation of the reservoir top.
For our exercise example, there is a fluid contact at 1151 m. The anomalous amplitudes and fluid contact reflection are not “flat” in TWT.

## Slide 21: Seismic Chimney
Hydrocarbon Indicators
  Amplitude Strength
  Impedance Signature
  AVO Response
  Evidence of Fluid Contact
    Flat Spot
    Polarity Reversal
    Abrupt Down-Dip Termination
    Fit-to-Structure
Other Indicators
  Chimneys
  Sag/Pull-Up
  Attenuation/Frequency
www.stockhouse.com/BullboardsMessageDe...NX&t=list
Disruption of reflections above a leaky reservoir
Chimney
Notes: There are three (3) other indicators that are positive indicators of HCs, but with lower degrees of confidence. The first is a seismic chimney – a wide zone of poor reflection continuity and amplitude. This can be due to gas leaking into rocks above the reservoir, causing chaotic changes to the velocity/impedance values. Standard processing yields inaccurate velocities for the chimney zone and thus poor imaging.
The presence of a chimney is a good news – bad news situation. The good news is that HCs were generated and trapped, but the seal is letting gas out. The bad news is that the seal does leak and perhaps all the HCs are gone. The pessimist says the trap is breached and so we should not drill. The optimist says gas is leaking, which means more room in the trap for oil!

## Slide 22: Sag/Pull-Up
Hydrocarbon Indicators
  Amplitude Strength
  Impedance Signature
  AVO Response
  Evidence of Fluid Contact
    Flat Spot
    Polarity Reversal
    Abrupt Down-Dip Termination
    Fit-to-Structure
Other Indicators
  Chimneys
  Sag/Pull-Up
  Attenuation/Frequency
Presence of low-velocity gas sands delays time and attenuates high frequencies
Chimney
Sag
Sag
Notes: Since the velocities of a HC-bearing zone is different from other rocks, there can be a sag or pull-up on TWT sections associated with the presence of HCs. A sag means lower than normal velocities, so it takes longer for rays to travel down and back to the surface. A pull-up means higher than normal velocities, so it takes less time for rays to travel down and back to the surface. Most of the time, the presence of HCs results in lower than normal velocities, so a sag is more likely.
Various other things can alter the velocities along a seismic section, such as lithologic changes. Thus, sags and pull-ups have many causes, and do not increase our confidence in the presence of HCs too much. We want to see other DHIs in addition to sag before we can consider it a true HC indicator.

## Slide 23: Attenuation
Hydrocarbon Indicators
  Amplitude Strength
  Impedance Signature
  AVO Response
  Evidence of Fluid Contact
    Flat Spot
    Polarity Reversal
    Abrupt Down-Dip Termination
    Fit-to-Structure
Other Indicators
  Chimneys
  Sag/Pull-Up
  Attenuation/Frequency
Presence of low-velocity gas sands delays time and attenuates high frequencies
Low Freq
Notes: As seismic energy passes through a HC zone, it is attenuated more severely than through other rocks. This results in image degradation below thick HC zones. There is also more attenuation of high frequencies, so there can be a noticeable change in frequency below HCs. The peaks and troughs appear “fatter” (lacking mid and high frequencies).

## Slide 24: Outline
What is a DHI?
Rock & Fluid Properties
DHI Analysis
DHI Characteristics
Predicting Seismic Responses
DHI Validity
Advanced Methods
Pitfalls
Notes: We are working our way down the list. We can use seismic modeling to verify what type of seismic response to HC we should expect.

## Slide 25: Two Key Questions
At the depth that we are interested in within the study area, should we expect a distinct seismic response if hydrocarbons are present in porous zones?
  Should an amplitude anomaly be observed?
  Should an amplitude vs. offset (AVO) anomaly be observed? AVO is the topic of the next lesson
Notes: Let’s say that we are working in the western Gulf of Mexico, and are interested in Middle Miocene sands at depths of 2000 to 2400 m. For this area and this depth range, would we expect a distinct seismic response if hydrocarbons are present in porous zones? First, should I expect an amplitude anomaly? And, second, should I expect an amplitude vs. offset? AVO is the topic of the next lesson.

## Slide 26: A Well with a Water Wet Reservoir
Reservoir
Reservoir
A Modeled Seismic Trace – Reservoir fluid = Water
Notes: Perhaps we have a well near the area of interest with Mid Miocene sands that are filled with brine. We can generate a 1D seismic model – a synthetic trace.

## Slide 27: What If It Contained Oil in the Reservoir?
Fluid Substitution Modeling - Reservoir fluid = Oil
Reservoir
Reservoir
Notes: If I know something about rock and fluid properties in my area, perhaps from other wells, then we can edit the 1D model. We can assign the Mid Miocene sand the velocity and density of an oil sand, and generate a seismic trace for what the seismic response should be for and oil-filled sand. We call this a “pseudo-well,” a “what if” well.

## Slide 28: What If It Contained Gas in the Reservoir?
Fluid Substitution Modeling - Reservoir fluid = Gas
Reservoir
Reservoir
Notes: Similarly, we can give the Mid Miocene sand the velocity and density of a gas sand. Then, we can generate a seismic trace for what the seismic response should be for and gas-filled sand.

## Slide 29: Comparison of Seismic Responses
Fluid Substitution Modeling
Water
Oil
Gas
For this case, I would expect a change in amplitude if there is a change in reservoir fluids
Reservoir
Moderate
Trough
Top Reservoir
Very High
Trough
High
Trough
Pseudo Well
Pseudo Well
Real Well
Notes: Here are the three (3) models for the three (3) fluid types. The model on the left is a real well. The models in the center and on the right are pseudo wells. These are zero offset (normal incidence) models. You’ll see in the next lesson that we can also model seismic traces for different incidence angles.

## Slide 30: Outline
What is a DHI?
Rock & Fluid Properties
DHI Analysis
DHI Characteristics
Predicting Seismic Responses
DHI Validity
Advanced Methods
Pitfalls
Notes: Our next topic is DHI Validity.

## Slide 31: DHI Validity
  If your prospect has one or more DHI characteristics, you have to evaluate the validity of these as true HC indicators
  Three factors need to be considered:
    DHI Quality – how good does the DHI appear to be?
    DHI Confidence – how confident are you of the data?
    DHI Collaboration – how many types of DHI characteristics support the validity that HCs are present?
Notes:   If your prospect has one or more DHI characteristics, you have to evaluate the validity of these as true HC indicators. Three (3) factors need to be considered:
  1. DHI Quality – how good does the DHI appear to be?
  2. DHI Confidence – how confident are you of the data?
  3. DHI Collaboration – how many types of DHI characteristics support the validity that HCs are present?

## Slide 32: DHI Quality
  What is the quality of each DHI signature?
    Amplitude Strength
    Impedance Signature
    Amplitude vs Offset (AVO) – next lesson
    Anomaly Terminations
    Lateral Impedance Contrast
    Fluid Contact Reflection
    Conformance to structure
Notes: Let’s say that I have identified a Middle Miocene prospect in the western Gulf of Mexico. It has several DHI characteristics/signatures. We need to rate the quality of each DHI signature that we see – perhaps on a scale of 0 to 10.

## Slide 33: DHI Confidence
  What is your confidence in the data that forms the basis of the DHI?
    Well Calibration
    Physical Property Data
    Impedance Signature
    Seismic Data Type (2D or 3D and vintage)
    Seismic Data Quality
    Seismic Data Quantity
Notes: I’d also have to consider the quality of the seismic data that forms the basis of the DHI. Do we have one, or six or 20+ nearby wells that we can calibrate the seismic response for an oil, gas and brine sand? Do we have a reasonable about of velocity and density data for different lithologies and fluid-fills? Do we have some seismic data that has been converted to impedance sections? What type of seismic data do we have and how recent are the seismic data sets (assuming newer data has better quality)?
For example, my prospect has a few 2D lines from the 1980s and one 3D survey from 2008. What is the quality of each seismic data set, perhaps on a scale of 1 to 5? How much seismic do we have?

## Slide 34: DHI Validity
  Use the three (3) factors to risk DHI validity:
Radar Plot of DHI Validity
Amplitude
HC
Contact
Anomaly
Definition
Well
Calibration
Seismic
Quality
DHI Quality
DHI Confidence
High
Risk
Low
Risk
Quality vs Confidence Cross Plot
Notes: There are a number of ways we can display the information. We can cross-plot DHI quality versus DHI confidence to get at a relative prospect risk, and we can generate a radar plot to show the relative strength or weakness of different factors.

## Slide 35: Outline
What is a DHI?
Rock & Fluid Properties
DHI Analysis
DHI Characteristics
Predicting Seismic Responses
DHI Validity
Advanced Methods
Pitfalls
Notes: There are some other methods that are becoming more available.

## Slide 36: Using a Vp/Vs Ratio
In this display, green (low Vp/Vs) indicates good sand with HCs
Typical display where colors emphasize very negative amplitudes (low impedance)
www.cggveritas.com/default.a...07&lang=1
Notes: HC-bearing sands tend to have much lower Vp/Vs ratios than other rocks with brine. People are starting to process seismic data so that they display Vp/Vs ratios (right). An explorationist can then use Vp/Vs sections or Vp/Vs seismic volumes.

## Slide 37: Electromagnetic Mapping
www.britishborneo.com/contentnew_technology/
Very recent technology allows EM surveys to be acquired, processed and used to map subsurface resistivity as a means to verify the presence of hydrocarbons
Notes: Another new technology is electro-magnetic (EM) surveys. These data have to be acquired, processed, and interpreted. HC zones have high EM resistivity. The EM data is interpreted in conjunction with seismic data/seismic interpretation.

## Slide 38: Potential Pitfalls/False DHIs
Flat reflections may not be related to fluid contacts:
    Stratigraphy
    Multiples
Reservoirs with low gas saturation
Low impedance rocks can be mistaken for hydrocarbon sands:
    Coal
    Porosity higher than expected in water sands
Poor fit to structure can be ‘rationalized’ as being caused by stratigraphic (facies) changes
Polarity of the data is incorrect (‘bright’ amplitude is a high impedance zone)
Notes: This slide lists some pitfalls with DHI analysis – the things that can go wrong. For example, a company had two prospects: one has a large anticline in the Gulf of Mexico (GOM) with a flat reflector cutting across it, and the other has a large rotated fault block in the North Sea with a flat reflector cutting across it. This company drilled the first prospect and sands were filled with brine. A post-drill analysis revealed that the flat reflector was an artifact – a seismic multiple. Having been burned in the GOM by a flat reflector, they decided to sell the North Sea prospect. Wrong decision – this prospect turned into a major gas field. The flat reflector was a true gas-water contact.

## Slide 39: Summary
Seismic DHI’s are anomalous seismic responses related to hydrocarbon presence.
Acoustic impedance of a porous rock decreases as hydrocarbon replaces brine in pore spaces of the rock, causing a seismic anomaly (DHI).
The DHI signatures with the highest correlation to success are:
    Amplitude anomaly
    Fluid contact reflection
    Fit to structure
    Abrupt reflection terminations
Notes: Summary.

## Slide 40
Questions?