## Slide 1: Exercise 26a/b
Exer 26a/b: DHI Modeling
DHI Modeling
Your Task:
  Use Gulf of Mexico/North Sea data to calculate several reflection coefficients and the seismic responses for a shale-capped reservoir that has a gas cap and an oil leg.
Shale
Shale
Water
Oil
A
D
B
C
Gas
E
Notes: Title slide with main task.

## Slide 2: Steps 1, 2 and 3
1) Shale: V = 8000 ft/s; Density = 2.20 gm/cc
2) Water sand: V = 7800 ft/s; Density = 2.15 gm/cc
3) Oil sand: V = 7100 ft/s; Density = 2.11 gm/cc
4) Gas sand: V = 6400 ft/s; Density = 1.96 gm/cc
You are given data representative of an area
For example, Gulf of Mexico data:
You will calculate five reflection coefficients:
1) Shale over water sand RC = ________
2) Shale over oil sand RC = ________
3) Shale over gas sand RC = ________
4) Gas sand over oil sand RC = ________ GOC
5) Oil sand over water sand RC = _______ OWC
Notes: Exercise 26a uses velocities and densities for the Gulf of Mexico (shown). Exercise 26b uses velocities and densities for the North Sea (given in the exercise instructions). Given these values, first impedances are computed (step 2) and five (5) RCs are calculated (step 3).

## Slide 3: Draw Four Zero-Phase Wavelets
Shale
Shale
Water
Oil
A
D
B
C
Gas
E
Given the RCs and a wavelet at location A (shale over water sand), you will draw wavelets at B, C, D and E
Notes: Knowing the sign and magnitude for shale over water (brine) sand from step 3 – location A, draw a zero-phase wavelet for locations B, C, D and E.
HINT: If the sign of the RC at the four (4) locations is the same as at A, then the wavelet has the same polarity. If the sign of the RC at the four (4) locations is the opposite that at A, then the wavelet is flipped - opposite polarity. The magnitude (absolute value) of the RCs relative to the magnitude at A dictates the amplitudes at the four (4) locations.

## Slide 4: Exercise 26a/b
Questions?