## Slide 1: Exercise 27
AVA Analysis
AVA Analysis
Your Task:
  Use some information from a seismic gather to predict hydrocarbon fill levels (gas cap, oil leg, water leg) within a reservoir on a seismic line.

## Slide 2: Introduction
Below is a seismic profile across an anticlinal trap. There is evidence for at least one (1) fluid contact. Alternatively, this could be a false fluid contact (e.g., multiple, stratigraphic surface).
Can we use AVO or AVA data to be more quantitative in predicting the fluids in the target interval?

## Slide 3: An AVA Gather
www.apexgeophysical.com/avaanalysis.html
Notes: A move out corrected (flattened) gather. Note the increase in amplitude of the trough at the target reservoir TWT. Color transitions from yellow to red.

## Slide 4: Amplitude vs Angle for the Gather
Intercept = ________
Slope = ________
DEGREE | AMPLITUDE
4 | -20
8 | -35
12 | -49
16 | -65
20 | -79
24 | -94
28 | -109
32 | -123
36 | -138
0 4 8 12 16 20 24 28 32 36
-20
-40
-60
-80
-100
-120
0
-140
Notes: Table on left has nine (9) angle (degree) & amplitude pairs. The first data point is marked on the graph. Students mark the other eight (8) points and fit a straight line (line shown is not correct- just an example). Then, they determine the intercept and slope values.

## Slide 5: Modeled AVA Response
From regional well data and fluid substitution modeling
4
8
Intercept
Slope
0
-4
-8
0
-10
10
-20
Shale Baseline
Brine
Oil
Gas
Notes: An intercept versus slope display for data from nearby wells. Fluid substitution was used to model the AVA response had each well had the two (2) different fluid fill types, e.g., if the well encountered brine, what would have been the response if it had oil and the response if it had gas. Note the shale trend (brown line), the brine “cloud,” the oil cloud and the gas cloud. The segregation of the data on this plot allows us to reduce risk of predicting fluids in our target reservoir.

## Slide 6: AVA Analysis – Top of Reservoir
0
4
8
-4
-8
0
-10
10
-20
Shale
Brine
Oil
Gas
Intercept
Slope
From local seismic data
Notes: This plot shows the AVA response of real gathers from our 3D survey data. The shale, brine, oil and gas “clouds” are distinguishable. The colors are PREDICTED fluid types based on the well calibration shown on the previous slide.

## Slide 7: Predict the HC Distribution
Gather
Possible
Fluid
Contact
Top of
Reservoir
Notes: This is Figure 5 from the exercise without and then with the fluid predictions that are based on how the AVA response lies in the different “clouds” on the previous slide. Based on this figure, students predict the fluid distribution at the crest of this anticline.

## Slide 8
Questions?
Notes: Slide Ex-27.8