## Slide 1: Petroleum Geology & Geophysics
Amplitude vs. Offset
Rpp
Zero
Offset
Near
Offset
Far
Offset
Top of Reservoir
Base of Reservoir
Incident p-wave
Rps
f1
q
q1
Tpp
Tps
f2
q2
Vp2, Vs2, r2
Vp1, Vs1, r1

## Slide 2: Outline
What is AVO?
Why We Care
Difference between Offset and Angle
How We Measure AVO
AVO Classes
Summary
Notes: The list of five (5) main topics we will cover. The first topic: What is AVO?

## Slide 3: What is AVO?
We can take seismic data and process it to include all offsets (full stack) or select offsets (partial stacks)
For HC analysis, we often get a near-angle stack and a far-angle stack
The difference in amplitude for a target interval on near vs. far stacks can indicate the type of fluid within the pore space of a reservoir rock
AVO analysis examines such amplitude differences
If the AVO is due to HC in a reservoir, it is a type of DHI
AVO = Amplitude vs. Offset
Notes: A definition for what AVO stands for and some main points.

## Slide 4: Zero Offset – Reflection Coefficient
Surface
Layer A
Layer B
Zero-Offset Case
Receiver
Source
CMP Location
I =
I below – I above
I below + I above
Reflection amplitude is a function of the incident angle, θ
Notes: This reviews what we mean by zero offset: the source and receiver are in the same location. The angle of incidence, measured from the vertical, is zero.

## Slide 5: Non-Zero Offset – Reflection Coefficients
Layer A
Layer B
Non Zero-offset Case
q
Receiver
Source
CMP Location
Reflection amplitude is a function of the incident angle, θ
RC = fn (θ)
Notes: This slide shows one non-zero offset. Θ is the take-off angle; it is also the angle of incidence and the angle of reflection. The RC (reflection coefficient) is related to the change in impedance AND θ.

## Slide 6: Another Complication
A P-wave incident from above generates four (4) waves:
- reflected P-wave (Rpp)
- reflected shear (Rps)
- transmitted P-wave (Tpp)
- transmitted S-wave (Tps)
The amplitudes of the scattered waves depend on the elastic properties of the two media and the angle of incidence of the P-wave
Incident p-wave
Rps
Rpp
Tpp
Tps
Vp1, Vs1, r1
f1
f2
q
q1
q2
Vp2, Vs2, r2
Seismic waves are partitioned at an interface
V
p
= P-wave or compressional velocity
V
S
= S-wave or shear wave velocity
q
= Incidence angle
Notes: For non-zero offset, there are other complications. An incident P wave gets partitioned into P and S reflected energy and transmitted energy. These factors also effect amplitudes.

## Slide 7: Reflection Coefficient Approximation
Hilterman’s modification of
Shuey’s equation, 1994
Notes: Shuey is a geophysicist that worked up a “messy” equation for reflection amplitude. Hilterman simplified the high-order equation into this two-term equation. Note that R0 is the normal incident equation we talked about in Lesson 6 on Seismic Reflection; for normal incidence θ = 0 and cos (0) = 1.

## Slide 8: Why Do We Care?
Reflection amplitude varies with the incident angle, θ, in ways that are related to the physical properties above and below the interface
        Rock or lithologic properties
        Properties of the fluids in the pores
The generation of shear waves is also controlled by the fluid type
By examining variations in amplitude with angle (or offset), we may be able to unravel lithology and fluid effects at the top of a reservoir
Notes: All of this becomes important to us in that reflection amplitude as a function of θ can, in certain cases, tell us the type of fluid in a reservoir: brine, oil or gas. Thus, in these special cases, amplitude vs offset (or reflection angle) can significantly de-risk a prospect.

## Slide 9: Why Do We Care?
Zero
Offset
Near
Offset
Far
Offset
Top of Reservoir
Base of Reservoir
More NEGATIVE with Offset
More POSITIVE with Offset
Well
Data
Notes: Here we have a simple model for a HC-bearing reservoir. The top of the reservoir is marked by a trough and the base by a peak. Compare the modeled response for a near-offset trace with a far-offset trace. The trough associated with the top gets more negative from near to far (an increase in the negative value). The peak associated with the base gets more positive from near to far. We would say that at both the top and base of the reservoir there is an increase of amplitude with offset or reflection angle.

## Slide 10: Outline
What is AVO?
Why We Care
Difference between Offset and Angle
How We Measure AVO
AVO Classes
Summary
Notes: We have defined AVO and talked about why we care. Next, we need to explain the difference between offset and angle.

## Slide 11: Effect of Target Depth on AVO
Angle Range = 1 - 30°
CDP Location
Far
Source
Near
Source
Mid
Source
Far
Receiver
Near
Receiver
Mid
Receiver
Shallow
Deep
Mid
Notes: We’ll use this diagram to compare reflection paths for a shallow (yellow) and a deep (purple) interface. There are four (4) source points and four (4) receiver points for a common midpoint. For this depth, reflection angles can vary between 1 and 30°.

## Slide 12: Offset = Angle
Angle Range = 1 - 30°
CDP Location
Far
Source
Near
Source
Mid
Source
Far
Receiver
Near
Receiver
Mid
Receiver
Shallow
Deep
Mid
/
In General:
-
Angle range decreases as target depth increases
-
AVO resolution decreases as a target depth increases
Angle Range = 0.5 - 18°
Notes: Now we’ll consider the deep (purple) reflector. For this depth, reflection angles can vary between 0.5 and 18°. The main point here is that there is a difference between offset (distance between source and receiver) and reflection angle. The equations tells us that the angles are what we would want; offset is easier/cheaper to obtain.

## Slide 13: Important to Note
Based on the physics, we are more interest in AVA, amplitude versus angle, than AVO
In industry, we use these terms rather loosely
Very few talk about AVA, even when the data they are using is near ANGLE and far ANGLE
It is always good to clarify if a study is using AVO or AVA
0
1000
2000
3000
4000
5000
1000
2000
3000
4000
5000
6000
7000
8000
Offset (m)
Two way Time (ms)
5
5
5
10
10
10
15
15
15
15
20
20
20
20
25
25
25
25
30
30
30
30
35
35
35
35
40
40
40
40
45
45
45
45
50
50
50
50
55
55
55
55
60
60
60
60
60
65
65
65
65
65
70
70
70
70
75
75
75
80
80
80
0
1000
2000
3000
4000
5000
Offset (m)
1000
2000
3000
4000
5000
6000
7000
8000
Two way Time (ms)
5
5
5
10
10
10
15
15
15
15
20
20
20
20
25
25
25
25
30
30
30
30
35
35
35
35
40
40
40
40
45
45
45
45
50
50
50
50
55
55
55
55
60
60
60
60
60
65
65
65
65
65
70
70
70
70
75
75
75
80
80
80
Near
Far
Near
Far
True AVA
Mid
Mid
True AVO
Notes: In industry, we really want to subdivide our data by angle (right) rather than offset (left). We need to spend more time/money to get AVA data. In terms of terminology, AVA is seldom used. Often people speak of AVO analysis, even through they have data subdivided based on angle.

## Slide 14: Outline
What is AVO?
Why We Care
Difference between Offset and Angle
How We Measure AVO
AVO Classes
Summary
Notes: Our next main topic is how we measure AVO.

## Slide 15: How Do We Measure AVO?
CDP Gather: A Gas Reservoir
Time
Angle/Offset
AVO Curve
Amplitude
Angle/Offset
Straight Line Fit
Negative Intercept
Negative Slope
Near
Far
Near
Far
Notes: How do we measure/quantify amplitude versus offset or angle? We have to examine pre-stack data. We arrange traces for a CMP as a function of angle (preferred) or offset. We identify a reflection corresponding to the top (and base) of our possible reservoir - like the marked red line in a trough. Then we display the amplitude of this trough as a function of angle or offset. We fit a straight line (blue line) through the data points (red dots). Then we calculate the intercept and slope of the straight-fit line. Thus, we quantify an AVO response by two numbers, the intercept and the slope.

## Slide 16: AVO Attributes
We quantify the AVO response in terms of two (2) parameters:
  Intercept (A) - where the curve intersects 0º
  Slope (B) - a linear fit to the AVO data
Angle/Offset
AVO Curve
Amplitude
AVO Crossplot
AVO Intercept (A)
AVO Slope (B)
Gas
Oil
Water
For some reservoirs, the AVO response differs depending on whether the pore space is filled with gas, oil or water
Negative Intercept
Negative Slope
Shale
Notes: For any CMP, we can analyze the AVO and quantify the AVO response by the intercept (sometimes referred to as A) and the slope or gradient (sometimes referred to as B). Think of the equation of a line being y= A + Bx. This is important because we can get a separation of shales from water (brine) sands and from oil sands and from gas sands.

## Slide 17: Some Real Gathers
www.apexgeophysical.com/avaanalysis.html
Gather
1230
Gather
1250
Gather
1240
AVO
Curve
AVO
Curve
AVO
Curve
Reservoir Zone
shows amplitude
increase with offset
For the Reservoir Trough
Notes: Here is a display of three (3) CMP gathers. Note the red trough marked by the arrow on the right. For each gather, the trough amplitude goes from moderate (yellow) negative values to high (red) negative values. We say that these is an increase in (absolute value of) amplitude with offset. This is the type of AVO typically associated with the presence of HCs, in this case probably gas.

## Slide 18: Map of the AVO Attributes
www.apexgeophysical.com/avaanalysis.html
AVO Intercept and Slope Cross-Plot Results
AVO Crossplot
AVO Intercept (A)
AVO Slope (B)
Gas
Oil
Water
Shale
Distance
Notes: We can generate a map that represents, at each x,y location, the distance between the local AVO value is from the shale line.
- small distances (purple-blue-green) = shales to water sands
- moderate distances (yellow) = oil or thin gas sands
- large distances (red) = gas sands.
For this display, I would predict three (3) gas prospects for the mapped trough.

## Slide 19: A Key Question
At the depth that we are interested in within the study area, should we expect a distinct AVO response as a function of fluid fill?
  What is the AVO response for a brine sand?
  What is the AVO response for an oil sand?
  What is the AVO response for a gas sand?
  Are the responses distinguishable?
Notes: As we talked about for DHIs, we can use seismic modeling to determine what sort of seismic response in terms of AVO we expect at our depth of interest in our study area. Again, we need appropriate values for rock and fluid properties.

## Slide 20: We Can Build Reservoir Models
Reservoir
(Fluid
Substituted)
}
Distributions: Gaussian
Skewed Gaussian
Uniform
Triangular
Exact Value
Reservoir Conditions
  Pressure
  Temperature
Fluid Properties
  GOR
  API
  Specific Gravity
  Salinity
Fluid
Water Saturation
1-D Layer Model of
Elastic Parameter
(Vp, Vs, Density)
Statistical
Scatter
(Optional)
Thickness
% Sand
Porosity
Rock Layers
Rock Physics
= Allowed to vary
Overburden
(Not Fluid
Substituted)
Non-Reservoir
(Not Fluid
Substituted)
Notes: We build a 1-D model of many layers – usually several reservoir layers with non-reservoir above and below. We assign values for thickness, % sand and porosity for each layer – both reservoir and non-reservoir. Then we assign properties to fluids with the reservoir layers – typically a model with brine, a second model with oil, and a third model with gas. We have the computer vary these models by adjusting the rock and fluid properties using different types of property distributions (e.g., Gaussian).

## Slide 21: Modeling the AVO Response
Porosity
(21 - 31%)
Sand Percent
(36 - 58%)
Thickness
(22 - 38 m)
Generate N reservoir models using distributions of thickness, sand percent and porosity
(e.g., N = 5000)
Step
1
Notes: We might generate 5000 models using Gaussian distributions for rock properties.

## Slide 22: Model AVO Response
Perform fluid substitution in the reservoir layers (gas, oil, and brine)
Gas
Sands
Oil
Sands
Brine
Sands
Step
2
Notes: For these 5000 models, we will also vary properties of brine, oil and gas. Here we show three reservoir intervals with shales (brown) above, below and in between.

## Slide 23: Model AVO Response
Brine Models
Oil Models
Gas Models
Model
Response
Brine Models
Oil Models
Gas Models
Well Log
Response
Calibrate the model using a nearby or analog well, if available
Step
3
Notes: We want to test the validity of our modeling. We will use nearby wells and their log response to get actual rock and fluid properties. From these, we can get the AVO intercept and slope for real rocks in our basin (left). This example is from the Gulf of Mexico where we have a lot of nearby wells. We can compare our real data to our 5000 * 3 models (right). The “clouds” of points for brine, oil and gas sands are similar, so our models seem to be reliable.

## Slide 24: Outline
What is AVO?
Why We Care
Difference between Offset and Angle
How We Measure AVO
AVO Classes
Summary
Notes: Now we can talk about the five (5) classes or types of AVO responses.

## Slide 25: AVO Class 3
Full-Stack Zero-phase Response
CDP Gather Response
Top of Reservoir: A moderately negative value that becomes an extremely negative number with angle
Notes: The easiest to find and most reliable AVO response is what we call AVO Class 3. The top of the reservoir is a decrease in impedance, a negative RC. We see a –RC as a trough is this and the following examples. Other people may show a – RC as a peak, so beware. For Class 3, there is a significant increase in amplitude with angle (becomes more negative). The top of the reservoir (-RC) has a trough that “brightens” with angle, and the base of the reservoir (+RC) has a peak that “brightens” with angle.

## Slide 26: AVO Class 3
Primarily occurs in Tertiary unconsolidated sediments - e.g., GOM slope, offshore W. Africa
Sands have high porosity, usually above 28%
Sediment velocity on the order of 5100 to 8000 ft/sec
Anomalies are due to the presence of light oils and gas
P E A K
T
R
O
U
G
H
Notes: On an amplitude vs. angle plot, the amplitude at the top of the reservoir is negative at 0 angle (intercept) and becomes more negative as the angle increases (curves down – negative slope).

## Slide 27: AVO Class 2
Full-Stack Zero-phase Response
CDP Gather Response
Top of Reservoir: A near-zero negative value that decreases to a moderately negative value
Notes: A Class 2 AVO response has a small negative amplitude value at the top of the reservoir at zero angle or offset. There is a significant increase in amplitude with angle (becomes more negative).
Class 2 differs from Class 3 in that all the amplitudes are lower:
- the intercept is a small rather than a moderate negative number.
- the slope is negative for both and can be about the same value.

## Slide 28: AVO Class 2P
Full-Stack Zero-phase Response
CDP Gather Response
Top of Reservoir: A moderate positive value that decreases to zero and then becomes moderately negative (a phase change)
P
Notes: A Class 2P AVO response has a small to moderate positive amplitude value at the top of the reservoir at zero angle or offset. There is a significant increase in amplitude with angle (changes polarity from positive to negative numbers). The “P” in 2P reminds me that there is a polarity reversal.
Class 2 differs from Class 3 in that all the amplitudes are lower:
- the intercept is a small rather than a moderate negative number.
- the slope is negative for both and can be about the same value.

## Slide 29: AVO Class 2P
Primarily occur in Tertiary sediments – e.g., GOM shelf, Offshore W. Africa
Sediments are more consolidated (deeper) than those of Class 3
Sand porosity is between 23% and 28%
Sediment velocity > 9000 ft/sec
Anomalies can occur in a Class 3 regime if reservoir holds heavy or low API oil
P E A K
T
R
O
U
G
H
Notes: On an amplitude vs. angle plot, Class 2P has a small to moderate positive amplitude value at the top of the reservoir. As the angle increases, the RC passes through zero and becomes negative. Overall the amplitudes decrease in value as the angle increases (curves down – negative slope). On a full stack seismic section, there may be very little response at the top or base of the reservoir since positive values will cancel some of the negative values.

## Slide 30: AVO Class 1
Full-Stack Zero-phase Response
CDP Gather Response
Top of Reservoir: A very positive value that becomes less positive with angle
Notes: A Class 1 AVO response has a moderate to large positive amplitude value at the top of the reservoir at zero angle or offset. There is a significant decrease in amplitude with angle (a decrease in positive numbers).
For Class 1:
- the intercept is a moderate positive number.
- the slope is negative.

## Slide 31: AVO Class 1
Primarily occur in older Tertiary sediments – e.g., North Sea Basin
Main signature is amplitude dimming from flank to crest
Sediments tend to be more consolidated than those of Class 2 & 3
Sand porosity is in high teens to low 20’s
Sediment velocity > 10000 ft/sec
P E A K
T
R
O
U
G
H
Usually associated with a fluid contact reflection
Notes: On an amplitude vs. angle plot, Class 1 has a moderate positive amplitude value at the top of the reservoir. As the angle increases, the RC passes approaches zero. Overall the amplitudes decrease in value as the angle increases (curves down – negative slope).
On a full stack seismic section, there may be very little response at the top or base of the reservoir since positive values will cancel some of the negative values.

## Slide 32: AVO Class 4
Same as Class 1, but opposite impedance with amplitude diming onto structure
Can occur in young or older Tertiary sediments - e.g.
  A relatively high porosity gas sand (GOM), or
  An older sand under a marl (Offshore South America)
Sand porosity is variable
Sediment velocity is variable
P E A K
T
R
O
U
G
H
Usually associated with a fluid contact reflection
Notes: Class 4 is theoretically possible, but is rare in nature. A Class 4 AVO response has a moderate to large negative amplitude value at the top of the reservoir at zero angle or offset. There is a significant decrease in negative amplitude with angle (a decrease in negative numbers).
For Class 4:
- the intercept is a moderate negative number.
- the slope is positive.

## Slide 33: DHI/AVO Classifications
Full-Stack Zero-phase Response
Digitized AVO Response
CDP Gather Response
Exploration Strategy
Higher Risk
Compaction
P
Notes: This table summarizes the characteristics for Class 3, 2P and 1.

## Slide 34: AVO Classification
Alistair Brown, 2010, Search and Discovery #40514
Class 3
Class 1
Class 2P
Notes: This figure, from Alistair Brown, shows seismic examples of three (3) AVO responses.

## Slide 35: Using Visualization
An attribute that indicates HC (or just sand) can be ‘visualized’ with existing wells to size and develop a field
www.pdgm.com/products/reservoir-characterization/probe.aspx
Notes: This slide is an example where a certain type of DHI/AVO anomaly has been isolated in a 3D seismic volume and then visualized using software with a backdrop of an interpreted surface. Four (4) wells already tap into this field. This type of analysis and display can be used to size and develop a field.

## Slide 36: What Causes AVO/AVA: Summary
Zero-offset reflection coefficient (RC) is a function of the impedance contrast between any two (2) layers
Offset RC is a function of the impedance and Poisson’s ratio contrast between any two layers, as well as the incidence angle of the energy that strikes the interface
If the rock and fluid properties are all favorable, then an AVO analysis may be able to differentiate the fluid within a reservoir
Three classes of AVO response are recognized; the type of response is largely controlled by compaction state
Notes: Summary

## Slide 37
Questions?